## Slide 1: CMS Recovery systems
M. C. Arena, A. D’Auria, R. Guida, B. Mandelli
CMS Gas System Status meeting, 21/03/2024

## Slide 2: Overview - CMS Gas Recuperation
CMS CSC CF4 Recovery System  recuperate CSC exhaust mixture (Ar/CO2/CF4) and separate good quality CF4
CMS RPC R134a Recovery System  recuperate RPC exhaust mixture (R134a/iC4H10/SF6) and separate good quality R134a
Storage system for both plants to inject the recovered gas in variable proportion into the mixer along with the fresh gas

## Slide 3: CSC CF4 Recovery system

## Slide 4: CSC CF4 RECUPERATION Monitoring
Daily monitoring of the status of the recovery system (efficiency, pressures, status of absorbers)
Weekly analyses of the gas recovered and stored in the batteries  30-50 analyses, 4 hours (necessary to reach the stability of gas composition)
Monitoring of the batteries to schedule the swap for the CF4 recuperated injection in the mixer
  analyses of CSC mixer before and after the battery swap
  analyses of the battery used for the injection to calculate the right ratio in the final gas mixture
  100-150 analyses, 1-2 days for the procedure
  Calibration and monitoring of SWPC system in parallel
CSC mixture
Recovery Battery

## Slide 5: CF4 recovery plant Recuperation process
Phase 0  CSC gas mixture is injected in the first module of the recovery system from the Exhaust module
Phase 1  the gas passes through the membrane module optimized for the CO2 separation; CF4 is recovered at the retentate side with 15% of Ar, 0.4% of CO2 and 2% of N2
Phase 2  All the remained CO2 is absorbed in the MS 4Å
Phase 3  CF4 is absorbed in the MS 13X, N2 and Ar are vented and the CF4 is then recovered through pressure swing adsorption
Phase 4 (3b)  CF4 is extracted and stored in the battery, ready to be reinjected in the mixer
Ar ~ 10% CF4 ~ 89.6%
N2 ~ 0.4%
Plant operational since 2012, a lot of tuning and upgrades realized

## Slide 6: Gas separation techniques Membrane separation
selectivity
Permeability A
Permeability B
Ability of a membrane to separate two molecules
Separation process is driven by 
  Partial pressure gradient
  Nature of membrane (chemical structure)
  Permeability  capability of a membrane to permeate gas molecules
  Solubility thermodynamic parameter given the amount of penetrant absorbed by membrane
  Diffusivity  dependent on geometry of penetrant: if molecular size increases the coefficient decreases
Notes: Aggiungere absorber

## Slide 7: CF4 recovery plant R&D Membrane module
 | Model | Working flow | Specifications
Membrane 1 | CO-C10 | Up to 300 l/h | High thickness and density gradient
Membrane 2 | CO-C10A | Up to 300 l/h | High thickness and density gradient
Membrane 3 | CO-C10A | Up to 300 l/h | High thickness and density gradient
Membrane 4 | CO-410A | More than 600 l/h | High thickness and density gradient
Memb. Highly sensitive | CO-C07FS | Up to 300 l/h | Reduced thickness and density gradient
=
Ar fraction in retentate stream is a contamination of our recuperate gas  C07FS not good for our purpose

## Slide 8: Gas separation techniques Thermal Swing Adsorption & Pressure Swing Adsorption
ABSORPTION
DESORPTION
PRESSURE SWING ADSORPTION (PSA)  contaminated feed stream is fed to the sieve beds at high pressure and then the sieve bed pressure is reduced to regenerate the MS and remove adsorbent contaminants. Vacuum regeneration has the advantage of not overheating the material, avoiding break down processes.
Schematic view of an absorber module of gas system
MS 3A
MS 4A
MS 5A
MS 13X
Structure model of 4Å molecular sieve
Notes: Aggiungere absorber

## Slide 9: CF4 recovery plant Recuperation batteries
Problem with pump module
2023-2024 average composition of the battery
Ar 11% CF4 88% N2 1.9%
O2 0.2%
Problem with pump module
The N2 concentration is reduced by a factor 10 in the recuperation system
Considering that CF4 (10% in the CSC mixture) is injected 50/50 fresh/recuperated, the N2 reinjected in the mixer is of the initial concentration

## Slide 10: CF4 recovery plant Recuperation summary
Efficiency mean value: 70% in the period January-November 2023, (higher than 2021 and 2022, 65% and 51% respectively)
In 2023, out of 358 m3 of CF4 injected into the mixer, 242 m3 were recovered CF4 (70%)
2023  300m3 and 60kCHF saved
2012  42m3
The CF4 recuperation system is also important to overcome possible CF4 shortage  in 2023 no fresh CF4 available

## Slide 11: CSC CF4 RECUPERATION Status & Plans
Smoothing of input flow from Exhaust module to improve the membrane separation
New membranes to test for the CF4 separation: 1. new polyimide membrane 2. carbon nanotube membrane 3. zeolite membrane
Code upgrading for the CF4 Absorber module (now Col 1 does more cycles than Col 2)
New compressor for Battery module

## Slide 12: RPc R134a Recovery system

## Slide 13: RPC R134a RECUPERATION Monitoring
Daily monitoring of the status of the recovery system (efficiency and status of the 4 columns)
uGC analyses of the gas recovered and stored in the bottle perfomed twice per week  30-50 analyses, 3 hours (necessary to reach the stability of gas composition)
Monitoring of the quality of the gas extracted by each column through uGC analysis check of the efficiency for the single column(30-50 analyses)
R&D
Lot of parameters still need to be tuned 
  New Huber installed changed the equilibrium of the system
  Daily tests to find the new best configuration (since beginning of February 2024)

## Slide 14: Gas separation techniques Distillation
Purification method to separate 2 or more compounds based on differences in boiling points or volatility
The composition of vapor phase depend on the initial one of the liquid phase  lighter (lower-boiling) component tend to concentrate in vapor phase heavier (higher-boiling) component tend toward the liquid phase
Simple distillation  Can be used when the components have widely different boiling points (>100˚C)
Fractional distillation  Fractionating column allows for many successive distillations to take place at once. It contains packing material with lots of surface area. The vapours temporarily condense on these surfaces and the heat of the distillation allows those pools of liquid to vaporize again. Every vaporization-condensation event (called a "theoretical plate") is like a simple distillation, and each event enriches the distillate in the lower boiling component.
Typical liquid-vapor plot
Minimum boiling point azeotrope
Notes: Aggiungere absorber

## Slide 15: RPC R134a RECUPERATION Plant Overview
ELECTRICAL RACK
SEPARATION MODULES
CHILLER
COMPRESSOR
New system installed in April 2023 and tests started in May 2023
Goal: to recover the R134a from the mixture R134a/SF6/iC4H10
Problem: R134a forms an azeotrope with iC4H10
2 racks for the separation columns, 2 columns each
The system was designed to work both in series and in parallel
The plant was designed following the tests done between 2020 and 2022

## Slide 16: RPC R134a RECUPERATION Separation process
Chart: T-xy @ 1 bar
| 0 | 0.16459299999999999 | 0.28070699999999998 | 0.36488599999999999 | 0.427423 | 0.474881 | 0.51154599999999995 | 0.54029000000000005 | 0.56313299999999999 | 0.58135700000000001 | 0.59607699999999997 | 0.60799400000000003 | 0.61766500000000002 | 0.62549900000000003 | 0.63186900000000001 | 0.63699099999999997 | 0.64108799999999999 | 0.64431899999999998 | 0.64684600000000003 | 0.64873499999999995 | 0.65017400000000003 | 0.65116399999999997 | 0.65180700000000003 | 0.65193100000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65203699999999998 | 0.652721 | 0.65381800000000001 | 0.65543399999999996 | 0.65769699999999998 | 0.66075899999999999 | 0.66480799999999995 | 0.67007099999999997 | 0.67683400000000005 | 0.68545299999999998 | 0.696384 | 0.71021199999999995 | 0.72770199999999996 | 0.74986600000000003 | 0.77805400000000002 | 0.81410400000000005 | 0.86054299999999995 | 0.920879 | 1
Bubble curve | -12.26 | -16.2697 | -19.5586 | -22.1584 | -24.226 | -25.8791 | -27.2066 | -28.2756 | -29.1394 | -29.8341 | -30.3934 | -30.8433 | -31.203 | -31.4868 | -31.7139 | -31.8893 | -32.0246 | -32.1269 | -32.2015 | -32.2548 | -32.293 | -32.3173 | -32.3319 | -32.3345 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3348 | -32.3349 | -32.333 | -32.3271 | -32.3147 | -32.2925 | -32.2565 | -32.2011 | -32.1199 | -32.0045 | -31.8443 | -31.6262 | -31.3335 | -30.9452 | -30.4349 | -29.7691 | -28.9055 | -27.7913 | -26.3612
Dew curve | -12.26 | -16.2697 | -19.5586 | -22.1584 | -24.226 | -25.8791 | -27.2066 | -28.2756 | -29.1394 | -29.8341 | -30.3934 | -30.8433 | -31.203 | -31.4868 | -31.7139 | -31.8893 | -32.0246 | -32.1269 | -32.2015 | -32.2548 | -32.293 | -32.3173 | -32.3319 | -32.3345 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3348 | -32.3349 | -32.333 | -32.3271 | -32.3147 | -32.2925 | -32.2565 | -32.2011 | -32.1199 | -32.0045 | -31.8443 | -31.6262 | -31.3335 | -30.9452 | -30.4349 | -29.7691 | -28.9055 | -27.7913 | -26.3612
Azeotrope  mixture that exhibits the same concentration in the vapor phase and the liquid phase. This contrasts with ideal solutions with one component typically more volatile than the other
Slow heating of liquified azeotrope (blue curve) allows to enrich the liquid of R134a and the vapor phase of iC4H10
Thermodynamic simulation done by M. Bruno (PoliTO)
Vapor&liquid
Vapor&liquid

## Slide 17: RPC R134a RECUPERATION Plant Overview
Heat exchangers
Top Buffers
Bottom Buffers
Optimal conditions:
  Filling rate  200 l/h up to 600 l/h Chiller Temp.  -36.2°C Top buffer P  10 mbar (C1&C2), 35 mbar (C3)
  Bottom buffer T  20°C Emptying rate  600 l/h (air)
80% of Recuperation Efficiency
Compressor module
FLAMMABLE EXHAUST

## Slide 18: RPC R134a RECUPERATION Software
Dedicated mixer line for R134a recuperated

## Slide 19: RPC R134a RECUPERATION Recuperated R134a Quality
More than 70 tests were performed to find the best parameters for the plant
Now new tests required to obtain the same conditions with new chiller
Now we are injecting 15% of recuperated R134a in the RPC gas mixture  40 ppm iC4H10

## Slide 20: RPC R134a RECUPERATION Status & Plans
DONE 
New cooling unit Huber installed
Recuperation system works with an input flow up to 500 l/h
NEXT
Tests ongoing to find the best temperature with the new chiller
Evaluation of parallel vs series cooling on the next plant
Buy spare chiller

## Slide 21: RPC R134a RECUPERATION New SF6 recuperation plant
SF6: 0,126 ISOBUTANE: 0,22
FREON: 0,62
N2: 0,04
SF6: 0,00189
ISOBUTANE: 0,85
FREON: 0,148
N2: 8,32-09
SF6: 0,013
ISOBUTANE: 0,7934
R134A : 0,19
N2 : 0,0036
SF6 : 0,591
ISOBUTANE : 1,27 E-10
R134A : 0,00022
N2: 0,408
SF6: 0,075
ISOBUTANE: 0,240
R134a: 0,684
N2: 1,23 E-13
Two distillation columns for reasonable reflux ratio (from 140 to 20/20)
output mixture composition:
59% SF6 , 40% N2, 1% freon + residue of isobutane
 Easier to separate in the second stage with a membrane or a MS that are more selective for SF6  test ongoing
Studies on SF6 solubility in R134a ongoing

## Slide 22: Conclusions
CSC - CF4 Recuperation Plant
  Recuperation efficiency ~ 70% reached in the last year (after completion of intense R&D activity done in 2020-2021)
  Plant operational at design condition recuperation + injection of recuperated CF4
  in few occasions recuperated CF4 allowed to overcome problems with standard CF4 fresh supply RPC - R134a Recuperation plant
  Recuperation efficiency ~ 80% Recuperated R134a of good quality
Improvements still necessary to reach operation requirements