Impedance and beam stability considerations
D. Amorim, E. Kvikne, E. Métral
Thanks to F. Batsch, J. S. Berg, F. Boattini, L. Bottura, X. Buffat, C. Carli,
A. Chancé, H. Damerau, M. Gast, A. Grudiev, I. Karpov, T. Pieloni,
D. Schulte, K. Skoufaris, L. Thiele
MuCol mini-workshop on RCS pulsed magnets and powering
CERN, 2024-05-14
This work was performed under the auspices and with support from the Swiss Accelerator Research and Technology (CHART) program (www.chart.ch).
Funded by the European Union (EU). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

---
Contents
- Introduction
- Impact of RF cavities
- Impact of normal conducting magnets beam pipe
- Summary and relevant topics for impedance and transverse beam stability

---
Contents
- Introduction
- Impact of RF cavities
- Impact of normal conducting magnets beam pipe
- Summary and relevant topics for impedance and transverse beam stability

---
Simulation setup for transverse beam
stability studies
- Bunch tracking through the RCS chain
- Check the transverse emittance at the end of the chain (ejection of
  RCS 4) versus at injection of RCS 1
- Can include impedance effects, transverse damper, chromaticity...
66 turns
55 turns
17 turns
55 turns
RCS 3
750 -1500 GeV
10 km
RCS 4
1.5 -5.0 TeV
35 km
RCS 1
63 – 313 GeV
6 km
RCS 2
313 - 750 GeV
6 km

---
Beam and machine parameters for the RCS
Machine parameters	Unit	RCS 1	RCS 2	RCS 3	RCS 4
Circumference	m	5990	5990	10700	35000
NC magnet length	m	3655	2539	4366	20376
Bunch intensity	1012	2.7	2.7	2.7	2.7
Beam momentum	GeV/c	63	313.8	750	1500
Energy increase per turn	GeV	14.7	7.9	11.3	63.6
Rev. frequency	kHz	50	50	28	8.6
RF frequency	MHz	1300	1300	1300	1300
Harmonic number		25957	25957	46295	151433
RF voltage	GV	20.9	11.22	16.1	90.0
αp		0.0024	0.0024	0.001	0.001
Avg. beta x/y	m	50 / 50	50 / 50	50 / 50	50 / 50
Chromaticity Q’x/Q’y		scan	scan	scan	scan
Detuning from octupoles x/y	m-1	0 / 0	0 / 0	0 / 0	0 / 0
Beam parameters	Unit	Value
Bunch length 1σ	mm	5.7
Bunch intensity	Particles per bunch	2.7e12
εx / εy	μm rad	25
# of macropaticles		400k
# of turns wakefield		5
# of slices wakefield		2000
Parameters from F. Batsch RCS tables

---
Example of start-to-end simulations
Chromaticity Q’ = 0, reduced impedance
Initial transverse offset = 1 mm at each machine injection
A 20-turn transverse damper is included in each ring (at station #9)
Transverse kick at injection is clearly visible
Damper effect as well

---
Example of start-to-end simulations
Chromaticity Q’ = 10, nominal cavities impedance
No initial transverse offset
A 20-turn transverse damper is included in each ring (at station #9)
We will look at the emittance growth ratio
ε(end of RCS 4)/ε(start of RCS 1)

---
Contents
- Introduction
- Impact of RF cavities
- Impact of normal conducting magnets beam pipe
- Summary and relevant topics for impedance and transverse beam stability

---
RCS parameters
- Impedance model for this study: RF cavities
  High Order Modes (HOMs) only
  - Single cavity: Low Loss TESLA type cavity, all transverse HOMs included.
    Assume all HOMs have Q=105. (see https://accelconf.web.cern.ch/p05/papers/tppt056.pdf)
  - Multiply by the number of cavities: there are (700, 380, 540, 3000) cavities in (RCS1, RCS2, RCS3, RCS4)
- Main assumptions for the RCS are
  - 32 RF stations in each machine
  - One transverse damper unit, located at RF station 9 (~¼ of the ring)
- Scan several parameters
  - Chromaticity Q’ from Q’=-20 to Q’=+20
  - Damper gain from 4-turn to 100-turn + no damper
  - Initial transverse offset of the bunch (in each RCS), from 1 μm to 1 mm

---
Results of scans versus positive chromaticity
Chain of 4 RCS (up to 5 TeV)
Large emittance growth (ratio > 10)
No emittance growth (ratio=1)

---
Results of scans versus positive chromaticity
Chain of 4 RCS (up to 5 TeV)
Strong damper (4-turn)
No damper

---
Results of scans versus positive chromaticity
Chain of 4 RCS (up to 5 TeV)
1 mm initial offset in each RCS
No initial transverse offset

---
Results of scans versus positive chromaticity
Chain of 4 RCS (up to 5 TeV)
- Withe the nominal HOMs, a strong damper, 4-turn to 10-turn range, combined with chromaticity Q’=20, are required to stabilize the beam
- The admissible offset is reduced to 1 μm level

---
Example of start-to-end simulation with RCS 4
Chromaticity Q’ = 20
No initial transverse offset
A 50-turn transverse damper is included in each ring (at station #9)
The instability clearly starts in RCS4

---
Reducing the R/Q of the modes
- Here the full impedance model is scaled by a factor 0.5 → like dividing the R/Q of every mode by 2
- We recover transverse coherent stability with larger offset

---
Contents
- Introduction
- Impact of RF cavities
- Impact of normal conducting magnets beam pipe
- Summary and relevant topics for impedance and transverse beam stability

---
Normal conducting magnets beam pipe
Iron yoke
- Normal conducting magnets have a very high ramp
  rate O(4.2 kT/s)
- Power loss from eddy currents scales as
  - Ḃ the ramp rate, a the chamber thickness
- In a continuous metallic pipe, large eddy current losses would be induced (see E. Kvikne presentation)
- Possible solution is to use a striped design for the RF shielding, with an insulating substrate
Ceramic
30mm
RF shield
100mm
Study and slides by E. Kvikne
P \propto \dot{B}^2 a^3

---
RF-Shield on the Inside of Insulating substrate
Iron yoke
- Copper stripes modeled as a thin cylindrical layer.
- For simplicity, the magnet is modeled as an infinitely thick layer of copper.
- We use IW2D to compute the impedance and scan over different copper thicknesses to find the amount of copper needed to provide the beam with sufficient RF-shielding.
- The inner radius is kept constant at 10mm while the ceramic thickness is set to 5mm.
Ceramic
30mm
RF shield
100mm
Impedance model
5mm
10mm
Study and slides by E. Kvikne
Copper
Ceramic

---
Beam Coupling Impedance
Transverse dipolar impedance of 1m of beam pipe
- In presence of a dielectric, large resonances appear in the impedance, at ~2 GHz and above
- A very thin (~nm) layer of copper can reduce these resonances
  - This effect is explained by Zotter on page 168 in “Impedances and Wakes in High Energy Particle Accelerators”
- Increasing the thickness of the copper layer to 10 μm can suppress these high frequencies resonances.
Study and slides by E. Kvikne

---
Stability simulation results up to RCS 4
- Impedance model: normal conducting beam pipe only
- A copper thickness of 10 μm is sufficient to keep the beam stable for all chromaticities (Q’ ranging from -20 to 20), as long as the initial offset at the entrance of each RCS is less than 1mm.
- Additionally, this implies that any copper shield thicker than 10 μm will also provide sufficient RF-shielding.
100 nm copper thickness
10 um copper thickness
Study and slides by E. Kvikne

---
Contents
- Introduction
- Impact of RF cavities
- Impact of normal conducting magnets beam pipe
- Summary and relevant topics for impedance and transverse beam stability

---
RF cavities: summary and relevant topics
for impedance
- Studies assume the Low Losses TESLA cavities.
- The HOMs have a strong impact on transverse beam stability, in particular in RCS 4
  - Mitigation measures are required, such as chromaticty + transverse damper,
    or HOMs shunt impedance reduction (a factor 2 at least)
- The list of HOMs can evolve and be updated in the model
- Relevant topics for impedance
  - Integration of RF in the machine: number of RF stations, transition design
  - RF cavity and HOM coupler design: R/Q and Q factor of HOMs, number of cavities

---
Magnets: summary and relevant topics
for impedance
- Normal conducting magnets
  - Around 2/3 of the total magnet length → can be a large impedance source
  - This is a first iteration on the vacuum chamber design considering eddy current and impedance effects
  - Relevant topics for impedance
    - Beam pipe geometry and materials
    - RF shielding for impedance effects
    - Continuity of the RF shielding: transitions between NC and SC magnets, aperture changes
- Superconducting magnets
  - Not yet included in the impedance model
  - Relevant topics
    - Beam pipe geometry and materials, operating temperature
    - Muon decay shielding

---
Thank you !
Funded by the European Union (EU).Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

---
References
- D. Amorim, Collective effects and start-to-end simulations, IMCC and MuCol annual meeting 2024
- D. Amorim, Stability thresholds of first RCS stage for resonator wakefield,
  9th HEMAC meeting
- E. Kvikne, Impedance Study of the RCS Normal Conducting Beam Pipe, to be presented at design meeting
- E. Kvikne, Eddy currents, IMCC and MuCol annual meeting 2024
- F. Boattini et al., Resistive magnets design and analysis baseline, IMCC and MuCol annual meeting 2024
- L. Thiele, RF parameters in the high energy acceleration chain, IMCC and MuCol annual meeting 2024
- M. Gast, Magnet and power converter optimization, IMCC and MuCol annual meeting 2024

---
Normal conducting magnets chamber impedance

---
Ceramic pipe with RF-shield on the outside
Design 1: Ceramic pipe with RF-shield (M. Kinsho)
- As per the Tentative parameter report the NC magnet aperture is 30x100mm.
- Beam pipe design for impedance computation:
  - Inner radius of 10 mm
  - Ceramic thickness of 5 mm
  - Varying thickness of copper used in calculations
5mm
10mm
Study and slides by E. Kvikne
Copper
Ceramic

---
Comparison of Beam Pipe and Cavity Impedance for RCS2
- The resonances caused by the ceramic are significantly larger than the ones from the cavities.
- Given that the resonances from the beam pipe are ~10x greater than those from the cavities, a stable beam is not achievable with this design.
Beam pipe length: 2539 m (NC magnet length)
Number of cavities: 374
Study and slides by E. Kvikne

---
Impact of TESLA cavities, with 3 RCS (63 GeV to 1.5 TeV chain)

---
Results of scans versus chromaticity
- Positive chromaticity is required to stabilize the beam, at least Q’=+15
- The transverse damper is not required for high chromaticities
- An initial transverse offset can be tolerated, up to 10-100 μm

---
Reducing the R/Q of the modes
- Here the full impedance model is scaled by a factor 0.5 → like dividing the R/Q of every mode by 2
- More relaxed situation: chromaticity can be reduced to Q’ > ~0
- An initial transverse offset can be tolerated, up to 10-100 μm

---
Summary for three RCS
	Positive Q’	Negative Q’
Nominal R/Q of the HOMs	Q’>15 + any damper offset up to 100 μm	Always unstable
Half R/Q of the HOMs	Q’>0 + any damper / Offset up to 100 μm	Q’< -15 + 4-turn damper Offset up to 100 μm

---
Summary for four RCS
	Positive Q’	Negative Q’
Nominal R/Q of the HOMs	Q’>15 + 10-turn damper offset up to 1 μm	Always unstable
Half R/Q of the HOMs	Q’>0 + any damper / Offset up to 100 μm	Q’< -15 + 4-turn damper Offset up to 100 μm