## Slide 1: Progress on the Magnetic Design of Superconducting Dipoles in Acceleration Stage
, , ,

## Slide 2: Accelerator Superconducting Magnets
Parameters
10 T at the center
Rectangular aperture 30 mm x 100 mm
Field quality in good field region TBD (ex. ) units
Considerations
Attempt to use uniform technology throughout the collider complex
  HTS windings (for robustness)
  High current density (for cost reasons)
  Operation at high temperature (for energy efficiency)
Parameter | Unit | 
Minimum central field | T | 10
Free aperture (height x width) | mm2 | 30x100
Field Quality limits | units | 10, 50 ( to be iterated with beam physics )
Field quality homogeneity (B1 change) | % | 
Good Field region (height x width) | mm2 | 10 mm x 20 mm
Operating temperature |  | TBD
HTS tape dimensions |  | 12 mm x ** mm
Magnet length |  | 
Parameter | Unit | 
 | T | 10
Free aperture (height x width) | mm2 | 30x100
Field Quality limits | units | 10, 50 ( to be iterated with beam physics )
Field quality homogeneity (B1 change) | % | 
Good Field region (height x width) | mm2 | 10 mm x 20 mm
Operating temperature |  | TBD
HTS tape dimensions |  | 12 mm x ** mm
Magnet length |  | 

## Slide 3: Overlap
  10 T at 20 K, 10 K margin
  Rectangular aperture 50 mm x 80 mm
  Field quality better than 1.5%
  Straight section length: 550 mm
  Conductor volume / m (straight sections): 0.0154
[1] Design and Plan of a 10 T HTS Energy Saving Dipole Magnet for the Italian Facility IRIS, MT-28
CEA-CERN HFM collaboration
  Demonstrator of metal-insulated ReBCO high field magnet coils

## Slide 4: IRIS 10 T energy saving Dipole ESMA
6 stacks of 12 mm tape pancakes
9 mm gaps for field quality
Metal insulated (SS) (not NI because of long ramp up time)
1.5 % field quality (150 units)
No Iron because it limits the optimal field quality to one field value – this magnet must be used at range of field values
5/15/2024
Initial Magnetic Design of Accelerator SC Dipoles
4
a
9 mm
12 mm
[1] L. Rossi and others, "Design and Plan of a 10 T HTS Energy Saving Dipole Magnet for the Italian Facility IRIS," in IEEE Transactions on Applied Superconductivity, vol. 34, no. 5, pp. 1-6, Aug. 2024, Art no. 4602406, doi: 10.1109/TASC.2024.3355357
Thank you to discussions with those who designed the dipole magnet ESMA (Lorenzo B., Stefano S., etc.)
structural
housing

## Slide 5: Conceptual Design (Reminder: previously ruled out more complex geometries)
Reference: IRIS - https://indico.cern.ch/event/1220254/contributions/5270734/attachments/2607808/4507319/REBCO%20I.FAST%20CCT%20&%20IRIS%2010%20T%20HTS%20dipole%20at%20INFN.pdf
2.1 Flat RT coils in midplane, with return leg on external part
2.2 Cloverleaf winding (novel)
Add construction complexity
Limited advantages (see [1])

## Slide 6: Radial Build
Important for defining space for magnets
Novelli, Daniel, et al.

## Slide 7: Magnet Design Status
100 mm
30 mm
1
2
3
A
B
B [T]
Ongoing conceptual design: two approaches taking place:
  Numerical optimization routine looking at conductor volume, field quality (w/o iron) and critical current density limit
  Optimization in ROXIE including Iron
First Goals:
Optimization study on possible configurations as a function of cost, field quality, and complexity (number of racetracks, uniformity..)
Mechanical analysis
MN
MN
Previously, single stacks of conductor were investigated in terms of cost, with some mechanical analysis (Annual Meeting)

## Slide 8: Field Quality Calculation (Updated Values)
Update: good field region 20 mm in x, 10 mm in y (roughly 6 beam)
-10 mm
-5 mm
+5 mm
+10 mm
+15 mm
-15 mm
Credit and thanks to Lisa Soubirou
Current assumption before update: 50 mm in x, 20 mm in y

## Slide 9: Numerical Optimization Routine
An approach to best optimize field quality and cost
Input constraints:
  Search resolution
  Space the RTs can exist in
  RT constraints (minimum length in x, thickness in y (12 mm))
  Current Density (<700 A/mm2)
Limitations: does not include Iron
30 mm
100 mm
  Racetrack Model 2D and 3D

## Slide 10
Establish grid where RT pancakes are allowed to exist (Ex. 2 mm dx dy)
Calculate field contribution from all grid elements
Create all unique configurations of 2, 3, 4, 5, and 6 pancakes
Numerical Optimization Routine - Method

## Slide 11
Numerical Optimization Routine - Method
A look at the contributions to higher order terms in this space

## Slide 12
T, Field quality < 10 units, 10 mm radius
Fixed to have same inner radius, but not length, and max distance apart of 16 mm
9k solutions (for previous grid shown, J < 700 A/mm2)
Numerical Optimization Routine – Example: 2 racetracks
x [m]

## Slide 13
Numerical Optimization Routine – Example: 2 racetracks
COMSOL or ROXIE
Full stress, critical current and field calculations
1.
2.

## Slide 14
Numerical Optimization Routine – Example: 2 racetracks
Goal

## Slide 15
T, field quality < 10 units, 10 mm radius
First 2 racetracks fixed to be the same, with a 10 mm gap. 3rd racetrack explored at a + 16 mm and +32 mm gap. Min length of 30 mm.
52k solutions (for previous grid shown, J < 700 A/mm2)
Numerical Optimization Routine – Example: 3 racetracks

## Slide 16
To investigate further to understand advantages/disadvantages compared to 2 racetracks, etc.
1.
2.
Goals going forward: finish study considering up to 6 racetracks, considering cost, field quality (*Updated), and engineering complexity Integrate with ROXIE simulations.
Numerical Optimization Routine – Example: 3 racetracks