## Slide 1
MuColl Target meeting 7th March 2024
Study of the spent proton beam extraction channel
J. Mańczak, D. Calzolari, A. Lechner

## Slide 2: 3 main concepts for the proton extraction
Concept 1
Concept 2
Double Chicane
The focus of this presentation is Concept2
This option gives the best platform for the spatial separation of the spent proton beam after the extraction
Concept 1, even though is the simplest, requires wide chicane aperture which might become costly in terms of keeping the desired field strength

## Slide 3: Concept 2 investigated
Parameters in the model:
- Bending radius
- Opening angle
- First half aperture
- Second half aperture
- Relative shift between the
two halfs
- Magnetic field / current density
in each coil
Current densities in the solenoid magnets have been fitted with the MINUIT2 minimizer to achieve 1.5T along the center line of the chicane
Long straight element with a fixed current density to stabilize the field at the of the chicane
This increase in the field strength comes from the fact that the current densities in the tapering magnets were not varied in the fit. The attempt to include just the last magnet did not improve the result.

## Slide 4: Chicane parameter adjustment
Spent primary protons with E > 4 GeV
Geometry prepared for a straight target configuration
Angle = 15 deg
Bending Radius = 22 m
Big aperture = 100 cm
Small aperture = 50 cm
Center of the narrow part aligned wit the center of the wide part
500 primaries

## Slide 5: Figure of merit – the muon emittance
Muons with Ek > 600 MeV basically do not reach the end of the chicane, they are dumped in the chicane walls.
In the following slides we will see what’s happening here
More statistic to be run before the annual meeting!
Alternatively, the binning be coarser

## Slide 6: Concept 2, beam shape
Particles entering the chicane are nicely centered.
Momentum spectrum
Out of interest

## Slide 7: Concept 2, beam shape
At it was shown before, the transverse emittance of muons in the center of the chicane blows up – here we can see it happens due to the vertical elongation. However, it gets compensated by the end of the chicane.
FWHM 17.7 cm
FWHM 16 cm
Here we observe all the particles crossing the dashed line including the ones hitting the magnets

## Slide 8: Concept 2, beam shape
The spent proton beam exiting the chicane is inclined slightly down – its center moves down in Y by 35 cm over a distance of ~5 m in Z.
143 cm
Momentum spectrum of particles only inside the solenoid!
FWHM 19 cm
FWHM 19.2 cm
~511 kW extracted!
Out of interest

## Slide 9: Concept 2, energy deposition to the most exposed magnets
Magnet | Integrated energy deposition [kW]
MagR45 | 2.09
MagR47 | 3.73
MagR49 | 5.32
MagR51 | 24.5
MagR53 | 8.63
MagR55 | 2.51
Total | 46.8
R45
R47
R49
R51
R53
R55
Possibly, the shape can be fine-tuned to reduce the energy deposition or spread it more evenly between the magnets.

## Slide 10: Summary
An example chicane confugration was invstigated in the scope of the spent proton beam extraction.
Figure of merit for optimization and future comparisons was developed in the process.
Energy deposition to the chicane magnets should still be reduced, but the power extracted from the system is already high.

## Slide 11: Backup

## Slide 12: Fitting the field
Data points corresponding to the center of each solenoid magnet and the field strength of 1.5T
The fit limits the parameters (current densties) to
16.57 A/m2 +/-60%
Field calculation based on the script developed by
D. Calzolari
The number of fit parameters is equal to the number of data points – the parameters are the current densities of each magnet
In the first part of the chicane, the fitter ramps up the current in one magnet to reduce it greatly in the neighbouring one
In the narrow part of the chicane, the current densities stay stable around the nominal 16.57 A/m2 (value inherited from MAP studies)
Reaching 26.5 A/m2