## Slide 1
Sapporo, March 2024
Muon Collider
D. Schulte
On behalf of the International Muon Collider Collaboration
This project has received funding from the European Union’s Research and Innovation programme under GAs No 101094300 and No 101004730.

## Slide 2: Motivation and Goal
2
Previous studies in US (now very strong interest again), experimental programme in UK and alternatives studies by INFN
New strong interest in high-energy, high-luminosity lepton collider
Combines precision physics and discovery reach
Application of hadron collider technology to a lepton collider
Muon collider promises sustainable approach to the energy frontier
limited power consumption, cost and land use
Technology and design advances in past years
review did not find any showstoppers
Goal is
10+ TeV collider
potential initial energy stage (e.g. 3 TeV)
higher energies to be explored later

## Slide 3: Muon Collider Overview
3
Short, intense proton bunch
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
Would be easy if the muons did not decay
Lifetime is τ = γ x 2.2 μs
Protons produce pions which decay into muons
muons are captured

## Slide 4: Initial Target Parameters
4
Parameter | Unit | 3 TeV | 10 TeV | 14 TeV
L | 1034 cm-2s-1 | 1.8 | 20 | 40
N | 1012 | 2.2 | 1.8 | 1.8
fr | Hz | 5 | 5 | 5
Pbeam | MW | 5.3 | 14.4 | 20
C | km | 4.5 | 10 | 14
<B> | T | 7 | 10.5 | 10.5
εL | MeV m | 7.5 | 7.5 | 7.5
σE / E | % | 0.1 | 0.1 | 0.1
σz | mm | 5 | 1.5 | 1.07
β | mm | 5 | 1.5 | 1.07
ε | μm | 25 | 25 | 25
σx,y | μm | 3.0 | 0.9 | 0.63
Target integrated luminosities
Note: currently focus on 10 TeV, also explore 3 TeV
Tentative parameters based on MAP study, might add margins
Achieve goal in 5 years
  Probably have more time
  FCC-hh to operate for 25 years
Aim to have two detectors
CLIC at 3 TeV
28
2 (6)

## Slide 5: Muon Collider Luminosity Scaling
Fundamental limitation
Requires emittance preservation and advanced lattice design
Applies to MAP scheme
Luminosity per power increases with energy
Provided technologies can be made available
Constant current for required luminosity scaling
High field in collider ring
Dense beam
High energy
High beam power
Large energy acceptance

## Slide 6: Muon Collider Promises
6
 | CME [TeV] | Lumi per IP [1034cm-2s-1] | Years to physics | Cost range [B$] | Power [MW]
FCC-ee | 0.24 | 8.5 | 13-18 | 12-18 | 290
ILC | 0.25 | 2.7 | <12 | 7-12 | 140
CLIC | 0.38 | 2.3 | 13-18 | 7-12 | 110
ILC | 3 | 6.1 | 19-24 | 18-30 | 400
CLIC | 3 | 5.9 | 19-24 | 18-30 | 550
MC | 3 | 1.8 | 19-24 | 7-12 | 230
MC | 10 | 20 | >25 | 12-18 | 300
FCC-hh | 100 | 30 | >25 | 30-50 | 560
US Snowmass Implementation Task Force: Th. Roser, R. Brinkmann, S. Cousineau, D. Denisov, S. Gessner, S. Gourlay, Ph. Lebrun, M. Narain, K. Oide, T. Raubenheimer, J. Seeman, V. Shiltsev, J. Straight, M. Turner, L. Wang et al.
Judgement by ITF, take it cum grano salis

## Slide 7: Goal and Accelerator R&D Roadmap
7
Muon collider is on European Accelerator R&D Roadmap
Reviews in Europe and US found no insurmountable obstacle
Implementing workplan
Goal: Project Evaluation Report and R&D Plan to next ESPPU/other processes
10+ TeV collider, potential 3 TeV initial stage
CERN has budget in MTP, hosting a collaboration
Design Study supported by EC, Switzerland, UK and partners contribute
Strong interest in US community to join and contribute at same level as Europe
We still need more resources
But doubled last year with EU Design Study
Might double with US joining
Preparing other requests
Exploitation of synergies
http://arxiv.org/abs/2201.07895

## Slide 8: Muon Collider Timeline (Roadmap)
8
Evaluation+decision
Technically limited timeline
To be reviewed considering progress, funding and decisions
Evaluation+decision
Muon collider important in the long term
Even after potential FCC-hh
But also plan B as next project in Europe and maybe plan A in US and elsewhere
Fast track option if require next as project after HL-LHC:
Lower energy initial option, e.g. 3 TeV
Upgrade to 10 TeV later
  Little extra cost
Subject to funding

## Slide 9: Muon Collider Community
Looking for new partners
In particular US
But also other regions
Increase resources of partners with other funding requests:
Submit to HORIZON-INFRA-2024-TECH
  Focus on magnet technologies
National funding agencies
EU Design Study helped to kick-start collaboration
(since March 2023, EU+Switzerland+UK and partners)
EU support also helps with funding in institutes
CERN-hosted collaboration
O(70) partners, 60+ already signed MoC

## Slide 10: MoC and Design Study Partners
10
IEIO | CERN
FR | CEA-IRFU
 | CNRS-LNCMI
DE | DESY
 | Technical University of Darmstadt
 | University of Rostock
 | KIT
SE | ESS
 | University of Uppsala
PT | LIP
NL | University of Twente
FI | Tampere University
LAT | Riga Technical Univers.
CH | PSI
 | University of Geneva
 | EPFL
EST | Tartu University
BE | Univ. Louvain
UK | RAL
 | UK Research and Innovation
 | University of Lancaster
 | University of Southampton
 | University of Strathclyde
 | University of Sussex
 | Imperial College London
 | Royal Holloway
 | University of Huddersfield
 | University of Oxford
 | University of Warwick
 | University of Durham
US | Iowa State University
 | Wisconsin-Madison
 | Pittsburg University
 | Old Dominion
 | BNL
 | Florida State University
 | RICE University
 | Tennessee University
China | Sun Yat-sen University
 | IHEP
 | Peking University
AU | HEPHY
 | TU Wien
ES | I3M
 | CIEMAT
 | ICMAB
KO | KEU
 | Yonsei University
India | CHEP
US | FNAL
 | LBL
 | JLAB
 | Chicago
IT | INFN
 | INFN, Univ., Polit. Torino
 | INFN, Univ. Milano
 | INFN, Univ. Padova
 | INFN, Univ. Pavia
 | INFN, Univ. Bologna
 | INFN Trieste
 | INFN, Univ. Bari
 | INFN, Univ. Roma 1
 | ENEA
 | INFN Frascati
 | INFN, Univ. Ferrara
 | INFN, Univ. Roma 3
 | INFN Legnaro
 | INFN, Univ. Milano Bicocca
 | INFN Genova
 | INFN Laboratori del Sud
 | INFN Napoli
Mal | Univ. of Malta

## Slide 11: US P5: The Muon Shot
11
Particle Physics Project Prioritisation Panel (P5) endorses muon collider R&D: ”This is our muon shot”
Recommend joining the IMCC
Consider FNAL as a host candidate
We welcome the US community
Already participation, also in leadership
Will increase and reorganise in 2024
Ambition of US to host collider is excellent news

## Slide 12: Key Challenges
12
3) Cost and power consumption limit energy reach
e.g. 35 km accelerator for 10 TeV, 10 km collider ring
Also impacts beam quality
4) Drives the beam quality
MAP put much effort in design
optimise as much as possible
1) Dense neutrino flux
mitigated by mover system and site selection
2) Beam-induced background
0) Physics case

## Slide 13: Muon Decay and Neutrino Flux
~600 m
But want to have negligible impact from arcs
Similar impact as LHC
At 3 TeV this is the case for 200 m depth
At 10 TeV use angle change of +/- 1 mradian to go from acceptable to negligible level
  Mockup of mover system planned
  Impact on beam to be checked
Impact of experimental insertions
3 TeV design acceptable with no further work
Maybe acquire land in direction of experiment, also for 10 TeV
t1
t2
Muon decays per bunch passage
235,000 m-1 at 3 TeV
58,000 m-1 at 10 TeV

## Slide 14: Neutrino Flux
14
Goal: similar to LHC: limit neutrino flux to have negligible impact, “fully optimised” (10% of MAP goal)
Verify performance of concept to be good for 14 TeV
Mover and support system
F. Bertinelli et al. (CERN, Riga)
G. Lerner, D. Calzolari, A. Lechner, C. Ahdida
FLUKA dose studies
G. Lacerda, Y. Robert, N. Guilhaudin (CERN)
Mitigation:
Site choice tool
Flux direction map / lattice design / mover impact on beam
C. Carli, K. Skoufaris (CERN)
C. Ahdida, P. Vojtyla, M. Widorski, H. Vincke
Conformity Verification Scheme

## Slide 15: Muon Decay and Detector Background
15
Muon decays produce electrons and positrons
Loss per unit length almost independent of energy
First results indicate that background does not increase much with energy
1.5 and 3 TeV studies, concept based on CLIC detector
Masks to mitigate background
Detailed FLUKA studies of masks/beamline
Tracking detector radiation level similar to HL-LHC
Studies with beam-induced background in progress
some channels are not affected by background
some improvement required for other channels
Concept for 10 TeV in progress
Detector team
O(69) authors, O(150 signatories)
D. Lucchesi, F. Meloni et al.

## Slide 16: Proton Complex and Target
protons
5 GeV proton beam, 2 MW = 400 kJ x 5 Hz
Power is at hand
ESS and Uppsala will focus on merging beam into high-charge pulses
Optimisation of parameters planned
pions
muons
in target
decay
Graphite Target
20 T solenoid
to guide pions and muons
Tungsten shielding
To protect magnet
400 kJ protons to produce 5 x 1013 captured muon pairs

## Slide 17: Target Design
CNGS
CNGS target
3.5 x 1013 protons/pulse, 400 GeV (2.2 MJ), 1/6 Hz
5 x 1014 protons/pulse, 5 GeV (0.4 MJ), 5 Hz
graphite rod with 15 mm radius
or liquid lead
or fluidised tungsten
A. Lechner, D. et al.
Target
Tunsten shielding
Vessel
Window

## Slide 18: Final Cooling Principle
Energy loss = cooling
Multiple scattering = heating
High field solenoids minimise beta-function and impact of multiple scattering

## Slide 19: Cooling: The System Chain
Y
Transverse Emittance (microns)
Longitudinal Emittance (mm)
For acceleration to multi-TeV collider
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Target
Phase
Rotator
Front End



Exit Front End
(15mm,45mm)
MAP collaboration

## Slide 20: Cooling Cell Technology
20
Will develop example cooling cell with integration
tight constraints
additional technologies (absorbers, instrumentation,…)
early preparation of demonstrator facility
RF cavities in magnetic field
MAP demonstrated higher than goal gradient
Improve design based on theoretical understanding
Preparation of new test stand, but needs funding
Test stand at CEA (700 MHz, need funding)
Test at other frequencies in the UK considered
Use of CLIC breakdown experiment considered
C. Marchand, Alexej Grudiev et al. (CEA, Milano, CERN, Tartu)
L. Rossi et al. (INFN, Milano, STFC, CERN),
J. Ferreira Somoza et al.
MuCool demonstrated >50 MV/m in 5 T
H2-filled copper
Be end caps
Windows and absorbers for high-density muon beam
Pressure rise mitigated by vacuum density
Plan window test in HiRadMat
Most complex example 12 T

## Slide 21: RF Test Stand
SC HTS coils
Pillbox test cavity
With cryostat
SC HTS coils
Two stage cryocooler
Thermal shield
Vacuum vessel
Coil support structure
Tie rods for repulsion and compression forces
RF Wave guide
Bare coils and RF cavity
Module work focuses on RF test stand at this moment
Important ensure timely R&D plan
Try to identify infrastructure for this
  CEA, INFN, Cockroft, CERN, …
  Will not be cheap so need to find resources
L. Rossi, C. Marchand, D. Giove, A. Gurdiev, G. Ferrand, M. Castoldi, S. Sorti et al.

## Slide 22: Solenoid R&D
Target solenoid, 20 T, 20 K
MIT “VIPER” conductor
A Portone, P. Testoni, J. Lorenzo Gomez, F4E
MuCol HTS conductor
Operating current: 61 kA
Final Cooling solenoid
Goal 40 T
Estimation of limit
Started HTS solenoid development for high fields
Synergies with fusion reactors, NRI, power generators for windmills, …
NHFML
32 T solenoid with HTS
15 T Nb3Sn with 5 T resistive insert
Or 20 T HTS seems possible
Relevant for advanced fusion reactors
ITER Central Solenoid Model Coil
13 T in 1.7 m (LTS)

## Slide 23: Acceleration Complex
EMMA proof of FFA principle
Nature Physics 8, 243–247 (2012)
Started work on key challenges
Integrated design of RCS
  Longitudinal dynamics
  Lattice with realistic hardware specifications
  Collective effects
Concept of key components
  Fast-ramping normal magnets
  HTS alternative
  Efficient power converters
  RF with transient beam loading
Core is sequence of hybrid pulsed synchrotron (0.4-11 ms)
Alternative FFA
Lattice and integration: A. Chance et al. (CEA)
Long. dynamics and RF systems: H. Damerell, U. van Rienen, A. Grudiev et al. (Rostock, Milano, CERN)
Power converter: F. Boattini et al.
Magnets: L. Bottura et al. (LNCMI, Darmstadt, Bologna, Twente)
FFA: S. Machida et al. (RAL)
MAP study S. Berg et al.
initial
final

## Slide 24: Collective Effects and RF Design
Longitudinal dynamics and RF important due to high bunch charge
A. Chance, H. Damerell, F. Batsch, U. van Rienen, A. Grudiev et al. (CEA, Rostock, Milano, CERN)
E. Metral, D Amorim et al. (CERN)
Long. Distribution assumed at injection in RCS1
Each bunch passage extracts few percent of energy from cavities
Single-bunch HOM power loss up to 10 kW during pulse
CW average is lower, development of high-capacity couplers needed
Orbit length changes require frequency tuning
1.3 GHz appears possible for longitudinal effects and stability
Collider ring single beam instability limits
Conservative feedback
  Copper coating beneficial (few microns)
  Beam-beam studies started
Bunch-induced voltages in RCS1
O(5% of the cavity gradient)

## Slide 25: Fast-ramping Magnet System
5.07 kJ/m
5.65…7.14 kJ/m
5.89 kJ/m
Management of the power in the resistive dipoles (several tens of GW):
Minimum stored magnetic energy
Highly efficient energy storage and recovery
Could also use HTS driven dipoles
F. Boattini et al.
Full wave resonance
Commutated resonance (new)
Differerent power converter options investigated
FNAL 300 T/s HTS magnet
Simple HTS racetrack dipole could match the beam requirements and aperture for static magnets

## Slide 26: Collider Ring
pT [%] | DAmin [σ]
0.07 | 5
0.08 | 4
0.09 | 3
0.1 | <1
Important progress: V0.6 good dynamic aperture at almost 0.1% off-energy, approaching the target
K. Skoufaris, Ch. Carli, support from P. Raimondi, K. Oide, R. Tomas
MAP developed 4.5 km ring for 3 TeV with Nb3Sn
magnet specifications in the HL-LHC range
Work progressing on 10 TeV collider ring
around 16 T HTS dipoles or lower Nb3Sn
final focus based on HTS
Challenges:
Very small beta-function (1.5 mm)
Large energy spread (0.1%)
Maintain short bunches

## Slide 27: Collider Ring Technology
Initial estimate of magnet field limits:
11 T for Nb3Sn, more for HTS/hybrid
Need stress management
Different cooling scenarios studied
< 25 MW power for cooling possible
Shield with CO2 at 250 K (preferred) or water
Support of shield is important for heat transfer
Discussion on options for magnet cooling
Power loss due to muon decay 500 W/m FLUKA simulation of shielding:
Require 30-40 mm tungesten
Few W/m in magnets
No problem with radiation dose
K. Skoufaris, Ch. Carli, D. Amorim, A. Lechner, R. Van Weelderen, P. De Sousa, L. Bottura et al.
R. Van Weelderen, P. De Sousa
L. Bottura et al.
A. Lechner
D. Calzolari (CERN)
Shielding
Coil

## Slide 28: CDR Phase, R&D and Demonstrator Facility
Broad R&D programme can be distributed world-wide
Models and prototypes
  Magnets, Target, RF systems, Absorbers, …
CDR development
Integrated tests, also with beam
Cooling demonstrator is a key facility
look for an existing proton beam with significant power
Different sites are being considered
CERN, FNAL, ESS …
Discussed at ACE at FNAL
Site at CERN possible
J-PARC also interesting as option
Could be used to house physics facility
Synergies workshop to explore good options
M. Calviani, R. Losito, J. Osborn et al.

## Slide 29: Test Facility Dimensions
Target
+ horn (1st phase) /
+ superconducting solenoid (2nd phase)
Momentum selection chicane, 10 m
Collimation and upstream diagnostics area, 10 m
Cooling area, 50 m
Downstream diagnostics area, 5 m
C. Rogers
Look for an existing proton beam with significant power
Different sites are being considered
CERN, FNAL, ESS are being discussed
J-PARC also interesting as option

## Slide 30: Implementation Considerations
Reviewing timeline (still evolving)
Uncertainties from physics case (e.g. HL-LHC), society development, budget profile etc.
Can concept be mature for decision before 2040 and start operation before 2050?
Identifying shortest possible “technically limited” timeline
Identified main technologies that might limit the timeline
  Muon cooling technologies and integration
  Magnet technology
  Detector technologies
Expect that other technologies can be accelerated with enough funding
To be reviewed by 2026

## Slide 31: Roadmap
Current findings:
Expect detector and muon production and cooling can meet the required timeline
Magnets are main limitation:
Consensus of magnet experts (review panel):
Anticipated mature technology in O(15 years):
  HTS solenoids in muon production target, 6D cooling and final cooling
    HTS tape can be applied more easily in solenoids
    Strong synergy with society, e.g. fusion reactors
  Nb3Sn 11 T magnets for collider ring (or HTS if available): 150mm aperture, 4K
  This corresponds to 3 TeV design
Still under discussion:
  Timescale for HTS/hybrid collider ring magnets

## Slide 32: Staging Approaches
Assumptions:
In O(15 years):
  HTS technology available for solenoids
  Nb3Sn available for collider ring
In O(25 years):
  HTS available for collider ring
Scenario 1: Energy staging
Start at lower energy (e.g. 3 TeV)
Build additional accelerator and collider ring later
Requires less budget for first stage
3 TeV design takes lower performance into account
Scenario 2: Luminosity staging
Start at with full energy, but less performant collider ring magnets
Main sources of luminosity loss are collider arcs and interaction region
  Can recover interaction region later (as in HL-LHC)
  But need full budget right away
  Some luminosity loss remains (O(1.5))
  More power for the collider ring required (lower magnet temperature)

## Slide 33: Collider Site Studies
Candidate sites CERN, FNAL, potentially others (ESS, JPARC, … )
Study is mostly site independent
Main benefit is existing infrastructure
Want to avoid time consuming detailed studies and keep collaborative spirit
Will do more later
Some considerations are important
Neutrino flux mitigation at CERN
Accelerator ring fitting on FNAL site
Potential site next to CERN identified
Mitigates neutrino flux
  Points toward mediterranean and uninhabited area in Jura
Detailed studies required (280 m deep)

## Slide 34: Conclusion
34
Muon collider unique opportunity for high-energy, high-luminosity lepton collider
Currently working toward 10+ TeV, potential 3 TeV intermediate stage explored
  Design
  Technology
  R&D programme preparation including demonstrator
Collaboration exists, promises to increase
  More request to EC and other funding agencies
  The US partners will join
  Hope to also grow in Asia
  Feel that there is important synergy with other facilities and technologies
http://muoncollider.web.cern.ch To join contact muon.collider.secretariat@cern.ch

## Slide 35: Reserve

## Slide 36: Alternatives: The LEMMA Scheme
LEMMA scheme (INFN) P. Raimondi et al.
45 GeV positrons to produce muon pairs
Accumulate muons from several passages
Excellent idea, but nature is cruel
Detailed estimates of fundamental limits show that we require a very large positron bunch charge to reach the same luminosity as the proton-based scheme
Need same game changing invention
Note: New proposal by C. Curatolo and L. Serafini needs to be looked at
Uses Bethe-Heitler production with electrons

## Slide 37: Organisation
Collaboration Board (ICB)
Elected chair: Nadia Pastrone
Steering Board (ISB)
Chair Steinar Stapnes
CERN members: Mike Lamont, Gianluigi Arduini
ICB members: Dave Newbold (STFC), Mats Lindroos (ESS), Pierre Vedrine (CEA), N. Pastrone (INFN)
Study members: SL and deputies
Will add US but wait for US decision on members
Advisory Committee
To be defined, discussion in SB
Coordination committee (CC)
Study Leader: Daniel Schulte
Deputies: Andrea Wulzer, Donatella Lucchesi, Chris Rogers

## Slide 38: EU Design Study
Kick-off meeting in March 2023:
https://indico.cern.ch/event/1219912
Many thanks to all that contributed
https://mucol.web.cern.ch
Has been approved summer 2022
Very helpful to kick-start collaboration
Reapproved early 2023
It appears that there has been some issue with the refereeing of several projects, probably not directly with the muon collider
Brings 3 MEUR from the European Commission, the UK and Switzerland and about 4 MEUR from the partners
Basically nothing for CERN
Sat celeriter fieri quidquid fiat satis bene

## Slide 39: US P5 Ask
39
S. Jindariani, D. Stratakis, Sridhara Dasu et al.
Goal is to contribute as much as Europe
Start of construction a bit later than in Roadmap
Will try to harmonise/define scenarios once US joins
Total resources would approach Roadmap
Some increase in Europe and Asia assumed
1-2 years delay
But profile is different

## Slide 40: Muon Collider Luminosity Scaling
Fundamental limitation
Requires emittance preservation and advanced lattice design
Applies to MAP scheme
Luminosity per power increases with energy
Provided technologies can be made available
Constant current for required luminosity scaling
High field in collider ring
Dense beam
High energy
High beam power
Large energy acceptance

## Slide 41: Staging
Ideally would like full energy right away, but
staging could lead to faster implementation
Substantially less cost for a first stage
Can make technical compromises
  e.g. 8 T NbTi magnets would increase collider ring from 4.5 to 6 km and reduce luminosity by 25%
Timeline might be more consistent with human lifespan
Upgrade adds one more accelerator and new collider ring
only first collider ring is not being reused

## Slide 42: Alternatives: The LEMMA Scheme
LEMMA scheme (INFN) P. Raimondi et al.
45 GeV positrons to produce muon pairs
Accumulate muons from several passages
Excellent idea, but nature is cruel
Detailed estimates of fundamental limits show that we require a very large positron bunch charge to reach the same luminosity as the proton-based scheme
Need same game changing invention
Note: New proposal by C. Curatolo and L. Serafini needs to be looked at
Uses Bethe-Heitler production with electrons

## Slide 43: Muon Decay
43
Neutrino flux to have negligible impact on environment
want to be negligible (same level as LHC)
opening cone decreases, cross section and shower energy increase with energy
Above about 3 TeV need to make beam point in different vertical directions
Mechanical system with 15cm stroke, 1% vertical bending
Length of pattern to be optimised for minimal impact on beam
About 1/3 of energy in electrons and positrons:
Experiments needs to be protected from background by masks
simulations of 1.5, 3 and 10 TeV
optimisation of masks and lattice design started
first results look encouraging
will be discussed at ICHEP
Collider ring magnets need to be shielded from losses
Losses elsewhere will also need to be considered but are less severe
D. Lucchesi, A. Lechner, C Carli et al.
~2 x 600 m

## Slide 44: Key Challenges
44
Proton complex
- Compressing protons to few bunches
Cooling channel
- Channel design
- Solenoids
- RF in magnetic field
- Absorbers
- Integration
RCS
- Beam dynamics
- Ramping magnets
- Power converter
- RF system
Collider ring
- Optics
- Magnets
- Neutrino flux
- Detector background
Target
- Target
- Solenoid

## Slide 45: Roadmap
45
In aspirational scenario can make informed decisions:
Three main deliverables are foreseen:
a Project Evaluation Report for the next ESPPU will contain an assessment of whether the 10 TeV muon collider is a promising option and identify the required compromises to realise a 3 TeV option by 2045. In particular the questions below would be addressed.
  What is a realistic luminosity target?
  What are the background conditions in the detector?
  Can one consider implementing such a collider at CERN or other sites, and can it have one or two detectors?
  What are the key performance specifications of the components and what is the maturity of the technologies?
  What are the cost drivers and what is the cost scale of such a collider?
  What are the power drivers and what is the power consumption scale of the collider?
  What are the key risks of the project?
an R&D Plan that describes an R&D path towards the collider;
an Interim Report by the end of 2023 that documents progress and allows the wider community to update their view of the concept and to give feedback to the collaboration.

## Slide 46: R&D Plan
The R&D plan will describe the R&D path toward the collider, in particular during the CDR phase, and will comprise the elements below.
An integrated concept of a muon cooling cell that will allow construction and testing of this key novel component.
A concept of the facility to provide the muon beam to test the cells.
An evaluation of whether this facility can be installed at CERN or another site.
A description of other R&D efforts required during the CDR phase including other demonstrators.
This R&D plan will allow the community to understand the technically limited timeline for the muoncollider development after the next ESPPU.

## Slide 47: Minimal Scenario
Will allow partially informed decisions
No conceptual design of neutrino flux and alignment system
No alternative superconducting fast-ramping magnet system
Several collider systems would (almost) not be covered, in particular
  the linacs
  the target complex
  the proton complex
  engineering considerations of the muon cooling cells
  alternative designs for the final cooling system, acceleration, collider ring
No RF test stand would be constructed for the muon cooling accelerating cavities
No conceptual design of a muon cooling cell for the test programme
No conceptual design of a muon cooling demonstrator facility
No concept of RF power sources
No tests/models to develop solenoid technology.

## Slide 48: Key Technologies
Magnets
Superconducting solenoids for target and cooling profit from developments for society
  target solenoid comparable to ITER central solenoid fusion
  6D cooling solenoids similar and wind power generators, motors
  final cooling solenoids synergetic with high-field research, NMR
Collider ring magnets
  profit from developments for other colliders FCC-hh, stress-managed magnets
Fast-ramping normal-conducting magnet system
  HTS alternative, power converter
RF systems
superconducting RF, normal-conducting RF, efficient klystrons
Target, cooling absorbers, windows, shielding
Neutrino mitigation mover system, cooling cell integration, …
Detector

## Slide 49: Key Technologies, cont.
RF systems
Normal-conducting cooling cavities in magnetic field
  profit from CLIC work
Superconducting accelerator RF
  profit from ILC, …
Efficient power sources
  profit from CLIC work
Beam-matter interaction
Proton target
Cooling absorbers
Shielding (accelerator and detector)
Mechanical system
Neutrino flux mitigation system
Muon cooling cell integration

## Slide 50: Collaboration Vision
IMCC is an international collaboration and aims to
Enlarge the collaboration
  Physics interest in all regions, strong US contribution to the muon collider physics and detector, interest in Japan
  First US university have joined collaboration, try to see how to move forward, also with labs
Combine the R&D efforts for the design and its technologies
  Critical contributions in all relevant fields in the US
Consider several sites for the collider
  CERN would be one, FNAL and others should also be considered
  A proposal with alternative sites is stronger for a single site
Consider several sites for the demonstrators
  E.g. Muon production and cooling demonstrator at CERN, FNAL, ESS, JPARC
  e.g. RCS at ESRF or elsewhere
  Target tests
  …

## Slide 51: Initial Target Parameters
51
Parameter | Unit | 3 TeV | 10 TeV | 14 TeV
L | 1034 cm-2s-1 | 1.8 | 20 | 40
N | 1012 | 2.2 | 1.8 | 1.8
fr | Hz | 5 | 5 | 5
Pbeam | MW | 5.3 | 14.4 | 20
C | km | 4.5 | 10 | 14
<B> | T | 7 | 10.5 | 10.5
εL | MeV m | 7.5 | 7.5 | 7.5
σE / E | % | 0.1 | 0.1 | 0.1
σz | mm | 5 | 1.5 | 1.07
β | mm | 5 | 1.5 | 1.07
ε | μm | 25 | 25 | 25
σx,y | μm | 3.0 | 0.9 | 0.63
Target integrated luminosities
Note: currently focus on 10 TeV, also explore 3 TeV
Tentative parameters based on MAP study, might add margins
Achieve goal in 5 years
FCC-hh to operate for 25 years
Aim to have two detectors
CLIC at 3 TeV
28
2 (6)

## Slide 52: US Snowmass
52
Meenakshi Narain: Energy Frontier / Large Experiments, Snowmass Community Summer Study July 17-26, 2022
Strong interest in the US community in muon collider
seen as an energy frontier machine
decoupled from LC
US community wants funding for R&D
Goal: match European effort
Community interested in the US to host a muon collider

## Slide 53: Muon Collider magnets
> 40 T, 60 mm
RCS
20 T, 200 mm
Radiation heat load ≈ 5…10 kW
Radiation dose: 80 MGy
NC ±1.8 T, 400 Hz 100 mm x 30 mm
SC < 10T
100 mm x 30 mm
SC dipole
NC dipole
NC dipole
SC dipole
16 T peak, 150 mm
Radiation heat load ≈ 5 W/m
Radiation dose ≈ 20…40 MGy
HTS !
HTS !
HTS ?
HTS ?

## Slide 54: US Snowmass
54
Meenakshi Narain: Energy Frontier / Large Experiments, Snowmass Community Summer Study July 17-26, 2022
Strong interest in the US community in muon collider
seen as an energy frontier machine
decoupled from LC
US community wants funding for R&D
Goal: match European effort
Community interested in the US to host a muon collider

## Slide 55: Coordination Committee Members
Physics | Andrea Wulzer
Detector and MDI | Donatella Lucchesi
Protons | Natalia Milas
Muon production and cooling | Chris Rogers
Muon acceleration | Antoine Chance
Collider | Christian Carli
Magnets | Luca Bottura
RF | Alexej Grudiev, Dario GIove
Beam-matter int. target systems | Anton Lechner
Collective effects | Elias Metral
US (detector) | Sergo Jindariani
US (accelerator) | Mark Palmer
Asia (China) | Jingyu Tang
Asia (Japan) | tbd
Cooling cell design | Lucio Rossi
Demonstrator | Roberto Losito
A strengthening on the physics and detector side is planned

## Slide 56: Physics Goals
56
Discovery reach
10-14 TeV lepton collisions are comparable to 100-200 TeV proton collisions for production of heavy particle pairs
Full lepton energy available for production of new particles, in protons only a fraction
Luminosity goal
(Similar to L(ECM > 0.99 ECM,0) CLIC at 3 TeV)
4x1035 cm-2s-1 at 14 TeV
Need more luminosity at higher energies as production cross section decreases
Yields constant number of events in the s-channel

## Slide 57: Physics Studies
57
Details on physics case, detector and accelerator can be found in
Snowmass white papers https://indico.cern.ch/event/1130036/
EPJC report in preparation
Used tentative detector performance specifications in form of DELPHES card
based on FCC-hh and CLIC performances, including masks against beam induced background (BIB)
Please find the card here: https://muoncollider.web.cern.ch/node/14
M. Selvaggi, W. Riegler, U. Schnoor, A. Sailer, D. Lucchesi, N. Pastrone, M. Pierini, F. Maltoni, A. Wulzer et al.
D. Lucchesi, F. Meloni et al.
Initial detector simulation studies at 1.5 and 3 TeV indicate that this is a good model
Now moving to 10 TeV
If you are interested to contribute please contact me or the responsible deputies:
Andrea Wulzer (Physics) and Donatella Lucchesi (Detector and MDI)

## Slide 58: Possible CERN Locations
M. Calviani, R. Losito, J Osborn et al.
Consider nTOF-like beam from PS for cooling experiment:
1 pulse of 1013 p at 20 GeV per 1.2 s, i.e. 27 kW
maybe O(100kW) possible
If SPL were, installed could use its beam, e.g. 5 GeV, 4 MW

## Slide 59: Collider Site Studies
Study is mostly site independent
However, some considerations are being made
Candidate sites are CERN, FNAL, potentially others (ESS, JPARC, … )
  FNAL takes test facility into account in their ACE plans
But need some site considerations
Potential site next to CERN identified
Mitigates neutrino flux
  Points toward mediterranean and uninhabited area in Jura
Detailed studies required (280 m deep)
Main site concern:
Neutrino flux mitigation
Neutrinos in direction of experimental insertions need to be mitigated by site choices
Main site benefit:
Potentially significant cost saving from reusing exiting infrastructure
Will study this later

## Slide 60: RF Test Stand
SC HTS coils
Pillbox test cavity
With cryostat
SC HTS coils
Two stage cryocooler
Thermal shield
Vacuum vessel
Coil support structure
Tie rods for repulsion and compression forces
RF Wave guide
Bare coils and RF cavity
Module work focuses on RF test stand at this moment
Important ensure timely R&D plan
Try to identify infrastructure for this
  CEA, INFN, Cockroft, CERN, …
  Will not be cheap so need to find resources
L. Rossi, C. Marchand, D. Giove, A. Gurdiev, G. Ferrand, M. Castoldi, S. Sorti et al.

## Slide 61: MICE: Cooling Demonstration
61
Principle of ionisation cooling has been demonstrated
Use of data for benchmarking is still ongoing
Nature vol. 578, p. 53-59 (2020)
More particles at smaller amplitude after absorber is put in place
More complete experiment with higher statistics, more than one stage required
Integration of magnets, RF, absorbers, vacuum is engineering challenge