## Slide 1
Integration Team: A. Pardons, E. Guran, V. Clerc (3D Drawings)
Update from 2020 document (P. Wiwattananon)
AWAKE Run2c vs Run2a&2b Infrastructure Integration

## Slide 2: Run 2ab vs Run2c
2
Run2c has 2 times large/complex equipment than Run2ab
Run2c requires at least x2 spaces/volume than Run2ab
In Run2c integration design take into account: the accessibility of equipment – obey rule for minimum passage (800mm width free) for emergency evacuation
In Run2c integration design take into account: the transportation of equipment to the AWAKE experimental area: transportation width = 1.3m
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 3: TAG41
3
TCV4
YWBPA03.TAG41=TAG41
YWBPB01.TSG40=TSG40
YWBPB02.4115=TT41
YWBPA04.TCV4=TCV4 YWBPA01.TT43=TT43 YWBPA03.TT43=TT41
YWBPA01.TSG41=TSG41
YWBPA08.TCV4=TCV4
YWBPA01.TSG4=TSG4
YWBPA02.TSG4=TSG4
YWBPA02.TSG42=TSG42
YWBPA01.TSG42=TSG42
YWBPA01.TCC4=TCC4
YWBPA02.TCC4=TCC4
YWBPB01.TSG4=TSG4
YWBPB01.TSG47=TSG47
YWBPB02.TSG47=TSG47
Bending Magnet
MBSG 410010
Beam Stopper
TBSE 410113
Bending Magnet
MBG 410147
Laser shutter LSSP1
YWBPA02.TSG40=TSG40
Laser shutter LSSe2
Laser shutter LSSe1
S0
TT40
S0
S1
ACCESS POINT
YDA01=TAG41
ACCESS POINT
YDA01=TT40
ACCESS POINT
YDA01=TAG42
S1
TJ8
CL
YWBPA02.TAG41=TAG41
S2
S5
S6
S3
YDPS01.TCV4=TCV4
YWBPA02.TCV4=TCV4
YWBPA01.TCV4=TCV4
YWBPA09.TSG41=TCV4 YWBPB01.TSG41=TSG41
S2
S4
S8
S9
S3
CL
YWBPA05.TCV4=TCV4 YWBVR01.TSG41=TSG41
YWBVR01.TCC4=TCC4
ECA4
YWBVR01=TAG41
YDAP01=TAG41
YDPZ01=TAG41
YDAM01=TAG41
YWBPC01=TAG41 YWBPA01.TAG41=TAG41
YWBVR01.TZ80=TZ80
YWBPB01.TZ80=TZ80
YWBPA04.TAG41=TAG41
Electrons RF
Electrons HV
YDPZ01=TAG42 YWBPB01.TAG42=TAG41
YDPS01.TAG42=TAG42
S1
Laser shutter LSSP2
YWBPA01.TSG40=TSG40
YWBPA03.TCV4=TCV4
YDPS02.TCV4=TCV4
S7
YDAP01=TAG42
YDAM01=TAG42
S0
 |  |  |  | Material Access device - MAD
 |  |  |  | Personal access Device - PAD
 |  |  |  | EIS-Beam ou Machine / EIS Laser ou Electron
 |  |  |  | End-of-Zone door
 |  |  |  | Sector Ventilation door
 |  |  |  | Sector Ventilation Door with line of sight door
S# |  |  |  | Sector n°
 |  |  |  | Patrol checkpoint
 |  |  |  | Laser Patrol checkpoint
CL |  |  |  | Door connected to cabled loop
 |  |  |  | Local RP veto release
YWBPB03.4115=TT41
YWBPB03.TCV4=TCV4
YWBPB04.TT41=TT41
YWBPB01.TSG42=TSG42
YWBPB02.TCV4=TCV4
YWBPB01.TCV4=TCV4
YWBPA07.TCV4=TCV4
YWBPA06.TCV4=TCV4
S2
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 4: Run2c vs Run2ab
Run2
2 Plasma Cells
2 Electron Sources
Klystrons
Spectrometer
Laser beam compressor 1
Laser beam compressor 2
2 WDL Chiller Units
AWAKE CNGS Area Dismantling is before & during LS3 (2025-2026)
Run2c Integration/installation is during LS3 (2026-2027)
Run1
Slide 5: Run2ab Experimental Area
TSG42
TSG43
TSG44
TSG45
CNGS area – to be dismantled
UV laser room
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 5: Run 2ab
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 6: AWAKE Run2ab – Transportation Path
1.25m H=2m
1.25m H=2m
1m H=1.8m
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 7
Extra Slides AWAKE Run2c
Run2c Plasma Cell1 Moves 40m Downstream Relative to Run1 Plasma Cell
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 8: AWAKE Run2c Infrastructure
AWAKE Run2ab
Slide 9: Upstream
Slide 10: Experimental Area
Slide 11: Klystron
Slide 12: Merging Mirror
Slide13: Electron Sources
Slide 14: Plasma Cells
Slide 15: Spectrometer
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 9: Upstream – TT41
AWAKE Run2ab
AWAKE Run2c
Laser Merging Mirror Equipment  move 35m downstream relative to Run2ab position.
Proton beam magnets  relocate to support the Run2c plasma cell1 location and avoid conflicts with infrastructure, e.g. doors, in the tunnel.
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 10
BEAM HEIGHT – TT41
BEAM 1.418m
0.270m
0.544m
About 1°

## Slide 11: Experimental Area – TCC4
AWAKE Run2ab Plasma Cell
AWAKE Run2c Plasma Cell1
AWAKE Run2ab Plasma Cell moves 40m downstream  AWAKE Run2c Plasma Cell1
Working spaces around the laser merging mirror, compressor1, and electron sources obey the safety passage rule!
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 12: Klystrons - TCV4
TSG41
Double spaces required for Run2c (additional) klystrons  TCV4 allows a perfect location with optimum waveguide length.
Transportation Path
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 13: Laser Merging Mirror Area – TCC4
Laser merging mirror
moves 35m from Run2ab
Compressor 1
Working table
TSG41
Equipment
transfer area
QTLD
Laser Beam Diagnostic
MDSV
QTSD
BPMI
Sufficient transfer (area) of equipment to the trailer.
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 14: Electron Sources – TCC4
Electron Source2
Electron Source1
Plasma Cell1
Working spaces around the electron sources obey the safety rule! Electron beams geometries obey technical requirements.
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 15
BEAM HEIGHT – TCC4 – BEFORE PLASMA CELL
Plasma Cell1
BEAM 1.585m
0.455m
0.450m

## Slide 16: Plasma Cells – TCC4
Plasma Cell2
Working table
Plasma Cell1
Working table
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 17: Spectrometer – TCC4
Dipole preferred
location for TSG45
TSG45
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 18
Plasma Cell2
BEAM 1.6m
BEAM HEIGHT – TCC4 – AFTER PLASMA CELL

## Slide 19: Available Space Downstream
TSG 46
TSG 47
35.39m
23.39m
TSG 45
Ventilation
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 20: Transportation

## Slide 21: Working space – obey the safety passage rule!
Transportation Path
TCC4 – TSG41 – TCV4 – TAG41
TSG45 TSG44 TSG43
Transportation of Large/Complex Equipment:
TSG42
Plasma Cells: via TAG41, TAG42 and TT41 - follow Run2ab procedures.
Electron Sources: via TSG41, TCV4, TCC4 – follow Run2ab transportation procedures.
MBXFD (dipole) at the spectrometer: follow Run2ab transportation procedures.
Klystrons: subcomponents must be assembled at the TCV4. No foreseen transportation issues.
Discussed, no blocking points.
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 22
1.3m
Laser merging mirror
moves 35m from Run2ab
Working table
Compressor 1
Laser Beam
Diagnostic
Meet required transportation width of 1.3m.
No equipment conflicts.
Access to
equipment
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 23: TCV4
2.1m
1.3m
TSG41
Klystron subcomponents can be transported via TAG41 and assembled onsite at the TCV4.
Update January 2024
AWAKE Run2ab vs Run2c Infrastructure Integration

## Slide 24
home.cern