## Slide 1: Beam delivery for HI-ECN3
Alexander Gorn on behalf of WP2 (Francesco Velotti and Laurie Nevay)
29.04.2024

## Slide 2: Delivery for ECN3: overview
Multiple locations, such as TNC, ECN4, ECN4 and TCC4 were concidered for BDF/SHiP. Eventually, ECN3 was approved providing the opportunity to benefit from slow-extracted beam from LSS2 and synergy with NA-CONS project.
*Study of alternative locations for the SPS Beam Dump Facility
*Study of alternative locations for the SPS Beam Dump Facility
Final SHiP location

## Slide 3: Delivery for ECN3: operation scenarios
Beam delivery for ECN3 starts in SPS LSS2 with slow-extraction to TT21. Then the beam is either split at the end of TT21 and TT22 or not depending on scenario. Downstream the line it passes through the T4 target in TCC2 and P42 line until it is finally transferred to T10 target in TCC8.
*Findings of the Physics Beyond Colliders ECN3 Beam Delivery Task Force

## Slide 4: Delivery for ECN3: beam parameters
Beam delivery for ECN3 starts in SPS LSS2 with slow-extraction to TT21. Then the beam is either split at the end of TT21 and TT22 or not depending on scenario. Downstream the line it passes through the T4 target in TCC2 and P42 line until it is finally transferred to T10 target in TCC8.
Findings of the Physics Beyond Colliders ECN3 Beam Delivery Task Force

## Slide 5: Slow extraction in LSS2: ZS activation problem
Beam losses on ES cause activation and, thus, limit max POT.
We need to significantly reduce these losses (x4) to keep the dose at the level of Run 3.
COSE: Constant Optics Slow Extraction
Goal > Run 3

## Slide 6: Slow extraction in LSS2: losses reduction (CS)
LSS2 gonio in OP since LS2
~30% loss reduction
Crystal shadowing of ZS is now proven technique:
  Operational goniometer in SPS LSS2
CERN in-house development of advanced crystal technology (DECRYCE project):
  Now: single crystal aligned in shadowing (VR) for LSS4 ~ factor 2 loss reduction
  Future: arrays of crystals aligned in volume reflection promising up to a factor 10 beam loss reduction and replacement of septa with crystals altogether
LSS4 gonio R&D:
~ 55% loss reduction

## Slide 7: Delivery for ECN3: splitting VS dedicated
Beam delivery for ECN3 starts in SPS LSS2 with slow-extraction to TT21. Then the beam is either split at the end of TT21 and TT22 or not depending on scenario. Downstream the line it passes through the T4 target in TCC2 and P42 line until it is finally transferred to T10 target in TCC8.
*Findings of the Physics Beyond Colliders ECN3 Beam Delivery Task Force
Losses
~ 5%
Deflected right by B field
Continues straight, undeflected
Shared delivery: splitting
B
No Losses
Dedicated delivery: no splitting
B
TT20 optics changed to transport beam through splitter aperture

## Slide 8: Delivery for ECN3: bumping around T4
On SHARED cycle one of the sheets in T4 target is aligned with the beam orbit. In case of DEDICATED cycle, there is no need to hit T4 target, so it is proposed to bump around using mdlv.2402, mcxca.x04301 and new mnpa 30 correctors.
Modifications to equipment in TCC2 for SHiP need urgent design and specification to meet NA-CONS Phase 1 deadlines (installation in LS3), namely a simplified P42 XTAX under vacuum.
mdlv.2402
mnpa 30
mcxca.x04301
bump off
bump on

## Slide 9: Delivery for ECN3: bumping around T4
On SHARED cycle one of the sheets in T4 target is aligned with the beam orbit. In case of DEDICATED cycle, there is no need to hit T4 target, so it is proposed to bump around using mdlv.2402, mcxca.x04301 and new mnpa 30 correctors.
An optimized solution for SHiP and future H6/H8 operation is under urgent design.
mdlv.2402
mnpa 30
mcxca.x04301
bump off
bump on

## Slide 10: P42 beam dump: location
Also, it is proposed to install a new dedicated absorber in the upstream part of P42 (Absorber face is 213 m downstream T4 center). Protons on the SHARED cycle will be dumped either if (1) transmission losses in P42 are above the acceptable level or (2) the beam pose problems for the experimental user in ECN3. Protons on the DEDICATED cycle will be dumped only in case of emergency.
*Damien Grenier, Rui Ximenes, Maria Ornedo, ECN3 High Intensity P42 Dump
213 m from T4

## Slide 11: P42 beam dump: operation
After LS3, but before ECN3 commissioning TIDVG will be installed with a vertical offset in order to block the beam from coming to ECN3 target and keep this area safe for intervention. During and after ECN3 commissioning the dump vertical position will be lowered, so the protons are dumped only when the upstream corrector is on.
213 m
115-150 m
TIDVG +63.5 mm
mdx
off
mdx
on
TIDVG
+0 mm
TIDVG
= 40 mm
Beam
Post LS3 before ECN3 commissioning
During/after ECN3 commissioning

## Slide 12
SPS Beam Dump Facility - Comprehensive Design Study: CERN-2020-002
Round beam with 𝛔 = 8 mm on target and 50 mm sweep radius @ 4 Hz
About 100 m drift = 0.5 mrad
BL = 1334 Tm x 0.5 mrad = 0.67 Tm
Possible solution - 4 MDX magnets (2 per plane)
Final focus and dilution system: requirements

## Slide 13
Final focus and dilution system: dilution failure
Since 4 magnets are needed we can do:
  /2 scheme: 2x orientated in H + 2x orientated in V, de-phased by 90 degrees
  /4 scheme: each magnet rotated by 45 degrees, and each de-phased by 45 degrees
Dilution system failure showed the 90 degrees scheme is better
Loss of one magnet for 1 full spill does not require replacement of the target in /2 scheme

## Slide 14
Final focus and dilution system: machine protection
Check beam dilution power converter’s FGC internal check at 1kHz and direct connection to BIS
XPOC-type of system with post-analysis of every extraction and interlocking in case of anomalies
Instantaneous beam losses (rate) with suitable placed BLM
Additional hardware system based on analogic signal could be considered, e.g. live monitoring of BTV or target instrumentation
We need to converge on an acceptable interlocking and machine protection approach to protect target

## Slide 15: Timeline
Critical deadlines for input to NA-CONS already impending in 2024: P42 XTAX design choice
TDR ready by mid-2025
P42 dump – To be installed with offset before the end of LS3 to allow commissioning of TCC2 in 2028
P42 dump to be realigned in 2029 or 2030 – to transfer beam to ECN3
2029/30 installation and commissioning of dilution system and target station

## Slide 16: Summary and future plans
SPS extraction:
  Improvements in losses main topics for extraction  currently can do x2 reduction  aim for x4!
  Different solutions under investigations
North area TL upgrades:
  Optics is rematched for DEDICATED cycle, optimization for SHARED cycle is ongoing
  Splitting optimization
  Minimization of losses in TCC2 (Bumping around T4 target, wobbling system and XTAX modifications)
Dilution system and final focus:
  Summarizing requirements in a FS with input needed from the target requirements (WP3)
  Interlock system will take this into account too

## Slide 17: Thanks for your attention!

## Slide 19: P42 beam dump: required modifications
Location for the dump corrector should be chosen between 115 and 150 m downstream T4 center depending on the magnet type. Two MDX with 100 gap give enough strength to install the corrector close to downstream quadrupole and be able to dump the protons at any vertical position on the absorber face with minimal losses.
213 m
115-150 m
TIDVG +63.5 mm
mdx
off
mdx
on
TIDVG
+0 mm
Post LS3 before ECN3 commissioning
During/after ECN3 commissioning

## Slide 20: P42 beam dump: required modifications
QNL.X0430169 and MCXCA.X0430171 will be replaced with QWL and MCXCA having larger apertures to minimize unwanted losses and provide more flexibility in dumping angle.
213 m
115-150 m
TIDVG +63.5 mm
mdx
off
mdx
on
TIDVG
+0 mm
During/after ECN3 commissioning
Post LS3 before ECN3 commissioning

## Slide 21: Hardware
4 MDX magnets (2 per plane)
4 SIRIUS_2S (1 per magnet):
  2S to get 1.8 kV for 4 Hz
  Fully programmable function
  4 quadrant operation (bipolar current & voltage)
  Info from Gilles Le Godec (2018)
Drift of 100 m from dilution system to target (no optics in between)
M. Fraser BDF/SHiP Final Focus and Dilution System HI-ECN3 WP2 meeting 10th April 2024

## Slide 22
Final focus and dilution system: beam instrumentation
For BDF/SHiP CDS BI considered:
    A 2D position & beam size monitoring system, screen-type, ~ 50m upstream the target for offline monitoring and images every 100 ms
    A beam current monitor
    A target beam monitoring system
To be discussed:
    Live beam position monitoring
    CCC in TCC8 or SEM device
    Do we need to look at target front-face