## Slide 1: Target complex introduction HI-ECN3 BDF target & target complex initial review
Jean-Louis GRENARD – WP4
Acknowledgement: J. M. Martin Ruiz, C. Ahdida, M. Calviani, R. F. Ximenes , M. Fraser, R. Jacobsson, L. Krzempek, G. Mazzola, C. Mucher
29-04-2024

## Slide 2: Target Complex presentations - goal
Set the scene with the current design
Highlight the key challenges
Detail ongoing and foreseen studies during the TDR phase
Identification of missing or unclear areas
Needs of technologies development

## Slide 3: Target complex agenda

## Slide 4: What do we call Target Complex?
The target area
  Target station which contain the target
  Associated shielding
  The space to perform target maintenance activities (inspections, replacement, repair…)
  Remote handling equipment (crane, spreaders, mobile robots)
  Confinement(s)
The target service building
  Air handling units
  Cooling stations
  Controls systems
  The space to perform post irradiation examination and preparation for target (and other activated components) final disposal

## Slide 5: Target Complex in an existing facility
CERN
Prevessin site
CERN
Meyrin site
SPS
ring
SPS extraction
towards North Area
ECN3
Implementation in the SPS North Area ECN3 designed at construction in 70’s for a High Intensity (NAHIF)
Currently used by NA62 experiment
SPS North Area beam lines and associated infrastructure being currently consolidated
Would require the dismantling fraction of current beam line, target station, the experiment
Only one target station can be accommodated in the cavern

## Slide 6: BDF/SHiP Target & Complex
New
Service Building
~ 500 – 700 m2
ECN3
Beam Dilution System
New
Access Shaft
(material only)
88 m2
TCC8
Existing
Access Shaft
48 m2
B918
B911
New Target Complex
containing the Beam Dump Target

## Slide 7: The TCC8 area
TCC8 cross section (length 170m)
8m soil
~10m bellow ground

## Slide 8: BDF Target complex integration
Target area
Confinement wall
Access chicane
Mobile Shielding
Above Coil Shielding
Magnetized
shielding
Water cooled proximity shielding
Target
Upstream Shielding
Collimator
Target station
SHIP experiment
Diluted Proton beam from SPS
Space for shielding temporary storage
Beam instrumentation
Vacuum confinement

## Slide 9
BDF Target complex integration - shielding
~12m
~8m
~4,8m
~ 180 m³ (~1400t) of cast iron + US1010
~ 360 m³ (~800t) of concrete / marble

## Slide 10: BDF Target complex integration extraction

## Slide 15
Installation of lifting tool
which include shielding

## Slide 26: Space requirement for target exchange
~30m

## Slide 27: The target service building
Nuclear ventilation system of the target complex
  Air handling units, filters, dehumidifiers (outside)
Target cooling systems
  Pumps, Filters, Heat exchanger, Cooling instrumentation, He circulation system (target primary confinement)
Target controls systems
  Target monitoring (sensors), Target control valves, vacuum vessel confinement
  Service cell
Evaporator
Electrical distribution system
~700m²

## Slide 28
Shielded buffer zone
Material access
Cooling equipment
Service cell
with a movable roof
*equipement shown based from ECN4 design
Control racks
Hotcell
New lorry access
Overhead travelling crane
Service building

## Slide 29
Service building within the BDF/SHiP complex

## Slide 30: Description of subsystems described in the next talks