## Slide 1: Target complex futur development HI-ECN3 BDF target & target complex initial review
Jean-Louis GRENARD – WP4
Acknowledgement: J. M. Martin Ruiz, C. Ahdida, M. Calviani, R. F. Ximenes , M. Fraser, R. Jacobsson, L. Krzempek, G. Mazzola, C. Mucher
29-04-2024

## Slide 2: Agenda
Target station vacuum confinement
Target handling
Target shielding extraction
Target Complex handling
Target utilities – cooling
Target positioning,
Systems failure scenarios

## Slide 3: Target station vacuum confinement
Overall dimensions: ~6.36 x 2.05 x 2.95 m
Can be fully fabricated and tested at a contractor premisses
Primary vacuum to optimize air activation around target
Water containment (in case of water leak)

## Slide 4: Target station vacuum confinement
500 mm
120 mm
Skin thickness: 30 mm
Grid of HE 100 M beams (each 120 mm tall) crossing each other at 90º, 500 mm separation
Skin thickness: 30 mm
Boundary condition: floor beams fixed to the floor in the vertical direction.
Max displacement 3 mm
Max VM stress in the sheet: ~200 MPa local peak, lower elsewhere
Max utilization factor of the beams:0.49
Buckling factor: 0.82
Simplified analysis using 1-d beams and 2-d shell elements
More detail vessel design

## Slide 5: Target station vacuum confinement
Utilities feedthroughs
Mechanical design ready to build a prototype
Design of radiation tolerant gaskets
Decommissioning plan

## Slide 6: Target handling
Target utilities removed to fit cask

## Slide 7: Target shielding extraction
Extraction on a trolley mounted on chain action rollers
~200t to move
Mainly developed around ‘’standard’’ cast iron blocks
In view of reuse of existing blocks from old facilities

## Slide 8: Target shielding wheels
Investigation for full stainless steel chain action rollers
Designed by specialized company:
  Type of stainless steel
  Number of rollers and configuration (8 rollers foreseen)
  Prototypes stainless steel rollers already at CERN ready for a test campaign (material selection assessment, test, ageing under harsh environment)

## Slide 9: Target extraction mechanism
Installed on purpose prior to target trolley extraction
Possible mechanisms
  Serapid chain (push/pull rigid chain)
  Hydraulic jacks

## Slide 10: Target Complex handling - coil
Remove coil tails
Lower Coil into cask
Coil utilities:
Power feeding
Support plugin system
Remotely compatible Lifting
Active cooling?

## Slide 11: Maintenance of the target complex - few ideas
Target exchange
  Connections of utilities located in ‘’human’’ accessible environment
  Remote handling features for the connections
  Support of remotely controlled crane and ROVs
  Size reduction for final disposal by shearing
  Transfer from the underground to surface in shielded casks
n-TOF target#2 pipes reduction with ROVs

## Slide 12: Target Complex handling
Existing overhead travelling crane 30t capacity replaced
  Redundancy on the 3 movements of the crane
  Integration of a video system
  Integration of a positioning system for the 3 movements
  Off-board control cubicles
  Cable festoon routing
  Remote tools connection on the hook
  Auxiliary hoist
  Investigation on possibility to optimize crane size
  Ongoing specification

## Slide 13: Target Complex handling
Lifting spreaders developments
  Target
  Shielding blocks
  Coil
  Casks

## Slide 14: Target Complex handling
Casks
One major limitation -> 30t object to handled + cask
Target cask
Coil cask

## Slide 15: Service building – Service cell - Hotcell
Purpose
  Repair of activated components
  Size reduction and material separation for final disposal to optimize cost using different elimination path
  Post Irradiation Examination
Tools envisaged
  Master-slave manipulators
  Robots (fixed and mobile)
  Custom built machinery

## Slide 16: Traget complex cooling circuit
Number from CDS

## Slide 17: Target cooling systems
~5m²
~5m²
~20m²
To be located in a shielded area (was located in the underground area in the CDS)

## Slide 18: Ventilation systems
~150m²
Number from CDS

## Slide 19
*equipement shown based from ECN4 design
Target station and service building air handling units
Ventilation systems

## Slide 20: Target positioning
Target alignment precision with respect to beam line 1cm! But…
Everything inside the vessel can’t be realigned after 1rst start of operation
  Target need to have alignment features on its side
  Robust plug-in system (should survive several target exchange)
  Need measurement jigs to measure references every time we replace the target
  Need of remote technic measurements?
Floor and building deformation to take in consideration

## Slide 21: Systems failure scenarios
Evaluation required for operation and maintenance scenarios
  Water leak
  Vacuum leak
  Fire
  Ventilation
  Cooling
  Extraction system
  Handling tools