## Slide 1: FalconD 12T: mechanical design
Date: March 18th, 2024
Authors: N. Sala on behalf of FalconD collaboration

## Slide 2: Mechanical structure: parameters
SS pad (xpad= 100 mm, ypad= 90 mm)
Aluminum shell (th = 50 mm)
SS stiffener (rstiff = 12 mm)
45o split iron yoke (ryoke = 275 mm)
SS or KAWA keys

## Slide 3
Nicola Sala
3
* «A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators» by G. Vallone (2023) DOI: 10.1109/TASC.2023.3248544
*
mechanical properties: MQXF*

## Slide 4
Material | Behaviour | E [GPa] | Stress limit [MPa] | Stress limit [MPa] | [mm/m]
 |  | @ R.T. (1.9K) | @R.T. | @1.9K | R.T. → 1.9K
Glidcop wedges | ductile | 100 (110) | 270 | 340 | 3.37
Fiberglass | - | - | - | - | -
SS316LN* pad | ductile | 193 (210) | 238 | 610 | 2.80
Kawa SS keys | ductile | 186 (204) | 320 | (?) | 1.80
Iron yoke* | fragile | 204 (225) | 250 | 720 | 2.00
Al7075* shell | fragile | 72 (79) | 480 | 490 | 4.20
Material | Behaviour | E [GPa] | Stress limit [MPa] | Stress limit [MPa] | 
 |  | @ R.T. (1.9K) | @R.T. | @1.9K | R.T. → 1.9K
Glidcop wedges | ductile | 100 (110) | 270 | 340 | 3.37
Fiberglass | - | - | - | - | -
SS316LN* pad | ductile | 193 (210) | 238 | 610 | 2.80
Kawa SS keys | ductile | 186 (204) | 320 | (?) | 1.80
Iron yoke* | fragile | 204 (225) | 250 | 720 | 2.00
Al7075* shell | fragile | 72 (79) | 480 | 490 | 4.20
ANSYS Mechanical model: properties*
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone

## Slide 5: Mechanical structure: protect coils
soft to assemble @ RT (absorb overstress @ RT)
hard to deform @ 1.9 K (“low” stress coils @ 1.9 K)

## Slide 6: Assembly: priorities
Vertical Key: pre-stress coils
()
45° Degree Stiffener: hard to deform @1.9K
Horizontal Key: alignment ()
1.
2.
3.

## Slide 7
vertical key @ R.T.
pumping of vertical bladder
insertion of vertical key ()
[MPa] | [mm]
5 | 0.07
10 | 0.2 (nominal)
15 | 0.4 (nom + 0.2)
20 | 0.6 (nom + 0.4)
5 | 0.07
10 | 0.2 (nominal)
15 | 0.4 (nom + 0.2)
20 | 0.6 (nom + 0.4)

## Slide 8
stiffening @ R.T.
pumping both horizontal & 45 degrees bladders
insertion of «stiffener» (no interference)
[MPa] | [mm]
30 | 0.35 (nom + 0.35)
30 | 0.35 (nom + 0.35)

## Slide 9
horizontal key @ R.T.
[MPa] | [mm]
30 | 0.4 (nom + 0.3)
30 | 0.4 (nom + 0.3)
keep pumping both horizontal & 45 degrees bladders
insertion of horizontal key ()

## Slide 10
end of assembly @ R.T.

## Slide 11
end of assembly @ R.T.
Loadstep | [MPa]
1 | 11
2 | 28
3 | 32
4 | 47
5 | 53
6 | 53
7 | 60
Loadstep | 
1 | 11
2 | 28
3 | 32
4 | 47
5 | 53
6 | 53
7 | 60

## Slide 12
cooling down (R.T. 1.9 K)
End of assembly
End of cool down
Stiffening !

## Slide 13
cooling down (R.T. 1.9 K)
End of assembly
End of cool down

## Slide 14
cooling down (R.T. 1.9 K)
End of assembly
End of cool down

## Slide 15
cooling down (R.T. 1.9 K)

## Slide 16
hard to deform @ 1.9 K

## Slide 17
hard to deform @ 1.9 K

## Slide 18
Energization 12T @ 1.9K

## Slide 19
SS Pad (ductile): static analysis
Loadstep | [MPa]
1 | 128
2 | 269
3 | 183
4 | 214
5 | 270
6 | 284
7 | 271
End of Assembly | 234
Cool-down (@1.9K) | 259
Energization (@1.9K) | 411
Loadstep | 
1 | 128
2 | 269
3 | 183
4 | 214
5 | 270
6 | 284
7 | 271
End of Assembly | 234
Cool-down (@1.9K) | 259
Energization (@1.9K) | 411
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | SS316LN* | Nitronic 40*
 | 238 | 682
 | 610 | > 1400
 | SS316LN* | Nitronic 40*
 | 238 | 682
 | 610 | > 1400

## Slide 20
SS Pad: fatigue analysis (compressive)
Loadstep | [MPa]
1 | -128
2 | -296
3 | -202
4 | -191
5 | -200
6 | -211
7 | -216
End of Assembly | -257
Cool-down (@1.9K) | -215
Energization (@1.9K) | -472
Loadstep | 
1 | -128
2 | -296
3 | -202
4 | -191
5 | -200
6 | -211
7 | -216
End of Assembly | -257
Cool-down (@1.9K) | -215
Energization (@1.9K) | -472

## Slide 21
SS Pad: fatigue analysis: (tensile)
Loadstep | [MPa]
1 | 92
2 | 267
3 | 192
4 | 197
5 | 250
6 | 271
7 | 251
End of Assembly | 214
Cool-down (@1.9K) | 245
Energization (@1.9K) | 256
Loadstep | 
1 | 92
2 | 267
3 | 192
4 | 197
5 | 250
6 | 271
7 | 251
End of Assembly | 214
Cool-down (@1.9K) | 245
Energization (@1.9K) | 256

## Slide 22
Copper wedges (ductile): static analysis
Loadstep | [MPa]
1 | 13
2 | 23
3 | 21
4 | 46
5 | 54
6 | 64
7 | 73
End of Assembly | 65
Cool-down (@1.9K) | 100
Energization (@1.9K) | 207
Loadstep | 
1 | 13
2 | 23
3 | 21
4 | 46
5 | 54
6 | 64
7 | 73
End of Assembly | 65
Cool-down (@1.9K) | 100
Energization (@1.9K) | 207
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | Copper
 | 270
 | 340
 | Copper
 | 270
 | 340

## Slide 23
SS keys (ductile): static analysis
Loadstep | [MPa]
1 | -
2 | -
3 | 204
4 | 162
5 | 178
6 | 184
7 | 184
End of Assembly | 334
Cool-down (@1.9K) | 237
Energization (@1.9K) | 677
Loadstep | 
1 | -
2 | -
3 | 204
4 | 162
5 | 178
6 | 184
7 | 184
End of Assembly | 334
Cool-down (@1.9K) | 237
Energization (@1.9K) | 677
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | SS316LN* | Nitronic 40*
 | 238 | 682
 | 610 | > 1400
 | SS316LN* | Nitronic 40*
 | 238 | 682
 | 610 | > 1400

## Slide 24
45° SS key static analysis
Loadstep | [MPa]
1 | -
2 | -
3 | -
4 | -
5 | -
6 | 8
7 | 9
End of Assembly | 7
Cool-down (@1.9K) | 10
Energization (@1.9K) | 574
Loadstep | 
1 | -
2 | -
3 | -
4 | -
5 | -
6 | 8
7 | 9
End of Assembly | 7
Cool-down (@1.9K) | 10
Energization (@1.9K) | 574
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | SS316LN* | Nitronic 40*
 | 238 | 682
 | 610 | > 1400
 | SS316LN* | Nitronic 40*
 | 238 | 682
 | 610 | > 1400

## Slide 25
Al7075 Shell (*brittle): static analysis
Loadstep | [MPa]
1 | 8
2 | 63
3 | 83
4 | 81
5 | 110
6 | 141
7 | 169
End of Assembly | 84
Cool-down (@1.9K) | 19
Energization (@1.9K) | 195
Loadstep | 
1 | 8
2 | 63
3 | 83
4 | 81
5 | 110
6 | 141
7 | 169
End of Assembly | 84
Cool-down (@1.9K) | 19
Energization (@1.9K) | 195
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | Al7075
 | 480
 | 490
 | Al7075
 | 480
 | 490

## Slide 26
Iron yokes (*brittle): static analysis
Loadstep | [MPa]
1 | 65
2 | 44
3 | 120
4 | 110
5 | 120
6 | 124
7 | 148
End of Assembly | 204
Cool-down (@1.9K) | 158
Energization (@1.9K) | 655
Loadstep | 
1 | 65
2 | 44
3 | 120
4 | 110
5 | 120
6 | 124
7 | 148
End of Assembly | 204
Cool-down (@1.9K) | 158
Energization (@1.9K) | 655
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | Magnetil | ARMCO
 | 250 | 286
 | 720 | 975
 | Magnetil | ARMCO
 | 250 | 286
 | 720 | 975

## Slide 27
Irons: fatigue analysis (compressive)
Loadstep | [MPa]
1 | -7
2 | -44
3 | -138
4 | -127
5 | -139
6 | -143
7 | -170
End of Assembly | -215
Cool-down (@1.9K) | -182
Energization (@1.9K) | -756
Loadstep | 
1 | -7
2 | -44
3 | -138
4 | -127
5 | -139
6 | -143
7 | -170
End of Assembly | -215
Cool-down (@1.9K) | -182
Energization (@1.9K) | -756
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | Magnetil | ARMCO
 | 250 | 286
 | 720 | 975
 | Magnetil | ARMCO
 | 250 | 286
 | 720 | 975

## Slide 28
Irons: fatigue analysis (tensile)
Loadstep | [MPa]
1 | 7
2 | 13
3 | 15
4 | 15
5 | 22
6 | 28
7 | 34
End of Assembly | 54
Cool-down (@1.9K) | 25
Energization (@1.9K) | 225
Loadstep | 
1 | 7
2 | 13
3 | 15
4 | 15
5 | 22
6 | 28
7 | 34
End of Assembly | 54
Cool-down (@1.9K) | 25
Energization (@1.9K) | 225
*A Review of the Mechanical Properties of Materials Used in Nb3Sn Magnets for Particle Accelerators by G. Vallone
[MPa] | Magnetil | ARMCO
 | 250 | 286
 | 720 | 975
 | Magnetil | ARMCO
 | 250 | 286
 | 720 | 975

## Slide 29
during assembly @ R.T.

## Slide 30
Increasing field @ 1.9 K
F(t) = force linearly scaled from 12T

## Slide 31
FalconD: Closed Cavity model
cons: Irons intercept part of the shell contraction, what fraction on the coils? How do I control?
We can «increase» the load (es. thk of Al shell but not the % of load on coils).

## Slide 32
FalconD: Closed Cavity model
Irons intercept part of the shell contraction, what fraction on the coils? How do I control?
Instrumented yoke lamination ?

## Slide 33
FalconD: Open Cavity model
+
Horizontal splitted Yoke
Assembly features

## Slide 34
pros: Cool Down easier to control (100% shriks on coils)
FalconD: Open Cavity model

## Slide 35
cons: softer system means higher stresses
FalconD: Open Cavity model

## Slide 36
FalconD: Open Cavity model

## Slide 37
Thank you For your attention!