## Slide 1: Energy deposition with and without IR3 upgrade
Predicted energy deposition with and without IR3 (IR7)dispersion suppressor collimators. Gain from collimators. Performance reach from comparing peak heat deposition with quench limit. Comparison with MD results.
Outline:
Benefit of the DS collimator for the (peak) power deposition on the super conductive coils and cables of the magnets in the DS;
Short discussion of the May 8th/9th MD (quenching test);
Vittorio Boccone for the FLUKA Team (EN/STI)

## Slide 2: Impact of the DS-collimator
The impact of the DS collimator (alias TCLD and formerly know as TCryo) as studied in the case of IR7 (2009 and 2010) at 7 TeV, nominal LHC (0.2h lifetime);
The scenario in IR3 is slightly different as the TCLD and Q10 are now swapped;
The differences do not change the overall effects of protection of the DS elements. For this reason the results for IR7 can still be considered “valid” from a point of view DS-power load and peak power on the coils of the downstream magnets.
transversely shifted by 3 cm
-3m shifted in s
+3m shifted in s
MQ.7R7.B1
MQTLI.7R7.B1
MCBCH.7R7.B1
MCDO.8R7.B1
MB.A8R7.B1
MCS.A8R7.B1
MB.B8R7.B1
MCS.B8R7.B1
MCDO.11R7.B1
MB.A11R7.B1
MCS.A11R7.B1
MB.B11R7.B1
MCS.B11R7.B1
old DS-collimator configuration R. Assmann ‘09
3m
3m
2
14/06/11
V.Boccone - Collimator Review 2011

## Slide 3
The benefits of the DS collimator from the point of view of the reduction of the peak power in the superconductive coils of the magnets were shown by F.Cerutti at the CDR LHC Phase II Collimation, April 2nd 2009 (DS in IR7, only horizontal losses);
The beneficial effect of the DS collimator were quantified. Peak power is below (but not far from) the quench limit. The 1.5 factor for the ultimate intensity does not change the picture.
Impact of the DS-collimator
Peak Power on superconductive coils in IR7 (2009)
Peak Power along the MQ.8R7 (7 TeV, 0.2h beam lifetime, LHC nominal)
[mW/cm3]
3
14/06/11
V.Boccone - Collimator Review 2011

## Slide 4
277 W
171 W
161 W
327 W
Power Impacting on the DS (IR7)
Impact of the DS-collimator
protons, no DS coll.
Pb-ions, no DS coll.
protons, DS coll. in tungsten @15σ
Pb-ions, DS coll. in copper @15σ
4
14/06/11
V.Boccone - Collimator Review 2011
from F. Cerutti (CDR LHC Phase II Collimation, April 2nd 2009)
Total power for 7 TeV, nominal LHC 0.2h beam lifetime scenario

## Slide 5
For the LHC proton beam, the addition of the TCLDs is expected to decrease the predicted peak power in the superconducting coils of the DS magnets by a factor from 5 (1m copper jaws) to 15 (1m tungsten jaws), which is critical for quench occurrence;
The total load on the cold magnets is decreased as well;
The benefits are not strongly dependent on the TCLD aperture (provided that it is not too large);
The reduction is even more significant for the lead beam (a factor of 10 with 1m Cu jaws);
Possible issues:
The 2009 loss maps (IR7) was only including protons SD from the horizontal TCP;
The 2011 loss maps (IR3) show a non negligible contribution of vertical component.
Impact of the DS-collimator
A recall to the conclusions of 2009
5
14/06/11
V.Boccone - Collimator Review 2011

## Slide 6: Few consideration about the May 8th/9th MD
Quenching limits assumptions (MB/MQ)?
3.5 TeV (I=6 kA) Ppeak≈ 41 mW/cm3;
7 TeV (I=12 kA) Ppeak≈ 15 mW/cm3;
Chart: Iop (A)
| 4000.0 | 5000.0 | 6000.0 | 7000.0 | 8000.0 | 9000.0 | 10000.0 | 11000.0 | 11850.0 | 12000.0 | 13000.0 | 13720.93
localized heat deposit (1 cable) | 118.3023 | 108.1531 | 97.4159 | 86.8932 | 77.6733 | 70.5735 | 62.4999 | 42.8494 | 35.0005 | 32.8468 | 20.4935 | 6.4105
distributed heat deposit (5 cables) | 48.4977 | 44.755 | 41.2936 | 38.2086 | 35.5394 | 33.1001 | 29.6835 | 18.7388 | 14.9829 | 14.3849 | 11.4355 | 4.4776
Estimated through the results of heat transfer measurements, in case of localized and distributed loss (courtesy of P.P. Granieri and E. Todesco).
6
14/06/11
V.Boccone - Collimator Review 2011
from P.P. Granieri
For a detailed analysis, description and discussion of the May 8th/9th MD
D.Wollman “Collimation setup and performance” (morning session);
A.Rossi “Proton beam performance with and without IR3 upgrade” (about an hour ago).
MD was on beam2 and (DS.left) but we have only the loss maps for beam1 (DS.right).
Question we try to answer only using FLUKA and the collimator loss map from SixTrack:
Where do we lose the protons?
Which was the power deposited on the magnets?
Are we compatible with the non quench scenario?

## Slide 7: Proton loss pattern in IR7 DS.R
FLUKA tracking from the impact maps on the primary collimators (provided by SixTrack only horizontal halo):
E=3.5 TeV intermediate collimator settings (R. Bruce, Nov. 2010), 10 μm mean impact parameter in the TCP.C6L7.B1
E=7 TeV nominal (tight) collimator settings (Jul. 2009), 20 μm mean impact parameter in the TCP.C6L7.B1
Few consideration about the May 8th/9th MD (2/5)
Very sensitive on
machine aperture
7
14/06/11
V.Boccone - Collimator Review 2011
protons lost in cell 8-9
protons lost in cell 11
protons exaping the DS

## Slide 8: Peak Power profile in sector 11
Few consideration about the May 8th/9th MD (3/5)
averaged over the cable radial thickness (15mm)
Below quenching limits
8
14/06/11
V.Boccone - Collimator Review 2011
Loss rate assumptions:
3.5 TeV: 9 1011 p/s
7 TeV: 4.3 1011 p/s (0.2h beam lifetime, nominal intensity)

## Slide 9: Peak Power profile in sector 8-9
Few consideration about the May 8th/9th MD (4/5)
9
14/06/11
V.Boccone - Collimator Review 2011
Loss rate assumptions:
3.5 TeV: 9 1011 p/s
7 TeV: 4.3 1011 p/s (0.2h beam lifetime, nominal intensity)
averaged over the cable radial thickness (15mm)
Results are self consistent with previous simulation for IR7
Below quenching limits

## Slide 10: Losses in the DS and BLM pattern
Few consideration about the May 8th/9th MD (5/5)
cell
8 - 9
cell
11
10
14/06/11
V.Boccone - Collimator Review 2011
Loss rate assumptions:
3.5 TeV: 9 1011 p/s
7 TeV: 4.3 1011 p/s (0.2h beam lifetime, nominal intensity)
Ratio (Fluka) LSS/Q11 ≈ 1.5 104
Ratio (Fluka) LSS/Q8 ≈ 0.6 104
BLM signal Ratio | MD 8th/9th May '11 | Fluka Calculations
LSS/Q11 | 1.44 104 | 1.5 104
LSS/Q8 | 1.5 103 | 6.0 103
Preliminary comparison (only local proton power deposition) between BLM pattern and Fluka calculation.
MD was on B2 (IR7 left) while we had loss maps only for B1 (IR7 right) => Possible issues with asymmetry in BLM positions.
The difference for Q8 is explained by the asymmetry of the BLM position and by the secondary particles leaking from the LSS (not considered in this preliminary results because of the short timescale of the simulation)
Ratio (MD) LSS/Q8 ≈ 1.5 103
Ratio (MD) LSS/Q11 ≈ 1.44 104

## Slide 11: Conclusion
11
14/06/11
V.Boccone - Collimator Review 2011
We recall the results of the DS-collimator simulation for the IR7 case. The addition of the TCLDs is expected to decrease the predicted peak power in the superconducting coils of the DS magnets up to a factor of 15 (1m tungsten jaws).
Peak power is below (but not far from) the quench limit. The 1.5 factor for the ultimate intensity does not change the picture.
Few consideration about the May 8th/9th MD:
  Simulated peak power in the elements of cell 8-9 and cell 11 were below the quenching limits for the MD at 3.5 TeV and for the 0.2h scenario at 7 TeV;
  Preliminary comparison of the BLM loss pattern with the one measured in the MD.

## Slide 12: BACKUP SLIDES
12
14/06/11
V.Boccone - Collimator Review 2011

## Slide 13: Dose on the tunnel floor
Peak power deposition on the superconductive BB links
Information needed for the relocation of the QPS
QPS possible
locations
13
14/06/11
V.Boccone - Collimator Review 2011

## Slide 14: TCLD model in the IR3 layout
The new DS-collimator optics (IR3) layout for the was implemented
The TLCD FLUKA model includes the BB rerouting in the cryogenic bypass (very close to Beam Pipe);
Implement a virtual BB rerouting in front of the MQ downstream the TCLD collimator;
TLCD Collimators opened at 15 sigma;
Two loss maps corresponding to the interaction of the horizontal and vertical primary collimators;
Peak power deposition on the superconductive BB links
Portion of the DS.R3
MB.B8
MQ.8
MB.A9
MB.9
MQ.9
MB.A10
MB.B10
MQ.10
TCLD.10
TCLD.8
Loading protons at the entrance of the collimator (proton map from SixTrack simulation by A.Rossi D.Wollmann)
M3
M2
M1
section at
beam height
M1
M3
M2
Beam 1
≈ 4 cm
14
14/06/11
V.Boccone - Collimator Review 2011
Calculation are ongoing.

## Slide 15: Details of the geometry
Peak power deposition on the superconductive BB links
BB Rerouting
Impacted Jaws
Virtual BB
Coils of the MQ
15
14/06/11
V.Boccone - Collimator Review 2011

## Slide 16: Uncertainties
V.Boccone, Review of Proposed LHC Collimation Work in DS for 2012
16
14/06/11
V.Boccone - Collimator Review 2011

## Slide 17: Beam Halo (protons)
Slide from: F. Cerutti, LCWG meeting, May 10th 2010
at the entrance of TCRYO.AR7.B1
[T. Weiler]
11% (→ 16%) above 30 sigma
16% (→ 23%) above 15 sigma
CDR LHC Phase II Collimation,
April 2nd 2009
91 (→128) W
132 (→179) W
[→ correction by FLUKA]
17
14/06/11
V.Boccone - Collimator Review 2011

## Slide 18: Power deposition in the MQ.8R7.B1 coils
[mW/cm3]
TCRYO jaw:
1m tungsten @ 15 sigma
for 0.2h beam lifetime
2cm x 3cm transverse section
[being z
the distance from
the magnet front face]
y [cm]
x [cm]
5.0
z = 290-300cm
1.1
z = 10-20cm
10cm x 20cm transverse section
0.30
z = 0-10cm
0.39
z = 0-10cm
z = 0-10cm
0.76
Slide from: F. Cerutti, LCWG meeting, May 10th 2010
18
14/06/11
V.Boccone - Collimator Review 2011

## Slide 19: Shielding options
ideally a continuous liner (here 3mm tungsten, green curve) is quite effective
end plates of limited help
assumed as totally absorbing! blue curve
L=2.5L0
Q1
Q1
Q2a
Q2a
Q2b
Q3
Q2b
Q3
Slide from: F. Cerutti HL-LHC Kick of internal meeting, April 11th 2011
as an alternative, a thick liner in Q1 (here 13mm stainless steel, purple curve) casting a shadow over Q2a
130mm coil aperture
the role of the interconnections! jump at the Q2a front face with liner limited to the first element, blue curve
19
14/06/11
V.Boccone - Collimator Review 2011

## Slide 20: The Pb beam Halo
Slide from: F. Cerutti, LCWG meeting, May 10th 2010
at the entrance of TCRYO.AR7.B1
[G. Bellodi]
0.22%
above 15 sigma
CDR LHC Phase II Collimation,
April 2nd 2009
175 W
2.6 W
161 W ± 2%
22.5 W ± 6% ]
[ at the entrance
of TCRYOB

## Slide 21: MB Quench Limit
The steady-state heat deposit the MB cables can withstand is estimated through the results of heat transfer measurements, in case of localized and distributed loss
The driving mechanism is indeed the heat transport through the cable electrical insulation. (Slightly) conservative assumptions are considered to account for the differences between the experimental setup and the real magnet
The considered heat deposit is
uniform in the cable cross-section, as
well as in the longitudinal direction
Further analyses are ongoing to
model the heat flux distribution in
the coil, thus allowing to improve
the quench limit estimation
Slide from P.P. Granieri - MB quench limit and stability
21
14/06/11
V.Boccone - Collimator Review 2011

## Slide 22: MB Stability
The stability of the MB cables with respect to transient heat deposit is estimated through numerical calculation
The mechanism that confers stability is the transient heat transfer between strands and helium in the cable. Hence the model pays particular care to its definition, considering the different helium phases
Strands and cable enthalpy represent
lower and upper limit for stability
The considered heat deposit is uniform
in the cable cross-section, as well as in
the longitudinal direction
Experimental tests would be needed to
obtain a deeper insight of the stability
underlying mechanisms
Slide from P.P. Granieri - MB quench limit and stability
22
14/06/11
V.Boccone - Collimator Review 2011