## Slide 1: Protection of beam vacuum with fast shutters or existing gate valves
Friday, 27th May 2011
Jérôme Chauré

## Slide 2: Introduction
Following the sector 3-4 incident in September 2008 it has been decided by the CERN management to consolidate the LHC beam vacuum system in order to minimise the possibility of collateral damage to LHC systems should a similar incident take place in the future.
Part of this consolidation will include the addition of fast shutters and / or an improvements to the current gate valves, which will allow a faster sectorisation of the beam vacuum and so prevent the propagation of contamination to sensitive in-vacuum equipment near to the site of the incident.

## Slide 3: Dynamic pressure wave
A dynamic pressure wave in the vacuum system can reach a velocity of 1000 ms-1 at room temperature and 35 ms-1 at cryogenic temperature.
valve
Zone to protect
Case 1: Incident in cold section (arc)
20ms closure
Debris at 35 ms-1
1s closure
0.7 m
NOK
NOK
35 m
OK
OK

## Slide 4: Dynamic pressure wave
A dynamic pressure wave in the vacuum system can reach a velocity of 1000 ms-1 at room temperature and 35 ms-1 at cryogenic temperature.
valve
Zone to protect
Case 2: Incident in LSS
20ms closure
Debris at 1000 ms-1
1s closure
20 m
NOK
NOK
1000 m
OK
OK

## Slide 5: Dynamic pressure wave
Following Cedric Garion’s studies, the cold stand alone magnets in the Long Straight Section aren’t long enough to significantly decrease the velocity of the dust and particles.
It is clear that it will not be possible to protect all equipment under all circumstances.

## Slide 6: Equipment to be protected
The purpose of these valves is to protect some LHC components with sensitive elements inside the beam vacuum that would either require replacement or extensive re-conditioning if contaminated.
RF cavities
The main RF accelerating cavities (ACS) are installed in one group of 4 modules symmetrically centred on IR4. They are sensitive to contamination by dust or larger particles. Contamination should be less than experienced by the cavities during assembly in a clean room.
injection kickers
Injection kicker magnets (MKI) are installed in groups of 4 in IR2L and IR8R. They are sensitive to contamination by dust or larger particles. They may also be sensitive to rapid changes in pressure.

## Slide 7: Addition of Fast Shutter
LEP Fast shutter.
Patrick Coly’s work:

## Slide 8: Addition of Fast Shutter
Studies from students at Oxford University Engineering Department:
Beam path
Open Position

## Slide 9: Improvement on existing Gate Valve
Position indicator
Solenoid
Pneumatic actuator
Gate

## Slide 10: Gate Valve
Source: VAT catalog

## Slide 11: Gate Valve
Damping to be kept

## Slide 12: Improvement on Gate Valve DN63 Type A

## Slide 13: Improvement on Gate Valve DN100 Type D

## Slide 14: Closing time improvement for a gate valve
These improvements are due to:
An implementation of a fast exhaust:
An improvement from the air pressure pipe:
  Addition of air reservoir near the valve.
  Increase in pipe diameter from 6*1 to 8*1 mm.
An improvement from the inlet and outlet diameters from the closed plates.
Source: Festo & VAT

## Slide 15: Conclusions

## Slide 16: Acknowledgements
Patrick Coly, Paul Cruikshank, Eugénie Gallay, Cedric Garion, Michael Guinchard, Hendrik Kos,
Willemjan Maan, Benoit Rio, Raymond Veness.