## Slide 1: Requirements/Specifications
In Hugo’s report, 0.65 T.m, from -2.5 m to +2.5 m along magnetic axis with respect to the magnet center, without reference

## Slide 2: Analytical formulation
H.Bajas’s 3D model
Updated model
 |  |  |  |  | Bedstead shape | Racetrack Shape
 |  | Hugo Resistive | Hugo Nb3Sn | Hugo MgB2 | MgB2 N72 | MgB2 N72
Acceptance Vertical | mm | 10000 | 10000 | 10000 | 6000 | 6000
Acceptance Horizontal | mm | 5000 | 5000 | 5000 | 4000 | 4000
Space reservation Vacuum vessel | mm | 100 | 100 | 100 | 100 | 100
Space reservation Coil support | mm | 100 | 100 | 100 | 100 | 100
Longitudinal | mm | 4000 | 4000 | 4000 | 4000 | 4000
Backleg thickness vertical | mm | 1000 | 1000 | 1000 | 1000 | 1000
Backleg thickness horizontal | mm | 1500 | 1500 | 1500 | 1500 | 1500
Backleg depth longi | mm | 3500 | 3500 | 3500 | 3500 | 3500
Mass of iron | tons | 1125 | 1125 | 1125 | 832 | 832
Gap | mm | 5400 | 5400 | 5400 | 4400 | 4400
Magnet efficiency | [-] | 0.9 | 0.9 | 0.9 | 0.9 | 0.9
B0 at I operation Design value | [T] | 0.15 | 0.15 | 0.15 | 0.148 | 0.148
NI total | A.turn | 716197 | 716197 | 716197 | 575787 | 575787
I operation | A | 3000 | 500 | 200 | 4000 | 4000
Number of turns | [-] | 239 | 1432 | 3581 | 144 | 144
Number of turns Design value | [-] | 240 | 1440 | 3600 | 144 | 144
Number of Coil | [-] | 6 | 6 | 6 | 2 | 2
Number of turns/coil mini | [-] | 39.8 | 239 | 597 | 72 | 72
Number of turns/coil design | [-] | 40 | 240 | 600 | 72 | 72
Number of layers/coil | [-] | 4 |  |  | 6 | 6
Number of turns/layer | [-] | 10 |  |  | 12 | 12
Coil width | mm | 522 |  |  | 141.4 | 141.4
Coil thickness | mm | 216 |  |  | 89.4 | 89.4
Length of one turn | m | 37.2 | 70.83 | 35.6 | 24.7 | 20.7
Cable Unit | m |  |  |  | 1778 | 1492
Length of cable | m | 8881 | 102000 | 128000 | 3556 | 2985
B0 at I operation Obtained in FEM | [T] | 0.153 |  | 0.153 | 0.157 | 0.145
Bending Field -/+ 2.5 m along the central axis at Operational current | [T.m] | 0.65 | 0.65 | 0.65 | 0.67 | 0.599
E, stored energy | [J] |  | 4.63E+06 | 4.60E+06 | 3.20E+06 | 2.88E+06
L, calculated from stored energy in report | [H] |  | 37 | 230 | 0.400 | 0.360

## Slide 3
Interturn distance | mm | 12
Interlayer distance | mm | 16
Cable diameter | mm | 9.4
Pole width | mm | 141.4
Pole thickness | mm | 89.4
12 turns/layer = 142 mm
6 layers/coil
1 coil/pole
Schematic cross section of conductor configuration around 1 pole. It features in blue the space reserved for cryostat, in purple the plates including the cooling circuit in purple and conductor in orange. *CAD model of the coil adapted from EESD phase 2
6 layers/coil = 90 mm

## Slide 4
Total cable length: ~ 3.6 km
Total cable length: ~ 3 km
H.Bajas’s 3D model
Bedstead shape coil
Racetrack shape coil

## Slide 5: Field Maps
In acceptance volume, traversal plan
  Field map
  Relative error wrt. B field at (0,0,0)
In acceptance volume, longitudinal plan
  Field map
  Relative error wrt. B field at (0,0,0)

## Slide 6
In traversal plan
Top row : Field maps
Bottom row: relative error wrt. B field at (0,0,0)
H.Bajas’s 3D model
P. Wertelaers model
Bedstead shape coil
Racetrack shape coil

## Slide 7
In longitudinal plan
Top row : Field maps
Bottom row: relative error wrt. B field at (0,0,0)
H.Bajas’s 3D model
Bedstead shape coil
Racetrack shape coil

## Slide 8
Bedstead shape coil
Racetrack shape coil
Hugo’s report

## Slide 12
Total cable length: ~ 3.6 km
Total cable length: ~ 3 km
Int B.dl [-2.5 m; 2.5m] = 0.599 T.m
Stored energy: ~ 2.88 MJ
Bp = 1.3 T
B0 = 0.145 T
3 double pancakes per coil,
12 turns per layer
4 kA per turn

## Slide 14: 3D Opera - Model
12 turns/layer = 142 mm
6 layers/coil
1 coil/pole
Schematic cross section of conductor configuration around 1 pole. It features in blue the space reserved for cryostat, in purple the plates including the cooling circuit in purple and conductor in orange. *CAD model of the coil adapted from EESD phase 2
Global view of the Opera 3D ¼ symmetric model for the SHiP HSS. It features in green color the iron yoke (dimension to be optimized) and in red the coils (1 coil per pole)
6 layers/coil = 90 mm
Magnetic field map on the acceptance limit rectangle on the transversal plan. Current par conductor = 4 kA
2x1x6x12 = 72 turns
Racetrack B0 = 0.149 T Integral B along longitudinal axis = 0.86 T.m
Stored energy = 786 kJ
B0 = 0.149 T

## Slide 15: 3D Opera - Model
Alternative bedstead coil design