## Slide 1: Formation of a forward beam of antihydrogen Status of the ESDA analysis R. Caravita

## Slide 2: What happens when antihydrogen annihilates
e+/Ps converter
MCP
Excitation lasers
4.6 keV e+
Rydberg Ps
B
1 cm
External Scintillation Detector Array (ESDA)
External Scintillation Detector Array (ESDA)
Antiproton plasma
Dissociated e+
π±
π±
π±

## Slide 3: Antihydrogen detector: digitized ESDA
Scintillator array for MIP detection
8 x EJ-200 scintillator slabs
Scintillators are read at both ends with photomultipliers
Each PMT is digitized at 250 MHz
Software coincidence to reject PMT noise
Amplitude cut to reject gamma background
PMT1
PMT2
EJ-200 scintillator slab
MIP threshold
MIP threshold

## Slide 4: The ESDA digitized acquisition chain in 2023
A 50/50 splitter for each 24 PMT (8 PMT @5Tesla, 16 PMT @1Tesla)
One end is directly connected to the discriminated acquisition chain continuosly monitoring antiproton annihilations
The other end is sent to the platform where it is 20 dB attenuated and digitizer for the acquisition of the antihydrogen signal
The splitter is connected directly to the PMT to minimize ringing due to the impedence mismatching.
Splitters have been installed in vertical orientation(top) except for the 8 top PMT @1Tesla that have been installed in horizontal orientation due to lack of space (bottom)
PMT2
PMT1
SPL
CAEN V1720
SIS COUNTER
SPL
ESDA single slab, 2024 config
20 dB
20 dB

## Slide 5: Dataset overview
Higher pbar flux
from ELENA
Lower pbar flux
from ELENA

## Slide 6: Software trigger and event discrimination
Baseline rms-amplitude Arms estimator from the first 10us of acquisition
Baseline follower: baseline_val = (1.0 – 0.005) * baseline_val + 0.005 .* A(i)
Threshold discriminator with hysteresis (Tup = 8 Arms, Tdown = 3 Arms)
Tup
Tdown

## Slide 7: Coincidence formation
Coincidences filtering
AND on the single PMT events
50 ns coincidence window
PMTn
PMTn+1
List of coincident events
Average time-of-arrival
Time difference between PMTs
Average deposited charge
Average amplitude

## Slide 8: Coincidence formation
No efficiency loss to
pbar/Hbar detection
Reduction in gamma ray background
Cancelling of PMT afterpulses
No coincidence, no charge cut
Coincidence, no charge cut
Coincidence, charge cut

## Slide 9: A beautiful observation of antiprotons swinging
e+ peak at Ps* formation
Antiproton losses in oscillations
Hbar search region

## Slide 10: Where are losses occurring?
Catching trap
Hbar trap
Here the plasma is largest

## Slide 11: A beautiful observation of antiprotons swinging
From 5T to 1T
From 1T to 5T
Midpoints
Theory: midpoints are the points of null velocity

## Slide 12: A beautiful observation of antiprotons swinging
From 5T to 1T
From 1T to 5T
Midpoints
Hypothetical conclusion: time calibration procedure was off by us
we were always sending positrons too early, i.e. with a forward boost
2.5 us
3.5 us
4.0 us

## Slide 13: Antihydrogen signal interpretation
500 ns
500 ns
Hypothetical conclusion: most of our current Hbar is hitting the target

## Slide 14: Backup

## Slide 15: Time calibration 1

## Slide 16: Time calibration 2