## Slide 1: RICH WG
M.Lenti

## Slide 2: RICH Situation: news
All the RICH mirrors at CERN since may
Aluminization will start at CERN in the coming weeks
Mirror support project to be finalized by the end of 2011, then start the tender
Aluminum disk for light collection (“Winston Cones” disks) and PM lodging (“PM disks”) in fabrication in Firenze

## Slide 3: CRATE POSITIONS
HV
SIG
HV
SIG
43U rack 21 POSITIONS
H=213 cm
9U BIN (without PS)
11U crate
3U AIR gap
11U crate
9U BIN (without PS)
43U TOTAL HEIGTH
16 X 32 CH HV FILTER
16 X 32 CH FE_DAQ
SLOW CNTRL GATEWAY
16 X 32 CH HV FILTER
16 X 32 CH FE_DAQ
SLOW CNTRL GATEWAY
R.Ciaranfi

## Slide 4: 3D PCB VIEW: HV FILTER BOARD
SHV CONNECTOR FROM CAEN HV-PS
BRACKET TO FIX BOARD TO THE 9U EMPTY CHASSIS
32 CH HV TO PMT
SPACERS SUPPORT FOR SECURITY COVER
R.Ciaranfi

## Slide 5: 3D VIEW: PM HV DIVIDER (SOCKET)
SOLDERED HV- CONNECTION
TOP AND BOTTOM SMD COMPONENTS
SIG OUT COAX
SOLDERED HV+ (GND)
COAX SHIELD AND HV+ SOLDERED TOGETHER
R.Ciaranfi

## Slide 9
2010:
Number of PMT | Delivery date | Cost (euro)
FIRENZE |  | 
80 | 24/02/2010 | 23728.66
100 | 01/04/2010 | 28978.08
PERUGIA |  | 
120 | 09/05/2010 | 38368.01
400 | 02/07/2010 | 131582.39
400 | 09/09/2010 | 134522.59
110 | 30/09/2010 | 35131.30
TOTAL | 1210 PM | 392311.03 €
2011:
Number of PMT | Delivery date | Cost (euro)
60 (at Firenze) | 25/02/2011 | 18900
40 (at Perugia) | 27/05/2011 | 12600
15 (at Perugia) | 28/07/2011 | 4725
40 (to be delivered) | November? | 12600 ??
M.Pepe
SPARES ?

## Slide 11
Conclusions
RICH on a critical path towards the Tech. Run
Market survey for the RICH vessel ongoing