Electronics Upgrade Meeting
Analog Electronics
COTS design
21/07/2011

---
Summary
COTS approach
Schematics
Board
Measurements
To do

---
COTS approach
Noise requirements impossible to achieve with commercial components.
Friis rule -> need to amplify before doing any other operation.

---
Different Clipping Approach
Clipping after amplifying → Impedance problem
Equivalent system found, same impulse response but no impedance problems.

---
Same Integration system
Integration
  - Delayed Lines Integrator as in the current CALO

---
Schematics
The COTS scheme requires 3 OP amps and 2 delay lines per channel

---
Preliminary measurements

---
DC-DC converters
Able to test DC-DC converters produced by CERN to evaluate possible noise contribution.
Mating connector: SAMTEC CLE-116-01-G-DV-A (female)

---
First Set of Prototypes

---
First Set of Prototypes
Analog Design
ADC test zone
ADCs
DC-DC converter
Switched Design
(ASIC)
10 Layer board
Stack:
70um conductors
100um FR4 for supplies
(better interplane capacity)
130um FR4 for external
(thin -> low crosstalk)
230um FR4 for internal
(minimum to achieve 50Ω )
1
3
4
2
5
3

---
Testing
On previous prototypes tested roughly analog design
On current prototype:
In depth analog testing
ADC testing
DC-DC evaluation

---
ADC testing
First measurents with ADC reveal some noise, slightly higher than theoretical predicted one, different mean because R tolerances
0.6513 LSB rms
vs.
0.54 LSB rms theoretical
1.1547 LSB rms
4Ksamples histogram, Red with short circuit at the input, blue without the short circuit (driven by a zeroed unitary gain driver)

---
Analog power supply
Can it have something to do with the power supply decoupling?
Measured the analog supply with a spectrum analyzer.
No isolated chamber:
1. Radio
2. TV
3. Mobile phone
No power
No Clock
1
2
3
3

---
Analog power supply
Clock drivers’ rise time ~500ps -> High frequency harmonics couple to analog supply.
Effect disappears without clock.
Should study if digital switching could be a relevant noise source.
Power on
Clock on

---
Board level simulation
Beginning Agilent’s ADS simulation
Electromagnetic Model
Gerber and stack import
Circuit Level Simulation Results
S-Parameter extraction
Simulation Component Generation
Spice-like Circuit Sim

---
To do
ADC test with CAT (now capturing with scope)
In depth study of analog proposal:
Noise
Linearity
Pulse Shape: Planarity, Baseline,...
Radhard qualification
Power integrity study (already started)
Verify signal integrity issues (already taken into account)

---
Electronics Upgrade Meeting
Backup Slides

---
First Set of Prototypes
Schematic view