Status of the NEAR activation activities.
Restarting the measurement campaign
Collaboration meeting
CERN
04/06-06-2024
F. García-Infantes, A. Mengoni, N. Patronis, M. E. Stamati, A. Manna, M. Bacak,
G. Tagliente and the n_TOF Collaboration

---
Outline of the presentation
Analysis status
Previous Results
Conclusions from previous results
New measures campaign
B4C filters and sample
HPGe detectors.
Measurement planning
First configurations
Previous talk from M. E. Stamati:
Status of the neutron capture measurements at NEAR using B4C filters
Status of the neutron capture measurements at NEAR using B4C filters
Status of the neutron capture cross section measurements using B4C filters at NEAR
Collaboration meeting - Valencia - 23/11/2023
Francisco Grcía-Infantes – U. Granada - CERN(SY/STI/BMI)
2

---
Analysis status
Francisco García-Infantes – U. Granada - CERN(SY/STI/BMI)
Collaboration meeting - CERN - 6/06/2024
3

---
Step of Data analysis - Overview
4

---
Results extracted from simulations
In order to compare SACS with MACS, It is needed to fix the temperature we will compare with.
Fitting the NEAR spectrum with a Maxwellian distribution can give us an indication.
E. Stamati et al, Status of the neutron capture measurements at NEAR using B4C filters
5

---
SACS vs MACS ratios
Four configurations measured: 2.5 mm, 5 mm, 7.5 mm and 1 cm in front. The same thickness back.
Five samples measured: Au as reference sample, Ge, Ce, Zr and Y.
The maximun temperature under this configuration is 3.09 keV.
Best results has been obtained for the Ge sample.
Filter thickness and corresponding temperature
E. Stamati et al, Status of the neutron capture cross section measurements using B4C filters at NEAR
6

---
Conclusions so far
As is, a SACS measurement can lead to a MACS estimation within a factor 2 or 3. Still important for exotic physics cases, cases in which only theoretical calculations exist.
Improvements:
Increasing the thickness of B4C filters. The maximun thickness so far has been 1 cm in front and 1 cm back.
The present situation could be further improved by shaping the initial spectrum even more with the use of a moderator.
Filter thickness and corresponding temperature
7

---
Why increse the thickness?
Two important points for increasing the thickness:
The agreement between the SACS and MACS has been improving while the thickness of the B4C has increased.
The maximun temperature for MACS is 3.06 keV with the maximun thickness measured so far. It’s important to go higher in energy for astrophysics applications.
M-SACS is the spectral averaged cross section for a Maxwellian distribution (at a given kT)
F-SACS is the spectral average for the NEAR station neutron spectrum, filtered with B4C of given thickness [mm]
It is important to remark from the plot the energy distribution as a function of the B4C filters thicknesses.
Results extracted from Alberto calculations. Thanks Alberto!
8

---
New measures campaign
9

---
B4C filters thickness and samples
Filters Suport + Filters and Sample
So far, there were available 3 filters of 5 mm thickness and 2 of 2.5 mm thickness.
There are 4 new filters available of 5 mm thickness for increasing the thickness.
Same reactions will be measured in this experimental campaign:
76Ge(n,γ)77Ge → pressed pellet of 76GeO2
140Ce(n,γ)141Ce →pressed pellet of CeO2
94Zr(n,γ)95Zr → 94Zr lumps
197Au(n,γ)198Au → 197Au foil
89Y(n,γ)90Y → 89Y foil
Filters + Sample
2.5 mm thickness
5 mm thickness
3 mm thickness
10

---
HPGe Detector problems
The new measured campaign started on May 10. The HPGe detector was cooled down and turned it on.
11

---
HPGe Detector problems
The new measured campaign started on May 10. The HPGe detector was cooled down and turn it on.
This noise signal correspond to the ones recorded direclty from the HPGe
Some noise started to appeared during this first time that we turn it on the HPGe detector.
This noise signal correspond to the ones recorded after the amplifier
12

---
HPGe Detector problems
The new measured campaign started on May 10. The HPGe detector was cooled down and turn it on.
This noise signal correspond to the ones recorded direclty from the HPGe
Some noise started to appeared during this first time that we turn it on the HPGe detector.
This noise signal correspond to the ones recorded after the amplifier
These noise starts to appear when the voltage applied to the detector is around 600 V. Before, the signals recorded from the detector look fine.
13

---
HPGe Detector problems
The new measured campaign started on May 10. The HPGe detector was cooled down and turn it on.
Some noise started to appeared during this first time that we turn it on the HPGe detector.
These noise starts to appear when the voltage applied to the detector is around 600 V. Before, the signals recorded from the detector look fine.
14

---
HPGe Detector problems
In order to undertand the problem, several solution and checks were performed before replacing the HPGe detector.
The new measured campaign started on May 10. The HPGe detector was cooled down and turn it on.
15

---
HPGe Detector problems
In order to undertand the problem, several solution and checks were performed before replacing the HPGe detector.
The new measured campaign started on May 10. The HPGe detector was cooled down and turn it on.
These checks were:
Cabling check.
Replaced the HV modul and the crate.
Replaced the Amplifier.
Warm it up and cool it down once again.
Conclusions, in all these checks the behaviour was exactly the same. The detector seemed work well, and the noise appear sharply once the detector reachs ~600 V.
16

---
HPGe Detector problems
In order to undertand the problem, several solution and checks were performed before replacing the HPGe detector.
The new measured campaign started on May 10. The HPGe detector was cooled down and turn it on.
These checks were:
Cabling check.
Replaced the HV modul and the crate.
Replaced the Amplifier.
Warm it up and to cool it down once again.
Conclusions, in all these checks the behaviour was exactly the same. The detector seemed work well, and the noise appear sharly once the detector reachs ~600 V.
In view of the problem:
The problem (most probably) is the Preamp.
We contacted people from Canberra enterprise. Still waiting for a replied.
In the meantime:
The second HPGe detector has been setup for the activation measures.
17

---
HPGe Detector problems
In view of the results:
The problem (most probably) is the Preamp.
We contacted people from Canberra enterprise. Still waiting for a replied.
In the meantime:
The second HPGe detector has been setup for the activation measures.
Thanks Michi and Nikolas!!!
18

---
HPGe Detector problems
In view of the results:
The problem (most probably) is the Preamp.
We contacted people from Canberra enterprise. Still waiting for a replied.
In the meantime:
The second HPGe detector has been setup for the activation measures.
Energy and efficiency calibration are on going, as the detector has been used at EAR1 and it should be checked. For the moment, resolution is good and it is ready to start the measures campaign.
Thanks Michi and Nikolas!!!
19

---
Measurement planning
20

---
First configurations
The measured campaign was re-started on May 31, last Friday.
The second HPGe detector has been cooling down and turned on. The energy and efficiency calibration are needed. As this detector has been on beam several time for the last years.
The plan is to start measuring the following configurations:
The first configuration, running now, consists in a gold sample without B4C filter in front.
Sample
Third Configuration
Gold sample with 5 mm thickness back.
21

---
First configurations
The measured campaign was re-started on May 31, last Friday.
The second HPGe detector has been cooling down and turned on. The energy and efficiency calibration are needed. As this detector has been on beam several time for the last years.
The plan is to start measuring the following configurations:
The first configuration, running now, consists in a gold sample without B4C filter in front.
The second configuration consists in a gold sample with 5 mm of B4C filter in front. In order to compare with a configuration from last year.
Sample
Third Configuration
Gold sample with 5 mm thickness back.
Second Configuration
Gold sample with both 5 mm thickness in front and back.
22

---
First configurations
The measured campaign was re-started on May 31, last Friday.
The second HPGe detector has been cooling down and turned on. The energy and efficiency calibration are needed. As this detector has been on beam several time for the last years.
The plan is to start measuring the following configurations:
The first configuration, running now, consists in a gold sample without B4C filter in front.
The second configuration consists in a gold sample with 5 mm of B4C filter in front. In order to compare with a configuration from last year.
The third configurations consists in one of the four sample: 76Ge, 140Ce, 94Zr or 89Y, with both 5 mm in front and back. In order to compare with a configuration from last year.
Sample
Third Configuration
76Ge, 140Ce, 94Zr or 89Y sample with 5 mm thickness in front and back.
23

---
First configurations
The measured campaign was re-started on May 31, last Friday.
The second HPGe detector has been cooling down and turned on. The energy and efficiency calibration are needed. As this detector has been on beam several time for the last years.
The plan is to start measuring the following configurations:
The first configuration, running now, consists in a gold sample without B4C filter in front.
The second configuration consists in a gold sample with 5 mm of B4C filter in front. In order to compare with a configuration from last year.
The third configurations consists in one of the four sample: 76Ge, 140Ce, 94Zr or 89Y, with both 5 mm in front and back. In order to compare with a configuration from last year.
The fourth configurations consists in one of the four sample: 76Ge, 140Ce, 94Zr or 89Y, with 10 mm in front and 5 mm back. In order to compare with the same configuration than last year in front and to assess the background contribution changing the thickness back.
Sample
Third Configuration
76Ge, 140Ce, 94Zr or 89Y sample with 5 mm thickness in front and back.
Fourd Configuration
76Ge, 140Ce, 94Zr or 89Y sample with 10 mm thickness in front and 5 mm back.
24

---
Conclusions
The maximum energy reachs, so far, has been 3.06 keV. If we want to go higher it is needed: use moderators or increase the thickness of B4C filter. For the moment, we will go trhough the incresment of the thickness.
The measurement campaign was restarted on May 10, but it was interrupted because problems were found in the HPGe detector used the last two years. No solutions from our side solved the problem. In contact with people from Canberra enterprise.
The second HPGe detector available at n_TOF has been setup and both energy and efficiency calibration are on going.
The first four weeks will be dedicated to check data between this and the previous year.
Once, we finish the first part of the measurement the plan it is to go ahead with the new filters and to increse them. For the moment, the plan is under discussion, depending mainly on the impact of the background varying the thickness back.
25

---
Thank you very much for your attention!!!
26