## Slide 1: R2E News
Failures observed during 2011 operation (Collimation (3x), Cryo PLCs (3x), QPS ISO, uFIP, PCs, UPS?, Biometry)
  Detailed analysis of respective radiation level is very important to check for 2011/2012 operation
  in general levels follow the predicted pattern
  performed actions (shielding RR73/77, UJ76, UJ23, UJ87, relocation actions, etc…) were important
Patch-Solutions asked for by the management – the planning for those also strongly depends on the detailed analysis of radiation levels
What’s about ‘hidden failures’, e.g., communication problems caused by Ethernet switches (failing early at CNRAD), how can we analyze this?

## Slide 2: R2E News
Weekly radiation reports: Quality of reporting is very good with high quality (it was worth the effort), few things to be followed (r-factor update, BLM tables,…)
Scrubbing-Run: radiation levels much lower than anticipated -> reason: beam-gas densities remained two orders of magnitude lower (heat load on beam-screen was ‘limiting’ factor)
Radiation levels: few question marks remain:
  Difference between UJ14/16 and UJ56 (FGCs don’t show counts)
  Linked: thermal neutrons and R-Factor -> seems to be lower (additional TLD analysis required)
  P4 levels keep rising -> possible impact to UX45 (cryogenics)?

## Slide 3: R2E News
H4IRRAD radiation tests more important than ever, long list of scheduled tests (see website)
R2E safety structure put in question by DSOs/RSOs and HSE, to be followed
Budget update upcoming
  End of June (before ‘summer break’) we have to review the budget estimates (focus on 2011/12)
  Iterations starts now, each responsible for a budget code has to prepare the respective analysis
LMC presentation on collimation control failure analysis (see link)
Update on P1 relocation/shielding options by Anne-Laure yesterday (see link)
R2E review to be scheduled for November