## Slide 1
Ultimate efficiency in linear beam devices.
Electro-vacuum technologies for FCCee
I. Syratchev, CERN

## Slide 2
Novel 400 MHz, 1MW HE Two-Stages MBK for FCCee. Performance summary.
Featured:
Very efficient. 86% @ Z,W,H and 83% @ ttbar2.
Compact. Total length <3m.
Low Voltage. Up to 64kV @ 1 MW.
High RF power gain. 43dB @ 1MW.
Broadband. 3.5 MHz @ -1dB.
Robust. Can handle mismatch up to -15dB.
Efficiency vs. saturated RF power at different klystron voltages
For FCCee, such an efficiency improvement from conventional 65% to 85% will allow to save 38MW of the grid electric power. That is compatible to the electric power needed for the entire FCCee cryogenic system (40MW).

## Slide 3
The new layout with one unique two-gaps cavity for Z,W,H poles, opens options of using one power source per single, or two cavities. Performance of the TS klystron is now optimized for both options with almost identical efficiency.
1 tube x 2 cavities
1 tube x 1 cavities
Bars show P/cavity + 15% power margin
With reduced power per klystron:
Reduced by ~50% collector volume.
Improved beam extraction quality into collector.
Reduced by 10% RF circuit length.
Reduced from 62kV to 47 kV operating voltage.
Reduced power in solenoid
Improved x2 life- time.
Single RF output.
With chosen technology, cost saving will be rather modest – no more than 20% when moving from 1MW tube to 0.5MW tube.
Will need x2 more klystrons.

## Slide 4
"Il n'y a de nouveau que ce qui est oublié« . Marie Antoinette (1785)
IOT (A. Haeff, 1939)
Klystrode
(H. Priest and M.B. Shrader 1982)
Tristron (A.D. Sushkov et. al. 1967)
MB Prototype tested in 1997, V. Tsarev:
FCCee 1MW, 400 MHz 10 beams gridded tubes performance (KlyC simulations)
1 MW, MB Tristron power-efficiency capabilities
Injection: 10 x 120 degrees RF phase bunches (C Class)
High Power Gridded Tubes
CERN, 2024
Rectangular bunch shape

## Slide 5
Tristron efficiency vs. beam perveance
Penultimate cavity tuning
0.906-0.15xP
Overall, tristron demonstrated excellent performance in terms of the ultimate efficiency in a wide range of operating perveance.
Optimized for bunch length of 120 degrees RF phase and fixed beam power (960 KW)

## Slide 6
Tristron 3D CST PIC simulations.
Direct benchmarking with CERN made fast 1.5D computer code KlyC
10 beams (1.6A, 60kV each)
Bz: 0.032T
Beam power 960kW
RF power: 880kW
Efficiency: 91.4%
Penultimate cavity
Output cavity
Bunches velocity modulation
Bunched beam current (4.8A peak; 1.6A average)
120 degrees RF phase long bunches (C class)
Single output port RF signal (440kW)
X10 individual collectors, each 30 cm long.
L total = 0.6m
91.4%
92.4%
CST
KlyC

## Slide 7
Realistic bunches in gridded tubes

## Slide 8
Particles velocity modulation (LRF=0.29m)
1500
1800
2200
Realistic bunches in gridded tubes
Average current 1.6A/beam
1MW, MB Triston efficiency (measured at RF port)
Distance between the cavities (LRF) and penultimate cavity tunings were taken from the ones optimized in KlyC for rectangular bunch shape (see page 4). The is some space left for post-optimization
LRF=0.29m
0.35m
0.435m
B
AB
C

## Slide 9
MB tristron vs. IOT power gain curves
B class (180 degrees bunches)
V beam=60kV
max=93%, 803kW (1.44A/beam)
tristron
tristron
max=74.6%, 600kW (1.33A/beam)
IOT
IOT

## Slide 10
More particles animations (AB Class)

## Slide 11
RF power limit in CW UHF/L-band gridded tubes
B Class
22 kV
30 kW CW L-Band (1.3GHz) IOT by CPI / Eimac
250kW, 267 MHz CW “Chalk River” IOT
68kV x 4.9A
“…We have approximately 664 high-voltage hours on the 250-kW CW klystrode at Los Alamos, and we have had to process the grid at least three times to remove material deposited on the grid by the cathode. We are afraid that the cathode is being overheated
by the RF drive power and that the result will be a reduced tube life…”
P dive=1.4kW
P gain= 22.5dB
In the gridded tubes CW RF power level will be limited by:
The average beam current (current interception on the grid - direct heating).
Cathode overheating by the dive power (material deposition on the grid).
More?
In MB tubes, the current and drive power per beam can be controlled/adjusted by beams number. In the FCCee MB tristron designs:
- 10 beams, 60kV, Pout 880kW; beam current is 1.6 A, P dive/beam = 440W (P gain=23 dB)
- 10 beams, 47kV, Pout 440kW; beam current is 1.0 A, P drive/beam = 220W (P gain=23dB).
Both cases look like a feasible options.

## Slide 12
MB input gridded cavity
From ESS MB IOT experience, input cavity can be rather expensive and complicated if composed of many individual cavities (coupled or not). It will be useful to investigate more compact and reliable solution with a ‘common’ volume (one of the concepts is shown above on the right).
ESS MB IOT prototypes

## Slide 13
400MHz Double-gap coaxial compact cavity concept (CERN).
Q0=3080, Qext=61.5 (Ohmic losses ~2%)
grid-cathode distance = 2mm
Vacuum volume is shown
Pin
With PRF=880kW, assuming 23 dB power gain (Pin=4.4kW) and Qext=61.5, average gap field is ~0.7MV/m. With 2mm gap distance, the gap RF voltage is about 1.4 kV.

## Slide 14
The MB Triston has a remarkable potential as an FCCee RF power source, both in terms of power handling and attainable efficiency – above 90%.
Compared to its TS MBK counterpart operated in similar conditions, it has numerous advantages:
Very compact (shorter by factor 3) – less then 1m long.
Reduced power in solenoid (factor ~ 10) due to the lower magnetic field and shorter RF circuit
Very compact and simple collector (factor ~6 in volume).
Reduce by factor 10 cooling capacity need (Tristron will never be operated in DC diode mode).
The cost of MB Tristron will be about 0.5 (or less) of those for TS MBK.
Directly scalable to 200 kW, 800MHz.
Tristron development is already planned as a part of the future CERN-Thales collaboration.