## Slide 1
Status of FCCee 400 MHz 1 MW Two-Stage Multibeam Klystron
Zaib Un Nisa for CERN & ULAN HE klystron team

## Slide 2
UHF/L-band (0.3-1.3GHz)
S-band (3GHz)
C-band (6GHz)
X-band
(12 GHz)
Large scale Particle
Accelerators:
LHC
ILC
CLIC
FCC
Muon_C
CEPC
HALHF
User facilities:
Spallation sources
Storage rings&
Light sources
X-FEL
Injectors
Compact facilities:
Medical
Technological
Industrial
CW, Pulsed.
Klystron, IOT, tetrode, SSPA.
Pulsed.
Klystron.
RF power sources for particle accelerators
Proposed layouts of almost all future colliders suggest operating them in CW or Pulsed regimes in a frequency range from 0.3GHz-1.3GHz (UHF/L-band). In this frequency range new technological solution for high efficiency (HE) RF power source can be scaled for different HEP applications.
That reduces the short-term development scope to a single HE demonstrator. In this context High-Lumi LHC and FCCee were identified as primary objectives for such a development.
Ka-band (30GHz+)
Exotic concepts
Very high gradient linacs
CW, Pulsed.
Klystron, Gyro-devices.
Beam instrumentation
(*SCRF)
C-cube

## Slide 3
To operate FCCee, 100 MW Continues Wave RF power is needed to accelerate particles and to compensate for the energy lost into synchrotron radiation.
Grid power required for the large-scale HEP Accelerators (FCCee)
State of the art
2020 and before
400 MHz, 1 MW klystron for FCCee
HEK project target
2026/27
Improving klystron RF efficiency from 65% in the best existing commercial devices to 85% in the new HE tubes will:
Save 32.2 MWh -> 253 GWh (7000h/year) -> 2.53TWh over 10Y.
Reduce cost and power consumption of power converters and cooling system (environmental impact).
https://fcc.web.cern.ch/overview

## Slide 4
Klystrons
Each Klystron should deliver 1MW @ 400MHz.
Preferably, klystron should be placed vertically in the tunnel.
The total length of Klystron should be about 3m.
The efficiency of Klystron is targeted >80%.
Bunker:HV
5.5m
1.3MW CW, 352MW, 100kV, 20A, eff.=63%.
FCCee (Z) accelerator tunnel integration

## Slide 5
High Efficiency klystrons activity was initiated at CERN in 2014. In 2021 it was transformed into a CERN’s project.
Objectives: Development, design, fabrication and testing of the new HE klystrons for application in various particle accelerators.
Task 1: Design & simulations
Maintenance and distribution of the CERN made klystron code KlyC.
High level expertise in using commercial tools like CST PIC, HFSS etc.
Task 2: HE LHC 400 MHz klystron
Retrofit upgrade of Thales klystron (60% to 70%) in close collaboration with industry.
A base line option for HL-LHC.
Task 3: Novel two-stage klystron technology with 80%+ RF production efficiency
Design, fabrication and testing of the 400 MHz 1MW CW klystron for FCC in collaboration with industry.
Promote this new technology towards CLIC, ILC and Muon_C.
Task 4: High efficiency X-band pulsed klystrons in the power range 10-50MW
Strong Collaboration with industry (Canon, CPI and Thales).
Important for multiple projects (CompactLight, DEFT, EUPRAXIA etc.).
Great show case for CERN’s technology and contribution to worldwide society.
First commercial X-band 10 MW HE (56%) klystron.
CERN-Canon collaboration.
Selected topic
High efficiency klystrons projects at CERN

## Slide 6
Two-Stage Multi Beam Klystron (TS MBK) technology in UHF/L-band
Bunching at a low voltage (high perveance). Very compact RF bunching circuit.
Bunched beam acceleration and cooling (reducing p/p) along the short DC voltage post-accelerating gap.
Final power extraction from high voltage (low perveance) beam. High efficiency.
For pulsed tubes, the second HV stage can be operated in DC mode. Thus, simplifying the modulator topology. (cost/volume) and increasing the modulator efficiency.
Simplified feedback for the first stage pulsed voltage. Improved klystron RF phase and amplitude stability.
Specific features
Additional advantages:
Drawbacks:
Reflected electrons from the output cavity and collector shall be avoided at any cost.
RF radiation into DC gap must be sealed.
Requires special HV isolated RF feedthrough to inject RF signal into input cavity.
Large bore (400mm) ceramic insulator on the 2nd stage.
V1
V2
Stage 1
Stage 2
HV insulators
Post accelerating gap
TS HE MBK
Efficiency 85%+
V
V1+V2
Commercial HE MBK
Efficiency 65%
GOOD FOR:

## Slide 7
FCC 400 MHz, CW TS MBK klystron design (KlyC)
Input parameters:
Frequency: 400 MHz
N beams: 10
RF power: 0.6-1.2MW
Perveance total: 0.11
Total HV: 55-65 kV
RF Efficiency: > 80%
Power gain > 40 dB
Total length: <3m
KlyC
(FCCee H-pole)
0.845 MW
0.108 (1st: 1.5)
60 (10+50) kV
88.1%
41.5
1.55m (RF)
HE featured:
4 cavities COM bunching circuit (1st stage).
RF bunching/linearization in DC gap by rotating/compressing bunch in the phase space).
Optimized congregation in the penultimate cavity.
‘Long’ gap in the output cavity allows control of the bouncing electrons (no reflected electrons) in a wide RF power/Voltage range/

## Slide 8: Beam Optics of TS HE MBK Gun in TRK Solver
Z = 600 mm
TRK
3D Magnetic field is imported from CST solenoid project.
3D effects brought by the MB topology are fully considered.
Current=17.8 A ,Perveance= 1.6 μA/V3/2, Beam Radius= 7.06 mm
Z = 1480 mm (Output cavity gap position)

## Slide 9: Solenoid Design in CST Software
Plot of Bz value along the z-axis generated from solenoid
Plot of transverse magnetic field 𝐵t along the z-axis
The 𝐵t value of the focusing magnetic field is limited under 0.5 Gauss from the cathode to exit of output-cavity.
Whole structure of solenoid together with the position of the collector coil
The ending pole-piece with 10 holes and a coaxial at the centre on a rear view of the solenoid
Magnetic Field = 0.095 T
Power Consumption= 8.08 kW
Using ρ value for Al (3.05E-08 )
Power Consumption= 14.35 kW

## Slide 10
TRK simulation of TS HE MBK Gun at Different Voltages
1st Stage Voltage, V1 = 10.75 kV
2nd Stage Voltage, V2= 53.75 kV
Current = 1.78 A
Perveance = 1.6 μA/V3/2
1st Stage Voltage, V1 = 10.0 kV
2nd Stage Voltage, V2= 50.0 kV
Current = 1.6 A
Perveance = 1.6 μA/V3/2
1st Stage Voltage, V1 = 9.40 kV
2nd Stage Voltage, V2= 46.20 kV
Current = 1.456 A
Perveance = 1.6 μA/V3/2
TRK simulation of TS HE MBK Gun for Z, WH and ttbar Machines using same Magnetic field 0.095 T.
Z
WH
tt bar

## Slide 11
Setting up CST3D PIC simulations
Special coaxial input coupler (at ground)
1st stage at a floating voltage
2nd stage at ground
DC gap
Rejectors
1st stage beam injection
Solenoid is simulated in CST separately and magnetic filed 3D map is imported into PIC simulations directly.
Output ports are used only for monitoring the power envelope and frequency spectrum. Efficiency is calculated by direct integration of the beam power at emission plane, integrated beam losses on the collector part and Ohmic losses in the output cavity:
=P spent beam (1-Qext/Q0)/( Ix U)

## Slide 12
FCC 400 MHz, CW TS MBK RF performance summary (CST3D PIC)
1MW in saturation

## Slide 13
13
-36 dB
1-8 dB
-5 dB
15.3kW
13.5 W
‘open’
Spectra of RF radiation into DC gap
Suppression of RF radiation into DC gap (concept)
‘open’
By using 3 radial resonant choke rejectors, total radiation into DC gap is suppressed by >30dB
Illustrated case uses bunched beam at 0.96 MW (16Ax60kV)/ H-pole
2nd Workshop on efficient RF sources, 23-25 Sept. 2024, Toledo, Spain

## Slide 14
14
307.3 mm
932 mm
 | Voltage | Current | dP/dS (max)
ttbar | 56.4 kV | 14.56 A | 211 W/cm2
WH | 60 kV | 16 A | 258 W/cm2
Z | 64.5 kV | 17.8 A | 285 W/cm2
Collector was optimised to maintain power loss density on the surface < 300 W/cm2 for DC operation
CST3D TRK simulations
TS MBK collector baseline design

## Slide 15
Specifics of MBK collector.
Azimuthal beam losses distribution.
L section=12.5mm
Averaged power over the section
#15
#16
#17
Section
9 degrees/sector
Azimuthal peak power density is about 400W/cm2 . We will need to:
Increase collector diameter by 10-20% (307mm -> 340/360mm).
Lengthen the input taper part so that first impact will happen at a grazing angle.

## Slide 16
Inner fillet of one beam hole
Outer fillet of the cavity nose
Flat Part of the nose
RF Loop
Multipacting Simulation at 1 MW RF
Courtesy: Franck Peauger

## Slide 17
2.95 m
400 MHz HE Two-Stages MBK for FCCee. Integration.

## Slide 18
The reduction of energy consumption in the future large-scale accelerators, like FCC, is of a great importance.
Novel two-stage (TS) klystron technology was introduced recently. It enables compact solution in UHF band, with potential to increase the efficiency from 65% in existing commercial tubes up to 80%.
Such a 400 MHz, 1.0 MW TS MBK klystron for FCC is now under development at CERN as a part of the High Efficiency Klystrons project.
RF circuit, beam optics and special axillaries, like HVRFT and DC accelerating gap rejector, have been evaluated and confirmed in simulation the tube conceptual feasibility with potential to reach target efficiency of >85%.
The next step will be integration of beam optics and RF circuit, followed by technological development and prototype fabrication in collaboration with industrial partner.
Multipacting effect has been checked.
FCC TS MBK Summary and outlook

## Slide 19
Project leader: Igor Syratchev
Project team @CERN: Zaib Un Nisa, Nuria Catalan Lasheras.
Project team@ Lancaster: Lee Millar, Graem Burt.
50%
60%
70%
80%