## Slide 1
A.Romero Francia, A.Perillo Marcone, A.Lechner, B.Humann, R.Seidenberg, M.Calviani [SY-STI]
S.Sgobba, M.Simoes [EN-MME]
22-05-2025
Preliminary technical design for the FCC-ee dipole shielding

## Slide 2: Outlook
Background and motivation.
FCC-ee arc shielding design and development.
  Feasibility Study Report (FSR) design.
  Current conceptual design.
Thermomechanical performance of the shielding.
Challenges, production and logistics.
Conclusions.

## Slide 3: 1. Background and motivation
Comprehensive long-term program maximizing physics opportunities.
Stage 1 (from 2040, 15 years): FCC-ee (Z, W, H, ttbar) as Higgs factory, electroweak & top factory at higher luminosities.
Stage 2 (from 2070, 25 years): FCC-hh (~100 TeV) as natural continuation at energy frontier, pp & AA collisions; e-h option.
For stage 1, the synchrotron radiation is too high for standard components. Dedicated shielding is required.

## Slide 4: 2. FCC-ee arc shielding design and development
# Dipoles: 2840
# Photon stoppers per dipole: 10
# Shielding units: 28400
Feasibility study report (FSR)
Current Conceptual design
Photon stopper
Busbar
Vacuum chamber
Shielding
Shielding
Yoke
Shielding material: Pb, Pb(2-4%)Sb
W considered, though high cost.
This presentation provides results for ttbar operation mode.
Photon stopper design: M.Morrone, R.Ady
Magnet design: J.Bauche, C.J. Eriksson, L.van Freeden

## Slide 5: 2. FCC-ee arc shielding design and development
Pb is not a structural material!
Low melting point (327 ), low thermal conductivity (35 W/m), highly ductile, yields at 2MPa, creep susceptible…
Feasibility study report (FSR)
Current Conceptual design
Photon stopper
Busbar
Vacuum chamber
Shielding
Shielding
Yoke
Shielding material: Pb, Pb(2-4%)Sb
W considered, though high cost.
This presentation provides results for ttbar operation mode.
Photon stopper design: M.Morrone, R.Ady
Magnet design: J.Bauche, C.J. Eriksson, L.van Freeden

## Slide 6: 2. FCC-ee arc shielding design and development
 | FSR | Conceptual
Photon stoppers | 68.1% (3.4kW) | 80.7% (4kW)
Radiation shielding | 20.4% | 3.7%
Vacuum chamber | 7.9% | 5.2%
Dipoles yokes | 3.4% | 9.6%
Dipoles busbars | 0.1% | 0.5%
Environment | 0.03% | 0.05%
 | FSR | Conceptual
Photon stoppers |  | 
Radiation shielding | 20.4% | 3.7%
Vacuum chamber | 7.9% | 5.2%
Dipoles yokes | 3.4% | 9.6%
Dipoles busbars | 0.1% | 0.5%
Environment |  | 
Higher energy deposited on shielding units.
Very complex integration within the dipole.
Higher complexity for series production.
Feasibility study report (FSR)
Current Conceptual design
Photon stopper
Busbar
Vacuum chamber
Shielding
Shielding
Yoke

## Slide 7: 2. FCC-ee arc shielding design and development
 | FSR | Conceptual
Photon stoppers | 68.2% (3.4kW) | 80.7% (4kW)
Radiation shielding | 20.4% | 3.7%
Vacuum chamber | 7.9% | 5.2%
Dipoles yokes | 3.4% | 9.6%
Dipoles busbars | 0.1% | 0.5%
Environment | 0.03% | 0.05%
 | FSR | Conceptual
Photon stoppers |  | 
Radiation shielding | 20.4% | 3.7%
Vacuum chamber | 7.9% | 5.2%
Dipoles yokes | 3.4% | 9.6%
Dipoles busbars | 0.1% | 0.5%
Environment |  | 
Lower energy deposited on shielding units.
Easier integration within the dipole.
Lower complexity for series production.
HEAT CANNOT BE RELEASED TO THE TUNNEL!
Feasibility study report (FSR)
Current Conceptual design
Photon stopper
Busbar
Vacuum chamber
Shielding
Shielding
Yoke

## Slide 8: 2.1 FSR shielding thermal management
Shielding block with peak energy deposition 640 W.
MELTING (327 °C)!
Pure Lead
Temperature [C]
Pure Lead
8-mm diameter SS pipes in cast lead.
Forced Convection water (0.75l/min)
Cooling pipes
Temperature [C]
Adding cooling
Only this block was modelled, as this conceptual approach is impractical to implement.
Feasibility study report (FSR) shielding
Calculations in steady state ttbar mode.
Input energy maps by B.Humann and A.Lechner
Only natural convection
natural convection + water cooling

## Slide 9: 2.1 FSR shielding structural behavior
Shielding block with peak energy deposition 640 W.
Beam-induced stresses are minimal, remaining well below 2 MPa (material’s yield)
Initial plasticity and creep assessments have been conducted; however, these did not include supporting contact conditions.
No additional analysis has been pursued, as the current design has proven to be impractical for implementation.
Feasibility study report (FSR) shielding
Only this block was modelled, as this conceptual approach is impractical to implement.
Calculations in steady state ttbar mode.

## Slide 10: 2.2 Conceptual shielding thermal management
Shielding block with peak energy deposition 130 W.
Temperature [C]
Pure Lead
Temperature [C]
Entire shielding unit modelled.
Cooling pipe
NO MELTING!
Adding cooling
Current conceptual design
Pure Lead
Pure Lead
Calculations in steady state ttbar mode.
Input energy maps by B.Humann and A.Lechner
Only natural convection
natural convection + water cooling

## Slide 11: 2.2 Conceptual shielding structural behavior
Equivalent plastic strain [mm/mm]
Beam-induced plastic deformation
Pure Lead
Calculations in steady state ttbar mode.
Cooling pipe
Water flow rate 1 l/min

## Slide 12: 2.2 Conceptual shielding structural behavior
Equivalent creep strain [mm/mm]
Beam-induced creep deformation
Pure Lead
Calculations in steady state ttbar mode.
Water flow rate 1 l/min 15 years operation

## Slide 13: Conclusions
from thermomechanical simulations…
The FSR shielding is impractical for implementation, though temperature and beam-induced stresses are manageable.
The conceptual design results in low beam-induced stresses, which means that after 15 years of steady operation, the structure does not experience significant deformation.

## Slide 14: 3. Challenges, production and logistics
Design and material selection
Due to in-series production, what are our design limitations?
Adding Sb into Pb improves strength, though its high-cost limits use to critical areas.
Pb
Pb
Pb
Pb
Pb(2-4%)Sb
Supports and interfaces
The Pb shielding wraps around the dipole magnet, fully encasing it. However, it must not support its weight, as this would lead to deformation over time due to creep.
Integration within the dipole
The shielding fits well around the dipole, but contact points need definition. Top/bottom plate cooling relies on surrounding components to be cooled.
Pb
Example for material selection proposal.

## Slide 15: 3. Challenges, production and logistics
Actively cooled plates
Embedded stainless steel pipe in cast lead
Stainless steel pipe cladded into two plates
Lowest thermal contact resistance.
Involves casting: higher complexity and cost.
Requires of a mould.
Higher thermal contact resistance.
Lower complexity.
Does not require of a mould.
Other options…
Cooling by forced gas convection instead of water (no stainless-steel pipes needed *).
Cooling by conduction, attaching a high conductivity body to the shield.
*: Water cannot be in contact with activated lead to avoid erosion-corrosion problems, as maintenance in the cooling loops would be extremely challenging (experience from nTOF#2).

## Slide 16: 3. Challenges, production and logistics
Transport, storage and installation
Safety, dismantle and recycle
Pb is a toxic material for humans. Radioactive resistance coatings are being studied to avoid direct contact with operators.
Pb is to be re-used/recycled after FCC-ee.
Transport capacity: 10k–15k t of Pb, using dedicated trucks (~25 t per transport).
With a 3 - 5 year production timeline, Pb must be stored in dedicated facilities.
Heavy Pb plates can imply significant deformations; straightening capability required before installation.
Next steps
Prototype construction and potential implementation in the arc cell mock-up.

## Slide 17: 4. Conclusions
Ongoing work focuses on optimizing the radiation shielding for the FCC-ee arc. Design implementation in collaboration with MME, VSC and MSC.
Thermomechanical simulations conducted so far have not revealed any critical issues.
Active cooling of the shielding is necessary to manage temperature, limit beam-induced stresses, and prevent heat dissipation into the tunnel environment.
Investigations are underway into methods for integrating stainless steel cooling pipes within the lead shielding.
The logistical challenges associated with large-scale production are currently being assessed; ongoing studies to optimize cost and design efficiency.