## Slide 1: Alignment system based on a Structured Laser Beam
Witold NIEWIEM
22/05/2025 Geodetic Metrology group - Future Projects section (BE-GM-FP)

## Slide 2: Content
Alignment of particle accelerators
SLB-based reference line
Alignment system prototype

## Slide 3: Alignment of particle accelerators
Large Hadron Collider (LHC)
Future Circular Collider (FCC)
Alignment of entire machine:
Accuracy LHC 200 μm / 150 m (sliding window)

## Slide 4: Reference line for alignment
Component I
Component II
Component III
Reference line
Assumptions:
Line is straight
Offsets are perpendicular
Wire measurement
Laser measurement

## Slide 5: Structured Laser Beam (SLB)
Example of theoretical transverse profile of an SLB at 225 m - Inner core ⌀ 3 mm, Outer ring 100 mm
Acquired transverse profile at 900 m
IC divergence 10 µrad
  Laser divergence
Advantages of SLB for alignment:
Low divergence of the IC
Theoretically, propagation to infinity
Easy-separable IC

## Slide 6: SLB generator and wavefront
  Laser divergence

## Slide 7: Alignment - SLB inner core reference
Component I
Component II
Component III
Generator
Reference line
Longitudinal profile of an SLB
Longitudinal profile of a Gaussian Beam
  Laser divergence

## Slide 8: Challenges
Structured Laser Beam - Divergence
Symmetry breaking
Reflection
Refraction - Vacuum system

## Slide 9: Shutter system - 140 m length
Measurement station 1
Measurement station 4
  Prototype setup

## Slide 10: Experimental setup - Prototype evaluation
Experimental setup for comparative assessment of the prototype with the WPS and HLS
Wire Positioning System (WPS)
Hydrostatic Levelling System (HLS)
wire
electrode
electrode
FSI
  Comparative assessment

## Slide 11: Assessment with WPS and HLS network
  Offset measurement
Offset of Station 4 relative to Stations 1 and 7 Two acquisition series of 3.5 hours each
Error bars based on SLB data variation
Precision
Standard deviation below 20 μm
Improvement: enhanced reference line stability by
extended vacuum system, thermal stabilisation,
multipoint measurement – Layers Beams.
Accuracy
Absolute bias horizontal 20 μm and vertical 50 μm
Improvement: modified the fiducialisation process by
lowering the vacuum system, fiducialisation in the metrology laboratory.

## Slide 12: Conclusion
SLB can be used for alignment thanks to low divergence, high IC contrast, and long beam propagation.
Multiple challenges were overcome to construct the prototype using a vacuum system.
The prototype achieved high precision, showing strong potential for future systems.
Addressing challenges with radiation, multipoint alignment, and multiple lines is a priority for future implementations.

## Slide 13
References:
W. Niewiem, K. Polak, M. Dusek, D. Mergelkuhl, J-Ch. Gayde, A. Wieser, M. Sulc, “Variation of structured laser beam pattern and optimization for an alignment reference line creation” Optics Express 31 (2023) https://doi.org/10.1364/OE.503016
W. Niewiem, K. Polak, S.Figura, D. Mergelkuhl, J-Ch. Gayde, A. Wieser, “The influence of symmetry breaking on the Inner Core of a Structured Laser Beam”, Express 33 (2025) https://doi.org/10.1364/OE.549391
W. Niewiem, S. Figura, D. Mergelkuhl, J-Ch. Gayde, A. Wieser, M. Sulc, “Speckle induced by reflections in pipe propagation of a Structured Laser Beams” Applied Optics 64 (2025), soon available
W. Niewiem, S. Figura, D. Mergelkuhl, J-Ch. Gayde, A. Wieser,, “Shutter-type multi-point optical alignment using a Structured Laser Beam in vacuum” JINST (2025), soon available

## Slide 14
Witold Niewiem

## Slide 16: Precision - Stability of reference
Support and SLB generator
  Reference line drift
IC position in global CS - drift
Distance from the generator
141.9 m
70.2 m
1.9 m

## Slide 17: Accuracy - Systematic error
CMM verified by in-house method
Least-squares (WPS, HLS) network with fiducialisation/calibrations
Laser tracker measurement – two steps
  Fiducialisation bias
Position of the IC in global coordinate system
Uncertainty propagation components

## Slide 18: Layer beams – Martin’s Dusek doctorate
    Layer beams – linear chip sensor
      Prototyping of the sensor with 4 linear CCDs with an aperture (allows for multipoint measurements at one instance in time)
      Position of the CCD sensors will be measured in metrology lab to be ready for future absolute misalignment measurements
Sensor prototype
Sensor mockup
Reference planes created by a Layer Beams

## Slide 19: Layer beams – Martin’s Dusek doctorate
Laboratory setup
Sensor mockup

## Slide 20
  3. Symmetry breaking
  2. Atmospheric refraction
  5. Reflection speckle
  1. Laser divergence
  4. Vacuum forces
  Project challenges and solutions

## Slide 21: Generator, intensity profile and wavefront
  Laser divergence

## Slide 22: Wavefront and profile
  Laser divergence
Large zero-phase gradient ring:
Small IC
Large OR
ξ = 0.1
ξ = 0.9
ξ = 0.5

## Slide 23: Inner Core and Outer Ring diameters
  Laser divergence

## Slide 24: Refraction and Vacuum
Component I
Component II
Component III
Reference line
Generator
  Atmospheric refraction
Vacuum pipe
Component I
Component II
Component III
Reference line
Generator

## Slide 25: Symmetry breaking - Vacuum pipe
  Symmetry breaking
Component I
Component II
Component III
Generator
Reference line
Inner Core and Outer ring vs Vacuum Pipe and Sensor size
Sensor
Vacuum Pipe
SLB

## Slide 26: Symmetry breaking - Far zone
  Symmetry breaking
Aperture
⌀ 50 mm

## Slide 27: Symmetry breaking - Near zone
  Symmetry breaking
Aperture
⌀ 50 mm

## Slide 28: Symmetry breaking - IC deformation
  Symmetry breaking
Rectangular obstacle in the near zone

## Slide 29: Vacuum forces - System defromation
  Vacuum forces
Component I
Component II
Component III
Vacuum forces
Vacuum pipe
Parameters for the vacuum system:
156 mm diameter
140 m length
23 segments
1 fix point
Constraint on the mechanical link between the vacuum system and measured components
Bellows

## Slide 30: Source of reflection - Speckle
  Reflection speckle
Propagation in vacuum pipe 140m
Propagation in free air 140 m

## Slide 31: Reflection reduction - Methods
Color
Structure
Pipe
Laser
Temporal coherence
Spatial coherence
  Reflection speckle
Rough
Baffles
Black
Wavefront (t)
Wavefront (t)
Black undulated
He Ne laser
Laser Diode

## Slide 32: Reflection reduction - Results
  Reflection speckle
140 m propagation
2 m propagation
Correlation index*
Pipe radial position [mm]
Inner Core
Correlation index* - Structure Similarity Index Measure (SSIM) between photos in free space and in the pipes (test at 2 m)
Reflective vacuum pipe
Free space
Black pipe

## Slide 33: IC position in global CS - drift
  Prototype evaluation
Mar 17th
Mar 24th

## Slide 34: Near and far optical zones
Add the wavefront

## Slide 35: Laser alignment systems - elsewhere
* The works on the laser alignment systems were also conducted at: SPring, CERN, CSNS, Dubna, Argonne and Nikhef
Institute* | Date | Divergence mitigation | Light sensor | Refraction mitigation ** | Expected accuracy | Current state | 
SLAC | 1960 – now partialy | Fresnel plates Poisson pattern | Manual readout | Vacuum 1.333 Pa | 250 microns 3,2 km | 2/3 of length disassembled | Test with classical methods Accuracy 5mm-3.2km 0.23mm-1.5
KEK | 1990 - 2010 | Fresnel plates Airy pattern | Quadrant Photodiode | Vacuum 1 Pa | 100 microns 500 m | Non-operational | Lack of testing method relative 0.1 on 268 m
DESY | 2000 - now | Poisson pattern | CCD camera | Vacuum 10 Pa | 200 microns 600 m | Operational | Relative 25 and 50 microns just by moving. Accuracy 0.18mm – 500 m there are 3 systems with differn lenght
** Standard atmosphere (atm) is defined as 101 325 Pa

## Slide 36: Shutter system principle
Setup side view
Feedthrough
Manipulator
Adapter flanges
Extension
Camera
Groove
Kinematic mount
Metrological plate
SLB generator
Manipulator
Manipulator

## Slide 37: Heat dissipation - simulation

## Slide 38: Camera calibration
Corner point name | X difference (μm) | Y difference (μm) | Z difference (μm)
TL | 6 | 11 | -4
TR | 14 | 10 | -2
BL | 8 | 5 | -4
BR | 15 | 5 | -2
Differences in-house method and CMM

## Slide 39: Free air propagation

## Slide 40: Optical beams GB and Bessel Beam
Forms of light waves propagating with small divergence
Gaussian beam
small focus
significantly diverges
Bessel beam
long longitudinal focus
limited range
zero divergence

## Slide 41: Field contribution – SLB applications
Laser pointer in a total station and LiDAR
Military and civil targeting and follow-up
Precise rotary level for civil engineering
Wireless communication
Precision cutting and engraving