## Slide 1: FCC-ee RF operation scenarios - new baseline
Ivan Karpov and Franck Peauger for FCC SRF WP1 with input from:
Xavier Buffat, Yann Dutheil, Giorgia Favia, Jiquan Guo (JLAB), Mauro Migliorati (INFN), Katsunobu Oide, Luca Sabato, Roxana Soos, Jorg Wenninger, Frank Zimmermann, Mikhail Zobov (INFN)
FCC Week 2025, 21.05.2025

## Slide 2: Challenging requirements for RF system
Beam current and energy loss for 50 MW synchrotron radiation (SR) budget
Low energy operating points:
High beam current and weak SR
Low RF voltage
Beam instabilities
Significant power losses due to high-order modes (HOM)
High energy points:
Low beam current and strong SR
High RF voltage to be reached with a small footprint
Instabilities suppressed by SR
Small power losses due to low beam current
A few single-cell cavities at low RF frequency (400 MHz)
Many multi-cell cavities at higher RF frequency (800 MHz)

## Slide 3: RF baseline evolution for collider
FCC Conceptual design report (2018)
Z
WW
ZH
Common RF for 2 beams
F. Peauger, FCC Week 2022 & FCC FS MTR (2024)
FCC FS Final Report (2025)
+
×104
×104
×272
×272
×372
Operational margins
Less HOM power for WW with 2-cell cavities
Same RF for WW & ZH
+
Common RF for 2 beams
×112
×264
×264
×264
×488
×264
×264
×264
×264
×408
+
Common RF for 2 beams
Same RF for Z, WW & ZH
One power source per cavity
6-cell for for cost reduction
Reverse Phase Operation (RPO) mode for Z is required to unify Z-WW-ZH RF system

## Slide 4: Reverse phase operation
Reverse phase operation (RPO) mode allows for increasing RF cavity voltage, having optimal static beam loading compensation (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
To minimize RF power requirements, the optimal quality factor needs to be used
Since , cavity voltage, enormous change of is required switching from Z to WW
Applicability of RPO for FCC-ee needs to be confirmed
A sketch of RPO mode for 12 RF cavities

## Slide 5: Reverse phase operation
Reverse phase operation (RPO) mode allows for increasing RF cavity voltage, having optimal static beam loading compensation (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
To minimize RF power requirements, the optimal quality factor needs to be used
Since , cavity voltage, enormous change of is required switching from Z to WW
Applicability of RPO for FCC-ee needs to be confirmed
A sketch of RPO mode for 12 RF cavities
Focusing cavities
Defocusing cavities

## Slide 6: RPO validation checklist
Static beam loading
Transient beam loading
Coupled-bunch instabilities
Higher-order-mode power losses
Availability aspects

## Slide 7: Static beam loading compensation
can be changed in discrete steps of
To avoid a movable fundamental power coupler design, and must be the same for all cavities for Z,WW, and ZH
To minimize RF power requirements optimal quality factor and optimal detuning must be used
Total RF voltage (e.g., A. Blednykh et al, 2022)
Closest but reduces RF acceptance
New proposal
Possible RF voltages for Z
RF voltage at Z needs to be slightly increased (89 vs 79 MV)

## Slide 8: RPO validation checklist
Static beam loading New total RF voltage proposed
Transient beam loading
Coupled-bunch instabilities
Higher-order-mode power losses
Availability aspects

## Slide 9: Transient beam loading
Gaps in beam filling scheme will result in modulation RF parameters
Present filling scheme with proposed 88 MV RF voltage results in ~50 % modulation of the effective RF voltage
Voltage amplitude and phase transients from small-signal model (F. Pedersen, 1992)
 |  | (MV) | (MV) | 
71 | 61 | 89 | 7.95 | 9.21e5
71 | 61 | 89 | 7.95 | 9.21e5

## Slide 10: Bunch-by-bunch spread of beam parameters
Synchrotron tune and bunch length spread can significantly degrade beam stability (e.g., due to X-Z instability, K. Ohmi, 2016):
Peak-to-peak spread of ~30% is a factor of 15 worse compared to 1-cell RF system
-21/+10 %
-9/+27 %
132 2-cell cavities RPO, 56 1-cell cavities normal phase

## Slide 11: Possible mitigations
where peak-to-peak beam phase spread
Synchrotron tune spread according small-signal model
Higher RF voltage and shorter gaps reduce spread
Evaluation of option with = 200 MV and original showed unacceptable reduction of lifetime to about 20 s compared to 1320 s given by radiative Bhabha scattering (K. Oide, 09.10.2024)
A new filling scheme with shorter gaps is necessary for reduction of the spread
5%
spread for 1.2 µs gap length
Relative contributions to spread
30%

## Slide 12: Results for smaller gaps between trains
With a new filling scheme (40 trains of 280 bunches), RF voltage spread was significantly reduced
Working point can be found for all bunches at nominal intensity, but not during non-uniform bootstrap injection needed for e-cloud mitigation (X. Buffat et al, 24.04.2025, also R. Soos et al, presentation yesterday)
Injection and extraction systems were adapted to decrease the rise time below 600-ns (G. Favia, presentation this afternoon)
FSR

## Slide 13: Alternative filling schemes
Hybrid filling schemes with 5-ns spacing micro-trains can suppress e-cloud limitations (L. Sabato, presentation yesterday)
Negligible impact on the RF voltage spread (15.3 % 16.8 %)

## Slide 14: RPO validation checklist
Static beam loading New total RF voltage proposed
Transient beam loading Shorter beam gaps are introduced
Coupled-bunch instabilities
Higher-order-mode power losses
Availability aspects

## Slide 15: Coupled–bunch instabilities due to fundamental mode
Standard analysis: compute growth rates and compare them with synchrotron radiation damping time
For short Gaussian bunches, the growth rate of the mode m is (J. L. Laclare, 1985)
with
Direct (DFB) and long-delay feedback (OTFB) systems can reduce impedance “seen” by the beam (F. Pedersen, 1992)
Loop delay of ns (like in LHC)
Cavity impedance at fundamental,
Feedback transfer function

## Slide 16: Coupled–bunch instabilities due to fundamental mode
For short Gaussian bunches, the growth rate of the mode m is (J. L. Laclare, 1985)
with
Direct (DFB) and long-delay feedback (OTFB) systems can reduce impedance “seen” by the beam (F. Pedersen, 1992)
Cavity impedance at fundamental,
Feedback transfer function
Loop delay of ns (like in LHC)
Standard analysis: compute growth rates and compare them with synchrotron radiation damping time

## Slide 17: Instability growth rates
Calculations for loop delay of ns, DFB gain 10, OTFB gain 20:
LCBI can be suppressed already with DFB, while OTFB gives additional stability margin
SR limit
132 2-cell cavities with RPO

## Slide 18: HOM-driven coupled-bunch instabilities
Longitudinal plane:
No trapped HOMs
impedance is well below the SR threshold
Updated 2-cell design with suppressed of 0-mode at MHz by 2 orders of magnitude (S. Gorgi Zadeh, 15.08.2024)
Only twice below SR damping limit for (might be larger due to limited bandwidth of circulator)
We gain a factor of 20 with 10 kHz frequency spread from cavity to cavity
Transverse plane:
Instabilities growth rates (min. rise time > 100 turns) are within capabilities of transverse feedback system (W. Hofle, 2024)
SR damping
SR damping

## Slide 19: RPO validation checklist
Static beam loading New total RF voltage proposed
Transient beam loading Shorter beam gaps are introduced
Coupled-bunch instabilities Active and passive damping is sufficient
Higher-order-mode power losses
Availability aspects

## Slide 20: RPO validation checklist
Static beam loading New total RF voltage proposed
Transient beam loading Shorter beam gaps are introduced
Coupled-bunch instabilities Active and passive damping is sufficient
Higher-order-mode power losses (S. Gorgi Zadeh, presentation this afternoon)
Availability aspects

## Slide 21: Availability challenges
Availability goals require 10% (minimum 4%) redundancy of the RF system (J. Heron, FCC Week 2024)
Critical questions for Z mode with RPO:
Coupled-bunch instability due to fundamental impedance
Cavity damage due to strong beam-induced fields
Missing RF voltage (RF power margin)
Consider only the case of RF source or LLRF trip (not a quench of the cavity)
For H and a 10% redundancy is assumed based on LEP experience

## Slide 22: Longitudinal coupled-bunch instability
Coupled-bunch instability due to fundamental mode could be suppressed by a longitudinal feedback system (main RF system as kicker) with damping time of (see, D. Teytelman, FCC week, 2019), but RF power requirements need to be evaluated
We are at the limit with one missing cavity
SR limit
Longitudinal damper limit
Instability growth rates with 1 tripped focusing cavity
Loop delay of ns (like in LHC)
Cavity impedance at fundamental,

## Slide 23: Simplified beam-cavity interaction model
Coupled differential equations are solved for four groups:
Focusing ( cavities)
Defocusing ( cavities)
Tripped focusing ( cavities)
Tripped defocusing ( cavities)
Combined with longitudinal equations of motion for one particle per bunch
Longitudinal damper is not implemented yet
RF cavity
Load
Circulator
Generator
–
+
Cavity voltage
Forward wave
Reflected wave
Error signal
Delay
Direct RF feedback
Phase pickup
Longitudinal damper
Reference signal
Beam
Tuner
+
+

## Slide 24: Trip of focusing cavity
Short RF voltage transients ~6%
Peak power of other cavities is modulated at synchrotron frequency (avg. <15%, peak <32%)
Initial bunch oscillation amplitude is <10% of rms bunch length
New RF power have sufficient margin for a single cavity trip (I. Syratchev, next presentation)
~ 48 ps
Trip
Reaction time
Controlled voltage increase

## Slide 25: Trip of focusing and defocusing cavities
Short RF voltage transients ~6%
Peak power of other cavities is modulated at synchrotron frequency (avg. <45%, peak <80%)
Initial bunch oscillation amplitude is <8% of rms bunch length
Not enough power margin to handle simultaneous trip of two cavities
~ 48 ps
Trip
Reaction time
Controlled voltage increase

## Slide 26: Higher total RF voltage
Moving from 89 to 195 MV reduces RF power transient:
Is there a room for this in LCC optics?
Can we profit from relaxed bunch charge for non-uniform filling schemes?
~ 48 ps
Trip
Reaction time
Controlled voltage increase

## Slide 27: RPO validation checklist
Static beam loading New total RF voltage proposed
Transient beam loading Shorter beam gaps are introduced
Coupled-bunch instabilities Active and passive damping is sufficient
Higher-order-mode power losses ~50 % increase wrt 1-cell design
Availability aspects: Beam can be preserved only in case of a single cavity trip

## Slide 28: Summary
Reverse Phase Operation (RPO) mode was the final ingredient to have the same 2-cell 400 MHz RF system for Z, WW, and ZH operating points.
Main aspects were evaluated, and the most critical item was identified:
Required 4% redundancy to achieve integrated luminosity goals cannot be achieved according to dynamic beam-cavity interaction model. RF power margins could be sufficient to preserve the beam only in the case of a single RF source trip. Higher total RF voltage is beneficial for reduction of RF power transients.
Not covered in this talk:
RPO is an essential part of FCC-ee high-energy booster (HEB) operation (L. Valle, presentation tomorrow)
Increased longitudinal impedance requires special attention for Z operating point of HEB (S. Gorgi Zadeh, presentation this afternoon)
Thank you for your attention!

## Slide 29: Backup slides

## Slide 30: Trip of focusing cavity
Short RF voltage transients ~6%
Peak power of other cavities is modulated at synchrotron frequency (avg. <15%, peak <32%)
Initial bunch oscillation amplitude is <10% of rms bunch length
Beam is unstable without longitudinal damper due to uncompensated impedance
~ 48 ps

## Slide 31: Trip of defocusing cavity
Similar results to the case of focusing cavity trip
Simultaneous trip of two cavities of any type leads to significant RF power overshoot
~ 48 ps

## Slide 32: Trip of 3 single-cell cavities (4% redundancy)
Smaller relative transient compared RPO scheme
Absolute peak power modulation exceeds 1 MW level
~ 48 ps

## Slide 33: Reverse phase operation
Reverse phase operation (RPO) mode allows for increasing RF cavity voltage having optimal static beam loading compensation (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
Phasors
RF waves
*Electron convention for synchronous phase:

## Slide 34: RF baseline evolution
FCC Conceptual design report (2018)
Z
WW
ZH
Separate RF systems
Common RF system
Separate RF systems
Common RF system
F. Peauger, FCC Week 2022 &
FCC FS Mid-Term Report (2024)
FCC FS Final Report (2025)
Separate RF systems
Common RF system

## Slide 35: Higher-order mode power
Unavoidable 15 kW increase in HOM power compared to single-cell design for option 1 and potentially up to 10 kW deposited in resonance mode (S. Gorgi Zadeh, 23.01.2024)
Verification of possible reduction of the tapering angle at the extremities of the cavity string is ongoing (K. Canderan, 29.10.2024)
K. Oide, 06.11.2024
2 coaxial HOM couplers
Option 2:
2.3 kW
4.2 kW
6.8 kW
4.3 kW
5.9 kW
5.1 kW
6.5 kW
5.5 kW
6.1 kW
4.8 kW
6.4 kW
6.4 kW
Option 1:
1.9 kW
3.7 kW
6.1 kW
3.7 kW
5.3 kW
4.5 kW
5.8 kW
4.9 kW
5.5 kW
4.2 kW
5.7 kW
5.3 kW
Option | (MV) | (mm)
1 | 103.00 | 14.6
2 | 117.86 | 13.7
Option |  | 
1 | 103.00 | 14.6
2 | 117.86 | 13.7
Tapers contribution to the HOM power
HOM power equation
In absence of resonant modes

## Slide 36: Baseline collider RF system configuration
 | Energy (GeV) | Current (mA) | RF voltage (GV)
Z | 45.6 | 1283 | 0.079
W | 80 | 135 | 1.05
H | 120 | 26.7 | 2.1
K. Oide, 29.05.2024
MTR recommendation:
Study options to avoid the 1-cell/2-cell RF cavity reconfiguration between Z and H/WW running to simplify the SRF system implementation and improve flexibility in the physics programme.
Courtesy of O. Brunner

## Slide 37: Baseline collider RF system configuration
Proposed solution:
Installation of 2-cell cavities with individual RF power sources (~0.5 MW level) from the beginning
Reverse phase operation (RPO) mode for Z, normal mode for W and H (combined RF system for 2 beams)
Applicability of RPO for FCC-ee needs to be confirmed
Courtesy of O. Brunner
Extra year of operation?
66
MTR recommendation:
Study options to avoid the 1-cell/2-cell RF cavity reconfiguration between Z and H/WW running to simplify the SRF system implementation and improve flexibility in the physics programme.

## Slide 38: Beam loading model: main equation
Generator current
Generator power
Fixed parameters are , , , , , while , , and can be adjusted
See, e.g., J. Tückmantel, CERN Report No. CERN-ATS-Note-2011- 002 TECH, 2011

## Slide 39: Derivations for arbitrary cavity phase (1/2)
Complex quantities: , , and
Generator current
, ,
Then splitting in real and imaginary parts:
0

## Slide 40: Derivations for arbitrary cavity phase (2/2)
= 0 for
Minimized for
Setting recovers classical equations for optimal parameters
Adjusting , can be modified to meet certain constraints
The minimum power

## Slide 41: RF power requirements
Starting with energy gain per turn
No RF power overshoot is needed for RPO if optimal detuning and optimal quality factor are used
Constraints:
- The same for all cavities to avoid a movable fundamental power coupler design
- The same to have the identical power sources and uniform power distribution (role of variations is under study)
Cavity voltage must be the same for all cavities: =

## Slide 42: Reverse phasing mode equations
Preservation of energy gain
Preservation of synchrotron tune
See, also A. Blednykh et al, EIC-ADD-TN-33, 2022
The aim is to keep , , and for Z, W, and ZH modes
Cavity voltage can be change in discrete steps of
Cavity voltage
Optimal detuning
Phases

## Slide 43: Critical impact of spread
A coherent beam-beam instability, X-Z instability (K. Ohmi, 2016)
Threshold
Working point chosen between resonances and
Higher
  stronger low order resonance but more space available between them
Bunches are ~50% shorter (assuming the same )
  stronger beamstrahlung ( increase is smaller)
  stronger impact of longitudinal impedance?
M. Migliorati, 2024

## Slide 44: Parameter sensitivity of RPO
Small, but visible impact of parameter spread on global parameters (e.g., )

## Slide 45: Steady-state beam loading
Increasing (43.890.6 Ohm) and reducing :
Large range for adjustment (a factor of ~75-600) starting from : possible FPC solutions under study (S. Gorgi Zadeh and E. Montesinos, CERN SRF, 2024; see also slides of F. Gerigk, FCC week 2024)
Incresed detuning enhances instability due to fundamental mode
Can the total voltage be increased for Z mode?
RF power for SRF cavities with circulators is minimized for optimal parameters:
Optimal detuning
Optimal quality factor
Optimal parameters for different scenarios

## Slide 46: New adjustable power coupler concept
Z
W
t
This length can be increased by λ/2 (374 mm) and get similar results
,
,
4,
,
,
,
,
,
  Two windows (LINAC4-like) are placed outside the cryomodule  integration challenge after cryostating
  A more robust and easier-to-cool down window design  easier to cover all four working points
  Providing ~1 MW in CW operation with variable coupling for Z, W, H, ttbar.
  HOM power see: F. Peauger & I. Karpov
  Prototyping starting.
normalized to 1J stored energy
W
Z