## Slide 1
FCCee RF power sources and powering schemes
I. Syratchev, CERN

## Slide 2
MB Tristron (concept)
MB TS Klystron
(design)
TH2167 HE klystron
(HL-LHC)
Electro-vacuum tubes technologies for FCCee developed at CERN.
Fully compatible with HL-LHC power needs and infrastructure.

## Slide 3
Tristron (A.D. Sushkov et. al. 1967)
MB Prototype tested in 1997, V. Tsarev:
48kV
46kV
400 MHz FCC tristron power /efficiency performance
IOT (A. Haeff, 1939)
Alike IOT, Tristron (a hybrid between triode and klystron) is a gridded tube with additional penultimate cavity that boosts the RF power production efficiency from 75% (IOT) to above 90%.
Tristron concept is almost 60 years old, but it never been fully commercialized before.
B class
FCCee MB Tristron.

## Slide 4
For the required RF power modulation (by LLRF only), the HV set point can be selected (46kV is an example) so that average efficiency will stay ultimately high: 89.6% . With TS MBK klystron average operational efficiency will be dropped from 86% (tube in saturation) down to 67%.
MB tristron is now select as a baseline option for 400MHz (500kW) and 800MHz (250kW) FCCee RF powers sources.
Transient RF power modulation will impose certain requirement on the HV supply bandwidth, for details see the talk by D. Aguglia.
Cavities RF power modulation, 4 MHz filtered; 88MV
Z, FOC, 88MV
Z, DeFOC,88MV
Tristron transient efficiency
46kV
+/- 20% modulation depth
MB Tristron operational efficiency for FCC: Z-pole/RPO.
46kV
4MHz@-3dB
Tristron bandwidth
+/- 20% modulation depth

## Slide 5
One cavity out of operation;88MV
Failure mitigation mode
Required RF power modulation; 88MV
Power sweep range: 320kW-540kW!
46V
Tristron transient efficiency
With a single cavity failure, required power modulation will be provided by LLRF system and tristrons will preserve overall very high operating efficiency.
Eff. FOC= 91%
Eff. DEFOC= 89.6%

## Slide 6
MB Tristron operational efficiency for FCC: W,H-poles.
Nominal operation
Failure mode: 6 cavities off
With nominal operation tristron will be set to its optimal voltage/efficiency point. In case of failure LLRF will be able to compensate the effect providing operational efficiency above 90% (6 cavities failure case is shown as an example).
nominal
6 cavities failure

## Slide 7
Multibeam gridded tubes technology is well established in industry. Two MB IOT (1.2 MW, 0.7GHz, 10% duty) prototypes were built and successfully tested about 10 years ago.
MB tristron has similar topology as an MB IOT with an additional cavity located before the output cavity.
The major cost/complexity of existing MB IOT is driven by an array of 10 separate input cavities (one per beam) that must be tuned to be almost identical.
Technology readiness.
State of the art.

## Slide 8
Completed:
RF design
Systems integration
Tolerances analysis
With-beam simulations
400MHz, 500kW, =92%
Total length 1.49m. External solenoid is not shown
FCCee 400MHz, 0.5MW MB Tristron design with a common input cavity (CERN).
RF E-field in the input cavity
RF input
RF output
DC/RF breaker
Input cavity
Penultimate cavity
Output cavity
Individual collector x 10

## Slide 9
At ground
V1=46kV
V1+/- V bias
Grid gap=300µm
Grid wire 150µm
Tristron's gridded cathode optics simulations in CST TRK (DC)
Next step will be import of RF fields
and full PIC simulation of the bunching processes.
RF E-filed in the gap area of the input cavity
This topology is used now for thermal stresses and mechanical deformation simulations.
Current emission sites
DC E-field
DC current
0.026T external Bz -field
No beam area compression!
Flat grid topology
External solenoid and collector designs are in progress.

## Slide 10
10
Layout of the FCCee SRF system
  Start operation in March 2047
  Duration: 10 years
  Start operation in March 2058 Duration: 5 years

## Slide 11
Collider | Z | W | ZH
 | 1 beam RPO | 1 beam | 2 beams
Total RF voltage [MV] | 89 | 1049 | 2098
Beam current [mA] | 1292 | 135 | 2 x 26.8
RF Frequency [MHz] | 400.79 |  | 
Operating temp. [K] | 4.5 |  | 
Cavity voltage [MV] | 7.95 |  | 
# cell/cavity | 2 |  | 
Eacc [MV/m] | 10.6 |  | 
Q0 | 2.70E+09 |  | 
RF power [kW] | 380 |  | 
Optimum coupling QL | 9.2E+05 |  | 
# CM (with 4 cav/CM) | 66 |  | 
# cavities | 264 |  | 
X 264
Superconducting elliptical cavity
400 MHz, 2-cell
1.5 m. long
Electropolished and seamless RF surface
Niobium thin film with HiPIMS
X 66
Cryomodule
Segmented design, 4 cavities
Vertical FPC, HOM damping and extraction
Frequency tuning system
Thermal and magnetic shielding
Multibeam Tristron
400 MHz
46 kV
500 kW, CW
X 264
RF Unit
RPO at Z
2 beams at ZH
500 kW per cavity with overhead
500 kW MB Tristrons
1 cavity + 1 circulator per RF source
16 cavities (4 CM) per RF unit
WR2300 WG
X 16.5
400 MHz system – collider Z, W, ZH

## Slide 12: 800 MHz system – booster Z, W, ZH
Booster | Z | W | ZH
 | RPO | RPO | 
Total RF voltage [MV] | 80 | 401.9 | 1961
Beam current [mA] | 16.2 | 6.2 | 2
RF Frequency [MHz] | 801.58 |  | 
Operating temp. [K] | 2 |  | 
Cavity voltage at extraction [MV] | 5.6 | 13.5 | 17.5
# cell/cavity | 6 |  | 
Eacc [MV/m] | 4.9 | 12 | 15.6
Q0 | 3E+10 |  | 
Max RF power [kW] | 42 |  | 
Coupling QL | 1E+07 |  | 
# CM (with 4 cav/CM) | 28 |  | 
# cavities | 112 |  | 
X 112
Superconducting elliptical cavity
800 MHz, 6-cell
1.5 m. long
Bulk Niobium with electropolished and doped RF surface (mid T baked)
X 28
Cryomodule
Segmented design, 4 cavities
FPC on side, HOM damping and extraction
Frequency tuning system
Thermal and magnetic shielding
Multibeam Tristron
800 MHz
250 kW, pulsed (high duty cycle)
X 28
RF Unit
RPO at Z&W booster
50 kW per cavity
200 kW MB tristrons
4 cavities per tristron
16 cavities (4 CM) per RF unit
WR 1150 WG
X 7
Could be replaced by SSPA (1/cav) if RF efficiency is good and solution is economically feasible and reliable.
800 MHz system – booster Z, W, ZH

## Slide 13: 800 MHz system – ttb (collider and booster)
 | ttb collider |  |  | ttb booster
 | 2 beams |  |  | 1 beam
Total RF voltage [MV] | 2098 | 9202 |  | 10180
Beam current [mA] | 10 |  |  | 0.4
RF Frequency [MHz] | 400.79 | 800.58 | 800.58 | 
Operating temp. [K] | 4.5 | 2 | 2 | 
Cavity voltage [MV] | 7.95 | 22.5 | 22.5 | 22.8
# cell/cavity | 2 | 6 | 6 | 
Eacc [MV/m] | 10.6 | 20.1 | 20.1 | 20.3
Q0 | 2.7E+9 | 3E+10 | 3E+10 | 
RF power [kW] | 78 | 195 | 195 | 8.9/12.7
Optimum coupling QL | 4.5E+06 | 4.1E+06 | 4.1E+06 | 9.2E+07/2.7E+07
# CM (with 4 cav/CM) | 66 | 102 | 102 | 112
# cavities | 264 | 408 | 408 | 448
X (408 + 448)
Superconducting elliptical cavity
800 MHz, 6-cell
Nb3Sn if R&D is successful
X (102 + 112)
Cryomodule
Segmented design, 4 cavities, 2 K
Operation at 4.5 K is R&D successful
X 28
Booster (SSA)
Collider (800 MHz tristrons)
X 26
X 448
Multibeam Tristron
800 MHz
250 kW, CW
Solid State Amplifier (SSA)
800 MHz
10-15 kW pulsed
X 408
RF Units

## Slide 14
Spare slides

## Slide 15
Why MB Tristron can be so efficient?
Multi-beam technology -> low perveance per beam
Gridded cathode provides fully saturated bunches -> 75% (best IOT performance)
Penultimate cavity controls optimal velocity spread (congregation) within the bunch, followed by bunch length compression in the drift -> 85% (basic of the Tristron concept).
‘Very’ long gap in the output cavity with negative detuning allows partial electrons bouncing -> 91% (discovered in our studies of the HE klystrons at CERN).
Hollow beam configuration reduces radial bunch stratification -> 93%.
FCC TS klystron
Optimized MB Tristron efficiency vs. perveance
FCC MB tristron
Bouncing electrons
Electron bunches velocity modulation in tristron
Optimal congregation
Penultimate cavity
Output cavity
Drift length provides optimal bunch length compression
Klystrons theoretical limit
Average velocity (0.1Ve/c)
Spent beam
Phase space animation
Tristron (fixed beam power)
CEPC CSM klystron

## Slide 16
Gridded tube bunch current generation B CLASS in CST PIC, design point 46kV, 1.07A/beam
I av.=1.07A

## Slide 17
RF power / efficiency measurement in CST
RF power at port
Balanced efficiency calibration (beam in a collector)
Beam current

## Slide 18
Issues with transient loading of the HV power supply (Z pole)
HV
Tristron
Transient power drain from HV power supply
Common HV
Tristron#1
Tristron#2
Transient power drain from common HV power supply
46kV, 88MV