## Slide 1: FCC-ee Power Coupler Design Overview
Shahnam Gorgi Zadeh
With inputs from: E. Montesinos, F. Peauger, R. Calaga, S. Jerome Calvo, C. Sharp, M. Timmins, V. Parma. K. Canderan

## Slide 2: Some cryomodule RF components
400 MHz cryomodule
800 MHz cryomodule
2-cell cavity
6-cell cavity
HOM coupler
HOM coupler
Fundamental Power coupler
Fundamental Power coupler
Fundamental power coupler is a critical component that transfers high levels of RF power from the generator to the cavity and ultimately to the beam.
Mainly RF aspects covered in this presentation.

## Slide 3: FCC-ee power requirement
Input power necessary to establish ​ in the cavity with a beam current
Z, W, H
400 MHz
tt, 400 MHz
tt, 800 MHz
Z, W, H booster
800 MHz
tt booster
800 MHz
Make this term zero by right detuning
Make this term minimum by choosing optimum
ttb: 10 Hz detuning
ttb: 20 Hz detuning

## Slide 4: Peak field in coaxial lines
E. Montesinos, RF power transport, CAS course on RF for Accelerators, Berlin July 2023
Minimum peak electric field occurs near 30 Ω impedance, while conductor losses are minimized around 77 Ω
Multipacting onset power is higher at larger impedances, due to the increased gap between inner and outer conductors
at of 500 kW

## Slide 5: Coaxial coupler update at 800 MHz
=801.58 MHz
=250 kW
coax air=280 kV/m
WG air=392 kV/m
window=134 kV/m
P1
P2
Courtesy: S. Calvo
Coaxial disk window is used in the coupler design
The cone shape helps lower peak fields on the window by reducing impedance to ~27 Ω on the upper part; the lower part maintains 75 Ω to reduce coaxial line losses on the vacuum side and avoid direct line-of-sight between the window and the cold cavity surface & beam
Coupler shape, waveguide height, step, and window location are optimized as part of the matching section to ensure low transmission at 801.58 MHz
The bandwidth is wide enough to damp lower-order modes of the cavity in the 785 MHz to 800 MHz range
WR1150
Notes: 31W loss in alumina at 250kW input power for tan delta of 1e-4

## Slide 6: tuning of 800 MHz FPC
Booster
cavities
tt collider
E field at U=1 J
U=169 J, =4.3e6
tuning is performed by changing the length of the waveguide behind the FPC on the air side
Larger preferred for booster cavities to avoid steep tuning curve → requires different antenna length
Notes: 23W power loss on the WG behind FPC

## Slide 7: 400 MHz power coupler
F. Gerigk, et al. The LINAC4 power coupler
Disk window based on the LINAC4 window design
The matching is done by adjusting the waveguide height and length, window location and the step size in front of the window
Robust design with large bandwidth. Peak fields centered, away from brazing joints. High thermal losses at window demand air-side cooling
Challenging to integrate into cryostat  see Karin’s presentation
For 500 kW input power
on WG air=173 kV/m
in vacuum=355 kV/m
on window=187 kV/m
400 mm
200 mm
Half-height WR2300
Courtesy: S. Calvo
Notes: 95W loss in alumina at 500kW input power for tan delta of 1e-4

## Slide 8: tuning of 400 MHz FPC
Air side
Vacuum side
is tuned by changing the stub tuner length on the air side
The of the 0-mode in the FM passband is similar to that of the fundamental mode
tt collider
Z,W, H collider
U=144 J
=9.49e5
FM:

## Slide 9: Summary and outlook
Outlook
Detailed mechanical design and thermal (cool-down) requirements are ongoing
The difficulties with space constraints and cryomodule integration have created a strong drive for more compact design solutions. The relatively lower power and tuning range in RPO facilitate this design shift. A more compact coupler design is being explored
Summary
800 MHz: coaxial disk window with conical shape to reduce peak electric fields on the window and “hide” window from the cold cavity surface
400 MHz: Linac4-style disk window on the waveguide for high power handling at 400 MHz
Both designs use 75 Ω impedance in the lower coaxial section to reduce losses and intensity of multipacting
tuning achieved via air-side waveguide geometry modifications and bandwidths are sufficient to cover lower-order modes within the FM passband
Courtesy: S. Calvo
400 MHz FPC concept similar to the 800 MHz FPC design

## Slide 10
Appendix

## Slide 11: Window families at CERN
E Montesinos, FCC couplers, SRF workshop CERN, 2024
E. Montesinos, RF power transport, CAS course on RF for Accelerators, Berlin July 2023
CERN power couplers since 2000’s

## Slide 12: 800 MHz FM passband
FM
3
4

## Slide 13: Lower order modes (I)
,
,
[mm] | Mode | [W] (at ) | [W] Inner coax (Cu) | [W] Outer coax (Cu) | [W] Upper WG (Al)
175 | 1 | 160 | 94 | 22 | 44
175 | 2 | 655 | 344 | 90 | 221
 | Mode |  |  |  | 
175 | 1 | 160 | 94 | 22 | 44
175 | 2 | 655 | 344 | 90 | 221
Mode 1
Mode 2
If one of the two modes trapped in the FPC gets excited by the beam, additional power could be induced and dissipated on the FPC outer wall and inner coax.

## Slide 14: LOM frequency shift
Mode 1:
Mode 2:
To address LOM excitation and potential coupler overheating in worst-case scenarios:
If beam spectral lines are known: Slightly adjust the inner antenna length in the initial design to shift the LOM frequency away from the beam spectral lines.
If beam spectral lines are unknown: Introduce flexibility in the geometry e.g., changing the volume above the FPC by 1 mm (as shown in the figure below by moving a short plane or membrane above inner coax) can shift mode frequencies by more than one bandwidth.

## Slide 15: MP in conical coax
Z0=75 Ω
Z0=50 Ω
Z0=75 Ω
Z0=50 Ω
Z0=50 Ω
Z0=50 Ω
Z0=75 Ω
Z0=75 Ω
P=200 kW, f=400.79 MHz, growth factor=5

## Slide 16: Multipacting analysis of the disk window
Average Multipacting order =9.1
There are hot zones of high order multipacting on the margins of the window

## Slide 17: MP in different LHC coupler zones
Zone 1
Zone 3
Zone 2
Zone 3
Zone 3
Zone 2
Zone 1
150 kW input power
https://edms.cern.ch/ui/file/194664/AE/lhcacsmc0069-vAE.pdf
Zone 4