## Slide 1: Availability, Efficiency and Integrated Luminosity: Rising to the challenge in the FCC-ee
Jack Heron, Hannah Dostmann, Lukas Felsberger, Daniel Wollmann, Jan Uythoven
22nd May 2025

## Slide 2: Availability and Luminosity
Stable Beams
Operation
Down Time
FCC-ee:
365 days
−120 (extended shutdowns)
− 30 (annual commissioning)
− 20 (machine development)
− 10 (technical stops)
185 days for physics

## Slide 3: Breakdown into Systems and Subsystems
FCC-ee
Failure Rate
Repair Duration
Availability
Integrated Luminosity
1) System failure rate
Extrapolate from reliability performance of existing accelerator systems

## Slide 4: RF System
Acknowledgement: Olivier Brunner, Andy Butterworth, Franck Peauger, Ivan Karpov
Using AFT fault data 2015-2024
LHC:
  16 SRF cavities
FCCee:
aft.cern.ch
aft-stats.web.cern.ch
 | Z |  | W |  | ZH |  | tt̄ | 
 | collider* | booster | collider* | booster | collider** | booster | collider** | booster
Cavities [#] | 132 | 112 | 132 | 112 | 264 | 112 | 672 | 448
Redundancy [cavities] | 1 | 0 | 6 | 0 | 26 | 11 | 67 | 44
Redundancy [%] | 0.75 | 0 | 4.5 | 0 | 10 | 10 | 10 | 10
* Per beam ** Both beams

## Slide 5: Electrical Network
External Network Perturbations:
  Independent at PA and PH-PD
Internal Equipment Faults:
  Scaled by number of Substations
Redundant link PA-PD:
  Only for non-child down time
  Changeover ~1 h
  Not applicable to PH
3
Genissiat
Line 1
Line 2
PA
PD
PH
# substations
PD
x4
x1.34
22 May 2025
Jack Heron | Availability, Efficiency and Integrated Luminosity in the FCCee
Acknowledgement: Charline Marcel, Mario Parodi
See presentation:
Hannah Dostmann
Technical Infrastructure Availability
Technical Infrastructure: Electricity & Energy Management
Tuesday 20th May
x3

## Slide 6: Power Converters
One dump every 3 days
5 days
LHC fault data
Same level of redundancy as LHC
Acknowledgement: Byamba Wicki, Serge Pittet
9 days
0.6 days

## Slide 7: Breakdown into Systems and Subsystems
FCC-ee
Failure Rate
Repair Duration
Availability
Integrated Luminosity
1) System failure rate
Extrapolate from reliability performance of existing accelerator systems
2) System repair duration

## Slide 8: Two fault types:
Remote Repair Faults
  Repair achieved from the control room
  E.g. by resetting components
Human Repair Faults
  Requires human intervention
  Approach time and/or cool down time
https://www.istockphoto.com/vector/isometric-control-center-gm164401684-15526568
https://www.flaticon.com/free-icon/technician_6342684

## Slide 9
LHC
FCC
Drive time
1h+
Human Repair Faults
  Requires human intervention
  Approach time 0.3-1.5 h
  Cool down time 1-24 h
https://www.istockphoto.com/vector/isometric-control-center-gm164401684-15526568
https://www.flaticon.com/free-icon/technician_6342684

## Slide 10: “Realistic” Repair Timeline:
Diagnosis + attempts to reset from control room
Approach time
Remote repairs
Human repairs
Humans in tunnel
We can’t fix it from here. Get someone out there!
Once human repairs start, they will finish.
1 h
Operation resumes if possible before humans are in the tunnel
20 min – 1.5 h
Repair
Operation
resumes here
Fault
Cool-Down time
1 - 24 h

## Slide 11: Breakdown into Systems and Subsystems
FCC-ee
Failure Rate
Repair Duration
Availability
Integrated Luminosity
1) System failure rate
Extrapolate from reliability performance of existing accelerator systems
2) System repair duration
Remote repairs
Human repairs
  Approach time
  Cool down time
3) Accelerator Performance

## Slide 12: FCC-ee Operation Cycle
Adjust
Set Up
10 min
10 min
Pilot bunch injection
10 min
Polarisation
1.5 h
Fill
Physics
20 h
Burn Off
Down for Repair
Dump
Default
Repair completed
Collider failure
Injector Complex failure
Stable Beams
Operation
Down
Time
  Z,WW
 | Z | WW | ZH | tt
Fill time (min) | 7.7 | 2.5 | 1.52 | 1.45
Lifetime (min) | 15 | 12 | 12 | 11
 | Z | WW | ZH | tt
 | 7.7 | 2.5 | 1.52 | 1.45
 | 15 | 12 | 12 | 11
  ,
Resonant depolarization is impossible
Acknowledgement: Jacqueline Keintzel

## Slide 13: Acknowledgements
Jacqueline Keintzel
Franck Peauger
Olivier Brunner
Andy Butterworth
Ivan Karpov
Serge Pittet
David Nisbet
Davide Aguglia
Ben Todd
Byamba Wicki
Jean-Paul Burnet
Klaus Hanke
Chris Roderick
Ioan Kozsar
Alessandro Masi
Damien Lafarge
Tomasz Ladzinski
Verena Kain
Frank Zimmerman
Markus Zerlauth
Jesper Nielsen
Mario Parodi
Charline Marcel
Manfred Wendt
Roderik Bruce
Anton Lechner
Marco Calviani
Antonio Perillo Marcone
Guillermo Peon
Inigo Martin Melero
Laurent Delprat
Yann Dutheil
Christoph Wiesner
Jan Uythoven
Jeremie Bauche
Wolfgang Hofle
Roberto Kersevan
Gregory Pigny
Rudiger Schmidt
Arjan Verweij
Benoit Salvant
Bernhard Holzer
Bettina Mikulec
Cedric Hernalsteens
Rama Calaga
Roberto Losito
Katsunobu Oide
Hannes Bartosik
Paolo Craievich (PSI)
Masanori Sato (KEK)
Sharon Vetter (SLAC)
William Corocho (SLAC)
Matt Gibbs (SLAC)
Ralph Boespflug (DESY)
Rainer Wanzenberg (DESY)
Michaela Schaumann (DESY)
Cristian Maccarrone (ESRF)
Laurent Hardy (ESRF)
Antoine Chance (CEA)
Jorg Wenninger
Gijs de Rijk
Daniel Valuch
Belen Maria Salvachua Ferrando
Matteo Solfaroli Camillocci
Alice Vanel
Luke Von Freeden
Robert Kieffer
Igor Syratchev
Helga Timko
Rafaele Tegas
Giacomo Lavezzari
Manuel Colmenero Moratalla
Milosz Blaszkiewicz
Markus Widorski
Andrew Coleman

## Slide 14: Results

## Slide 15
Overall Performance
Delivered integrated luminosity below design in all energy modes
Due to low availability and low efficiency
Particularly in Z and W modes due to long turnaround time following dump
 | Z | W | H | tt
Integrated luminosity target [ab-1] | 205 | 19.2 | 10.8 | 3.12

## Slide 16
Unavailability & Lost Luminosity
Injector Complex

## Slide 17
RF System
Failed RF cavities each week
Repairs needing human tunnel access
Redundancy
Results assume perfect redundancy (invisible to operation, no common mode failures)
We need to look closer at subsystems + auxiliaries
Collider
Booster
Z
W
H
tt
Z
W
H
tt
 | Z |  | W |  | ZH |  | tt̄ | 
 | collider | booster | collider | booster | collider | booster | collider | booster
Cavities [#] | 132 | 112 | 132 | 112 | 264 | 112 | 672 | 448
Redundancy [cavities] | 1 | 0 | 6 | 0 | 26 | 11 | 67 | 44
Redundancy [%] | 0.75 | 0 | 4.5 | 0 | 10 | 10 | 10 | 10
Redundancy eliminates down time completely
Operational Cost Factors:
High failure rate of cavities, esp. in tt (1120 cavities) - hard-working maintenance service

## Slide 18: Electrical Network
Chart: LHC Electrical Network Down Time 2015-2025
| Internal Equipment | Internal Child Faults | External Child Faults | External Perturbations
LHC Electrical Network Down Time 2015-2025 | 394.91 | 110.29 | 158.45 | 17.7
Internal Equipment
External Perturbations
Child faults in other systems
40%
58%
2%
Redundancy in the internal network could be powerful
However – we need a solution for child faults!
  Rigorous design requirements for resilience to power disturbance
  How to dampen voltage deviations (internal + external) ?
LHC Child Down Time (h, #)
External Perturbations
Internal Equipment
See presentation:
Hannah Dostmann
Technical Infrastructure Availability
Technical Infrastructure: Electricity & Energy Management
Tuesday 20th May

## Slide 19: Power Converters
Z
W
H
tt
Z
W
H
tt
Collider
Booster
Current optics configuration:
  Sextupoles powered in groups of four
  Correctors powered individually
How many power converters can we lose without dumping the beam?
  Needs a detailed study from optics and machine protection
Assumes the same degree of redundancy as exists currently in LHC
Huge number of converters due to many sextupole & corrector magnets

## Slide 20: Solution: Injection of Polarised Bunches
  Z,W
More than doubles delivered integrated luminosity

## Slide 21: Parameter Scan: Reliability
Only systems above the required dump rate need to improve
Unreliability
Most efficient way to allocate resources for reliability consolidation:

## Slide 22
Reliability equivalent to polarised injections
Target Achieved with polarised injections
2025
Target Achieved with reliability only
Parameter Scan: Reliability

## Slide 23: Conclusions
R&D Opportunity:
  Injection of polarised bunches
Forecasted integrated luminosity is below design in all energy modes
  Low availability and low efficiency
Systems of highest concern:
  RF
  Power Converters
  Injector Complex
  Technical Infrastructure
  Beam Losses

## Slide 24: Outlook
Short Term:
Requirements and milestones, performance benchmarking
More nuanced reliability models in parallel with design process
“Low-hanging fruit” – R&D opportunities evaluation
Performance/Cost optimisation over the whole machine
Develop a coherent support framework for all system designs
TDR & Beyond:
  Design for reliability:
    Detailed modelling
    Redundant / modular / hot-swappable paradigm
    Interfacing between systems
  Tools, training, expertise
  Extensive hardware testing & validation
  Diagnostics & Health Monitoring
  Fault prediction
  Fault tracking & Analytics
  Lifecycle Reliability
Success in FCC requires machine-wide improvement in reliability
Systematic Reliability / Availability Support Framework