## Slide 2: FCCee top-up injection
Y. Dutheil, on behalf of SY-ABT and the top-up injection WG CERN, Geneva, Switzerland

## Slide 3: Outline
Context
Baseline scheme choice
  Concept
  Implementation in PB
  Hardware choice
Top-up injection working group
  Activities and outcomes
  Objectives for 2025
Conclusion

## Slide 4: Context
The FCCee collider will deliver lepton collisions for sustainable physics [2]
  Short beam lifetime and high luminosity require continuous refilling of the circulating bunches
  Swap-out injection is not possible due to the high bunch charge HEPS-scheme [1] has not been explored
  Top-up injection is required to maintain the collider bunch charge and luminosity
Top-up injection in numbers
  For Z-mode
    10 successive injections within 30 s, per beam
    18 MJ per beam, 180 kJ per injection
  Injector complex is sized with a minimum injection efficiency of 80%
[1] Z. Duan et. al., The Swap-Out Injection Scheme for the High Energy Photon Source, IPAC2018, Vancouver, BC, Canada [2] M. Benedikt, FCC Feasibility Study Results, FCCweek 2025, Vienna, Austria
[2]

## Slide 5: Top-up injection in numbers
FCCee collider parameter [1]
FCCee booster parameter
H & T modes:
Enhance injection efficiency by increasing energy offset
W mode:
Large beam emittance
[1] K. Oide, Collider GHC lattice, [2]Booster lattice, GitLab
Beam energy GeV | 45.6 | 80 | 120 | 182.5
Horizontal emittance [nm] | 0.71 | 2.16 | 0.66 | 1.58
RF acceptance [%] | 1.21 | 3.32 | 2.06 | 3.07
Energy acceptance (MA) [%] | 1.0 | 1.0 | 1.9 | -2.8/+2.5
Energy Spread (BS) [%] | 0.115 | 0.105 | 0.176 | 0.186
Septa blade thickness (mm) | 2.8 |  |  | 
Beam energy GeV | 45.6 | 80 | 120 | 182.5
Horizontal emittance [nm] | 0.71 | 2.16 | 0.66 | 1.58
RF acceptance [%] | 1.21 | 3.32 | 2.06 | 3.07
Energy acceptance (MA) [%] |  |  |  | -2.8/+2.5
 | 0.115 | 0.105 | 0.176 | 0.186
Septa blade thickness (mm) | 2.8 |  |  | 
Beam energy GeV | 45.6 | 80 | 120 | 182.5
Horizontal emittance [nm] | 0.12 | 0.27 | 0.6 | 1.4
Energy spread [10-3] | 0.38 | 0.67 | 1.01 | 1.53
Extraction bunch length [mm] | 2.43 | 2.56 | 2.26 | 1.98

## Slide 6: Baseline scheme : concept and objectives
Objective of the injection scheme
  No perturbation to the circulating beam outside injection region
  No perturbation to the IRs and experiment
  Exploiting existing technologies
  Highly reliable and resilient to accidental scenario
Selected concept
  Conventional injection scheme
  On-axis injection : separation between injected and circulating beams is provided by dispersion and an energy offset
    Faster damping since the injected beam undergoes longitudinal oscitations
    Flat trajectories in the achromatic experimental straight sections minimises radiation doses to experiments
    Overall, less affected by injection errors and provided better injection efficiency at higher beam current [1]
[1] Collier, Paul. "Synchrotron phase space injection into LEP." Proceedings Particle Accelerator Conference. Vol. 1. IEEE, 1995.
Bumped orbit
Off energy orbit

## Slide 7: Baseline concept : implementation in PB
Layout in PB
F. Valchkova-Georgieva, FCCee Underground Structure point B, PLM reference, EDMS reference

## Slide 8: Baseline concept : implementation in PB
Layout in PB
  First half of the straight section
  Booster extraction at the middle of the straight section
  Collider injection near the end of the straight section
Present implementation only in GHC V25.1
  Fixed optics with m and
  Optics change at the injection point may require significant tuning
Positron beam direction

## Slide 9: Baseline concept : orbit bump
The conventional scheme
  Bump amplitude of 10σ + septum thickness
  Fast bump lasting only 1 turn
Pi-bump
  Kicker strength: 40 µrad and 60 µrad (due to different beta function at the two locations)
  Rise and fall time of 600 ns flat-top time: 304 µs for full turn filling
Kicker hardware discussed on Wednesday (Overview of and Challenges for the FCCee Fast Pulsed Beam Transfer Systems by G. Favia)
kicker
kicker
septum

## Slide 10: Baseline concept : septum hardware choice
Thin magnetic septum
  Long flat-top requirement prevents the use of eddy current septum
  Completely under vacuum to minimise the apparent thickness
Specifications
  Blade thickness of 2.8 mm
  Flat-top duration of 304 μs
See poster by L. Porta on Thursday
Phase space at the injection point for Z-mode
Mechanical design concept for the collider

## Slide 11: Top-up injection WG
Context
  Significant penalties on injection performance at higher circulating currents have been major challenges at other lepton colliders [1, 2]
  Unique challenges of FCCee due to the beam energy and machine protection aspects
  Top-up injection requires the combined expertise of multiple experts (optics, beam dynamics, injection systems, collective effects, …)
Regular meeting to converge towards comprehensive studies of the injection scheme
  Meeting category here and open egroup fcc-ee-topup-injection
  Possible reporting to the optics design meeting
  Input to the layout & optics meeting
  Precise mandate remains to be established
[1] M. Masuzawa, et al., in 7th International Beam Instrumentation Conference (JACoW, 2019), p.TUPC13. https://doi.org/10.18429/JACoW-IBIC2018-TUPC13
[2] P. Collier. Transfer and injection into LEP. Presented at the 7th LEP Performance Workshop, Chamonix, France (1997). URL https://cds.cern.ch/record/348081

## Slide 12: Top-up injection WG: baseline scheme optimisation for the FSR
First simulation of injection with beam-beam element
  Conducted at the Z-mode and with GHC v25.1
  Revealed important particle loss for the baseline injection scheme
Hybrid scheme
  Momentum offset may be reduced at the expense of betatron oscillations
  Red line in the DA/MA denotes the geometrical condition for injection
  New hybrid working point with 1-2 σ betatron offset validated and providing high injection efficiency
Quarter quadrant representation of the dynamic aperture and momentum acceptance without beam-beam. Crosses denote the three injection settings simulated with beam-beam
Evolution of the captured fraction of injected beam for three different injection betatron offset, modelled with Xsuite using the beam-beam element under nominal conditions.

## Slide 13: Top-up injection WG: Quasi-Strong-Strong Beam-Beam
Tracking with Quasi-Strong-Strong Beam-Beam
  Uses the full lattice with SAD
  Modelling of bootstrapping from low intensity
Preliminary observation
  Vertical optics mismatch in the presence of beam-beam
  Increase of longitudinal emittance with intensity
  Tool to identify and optimise the beam parameters
Poster by T. Mori on Thursday
T. Mori, top-up injection modelling and quasi-strong-strong beam-beam effects, top-up injection meeting, 03/04/2025
T. Mori, Updates of Injected Beam Study, 205th FCC-ee Accelerator Design Meeting

## Slide 14: Top-up injection WG: Injection losses [1]
Example of Z-mode
  18 MJ of circulating beam and 180 kJ injected every 3s
Injection losses modelling
  Local losses at the injection septum from the circulating beam
  Distributed losses around the ring from the injected beam
Injection protection requirement
Background to experiments -> Talk by G. Nigrelli : “First look at injection backgrounds” on Thursday
Injected beam
Circulating beam halo
[1] G. Nigrelli, preliminary results on injection losses, FCC-ee top-up injection

## Slide 15: Top-up injection WG: beam dynamics and benchmark
Injected beam dynamics [1]
  Vertical beam emittance increase during injection tracking seem understood
  Highlights the importance of chromatic matching and the role of beam-beam
Code benchmark
  Presently Xsuite and SAD used in parallel
  Simulation in gitlab CI being implemented for continuous comparison
  Collider injection git repo
[1] K. Skoufaris, Injection performances and emittance evolution for v25.1_GHC, 205th FCC-ee Accelerator Design Meeting

## Slide 16: Top-up injection WG: objective in 2025
Optics and implementation
  Possible update to the optics requirement for the GHC lattice and validation of lower energy offset (0.85 % to 0.90 %)
  Implementation of the injection scheme into the LLC lattice
Reviewed injection scheme
  Using a full 4-bump system for flexibility and independence from optics
  Feasibility and advantages of a multipole injection kicker
Beam dynamics and benchmark
  Maintain simulation for both SAD and Xsuite
  Review and optimisation of the injected beam optics requirements
Input to the optics & layout for comparison of GHC and LCC lattices
  Injection efficiency and hardware requirements
  Injection losses and background to experiment
  Machine protection and accidental scenario
Timeline and deliverables towards the pre-TDR

## Slide 17: Conclusion
Baseline scheme established for the FSR
  Exploits a robust concept with the aim of frequent and reliable injection with minimal perturbation to the experiments
  Hardware solution identified for the FSR but development timeline to installation requires a commitment to the selected parameters
  Presently only implemented in the GHC lattice, must be done for the LCC
  Some aspects need reviewing (reduced momentum offset, 4-bump layout)
  Is there an interest to enforce an on-axis baseline or hybrid is sufficient ?
Top-up injection WG
  Resuming activities in 2025 and already swift progress (benchmark, beam dynamics, injection losses, beam-beam, …)
  Clear mandate is being established
Input to the layout and optics meeting by the end of 2025
  The format and precise list of criteria remain to be established
  Complete comparison is not possible within the required timeline but the present level of study on GHC could certainly be applied to the LCC

## Slide 18: Required dispersion
Increased dispersion is needed to reduce the injected beam energy offset
Based on Collider GHC V25.1 and Booster V24_FODO