## Slide 1
Impact of Collimators' Geometric Impedance on Beam Stability in the FCC-ee
Analysis and Optimization Techniques
Dora Gibellieri1,2,3, Carlo Zannini1, Adnan Ghribi2,3, Mauro Migliorati4,5 and Mikhail Zobov4,5
1CERN 2University of Caen Normandy 3GANIL 4Sapienza University of Rome 5INFN
FCC week 2025 - 11th edition of the Future Circular Collider Conference , Vienna, Austria, 20 May 2025

## Slide 2
20.05.2025 | FCC week 2025 | Dora Gibellieri
Outline
02
Introduction
  FCC-ee main parameters for Z configuration
  FCC-ee main ring impedance model
FCC-ee beam coupling impedance of the collimation system
  Collimators geometrical impedance
    Optimization strategies
  Collimators RW impedance
    Comparison between different optics
Conclusion and next steps

## Slide 3
Outline
Introduction
03
20.05.2025 | FCC week 2025 | Dora Gibellieri
Introduction
  FCC-ee main parameters for Z configuration
  FCC-ee main ring impedance model
FCC-ee beam coupling impedance of the collimation system
  Collimators geometrical impedance
    Optimization strategies
  Collimators RW impedance
    Comparison between different optics
Conclusion and next steps

## Slide 4
FCC-ee main parameters for Z configuration
Introduction
Necessity of having a highly flexible model to account for all changes during the feasibility study development phase
04
20.05.2025 | FCC week 2025 | Dora Gibellieri
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.18
RF frequency (MHz) | 400
RF voltage (MV) | 88.5
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/2.1
Bunch length (mm) (SR/BS)* | 5.15/15.2
Energy spread (%) (SR/BS)* | 0.039/0.115
Piwinsky angle (BS)* | 25.8
/ | 0.023/0.098
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 144
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.18
RF frequency (MHz) | 400
RF voltage (MV) | 88.5
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/2.1
Bunch length (mm) (SR/BS)* | 5.15/15.2
Energy spread (%) (SR/BS)* | 0.039/0.115
Piwinsky angle (BS)* | 25.8
 | 0.023/0.098
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 144
*SR: synchrotron radiation, BS: beamstrahlung

## Slide 5
FCC-ee main parameters for Z configuration
Introduction
Necessity of having a highly flexible model to account for all changes during the feasibility study development phase
05
20.05.2025 | FCC week 2025 | Dora Gibellieri
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.18
RF frequency (MHz) | 400
RF voltage (MV) | 88.5
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/2.1
Bunch length (mm) (SR/BS)* | 5.15/15.2
Energy spread (%) (SR/BS)* | 0.039/0.115
Piwinsky angle (BS)* | 25.8
/ | 0.023/0.098
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 144
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.18
RF frequency (MHz) | 400
RF voltage (MV) | 88.5
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/2.1
Bunch length (mm) (SR/BS)* | 5.15/15.2
Energy spread (%) (SR/BS)* | 0.039/0.115
Piwinsky angle (BS)* | 25.8
 | 0.023/0.098
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 144
*SR: synchrotron radiation, BS: beamstrahlung

## Slide 6
FCC-ee main ring impedance model
IRIS / IW2D · GitLab
20.05.2025 | FCC week 2025 | Dora Gibellieri
Introduction
06
Identify main impedance contributors
3D EM Simulations and Analytical Model
Accelerator I/W Model

## Slide 7
FCC-ee main ring impedance model
ImpedanCEI/fcc_ee_IW_model: Impedance/Wake model of the Future Circular Collider (FCC)
20.05.2025 | FCC week 2025 | Dora Gibellieri
FCC-ee I/W model
Introduction
07
Identify main impedance contributors
3D EM Simulations and Analytical Model
Accelerator I/W Model

## Slide 8
Highly flexible I/W model
20.05.2025 | FCC week 2025 | Dora Gibellieri
Thanks to its flexibility, the developed model integrates seamlessly with IW2D. Variations in material properties or coating thickness—such as changes to the NEG coating of the beam pipe—can be readily incorporated, enabling rapid evaluation of their impact on the overall impedance.
Introduction
08
Identify main impedance contributors
3D EM Simulations and Analytical Model
Accelerator I/W Model
Flexible & modular model

## Slide 9
FCC-ee main ring impedance model
Beam Dynamics Simulations
Output:
Assessment of beam stability
20.05.2025 | FCC week 2025 | Dora Gibellieri
Introduction
09
Identify main impedance contributors
3D EM Simulations and Analytical Model
Accelerator I/W Model

## Slide 10
FCC-ee main ring impedance model
Constant Model Optimization
20.05.2025 | FCC week 2025 | Dora Gibellieri
Flexible & modular model
Introduction
10
Identify main impedance contributors
3D EM Simulations and Analytical Model
Accelerator I/W Model
Beam Dynamics Simulations
Output:
Assessment of beam stability

## Slide 11
20.05.2025 | FCC week 2025 | Dora Gibellieri
Outline
Introduction
  FCC-ee main parameters for Z configuration
  FCC-ee main ring impedance model
FCC-ee beam coupling impedance of the collimation system
  Collimators geometrical impedance
    Optimization strategies
  Collimators RW impedance
    Comparison between different optics
Conclusion and next steps
11
FCC-ee beam coupling impedance of the collimation system

## Slide 12
FCC-ee beam coupling impedance of the collimation system
12
Identify main impedance contributors
3D EM Simulations and Analytical Model
Accelerator I/W Model
FCC-ee I/W model
The visualization of certain parameters, such as the imaginary part of the y-dipolar impedance of various contributors, enables the identification of the primary impedance sources.
Criticality of the collimation system
FCCee_z_v23_coll_TCTs
Collimation optics:
20.05.2025 | FCC week 2025 | Dora Gibellieri

## Slide 13
Collimation system: study process
Collimators were simulated in CST Studio Suite, initially using a simplified model to isolate geometric and resistive wall dependencies.
Schematic design
FCC-ee beam coupling impedance of the collimation system
13
While previous models accounted only for the resistive wall (RW) contribution, this study includes both resistive and geometric effects, enabling a more comprehensive understanding of the system’s impact on beam stability.
The model accurately reproduces the actual jaw lengths and apertures and effectively highlights critical parameters that can be optimized to mitigate impedance.
A linear taper with an angle of 15 degrees was initially proposed.
By enabling the isolation of geometric effects, this model served as a baseline for next refinements

## Slide 14
Collimation system: study process
SuperKEKB design
Schematic design
Design based on collimators for SuperKEKB.
FCC-ee beam coupling impedance of the collimation system
14
Courtesy of Regis Seidenbinder

## Slide 15
Collimation system: study process
Winglets design
Schematic design
Design based on collimators for SuperKEKB, with circular pipe and winglets.
FCC-ee beam coupling impedance of the collimation system
15

## Slide 16
Collimation system: study process
Winglets design
Schematic design
Final proposed design with circular pipe without winglets at the collimator injection.
Non-winglets design
FCC-ee beam coupling impedance of the collimation system
16

## Slide 17
Optimization strategies
Since the geometrical contribution of the collimators has been identified as the primary source of impedance, an optimization of the taper angle for all vertical collimators has been proposed, reducing it from 15 degrees to 2.5 degrees. The most recent optimization refers to latest collimators design.
17
20.05.2025 | FCC week 2025 | Dora Gibellieri
tcp.v.b1
Coll. length = 250 mm
Taper length = 110mm
Taper angle = 15 degrees
tcp.v.b1
Coll. length = 250 mm
Taper length = 630 mm
Taper angle = 2.5 degrees
It is worth noting that the achievable taper angle could be limited by spatial and mechanical constraints
Collimators geometrical impedance

## Slide 18
20.05.2025 | FCC week 2025 | Dora Gibellieri
18
Collimators geometrical impedance
Geometrical impedance mitigation
Thanks to the optimization of the taper angle for all vertical collimators by reducing it from 15 degrees to 2.5 degrees, the y-transverse impedance drastically reduces.
Horizontal and vertical collimator taper angle of 15 degrees
Horizontal collimator taper angle of 15 degrees and vertical taper angle of 2.5 degrees
Optimization
FCCee_z_v23_coll_TCTs

## Slide 19
20.05.2025 | FCC week 2025 | Dora Gibellieri
Outline
Introduction
  FCC-ee main parameters for Z configuration
  FCC-ee main ring impedance model
FCC-ee beam coupling impedance of the collimation system
  Collimators geometrical impedance
    Optimization strategies
  Collimators RW impedance
    Comparison between different optics
Conclusion and next steps
19
Collimators RW impedance

## Slide 20
Comparison between different optics
20
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
V24.4
v23
V25.2
K. Oide: FCCWeek_Optics_Oide_230606
K. Oide: Optics_Oide_bx*:techi_250424
K. Oide: Optics_Oide_241106
Different optics have been analyzed:

## Slide 21
Name | Length (m) | gap/2 (mm) | Material | (m) | (m)
tcp.h.b1 | 0.25 | 6.7 | MoGr | 517.98 | 755.84
tcp.v.b1 | 0.25 | 2.5 | MoGr | 519.09 | 756.98
tcs.h1.b1 | 0.3 | 3.8 | Mo | 117.58 | 789.74
tcs.v1.b1 | 0.3 | 2.5 | Mo | 421.47 | 587.39
tcs.h2.b1 | 0.3 | 5.1 | Mo | 214.69 | 759.20
tcs.v2.b1 | 0.3 | 3.0 | Mo | 32.80 | 827.50
tcp.hp.b1 | 0.25 | 4.2 | MoGr | 72.05 | 125.94
tcs.hp1.b1 | 0.3 | 4.6 | Mo | 64.12 | 186.88
tcs.hp2.b1 | 0.3 | 16.7 | Mo | 855.10 | 368.74
tcr.h.wl.2.b1 | 0.1 | 17 | W | 2056.83 | 8840.68
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 16 | W | 2099.51 | 5012.40
Name | Length (m) | gap/2 (mm) | Material |  | 
tcp.h.b1 | 0.25 | 6.7 | MoGr | 517.98 | 755.84
tcp.v.b1 | 0.25 | 2.5 | MoGr | 519.09 | 756.98
tcs.h1.b1 | 0.3 | 3.8 | Mo | 117.58 | 789.74
tcs.v1.b1 | 0.3 | 2.5 | Mo | 421.47 | 587.39
tcs.h2.b1 | 0.3 | 5.1 | Mo | 214.69 | 759.20
tcs.v2.b1 | 0.3 | 3.0 | Mo | 32.80 | 827.50
tcp.hp.b1 | 0.25 | 4.2 | MoGr | 72.05 | 125.94
tcs.hp1.b1 | 0.3 | 4.6 | Mo | 64.12 | 186.88
tcs.hp2.b1 | 0.3 | 16.7 | Mo | 855.10 | 368.74
tcr.h.wl.2.b1 | 0.1 | 17 | W | 2056.83 | 8840.68
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 16 | W | 2099.51 | 5012.40
Collimation optics: v23
21
tcp: primary, tcs: secondary, tcr: synchrotron radiation, h: horizontal, v: vertical, , , . . Table courtesy of Giacomo Broggi.
Collimator parameters from the version 23 of the collimation layout optics. The current layout consists of 17 beam halo collimators - 3 primary, 6 secondary, and 8 tertiary units- and 24 synchrotron radiation (SR) collimators. Among these, the main contributors to the overall impedance are listed below.
20.05.2025 | FCC week 2025 | Dora Gibellieri
Due to small half-gaps and large beta functions, primary collimators contribute significantly to transverse RW impedance, with collimator tcp.v.b1 identified to be the most critical.
Collimators RW impedance

## Slide 22
Name | Length (m) | gap/2 (mm) | Material | (m) | (m)
tcp.h.b1 | 0.25 | 10.4 | MoGr | 911.81 | 34.32
tcp.v.b1 | 0.25 | 1.7 | MoGr | 188.47 | 532.53
tcs.h1.b1 | 0.3 | 5.0 | Mo | 185.29 | 35.39
tcs.h2.b1 | 0.3 | 5.0 | Mo | 183.71 | 102.12
tcs.v1.b1 | 0.3 | 1.6 | Mo | 50.78 | 278.68
tcs.v2.b1 | 0.3 | 1.6 | Mo | 24.68 | 262.12
tcp.hp.b1 | 0.25 | 18.4 | MoGr | 994.99 | 218.02
tcs.hp1.b1 | 0.3 | 5.5 | Mo | 74.63 | 285.37
tcs.hp2.b1 | 0.3 | 2.9 | Mo | 21.22 | 298.16
tcr.h.wl.2.b1 | 0.1 | 21.7 | Inermet180 | 3036.07 | 4953.05
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 16.96 | Inermet180 | 1851.88 | 5017.33
Name | Length (m) | gap/2 (mm) | Material |  | 
tcp.h.b1 | 0.25 | 10.4 | MoGr | 911.81 | 34.32
tcp.v.b1 | 0.25 | 1.7 | MoGr | 188.47 | 532.53
tcs.h1.b1 | 0.3 | 5.0 | Mo | 185.29 | 35.39
tcs.h2.b1 | 0.3 | 5.0 | Mo | 183.71 | 102.12
tcs.v1.b1 | 0.3 | 1.6 | Mo | 50.78 | 278.68
tcs.v2.b1 | 0.3 | 1.6 | Mo | 24.68 | 262.12
tcp.hp.b1 | 0.25 | 18.4 | MoGr | 994.99 | 218.02
tcs.hp1.b1 | 0.3 | 5.5 | Mo | 74.63 | 285.37
tcs.hp2.b1 | 0.3 | 2.9 | Mo | 21.22 | 298.16
tcr.h.wl.2.b1 | 0.1 | 21.7 | Inermet180 | 3036.07 | 4953.05
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 16.96 | Inermet180 | 1851.88 | 5017.33
Collimation optics: v24.4
Collimator parameters from version 24.4 of the collimation layout optics, which includes 17 beam halo collimators and 24 synchrotron radiation (SR) collimators. Particular attention is given to changes in the vertical primary collimator tcp.v.b1, which plays a critical role in the overall impedance of the collimation system.
tcp: primary, tcs: secondary, tcr: synchrotron radiation, h: horizontal, v: vertical, , , , . Table courtesy of Giacomo Broggi.
  Compared to v23 for tcp.v.b1, there was a decrease in the half-gap:
  2.5 mm  1.7 mm
  Decrease of :
  756.98 m  352.53 m
22
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
Notes: Inermet 180: Tungsten alloy

## Slide 23
Name | Length (m) | gap/2 (mm) | Material | (m) | (m)
tcp.h.b1 | 0.25 | 5.8 | MoGr | 511.92 | 54.50
tcp.v.b1 | 0.25 | 1.4 | MoGr | 12.16 | 432.13
tcs.h2.b1 | 0.3 | 6.5 | Mo | 513.94 | 182.99
tcs.v1.b1 | 0.3 | 2.2 | Mo | 219.74 | 620.70
tcs.h1.b1 | 0.3 | 6.2 | Mo | 467.70 | 309.59
tcp.hp.b1 | 0.25 | 12.5 | MoGr | 654.03 | 413.61
tcs.v2.b1 | 0.3 | 3.6 | Mo | 127.59 | 1575.71
tcs.hp1.b1 | 0.3 | 11.0 | Mo | 209.69 | 965.22
tcs.hp2.b1 | 0.3 | 8.3 | Mo | 118.34 | 390.65
tcr.h.wl.2.b1 | 0.1 | 20.4 | Inermet180 | 4253.95 | 5717.45
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 18.0 | Inermet180 | 3323.15 | 5366.42
Name | Length (m) | gap/2 (mm) | Material |  | 
tcp.h.b1 | 0.25 | 5.8 | MoGr | 511.92 | 54.50
tcp.v.b1 | 0.25 | 1.4 | MoGr | 12.16 | 432.13
tcs.h2.b1 | 0.3 | 6.5 | Mo | 513.94 | 182.99
tcs.v1.b1 | 0.3 | 2.2 | Mo | 219.74 | 620.70
tcs.h1.b1 | 0.3 | 6.2 | Mo | 467.70 | 309.59
tcp.hp.b1 | 0.25 | 12.5 | MoGr | 654.03 | 413.61
tcs.v2.b1 | 0.3 | 3.6 | Mo | 127.59 | 1575.71
tcs.hp1.b1 | 0.3 | 11.0 | Mo | 209.69 | 965.22
tcs.hp2.b1 | 0.3 | 8.3 | Mo | 118.34 | 390.65
tcr.h.wl.2.b1 | 0.1 | 20.4 | Inermet180 | 4253.95 | 5717.45
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 18.0 | Inermet180 | 3323.15 | 5366.42
Collimation optics: v25.2
Collimator parameters from version 25.2 of the collimation layout optics, which includes 17 beam halo collimators and 24 synchrotron radiation (SR) collimators. Importance to highlight the changes on the vertical primary collimator tcp.v.b1, which plays a critical role in the overall impedance of the collimation system.
  Compared to v23 for tcp.v.b1, there was a decrease in the half-gap:
  2.5 mm  1.4 mm
  Decrease of :
  756.98 m  325.49 m
23
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
tcp: primary, tcs: secondary, tcr: synchrotron radiation, h: horizontal, v: vertical, , , , . Table courtesy of Giacomo Broggi.
Notes: Inermet 180: Tungsten alloy

## Slide 24
Comparison between different optics
To highlight the impact of the new collimation optics, the RW impedance of the vertical collimator tcp.v.b1 under different optics is compared with that of the circular copper pipe, with 30 mm radius and 150 nm NEG coating. The plot presents the imaginary part of the vertical dipolar impedance.
  Decrease in half-gap
  for tcp.v.b1:
  2.5 mm  1.7 mm  1.4 mm
24
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
Notes: Inermet 180: Tungsten alloy

## Slide 25
Comparison between different optics
Imaginary part of the vertical transverse dipolar impedance: total RW contribution from all collimators, comparing optics versions 23, 24.4, and 25.2, along with the RW impedance of the beam pipe (considering a circular copper pipe with 30 mm radius and 150 nm NEG coating).
25
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
  Collimator RW impedance exceeds beam pipe RW in v24.4 and v25.2
Notes: Inermet 180: Tungsten alloy

## Slide 26
Comparison between different optics
Estimation of impedance considering the RW contributions from the beam pipe and collimators, with an analysis of collimators based on different optics layouts.
26
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
V24.4
v23
V25.2
Already with v23, the beam operates close to the stability limit, requiring the combined action of an ideal bunch-by-bunch feedback system over 4-turns and positive chromaticity (see M. Migliorati: 2025_05_20_FCC-IS_week.pdf).

## Slide 27
Comparison between different optics
27
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
V24.4
v23
V25.2
Already with v23, the beam operates close to the stability limit, requiring the combined action of an ideal bunch-by-bunch feedback system over 4-turns and positive chromaticity (see M. Migliorati: 2025_05_20_FCC-IS_week.pdf).
Estimation of impedance considering the RW contributions from the beam pipe and collimators, with an analysis of collimators based on different optics layouts.

## Slide 28
Comparison between different optics
28
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
V24.4
v23
V25.2
Already with v23, the beam operates close to the stability limit, requiring the combined action of an ideal bunch-by-bunch feedback system over 4-turns and positive chromaticity (see M. Migliorati: 2025_05_20_FCC-IS_week.pdf).
Estimation of impedance considering the RW contributions from the beam pipe and collimators, with an analysis of collimators based on different optics layouts.

## Slide 29
Comparison between different optics
29
20.05.2025 | FCC week 2025 | Dora Gibellieri
Collimators RW impedance
V24.4
v23
V25.2
Already with v23, the beam operates close to the stability limit, requiring the combined action of an ideal bunch-by-bunch feedback system over 4-turns and positive chromaticity (see M. Migliorati: 2025_05_20_FCC-IS_week.pdf).
Estimation of impedance considering the RW contributions from the beam pipe and collimators, with an analysis of collimators based on different optics layouts.

## Slide 30
Introduction
  FCC-ee main parameters for Z configuration
  FCC-ee main ring impedance model
FCC-ee beam coupling impedance of the collimation system
  Collimators geometrical impedance
    Optimization strategies
  Collimators RW impedance
    Comparison between different optics
Conclusion and next steps
20.05.2025 | FCC week 2025 | Dora Gibellieri
Outline
Conclusion and next steps
30

## Slide 31
Simulations made on Xsuite
FCC-ee Impedance Model available on GitHub
Impedance budget space (common to booster and collider) on CERN gitlab
Calculations made on several computing clusters : LXPLUS (CERN), FEYNMAN (CEA), and with dedicated computing resources on Jean-Zay (IDRIS) and CC IN2P3
Dedicated chat spaces for the high energy booster and the collective effects studies on mattermost
Conclusion and next steps
Status updates: tools, models, and resources
31
20.05.2025 | FCC week 2025 | Dora Gibellieri

## Slide 32
Conclusion and next steps
Conclusion
32
20.05.2025 | FCC week 2025 | Dora Gibellieri
🔹 Impedance/Wake model development for critical design decisions:
  The extremely short bunch length makes impedance and wakefield simulations highly challenging.
  Ensured model flexibility to facilitate impedance and wakefield updates in optics, material choices, coating thickness, geometries, and new machine elements.
  Enabled impedance assessments of different scenarios.
🔹 Criticality of the collimation system:
  A step-by-step approach is being adopted to explore computational limits and propose optimized impedance solutions.
  Collimators geometrical impedance:
    Optimization strategy  taper optimization.
      Solutions developed in collaboration with the design and collimation groups to address spatial and mechanical constraints.
  Collimators RW impedance:
    Comparison between different optics layouts.
    Optimization strategy  optics designed to maximize the collimator aperture and favor materials with high electrical conductivity.

## Slide 33
Conclusion and next steps
Ongoing activities: example
33
20.05.2025 | FCC week 2025 | Dora Gibellieri
Features:
  9.4° taper (1:6 ratio) with circle-to-square transition
  Small flats at ±10 mm from jaws for BPMs
  Configured for 5 mm half-gap (adjustable)
Advantages:
  Simplified mechanical design: flexibility needed in only one direction
  More robust RF fingers
  Enhanced mechanical reliability
Status:
  Impedance evaluation in progress
  Taper length: 180 mm each side (excluding BPM)
  Lengths adjustable; taper is not a limiting factor unless angle < 2.5°
Proposed taper section design for collimators
Courtesy of Richard Jonathan Cowan

## Slide 34
Conclusion and next steps
Ongoing activities: example
34
20.05.2025 | FCC week 2025 | Dora Gibellieri
Jaw flat
10mm from jaw flat
Jaw end (30mm from jaw flat)
End of jaw
+ 60mm
+ 90mm
+ 210mm
Beam
Flexible element – 300mm radius blend
30mm from beam
Circle to square transition
BPM
Taper 1
Taper 2
The design allows the use of flexible elements in only 1 direction, offering improved conductance and more robust shielding around the edge of the jaw and simplifying mechanical design
Small flat for transition
Courtesy of Richard Jonathan Cowan
Proposed taper section design for collimators

## Slide 35
Conclusion and next steps
Acknowledgements
35
Project part of FCCIS – The Future Circular Collider Innovation Study. This INFRADEV Research and Innovation Action project receives funding from the European Union’s Horizon 2020 Framework Programme under grant agreement no. 951754.
20.05.2025 | FCC week 2025 | Dora Gibellieri
Many thanks to M. Boscolo, G. Broggi, R. Bruce, X. Buffat, C. Carli, L. Giacomel, G. Iadarola, T. Ishibashi, A. Lechner, E. Macchia, A. Perillo-Marcone, S. Marin, K. Oide, S. Redaelli, G. Rumolo, R. Seidenbinder, R. Soos, F. Zimmermann, and all FCC-ee/FCCIS colleagues for their valuable contributions and support.

## Slide 36
Thank you for your attention 
FCC week 2025 - 11th edition of the Future Circular Collider Conference , Vienna, Austria, 19 - 23 May 2025