## Slide 1: Studies towards a depolariser design
11th FCC Week 22.05.2025
presented by W. Hofle
CERN SY-RF-BR
Acknowledgements:
I. Karpov, D. Sittard, L. Thiele,
Epol WG

## Slide 2: Depolariser kickers and transverse feedback
Recapitulation
due to similar requirements for bandwidth synergy between the needed kickers for the transverse feedback and the depolariser have been explored
long, O(m), stripline kickers operating at a multiple of the bunch repetition frequency offer good RF power efficiency and sufficient bandwidth
differences in requirements between transverse feedback and depolarizer kickers are
  depolarizer kicker only needed for vertical kicks, transverse feedback also for horizontal plane kicks
  implementation of depolariser excitation as a modulated local orbit bump requires one or several sets of pairs of kickers with bending magnets in between
    no perturbation on experimental points permitted, recommended to have a tuning possibility with a third kicker per set of kickers
  kick strength required for depolarizer is high (10 mrad) and adequate protection is needed to prevent acting on Physics bunches (loss of synchronisation with gaps)
Wolfgang Hofle
11th FCC Week 22.05.2025

## Slide 3: Filling pattern Z-pole – update of 2024
e-cal bunches of at least one gap are affected by injection bump risetime, so effectively 175 (one beam), 176 (the other beam) useful bunches at maximum
Wolfgang Hofle
11th FCC Week 22.05.2025
H. Bartosik, FCC week 2024
(new alternate filling schemes with short trains (e-cloud mitigation of 5 ns spaced bunches need study)

## Slide 4: Considerations for placement in ring
arcs adjacent to technical sites PL, PB, PF, PH now preferred
  see K. Oide FCC week 2025 for proposal for integration of kickers in GHC optics
  assume similar possibilities in LCC optics exist, but needs check, LCC optis has somewhat lower beta functions  impacts efficiency at least for transverse feedback part
experimental sites (PA, PG, PD, PJ)
  spaces that were considered:
    return arc (optics not really suited)
    regular arc, out-going beam, still a possibility
PB:collider
transverse feedback kickers & depolarizer (1)
booster
transverse feedback kickers
Wolfgang Hofle
Update 2025:
PH: collider
transverse feedback kickers & depolarizer (3)
PL: collider
transverse feedback kickers & depolarizer (4)
PF: collider
transverse feedback kickers & depolarizer (2)
11th FCC Week 22.05.2025

## Slide 5: Placement in regular arc under study
positron beam outgoing (clockwise) / right of Ips, see also K. Oide FCC week 2025
Following proposal by I. Koop, update see K. Oide, FCC week 2025
Wolfgang Hofle
split system over eight locations, left and right of four points, four per beam
chose kickers of lengths of 1 m
 at least 8 kickers per beam for four full wave bumps per beam
+ a third kicker to ensure bump closure (another 4 kickers per beam)
24 kickers in total
Kicker 1
Kicker 2
Kicker 3
optional kicker 3 to ensure full wave bump is closed
https://indico.cern.ch/event/1471324/contributions/6220925/attachments/2963259/5212471/Koop-depolarizer%20review.pdf
If split as proposed over four locations, angle is 2.5e-6 and position peak also factor 4 smaller  more realistic
11th FCC Week 22.05.2025

## Slide 6: Depolariser and distributed transverse feedback
distrubuted system with four-fold symmetry
kickers and pick-ups installed at on out-going beam at start of arc
points “Q,R,S,T” can be either experimental points or technical points
  arcs adjacent to technical sites now preferred !
three kickers per point and beam (12 per beam, 24 total)
  two strong kickers (also main depolarizer bump kickers)
  one shorter kicker (polarizer bump correction)
    can have a higher frequency reach (100 MHz)
four pick-ups per point and beam (16 per beam, 32 total)
  spacial sampling, i.e. betatron phase advance between pick-ups 60-120 degrees, covering one period of betatron oscillation
  pick-ups down stream of kickers (immediate monitoring of system malfunction, machine protection! )
low latency data links connecting the four processing nodes per beam
  simulations needed to determine what processing will provide additional damping to the low order coupled bunch modes using these links
processing
processing
processing
processing
kickers(2+1)
pick-ups (4x)
11th FCC Week 22.05.2025

## Slide 7: Stripline kicker: arc compatible version (1st version)
Characteristics (good for transverse feedback, but too low shunt impedance for depolariser with arc compatible diameter)
four electrodes arranged at 45 degrees
leaves horizontal plane free for synchrotron radiation absorbers similar as for BPM designs
compatible with vacuum chamber diameters of 60-70 mm foreseen for arcs (initial proposal)
small diameter also desirable for increased shunt impedance, but matching to 50 Ohm must be considered for both differential mode and common mode
universal design that can be powered to provide vertical or horizontal kicks, even simultaneously, power can be directed to plane that needs high level kicks
device is a backward coupler, powered at beam downstream ports and terminated at upstream ports
action on beam provided in equal parts from magnetic and electric fields
length can be adjusted to match actual needs for bandwidth
total kick strength provided by set of kickers, placed at the appropriate phase advance / optics as needed
Wolfgang Hofle
D. Sittard (CST)
RF power
RF power
RF loads
RF loads
up to 1m long
11th FCC Week 22.05.2025

## Slide 8: Stripline kicker: field plots (70 mm chamber)
Electric field (vertical)
Magnetic field field (horizontal)
Wolfgang Hofle
D. Sittard
vertical kick evenly split between electric and magnetic fields
optimization is planned to start this year (beam impedance, details of the design compatible with short bunch length … )
11th FCC Week 22.05.2025

## Slide 9: Shunt impedance kicker (four electrode version)
 power need reduced by factor 15.6
70 mm vacuum chamber diameter (directly arc compatible)
Adaptation of length to bandwidth also possible (using 1 m long kickers for 40 MHz +/- 20 MHz)
26 mm vacuum chamber ( 18 mm between electrodes)
40 MHz
80 MHz
160 MHz
D. Sittard
Wolfgang Hofle
@40 MHz, 700 kW
4x4x 2.26 kW
4x4x 35 kW
integrated transverse kick 450 kV needed (split voltage over four kickers):
looks feasible, 1 m length
beam impedance check with BE-ABP ongoing, tapers (minimize broadband impedance!)
minimum bunch length ?!
total length per beam for kickers ~10 m (+ overhead tapers)
3 m per location per beam (if split over four points per beam)
4 kickers
4 electrodes
RF power
for 10 mrad @ 45.6 GeV
11th FCC Week 22.05.2025

## Slide 10: Stripline kicker: field plots (26 mm chamber)
Electric field (vertical)
Magnetic field field (horizontal)
Wolfgang Hofle
D. Sittard
vertical kick evenly split between electric and magnetic fields
18 mm diameter stay clear aperture, tight tapers needed for impedance  possibly adds to installation length !
18 mm
11th FCC Week 22.05.2025

## Slide 11: Kick voltage and kick angle summary
10 mrad at 45 GeV  450 keV/c transverse momentum kick needed for the depolariser function, several kickers needed to implement this modulated closed bump
stripline kickers offer a viable solution
split over four locations per beam
  use sets of 1 m long kickers (RF matched to 50 W) with four electrodes for each location to create local modulated bump (2x4x2.26 kW = 18 kW RF power per bump)
  four such systems per beam
  24 kickers in total for both beams combined
    for 16 main kickers: 144 kW RF power
    for 8 adjustment kickers: 36 kW RF power
    bandwidth for adjustment kicker can be higher
Wolfgang Hofle
11th FCC Week 22.05.2025
Kicker lengths and powers (table is for one of four locations)

## Slide 12: Next crucial steps – my view
optimization of kickers with respect to having high power efficiency (shunt impedance) in operating band and acceptable beam impedance overall
  optimization of electrode design, possible consideration of advantages of higher line impedance kicker
  decision on minimum bunch length for design specification
simulations with new tools available to confirm kick strength is sufficient for depolarisation as needed, see G. Iadaorola FCC week 2025 (Xsuite)
move to prototyping depolariser kicker once a solid electromagnetic design is established (prototyping not before 2026), clarify where a prototype could be tested
converging on exact installation location and optics including the space needed with tapers
follow-up on machine protection considerations
Wolfgang Hofle
11th FCC Week 22.05.2025

## Slide 13: Thank you for your attention.
13
Wolfgang Hofle
11th FCC Week 22.05.2025

## Slide 14: Spare
11th FCC Week 22.05.2025

## Slide 15: FCCee collider and booster transverse feedback
Key requirements
need bunch-by-bunch operation at 25 ns bunch spacing  defines bandwidth
can operate at multiple of bunch repetition frequency (short bunches)  no need to work in “base-band” as in LHC  helps as it reduces relative bandwidth
sets of RF matched strip-lines with carefully chosen length as kickers seem obvious choice
Booster:
  request to also operate to damp a significant transverse injection error  defines maximum kick requirements
    needs estimate of injection errors, filamentation time, … to define system
  moderate damping times only for instabilities (not beyond experience from LHC)
  single location in ring sufficient, but also resonant depolarizer function if polarized beams are injected
Collider:
  need to damp very fast transverse instabilities  four turns risetime, high gain system
    favors distributed system with multiple pick-ups and kickers
    possibility of synergy with exciter for resonant depolarization (as in LEP)
Wolfgang Hofle
11th FCC Week 22.05.2025

## Slide 16: Recapitulation TFB for FCC-ee
FCC-ee requires a coupled bunch transverse feedback system
fast rise times of the instability of 4 turns caused by the resistive wall impedance are predicted for the lowest order coupled bunch modes, see M. Miglorati (FCC week 2025)
requires shortest possible latency (1-2 turns), short latency ensures transverse FB disentabled from orbit FB
  use several pick-ups for “spacial sampling”, see D. Teytelman (FCC week 2024)
  notch filter for closed orbit supression
  distributed kicker system for possibly feeding back low frequency mode with less than 1 turn delay, see A. Drago (FCC week 2018)
lowest betatron frequency can be as low as 500 Hz for a tune fractional tune of 0.15
  the feedback system should cover all unstable modes, i. e. frequencies up to half the bunch repetition frequency  20 MHz bandwidth for baseline 25 ns bunch spacing
  when introducing shorter bunch spacings (5 ns) at least a few feedback kickers are needed to cover frequencies up to 100 MHz, the mixed scheme proposed for electron cloud mitigation needs further scrutiny on how the bunches oscillate, and simulations with realistic feedback
11th FCC Week 22.05.2025

## Slide 17: Machine Protection considerations (03.10.24)
What can go wrong?
excitations not correctly synchronized
excitation amplitudes not correct leading to not closed depolarizing bumps
any of the other excitations that will certainly be used (AC dipole mode etc.) need to be protected against failures
very strong kicks possible comparable or even larger than at LHC injection
protection with BLMs of limited or of no use due to small beam size, absence of significant halo
monitoring of positions at appropriate distance from kickers at specific phase advance
global monitoring of beam position required turn-by-turn, independent of pick-ups used for TFB
interlocks need to be derived from this monitoring
  use also down strip TFB pick-ups for monitoring
beam stoppers?
Mitigation
Wolfgang Hofle
machine protection task force working group requested examination of failure scenarios and mitigations
from MP point of view not clear if entangling TFB and depolarizer system into one system is the optimum due to the different kick strength required for both systems and the possible failure scenario
  possibility to have common kickers, with combination of signals before kicker (pulsed system for de-polarizer, cw system for feedback function)
11th FCC Week 22.05.2025

## Slide 18
LHC ADT kicker (LHC transverse feedback)
  high impedance tetrode amplifiers
  kicks with electric field only
  6 m effective length split over 4 kickers twice as strong as depolarizer kicker system (2 mrad at 450 GeV/c)
  full amplitude not as bunch selective as needed for FCCee
  due to resonances not (readily?) suitable for short electron bunches
W. Hofle et al. PAC 2001
Wolfgang Hofle
11th FCC Week 22.05.2025