## Slide 1: Numerical tools for beam-beam studies
Peter Kicsiny, G. Broggi, X. Buffat, V. Gawas, G. Iadarola, S. Kostoglou, K. Oide, T. Pieloni, J. Salvesen, K. Skoufairs, R. Soos, L. van Riesen-Haupt
for the beam-beam working group, with special thanks to:
H. Burkhardt, C. Carli, F. Carlier, M. Hofer, D. Schulte, M. Seidel, D. Shatilov, D. Zhou
FCC Week
20 May 2025
Work supported by the Swiss Accelerator Research and Technology (CHART)

## Slide 2
Overview
  FCC-ee will be a highly complex machine
  Interplay of various effects
  Presence of beam-beam collisions further complicates beam dynamics
  Self-consistent simulations are challenging
beam-beam
errors &
misalignments
electron cloud
impedances
collimation
radiation
lattice nonlinearities
Notes: The fcc will be a highly complex machine where the beam dynamics will be shaped by the interplay of different mechanisms. The presence of beambeam collisions makes the dynamics even more complicated as they interplay with all these other components of the machine. Because of this complex dynamics the self consistent simulation of the machine is very challenging but crucial for the success of the design study.

## Slide 3
 | Weak-strong 6D | Quasi-strong-strong 6D | Strong-strong 6D |  | Beamstrahlung | Bhabha-scattering | Transverse wakefields | Longitudinal wakefields | Linear tracking | Nonlinear tracking | Open source | 
GUINEA-PIG [1] |  |  |  |  |  |  |  |  |  |  |  | 
COMBI [2] |  |  |  |  |  |  |  |  |  |  |  | 
BBWS [3] |  |  |  |  |  |  |  |  |  |  |  | 
BBSS [4] |  |  |  |  |  |  |  |  |  |  |  | 
SCTR [5] |  |  |  |  |  |  |  |  |  |  |  | 
IBB [6] |  |  |  |  |  |  |  |  |  |  |  | 
LIFETRAC [7] |  |  |  |  |  |  |  |  |  |  |  | 
BeamBeam3D [8] |  |  |  |  |  |  |  |  |  |  |  | 
Xsuite [9] |  |  |  |  |  |  |  |  |  |  |  | 
Available
Not available
Tools
Different beam-beam codes exist, with different features
FCC-ee: self-consistent & fast modeling needed including many effects
Xsuite: development driven by needs for FCC-ee
Weak-strong 6D
Quasi-strong-strong 6D
Strong-strong 6D PIC
Beamstrahlung
Bhabha-scattering
Transverse wakefields
Longitudinal wakefields
Linear tracking
Lattice tracking
Open source
Runs on GPU
Strong-strong 6D SG
G. Iadarola talk @ this conference
3
Notes: There exist several numerical tools to model the fccee beam-beam effects that are collected in this table. The columns show the various features that are important for the FCC-ee. You can see that each of them has different features but none is able to tick all the boxes. Therefore for many of these studies we are using xsuite, general purpose beam dynamics simulation tool, developed at CERN, that is developed by taking into account the simulation needs of the FCC-ee. We have a dedicated beam-beam working group working on various aspects of beam-beam effects.

## Slide 4: Transition to Xsuite
Phase out legacy codes
Integrate their features into Xsuite
Thorough benchmark of features
Xsuite advantages:
  Self contained
  Maintenance & user support
  Growing community
  Python based
Xwakes
Xsuite PIC
COMBI, SixTrack [1], GUINEA-PIG, PyHEADTAIL [2]
R. Soos
Notes: The idea is to gradually phase out legacy tools by integrating their features into Xsuite. This integration has to be followed by a thorough benchmark of these features. For example on the top right there is a plot showing the number of emitted beamstrahlung photons from a single collision with xsuite PIC solver and other already existing models. The advantages here are that xsuite is manitained and has a growing user base and user support, whereas the other tools are not supported anymore, and it is python based so the learning curve is short for newcomers.

## Slide 5: Studies made possible by Xsuite beam-beam [1]
Lattice optimization
Luminosity and beam lifetime [2]
Footprint & FMA
Lattice interplay with beam-beam (e.g. emittance) [1]
Dynamic aperture (DA) / momentum acceptance (MA) [3]
Errors & corrections
Top-up injection [4]
Collective effects and instabilities
3D flip-flop [5, 6]
Incoherent and coherent X-Z instability [6, 7]
Collimation and MDI
Loss maps
Detector background
IP tuning & feedback
G. Broggi, talk @ this conference
J. Salvesen talk & V. Gawas poster @ this conference
Notes: The implementation of the beambeam model in xsuite has made possible several beam dynamics studies. For example we are able use Xsuite for lattice optimization, study the interplay of lattice with beambeam to see for example equilibrium emittances, study DA MA, errors and corrections and study top up injection. In terms of collective effects we have already used Xsuite to study the 3d flipflop and the incoherent and coherent instabilities.
Other teams such as collimation and MDI are also using xsuite beambeam to study loss maps, detector background and IP tuning and feedback.

## Slide 6: Standardizing performance evaluation: DA/MA
L. van Riesen-Haupt
A. Piveteau
Notes: One important line of work right now is to standardize the performance evaluation of the FCC-ee. One example is the calculation of DA/ MA for which several methods exist.
We can do it by fitting the largest ellipse into the DA, we can create joint DA + MA plots from 4 phases + delta offset or we can do a more granular angular sampling of the phase space and calculate DA from that.

## Slide 7: Standardizing performance evaluation: correlations
Main FCC-ee metrics: luminosity and lifetime
Lattice optimization to be done including beam-beam
Ongoing studies with errors & corrections
  Need standardized way to do DA, MA, FMA
Idea: exploit correlations between various metrics could speed up optimization process
  E.g. lifetime vs DA studies
Z
L. van Riesen-Haupt talk @ this conference
Notes: The main metrics of the FCC-ee are luminosity and beam lifetime. The lattice optimization has to be performed including beambeam otherwise the optimization is not indicative of the final collider performance. We have ongoing studies related to adding errors and corrections to the FCC-ee lattice with beambeam and estimating DA, MA, lifetime and footprint.
On the plot on the right there is an example study with the Z lattice where we introduced vertical sextupole misalignments and scanned their magnitude and simulated lifetime, luminosity and DA. Some simulations such as DA take shorter than for example lifetime simulations so here we are trying to find correlations between these different metrics to reduce simulation needs. For example a better lifetime is generally correlated with a better DA and so on.
add to table collimation time with bb
e.g. SAD and MAD-X still used for DA/MA

## Slide 8: Standardizing performance evaluation: Footprint & FMA
Different libraries (harpy, nafflib)
  Same thing, difference in maintenance
Ongoing work on built-in tool to compute footprint + FMA
  Linear/nonlinear lattice
  Compute diffusion
  Noise or different filters
  GPU support
best seed
worst seed
ttbar
Notes: Another example is FMA and tune footprint computation. There are different libraries like harpy and nafflib, these are python libraries, to interpolate and find a peak on a fourier spectrum. They all do the same thing, the difference is in their maintenance. Currently we are trying to build a tool in Xsuite to compute footprint and FMA for linear and nonlinear lattice models, compute diffusion coefficient, with the ability to add noise or different filters, and preferably GPU support.
An example usecase of the footprint and fma for fccee is shown on the right where we scan quadrupole misalignments and for each setup we obtain the equilibrium luminosity with a number of random seeds. Then there will be a variation in the final lumi depending on the seed and we can investigate the reason of difference between the best and worst seed by for example looking at the footprint and finding resonance lines. Such as in this case the quadrupolar resonance line seeems to attract many particles in case of the worst seed.
where are the limits
current tool in xsuite is slow 1 core doesn’t do diffusion
option to use different filters, interpolation nafflib to this builtin tool
noise
make them work for gpu
- need to split into chunks CPU
- submission script and tricks are specific to each cluster
- these are not builtin in xsuite
- we can standardize them with xutil

## Slide 9: Standardizing performance evaluation
Simulation | Number of Particles | Number of Turns | Model | Typical timescale
Optics | ~1 | ~few | full lattice + WS BB | sec
Emittance – Matrix | ~1 | ~few | linear map + WS BB | sec
Coarse Dynamic Aperture | ~100 | ~𝜏SR (50-5000) | full lattice + WS BB | min
Emittance – Tracking | ~1k | ~𝜏SR (50-5000) | full lattice + WS BB | min
Fine DA / MA | ~10k | ~𝜏SR (50-5000) | full lattice + WS BB | min
Luminosity | ~10k | ~𝜏SR (50-5000) | linear map / full lattice + WS BB | hour
Collective effects | ~1M | ~𝜏SR (50-5000) | linear map + SS BB | week
Footprint + FMA | ~10k-1M | ~1-10k | linear map / full lattice + WS BB | hour
Lifetime | ~100k | ~20k | full lattice + WS BB | day
Notes: Here im showing a table of the most common beambeam studies we are doing for the fccee. The columns show a rough estimate of the typical number of particles and turns needed and the lattice and beambeam model used. The last column shows the order of time each simulation takes.
collective effects are:
vertical mode coupling instab
x-z instab
strong-strong bb, linear map
1M particles
few damping times tracking
HTCOndor 16 cores CPU ~1week for Z
GPU not yet used
Collective effect studies are done less often so I can accept long sim time without GPU. The things we do often should be made fast like lifetime, emittance.
full lattice + ss we dont do
at some poont we need some banchmarks but this has to be on gpu, future work
we have capability but its not the priority study, like PIC
PIC is difficult for Z
put single CPU time
more CPU
in xsuite twiss params are taken out of tracking, i track two closed parameters, is simplecticity violated? no
madx and sad computes matrixes diagonlizing them and finding optics from that
iscollective is now fixed we dotn need it for Ws but we need
add pic tune scan with CW dist no gaussian, pic needed to verify it doesnt have a big impact, do not often do but still needed as check

## Slide 10: Standardizing performance evaluation
Simulation | Number of Particles | Number of Turns | Model | Typical timescale
Optics | ~1 | ~few | full lattice + WS BB | sec
Emittance – Matrix | ~1 | ~few | linear map + WS BB | sec
Coarse Dynamic Aperture | ~100 | ~𝜏SR (50-5000) | full lattice + WS BB | min
Emittance – Tracking | ~1k | ~𝜏SR (50-5000) | full lattice + WS BB | min
Fine DA / MA | ~10k | ~𝜏SR (50-5000) | full lattice + WS BB | min
Luminosity | ~10k | ~𝜏SR (50-5000) | linear map / full lattice + WS BB | hour
Collective effects | ~1M | ~𝜏SR (50-5000) | linear map + SS BB | week
Footprint + FMA | ~10k-1M | ~1-10k | linear map / full lattice + WS BB | hour
Lifetime | ~100k | ~20k | full lattice + WS BB | day
Currently for most studies weak-strong beam-beam is used
For longer studies (lifetime) GPUs are necessary but currently not exploited
For most studies GPUs are not necessary but would boost productivity
Studies which have to be performed often (lifetime, lumi, emittance) should exploit GPU power
Notes: The main takeaway here is that for most studies the weakstrong beambeam is used. There are longer studies such as beam lifetime where we have to track many particles for many turns to get good statistics, and shorter studies such as DA or luminosity. For the longer studies GPUs are necessary to obtain results in reasonable timeframe. At the moment GPUs are currently not exploited by the community. Studies which have to be performed often should make use exploit the GPU power.
be more positive gpus are necessary
spc cluster at cern

## Slide 11: Exploiting hardware infrastructure
INFN Bologna & CERN slurm cluster (slurm)
~800 CPU cores
4 GPUs
Designed for many-core CPU jobs (MPI, OpenMP)
No priority system (first come first served)
CERN cluster (HTCondor)
~105 CPU cores
~100 (modern) GPUs
Group priority system
Xsuite GPU capabilities ready, but unexploited by community
Other resources
CERN slurm cluster (hpcbatch)
CEA cluster in France
Xboinc: volunteer computing
CSCS: Swiss National Supercomputing Centre
Notes: We are running most of our beambeam simulations on the CERN cluster which is shared with other CERN groups so the access to a sufficient amount of resources is not always guaranteed. The cluster has around 100 state of the art GPUs which can already be exploited with xsuite as the capability is there but currently it is not exploited by the community.
In addition we have access to a slurm cluster in Bologna by INFN that is best designed for many CPU jobs with openmp and mpi. These are the 2 most commonly used hardware resources but there are plans to use or gain access to other clusters such as one by CEA in France or one in Ticino in Switzerland. There are also considering to revive a volunteer computing type of model, used for the LHC in the past, with Xsuite called Xboinc.
Different commands and setup scripts are needed for each. We need to have out of the box examples and submission scripts.
xboinc, refresh for collimation, little work needed to upgrade, ml to optimize, case study on lhc DA with surroagate models
storage of simulation data, big parameter scans
120k volunteers previously
with python compilation benchmark on different platforms not easy
exploring optimization algorithms and new cscs potential future
cea booster guys questionnaire
criann adnan optics meeting 195
smart algorithm to reduce number of simulations needed
80 nodes on sbatch add sbatch but reasont that only if i use full cluster i have equivalent of the GPU so with 100 gpus we get more
more power available with GPUs

## Slide 12: Current priorities
SAD-like solenoid (coordinates transformed depending on orbit) for polarization studies
Standardized lattice knobs for IP tuning & correction
Pair production for IP feedback & tuning
Better structuring of most common simulations with Xutil [1]: example scripts, tutorials
J. Keintzel, S. Jagabathuni, L. van Riesen-Haupt talk @ this conference
Y. Wu, J. Salvesen talk @ this conference
V. Gawas poster @ this conference
V. Gawas
J. Salvesen
K. Skoufaris talk @ this conference
Notes: There is an overview of the current development priorities for fcc-ee studies in xsuite.
One item is multiturn tracking with the detector solenoid in Xsuite. A solenoid element has been developed and has been benchmarked for superkekb. Here on the right you see the matched optics of the superkekb LER with sad and xsuite, in the solenoid region. The solenoid is important for beam dynamics and polarization studies. More on polarization you can find in Yi’s talk and more on the solenoid and superkekb benchmarks you can find out from Jack’s talk on Thursday.
Another line of work is the development of standardized lattice knobs for ip tuning and feedback. More details on the status you can find out from the talks of Jacqueline, Satya and Leon later today. There will also be a poster on using machine learning for IP feedback with luminosity, beamstrahlung and pair production signals from Vaibhavi.
Now that many of the tools are ready to use, we also want to organize our simulations in a more systematic way by standardizing the most common simulations such as lifetime, DA, emittance into example scripts and tutorials and we are developing a new package called Xutil which aims to contain these standardized scripts.
radiation from solenoid no right vector potential
synrad integrals are there, there was an update,
standardized tuning tools
xsuite multisetter does not give correct results: add shift in all elements, faster, not correct
shift misalignments work in regular way including solenoid
add shifts madx translate into xsuite. madx works. reproduce same error in different lattices.
corrections are done in mad. people have scripts.
no xsuite to sad error translation. need script but doable
xsuite had nothing until last year.
ground wave orbit feedback needs twiss every 2 ms. static ones dont care make lattice once.
feature 606 I1 to I5. damping times partition numbers characterize the lattice.
ws ss pic which is good for which studies, who needs what.
mdi might do pic
ss for luminosity.
not enough gpus.
utilization of multi cpu on gpu.
pair prod in pic
computing time in pic
conversion to cpu array if on gpu
track core it diffuses into halo then throw away core
expensive
they are interested in halo only
but bb for diffusion need core ask giacomo how they do it
ws easy dont need the core of weak beam
lifetime with 96 cores takes 1 h; 2400 particles, Z 50000 turns; due to dist we need many turns; 25k turns;
- 1h / 50000 = 0.072 s per turn - -> 0.21 s per turn on 32 cores
xsuite 32 cores 2e3 macroparts takes 1s per turn,
DA: shorter, Z 4000 turns, tt 40 turns 400 particles, 1 min for Z, 96 core.
in lhc nonlinearity is small so simplified lattice works but not in fcc bc of many nonlinearities
reweighting uniform dist doesnt work bc we have damping so particles move from tail to core
in tools be precise how to set up lattice how to init the beam etc
plot showing gpu usage last year
pyat and madx have correction schemes
directly linked to the tools not mentioned:
add gpus, pic, using the platform like htcondor in an efficient way-> xutil adjust last sentence

## Slide 13: Summary
Xsuite: main tool for self consistent FCC-ee beam dynamics studies
Most studies use weak-strong beam-beam model
Longer studies (lifetime) could be replaced by shorter studies (DA)
Standard setup and submission scripts, DA/MA, FMA evaluation tools are being developed
GPUs are needed but currently under utilized for FCC-ee studies
Thank you!
Notes: I have come to the summary. Over the past few years Xsuite has become the main tool for self consistent FCC-ee beam dynamics studies, and it already replaces several older legacy tools. Most beam dynamics studies use the weak strong beambeam model. There are some studies which take days and these could potentially be replaced by shorter studies which take in the order of hours if we find correlations between the observables. We are working on standardizing common simulations with cluster submission scripts, python files etc. and working on standardized evaluation tools for DA MA and FMA. In terms of computing infrastructure, our team runs most jobs on CPUs but the simulations would largely be accelerated by having a sufficient amount of GPUs which would save a lot of time and allow for more studies to be performed. The challenge here is that the submission script and tricks are specific to each cluster and these are not builtin in xsuite but we can standardize them with xutil.

## Slide 14: References slice 3
  [1] D. Schulte, GUINEA-PIG https://cds.cern.ch/record/331845/files/shulte.pdf
  [2] T. Pieloni, W. Herr, COMBI https://accelconf.web.cern.ch/p05/PAPERS/TPAT078.PDF
  [3] K. Ohmi, BBWS https://indico.cern.ch/event/438918/contributions/1085290
  [4] K. Ohmi, BBSS https://oraweb.cern.ch/pls/hhh/code_website.disp_code?code_name=BBSS
  [5] K. Ohmi, SCTR https://indico.cern.ch/event/1398060/contributions/5876155
  [6] Y. Zhang, IBB https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.23.104402
  [7] D. Shatilov, LIFETRAC http://cds.cern.ch/record/1120233/files/p65.pdf
  [8] J. Qiang, BeamBeam3D https://amac.lbl.gov/~jiqiang/BeamBeam3D/
  [9] G. Iadarola et al., Xsuite https://doi.org/10.18429/JACoW-HB2023-TUA2I1

## Slide 15: References slide 4
  [1] SixTrack https://sixtrack.web.cern.ch/
  [2] PyHEADTAIL https://github.com/PyCOMPLETE/PyHEADTAIL

## Slide 16: References slide 5
  [1] P. Kicsiny, PhD thesis https://infoscience.epfl.ch/entities/publication/9f194f9b-76e8-4ba8-ab62-b19b17597ccc
  [2] P. Kicsiny et al., Multiturn simulation of radiative Bhabha scattering in the equivalent photon approximation Phys. Rev. Accel and Beams https://doi.org/10.1103/PhysRevAccelBeams.27.091001
  [3] L. van Riesen-Haupt, Impact of lattice errors and correction with beam-beam
  eeFACT 2025 https://indico.jacow.org/event/75/contributions/6860/
  [4] P. Kicsiny et al., Impact of beam asymmetries at the Future Circular Collider 𝑒+𝑒−
  Phys. Rev. Accel and Beams https://doi.org/10.1103/PhysRevAccelBeams.27.121001
  [5] K. Le Nguyen Nguyen et al., Impact of bunch intensity asymmetry in colliders featuring strong beamstrahlung https://arxiv.org/abs/2404.09012
  [6] P. Kicsiny et al., Incoherent horizontal emittance growth due to the interplay of beam-beam interaction and longitudinal wakefield in crab-waist colliders
  Accepted in Phys. Rev. Accel and Beams https://arxiv.org/abs/2501.04609
  [7] R. Soos, Impedance and beam-beam effects for FCC-ee
  eeFACT 2025 https://indico.jacow.org/event/75/contributions/6848/

## Slide 17: References slide 12
  [1] K. Skoufaris, Xsuite utility toolkit (Xutil) https://indico.cern.ch/event/1545057/contributions/6503334

## Slide 18: backup

## Slide 19
best seed
worst seed
Notes: where are the limits
current tool in xsuite is slow 1 core doesn’t do diffusion
option to use different filters, interpolation nafflib to this builtin tool
noise
make them work for gpu

## Slide 20
Beam-beam force
Consolidation...
Radiation (synchrotron radiation, beamstrahlung, Bhabha)
IP tuning & feedback
Beam asymmetries
Top-up injection
linear model
w/o radiation
High lumi strong beam-beam force
Notes: optmizations of the machine for high luminosity have already done for baseline design. but high lumi implies a strong bb force which can be characterized by the xi. but we want to consolidate these estimates eg lumi lifetimes with more detailed models using simulatons of radiation ip tuning topup and beam symm so these are the studies that i will highlight in this preso.
during beambeam collisions the beams experience the EM field of each other. This perturbation leads to a change in the optical beta function, called beta beating and causes an amplitude dependent tune shift. The consequnece of this is that the beam will have a lartge tune footprint which potentially crosses many resonance lines which can be dangeorus for the beam stability. the beambeam force that the particles experience from each other at collisions is highly nonlinear. For small amplitudes this beambeam force can be characterized by this parameter xi, shown in the top right plot, which can be expressed in terms of the beam parameters.
For the machine design a small value for xi is crucial, but at the same time luminosity has to be maximized. This is challenging as you can see the luminosity can be expressed as a function of the xi, so on one hand we minimize xi but also want to keep L at maximum.

## Slide 21: Dynamic aperture with beam-beam

## Slide 22: Vertical emittance
full lattice
w/ beam-beam +beamstrahlung
Xsuite tracking
Reference data by K. Oide
error bars: stat. of last 2500 turns
Independent benchmarks with SAD & Xsuite
Good agreement

## Slide 23
Tolerances to parameter asymmetries
fixed bunch: init. with nominal parameter u0
perturbed bunch: init. with u=ζu0 & scan ζ
Track with linear transfer map until equilibrium
Tolerance: 50% blowup in σy w.r.t. ζ=1 case
50% blowup

## Slide 24
  Lorentz transform into head-on frame
  Longitudinal slicing
  Beam-beam kick in soft-Gaussian approximation [4]
Beam-beam in Xsuite
Notes: 1 min
In Xsuite we model the collision of two bunches at a time. We have a collision with a crossing angle and first we perform a lorentz boost and a rotation to move to a head-on frame where the description of the EM potential is easier.
Then we slice the bunches longitudinally and slide them across each other in discrete steps. At each step there will be a number of slices from bunch 1 overlapping with bunch 2. For these overlapping slices we compute the statistical moments and apply the beambeam kick on the particles of the opposite slice.
This beambeam kick is computed using the so called soft Gaussian approximation, which assumes a Gaussian transverse beam profile. This is a fast and accurate way of getting the force but it is valid only for Gaussian bunches. You can see the formula for the soft-gaussian kick. In red you see that it uses the statistical moments of the opposite slice. In blue I denoted the coordinates of a single particle that interacts with hte slice. The w is the complex error function.

## Slide 25: Simplified tracking simulations with Xsuite
repeat
  First studies with 2 IP baseline from CDR [5]
  Recent studies with 4 IP design from [6]
  Xsuite tracking setup:
    1 IP + tracking over arc superperiod with linear transfer matrix
    Arc split into 3 segments
    2 crab sextupoles between arc segments (βx=3 m, βy=500 m)
    Each iteration begins in front of the right sextupole
      Observation point for coordinates
    Synchrotron radiation (damping+noise) in arc, beamstrahlung+bhabha scattering in beam-beam element
IP + BS | lin. arc | sext. | lin. arc + SR | sext. | lin. arc
START
Notes: 1 min
Next I will explain our tracking setup in xsuite. In our first studies we used the baseline FCC setup which has 2 Ips, but in our newer studies we switched to the more recent 4IP design. In any case the tracking setup contains one 1 ip followed by a linear transfer map representing a half or a quarter ring, depending on the setup.
The arc is split into 3 segments and 2 sextupoles are inserted between the segments to implement the crab waist scheme.
Then each tracking iteration begins in front of the right sextupole and this point is chosen of observation of the beam coordinates.
The synchrotron radiation is implemented by an effective model of the damping and gaussian noise for quanctum excitation in the middle arc element and at the ip in the beambeam element we have the option to simulate beamstrahlung or bhabha scattering.

## Slide 26: Flip-flop
“weak bunch”
Nb-ΔN
“strong bunch”
Nb+ΔN
Flip-flop instability (1D) observed in other colliders (VEPP-2000) [7]
For FCC-ee: 3D flip-flop - direct consequence of beamstrahlung, triggered by an initial asymmetry in bunch intensity [8]
Inflation of one bunch beam loss
Above a threshold ξ0 longitudinal blowup drives transverse diffusion 3D flip-flop
Relevant for FCC-ee top-up injection
Slightly more populated bunch: Nb+ΔN
Undergoes less intense beamstrahlung
Bunch length decreases
Undergoes even less Beamstrahlung
Bunch length decreases even more
Slightly less populated bunch: Nb-ΔN
Undergoes more intense beamstrahlung
Bunch length increases
Undergoes even more Beamstrahlung
Bunch length increases even more
ξ < ξ
ξ < ξ
Notes: 2 min
The flipflop instability it the blowup of one bunch and the while the other bunch shrinks or remains unchanged. It has been observed in previous machines like veep where this effect is 1D caused by the nonlinear dynamics.
In the fcce flip flop has been observed in simulations and here it is a direct consequence of BS. It is triggered by an initial small asymmetry in the bunch intensities and this initial perturbation determines which of the bunches will blow up. The bunch intensity is directly related to the intensity of beamstrahlung.
So when we have a collision with a slight asymmetry in the charge. The bunch which experiences a stronger beambeam force from the other beam will undergo more beamstrahlung so its bunch length will increase while the bunch which undergoes a slightly less beamstrahlung than the equilibrium will experience a reduction of the bunch length.
Since we collide with a crossing angle, the beambeam force will depend on the bunch length. Therefore the now shorter bunch will exert an even stronger beambeam force on the other bunch so that will undergo an even stronger BS and the cycle repeats. This process eventually leads to the inflation of one bunch which will lose particles. It is called 3D flipflop because above a certain threshold in the strnegth of the beambeam force, the change of the bunch length is coupled to the change of the transverse beam sizes. So the beam which blows up longitudinally will also experience a transverse blowup.
This effect hasnt been studied before FCC but with the fcc it is open question whether this dynamics is triggered during the topup injection of the machine, where a small intensity bunch is injected and merged with the higher intensity stored bunch. So now that we have the tools it is very important to study this mechanism in this context.

## Slide 27: Workflow for emittance scan – everything in Xsuite
Prepare Xtrack line once [6]:
load MAD-X sequence [7]
add wigglers
slice sequence
build + twiss 4D
build + twiss 4D
convert to Xtrack line
save Xtrack line
Loop over a range of εy values:
twiss 6D mean synrad + tapering
match εy
build + twiss 4D
load Xtrack line
twiss 6D mean synrad + tapering
...
add beam-beam element (optional)
build
set quantum synrad
track
...
repeat with next εy
add observation point @ RF

## Slide 28: Emittance scan results
Small discrepancy compared to SAD results
Xsuite likely not yet converged
Need more turns to see fully converged emittances

## Slide 29: Small angle Bhabha scattering [6]
Dominated by t-channel (scattering) process
Main limitation of FCC-ee beam lifetime (alongside beamstrahlung)
primary particles lost within a turn
luminosity in lepton colliders

## Slide 30: Bhabha lifetimes
τ: Bhabha lifetime [s]
Nb: bunch intensity [1]
σBhabha: Bhabha cross section [m^2]
NIP: number of Ips [1]
Linst=L*frev: instantaneous lumi of 1 bunch crossing [m^-2 s^-1]
L: integrated lumi of a single collision (luminosity per bunch crossing) [m^-2]
frev: revolution frequency [s^-1]
Rb= σBhabha*L: number of emitted Bhabha photons with E above mom. acceptance [1]

## Slide 31: Dynamic aperture test grid

## Slide 32: Beam-beam in Xsuite
: compute statistical
moments of slice
t
Slower & more accurate
Faster & less accurate
Multiturn tracking
IP | arc | IP | arc | IP ...
...
Weak-Strong
(WS)
...
Strong-Strong
(SS)
...
Quasi-Strong-Strong (QSS)
(e.g. fupdate= 2)
FCC-ee
: bunch slice with
macroparticles
: soft-Gaussian kick
: untracked bunch
with fixed moments
Notes: 2 min
Next i will try to demonstrate in graphically how a single collision is simulated in xsuite. Lets take for example a simple setup wherre each bunch is sliced into 2 longitudinal slices. Then we have 3 steps in time, as the bunches pass through each other. In the code we can perform the beambeam interaction in 3 ways.
In the weak-strong approximation we track only one beam and the other beam is frozen. For this frozen bunch we input the statistical moments of the slices manually and they stay hardcoded for the whole simulation. The particles of the other beam are just passed through these slices and at every step the soft-Gaussian kick is applied. For multiturn tracking it would look like this on this simplified drawing.
The second model is the quasi strong strong. In this one we track both beams and at he beginning of the collision we compute the statistical moments of each slice of both beams. Then we use these moments in the soft-gaussian kick. In multiturn tracking this will look something like this. The frequency of recomputing the moments can be varied depending on the simulation.
The third model is the strong-strong where we recompute the moments before each timestep to model the variation of the beambeam force within a single collision.
In general there is a speed versus accuracy tradeoff between the models. The weakstrong model is the fastest but the least accurate, and the strongsterong is the most realistic but slowest. The best choice to use depends on the instability and the beam configuration we want to study. In general for the FCC-ee the quasi strong strong model is an optimal choice.