Impedance Study of the RCS Normal Conducting Beam Pipe
Erik Kvikne
David Amorim, Elias Metral
Accelerator design meeting
27-05-2024
Funded by the European Union (EU). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

---
Beam pipe design
The fast ramping normal conducting magnets of the RCS, makes a continuous metallic beam pipe impractical due to large Eddy current losses. (Presentation, Annual meeting 2024 )
Some metal is still required to shield the beam in order to keep the beam coupling impedance low.
By segmenting the beam pipe into thin metallic strips, we can drastically reduce Eddy current losses.
We will explore the beam coupling impedance in two different beam pipe designs.
Design 1: Ceramic pipe with RF-shield, J-PARC (M. Kinsho)
Design 2: RF-shield on the inside of insulator
(The proton driver design study, 2000)
Insulating substrate
Metallic stripes
Dipole magnet
Vacuum skin

---
Design 1: Ceramic pipe with RF-shield on the outside
Beam Pipe Cross Section
- Design 1 is based on the design used at the 3 GeV-RCS at J-PARC. It uses a ceramic beam pipe coated with thin longitudinal copper stripes on the outside, serving as an RF shield.
- The impedance of this design was computed using IW2D.
- Since IW2D assumes a cylindrical geometry, we modeled the copper stripes with a thin, continuous copper layer.
- This assumption was investigated by Y. Shobuda et al. and shown to be a very good approximation at high ɣ.
Copper
Ceramic

---
Design 1: Ceramic pipe with RF-shield on the outside
Simplified Beam Pipe Cross Section
- Design 1 is based on the design used at the 3 GeV-RCS at J-PARC. It uses a ceramic beam pipe coated with thin longitudinal copper stripes on the outside, serving as an RF shield.
- The impedance of this design was computed using IW2D.
- Since IW2D assumes a cylindrical geometry, we modeled the copper stripes with a thin, continuous copper layer.
- This assumption was investigated by Y. Shobuda et al. and shown to be a very good approximation at high ɣ.
Copper
Ceramic

---
Design 1: Ceramic pipe with RF-shield on the outside
- As per the Tentative parameter report the NC magnet aperture is 30x100mm.
- Beam pipe design for impedance computation:
  - Inner radius of 10 mm
  - Ceramic thickness of 5 mm
  - Varying thickness of copper used in calculations
- See appendix for material properties.
5mm
10mm
Copper
Ceramic

---
Design 1: Beam Coupling Impedance
- Changing the copper thickness has an impact on the lower frequency region of the impedance.
- However there are resonances caused by the ceramic that remains unaffected by the change in copper thickness.
- The impedance of these resonances are orders of magnitudes larger than the resistive-wall impedance we get without the ceramic layer.

---
Design 1: Beam Coupling Impedance
- Changing the copper thickness has an impact on the lower frequency region of the impedance.
- However there are resonances caused by the ceramic that remains unaffected by the change in copper thickness.
- The impedance of these resonances are orders of magnitudes larger than the resistive-wall impedance we get without the ceramic layer.

---
Design 1: Beam Coupling Impedance
- Changing the copper thickness has an impact on the lower frequency region of the impedance.
- However there are resonances caused by the ceramic that remains unaffected by the change in copper thickness.
- The impedance of these resonances are orders of magnitudes larger than the resistive-wall impedance we get without the ceramic layer.

---
Design 1: Comparison of Beam Pipe and Cavity Impedance for RCS2
- RCS2 Specifications:
  - Beam pipe length: 2539 m (identical to NC magnet length)
  - Number of cavities: 374
- The resonances caused by the ceramic are significantly larger than the ones from the cavities.
- David has shown that the impedance from the cavities is already close to the instability threshold in the 4 RCS chain simulation.
- Given that the resonances from the beam pipe are ~10x greater than those from the cavities, a stable beam is not achievable with this design.

---
Design 1: RCS2 Cavity and Beam Pipe Wake
- The wake was computed from the impedance in order to run XSuite simulations.
- As expected from the impedance plot, the beam pipe wake is significantly larger than the cavity wake.
- Changes in the copper thickness have little impact on the beam pipe wake due to the dominance of the ceramic resonances.
- The full RCS chain XSuite simulations showed, consistent with our expectations, that all the particles were lost within the first two RCS.

---
Design 2: RF-Shield on the Inside of Insulating substrate
Iron yoke
Ceramic
- The second design was first conceived by Bruno Zotter, featuring copper stripes attached to the inside of an insulating material, which we will assume to be ceramic.
- We will again make the assumption that the copper stripes can be modeled as a thin cylindrical layer.
- For simplicity, the magnet is modeled as an infinitely thick layer of copper.
- We use IW2D to compute the impedance and scan over different copper thicknesses to find the amount of copper needed to provide the beam with sufficient RF-shielding.
- The inner radius is kept constant at 10mm while the ceramic thickness is set to 5mm.
30mm
RF shield
100mm
Impedance model
5mm
10mm
Copper
Ceramic

---
Design 2: Beam Coupling Impedance
- Even with a very thin (~nm) layer of copper we are able to suppress the resonances we saw in Design 1.
  - This effect is explained by Zotter on page 168 in “Impedances and Wakes in High Energy Particle Accelerators”
- Increasing the thickness of the copper layer can significantly reduce the impedance at higher frequencies.

---
Design 2: Beam Pipe Wake
- The wake has a strong dependence on the thickness of the copper layer. By decreasing the copper thickness, we see an increase in the wake magnitude.
- By setting the copper thickness to zero, we are essentially left with Design 1 with an infinitely thick copper layer.
- To determine the thickness of copper needed to provide sufficient RF-shielding to the beam, we will conduct full RCS chain simulations using XSuite.
10 μm
100 nm

---
Design 2: Beam Pipe Wake
- The wake has a strong dependence on the thickness of the copper layer. By decreasing the copper thickness, we see an increase in the wake.
- By setting the copper thickness to zero, we are essentially left with Design 1 with an infinitely thick copper layer.
- To determine the thickness of copper needed to provide sufficient RF-shielding to the beam, we will conduct full RCS chain simulations using XSuite.

---
Design 2: Beam Pipe Wake
- The wake has a strong dependence on the thickness of the copper layer. By decreasing the copper thickness, we see an increase in the wake.
- By setting the copper thickness to zero, we are essentially left with Design 1 with an infinitely thick copper layer.
- To determine the thickness of copper needed to provide sufficient RF-shielding to the beam, we will conduct full RCS chain simulations using XSuite.

---
Beam and machine parameters
Machine parameters	Unit	RCS 1	RCS 2	RCS 3	RCS 4
Circumference	m	5990	5990	10700	35000
Bunch intensity	1012	2.7	2.7	2.7	2.7
Beam momentum	GeV/c	63	313.8	750	1500
Energy increase per turn	GeV	14.7	7.9	11.3	63.6
Rev. frequency	kHz	50	50	28	8.6
RF frequency	MHz	1300	1300	1300	1300
Harmonic number		25957	25957	46295	151433
RF voltage	GV	20.9	11.22	16.1	90.0
αp		0.0024	0.0024	0.001	0.001
Avg. beta x/y	m	50 / 50	50 / 50	50 / 50	50 / 50
Chromaticity Q’x/Q’y		scan	scan	scan	scan
Detuning from octupoles x/y	m-1	0 / 0	0 / 0	0 / 0	0 / 0
Length of NC section	m	3655	2539	4366	20376
Parameters used for the XSuite simulation:
Beam parameters	Unit	Value
Bunch length 1σ	mm	5.7
Bunch intensity	Particles per bunch	2.7e12
εx / εy	μm rad	25
# of macropaticles		50k
# of turns wakefield		1
# of slices wakefield		2000
Parameters from F. Batsch RCS tables

---
XSuite Simulation Parameters and Setup
- D.Amorim’s presentation at the 2024 IMCC and MuCol Annual Meeting details the general setup for start-to-end XSuite simulation of the RCS chain.
- Simulations were conducted scanning over different chromaticities, horizontal damper strengths and initial offsets at the entrance of an RCS, focusing on analyzing the wake effects of the Design 2 beam pipe at different copper thicknesses.
XSuite Simulation Parameters
Copper thickness:
0 nm , 1 nm, 100 nm, 10 μm, 1mm
Chromaticity:
-20, -15, -10, -5, 0, 5, 10, 15, 20
Damping time (# of turns):
4, 10, 20, 50, 100, ∞
Initial offset:
0, 1 μm, 10 μm, 100 μm, 1000 μm
66 turns
55 turns
RCS 4
1.5 -5.0 TeV
17 turns
55 turns
RCS 3
750 -1500 GeV
RCS 1
63 – 313 GeV
RCS 2
313 - 750 GeV
Courtesy D. Amorim

---
Result Plots of XSuite Simulation
- The result of the simulations are presented as heat maps
- The color intensity on these maps represents the normalized horizontal emittance growth between the beginning of RCS1 and end of RCS4.
- The x-axis represents the initial transverse offset at the entrance of each RCS
- The y-axis indicates the damping time, measured in number of turns.
- The plot title includes the chromaticity and an impedance scaling factor.

---
Result Plots of XSuite Simulation
- The result of the simulations are presented as heat maps
- The color intensity on these maps represents the normalized horizontal emittance growth between the beginning of RCS1 and end of RCS4.
- The x-axis represents the initial transverse offset at the entrance of each RCS
- The y-axis indicates the damping time, measured in number of turns.
- The plot title includes the chromaticity and an impedance scaling factor.
No emittance growth (ratio=1)
Large emittance growth (ratio≥10)

---
Result Plots of XSuite Simulation
- The result of the simulations are presented as heat maps
- The color intensity on these maps represents the normalized horizontal emittance growth between the beginning of RCS1 and end of RCS4.
- The x-axis represents the initial transverse offset at the entrance of each RCS
- The y-axis indicates the damping time, measured in number of turns.
- The plot title includes the chromaticity and an impedance scaling factor.
1mm offset
No initial offset

---
Result Plots of XSuite Simulation
Strong damper
- The result of the simulations are presented as heat maps
- The color intensity on these maps represents the normalized horizontal emittance growth between the beginning of RCS1 and end of RCS4.
- The x-axis represents the initial transverse offset at the entrance of each RCS
- The y-axis indicates the damping time, measured in number of turns.
- The plot title includes the chromaticity and an impedance scaling factor.
No damper

---
Result Plots of XSuite Simulation
Impedance scaling factor
Chromaticity
- The result of the simulations are presented as heat maps
- The color intensity on these maps represents the normalized horizontal emittance growth between the beginning of RCS1 and end of RCS4.
- The x-axis represents the initial transverse offset at the entrance of each RCS
- The y-axis indicates the damping time, measured in number of turns.
- The plot title includes the chromaticity and an impedance scaling factor.

---
10 μm Copper Shield Results
- A copper thickness of 10 μm is sufficient to keep the beam stable for all chromaticities (Q’ ranging from -20 to 20), as long as the initial offset at the entrance of each RCS is less than 1mm.
- Additionally, this implies that any copper shield thicker than 10 μm will also provide sufficient RF-shielding.

---
100 nm Copper Shield Results
- With a copper thickness of 100 nm, we see instabilities arise under certain chromaticities and simulation settings.
- The beam is consistently unstable for negative chromaticity values (Q’<0).
- At chromaticity of zero, or when sufficiently high (Q’≥15), the beam mostly remains stable.

---
Instabilities in RCS4
- Many of the observed instabilities develop in RCS4, primarily due to its longer sections of NC magnets.
- Having a thicker layer of shielding within RCS4 could help mitigate some of these instabilities.
Fig: 100 nm copper, horizontal damping time 50 turns.

---
Instabilities in RCS4
- Many of the observed instabilities develop in RCS4, primarily due to its longer sections of NC magnets.
- Having a thicker layer of shielding within RCS4 could help mitigate some of these instabilities.
Fig: 100 nm copper, horizontal damping time 50 turns.

---
Conclusion
- Beam Pipe Design Impact:
  - A design with ceramic and an outer copper layer results in resonances too large for stable beam operation. Placing the copper layer inside the beam pipe effectively suppresses these resonances.
- Simulation Insights:
  - IW2D simulations indicate that the thickness of the copper layer significantly affects the wake.
  - XSuite simulations demonstrate that a copper layer thickness of approximately 10μm is sufficient to prevent beam instability across RCS1-RCS4 for all chromaticities tested.
  - Thinner shielding of about 100nm works for sufficiently high positive chromaticities (≥15) or 0 chromaticity.
  - For RCS4, where the instabilities often develop, a thicker shielding could prove beneficial.
- Next Steps:
  - Improve the RCS impedance model by accounting for non-circular beam pipes and developing an impedance model for the SC beam pipe.
  - Integrate beam pipe and cavity impedance into a unified RCS impedance model.

---
Appendix

---
Material properties
Copper
- DC Resistivity:	1.7 • 10-8 Ohm-meter
- Resistivity Relaxation Time: 0.027 • 10-12 seconds
- Relative Dielectric Constant: 1
- Magnetic Susceptibility: 0
- Permeability Relaxation Frequency: Infinity
- Reference: CRC Handbook of Chemistry and Physics, 103rd Edition
- Comments: Pure copper at 293 K
Ceramic (HA997)
- DC Resistivity:	1 • 1012 Ohm-meter
- Resistivity Relaxation Time: 0 seconds
- Relative Dielectric Constant: 10
- Magnetic Susceptibility: 0
- Permeability Relaxation Frequency: Infinity
- Reference: A. Chao, Accelerator Handbook, p.463
- Comments: Ceramic at room temperature

---
RCS1-RCS3 vs. RCS1-RCS4
Simulations stopping after RCS3
By comparing simulations that include RCS4 to ones that stop after RCS3, we can see that some instabilities start in RCS4.
Simulations including RCS4
Fig: 100 nm copper.

---
10 μm Copper Shield Results, Negative Q’

---
10 μm Copper Shield Results, Positive Q’

---
100 nm Copper Shield Results, Negative Q’

---
100 nm Copper Shield Results, Positive Q’