## Slide 1: Simulation of Intrabeam Scattering
A. Vivoli*, M. Martini
Thanks to : Y. Papaphilippou and F. Antoniou
* E-mail : Alessandro.Vivoli@cern.ch

## Slide 2: CONTENTS
Introduction
Conventional Calculation of IBS
SIRE code
Benchmark with conventional theories
Analysis of simulation results
Conclusions

## Slide 3
IBS is the effect due to multiple Coulomb scattering between charged particles in the beam:
P1
P2’
P2
P1’
IBS Growth Times
IBS
Radiation Damping
Quantum Excitation
Introduction: Intra-Beam Scattering in DR
Evolution of the emittance:
Tk contain the effect of all the scattering processes in the beam at a certain time.
F. Antoniou, IPAC10

## Slide 4
Introduction: Conventional theories of IBS
Conventional IBS theories in Accelerator Physics (Bjorken-Mtingwa, Piwinski–Martini) derive Tk by the formula:
The particle distribution is inserted from outside the theory.
The integral is too complicate.
In practise, the integral has been solved only for Gaussian particles distribution.
In this case the formulas for the growth times reduce to:
Growth rates are calculated at different points of the lattice and then averaged over the ring:
s2
s1
s4
s3
s6
s5

## Slide 5
Software for IBS and Radiation Effects
s2
s1
s4
s3
s6
s5
6-dim Coordinates of particles are calculated.
Particles of the beam are grouped in cells.
Momentum of particles is changed because of scattering.
Invariants of particles are recalculated.
The lattice is read from a MADX file containing the Twiss functions.
Particles are tracked from point to point in the lattice by their invariats (no phase tracking up to now).
At each point of the lattice the scattering routine is called.
A routine has also been implemented in order to speed up the calculation of IBS effect.
Radiation damping and excitation effects are evaluated at the end of every loop.
Goals:
Follow the evolution of the particle distribution in the DR (we are not sure it remains Gaussian).
Calculate IBS effect for any particle distribution (in case it doesn’t remain Gaussian).

## Slide 6
SIRE: Motion in the DR
Transversal invariants:
Longitudinal invariant:
The motion of the particles in the CLIC damping rings can be expressed through 3 invariants (and 3 phases).
Emittance:

## Slide 7
Zenkevich-Bolshakov algorithm (from MOCAC)
Relativistic Center of Mass Frame:
Laboratory Frame:
(P.R. Zenkevich, O. Boine-Frenkenheim, A. E. Bolshakov, A new algorithm for the kinetic analysis of inta-beam scattering in storage rings, NIM A, 2005)
Radiation damping and quantum excitation are calculated with the formula:

## Slide 8
Lattice Recurrences
Elements of the lattice with twiss functions differing of less than 10% are considered equal.
Lattice:
First reduction:
+ 3 X
+
+ 3 X
+
Second reduction:
+ 2 X
(
+ 3 X
+
)
+
CLIC DR LATTICE: 14400 elements
420 elements

## Slide 9
SIRE: Benchmarking (Gaussian Distribution) CLIC DR
F. Antoniou, IPAC10

## Slide 10
SIRE: Distribution Study
Case studies:
A – Damping + QE
B – Damping + IBS + QE
C – Damping + IBS
D – IBS
Parameter | A | B | C | D
INITIAL gex, gey,szsp (m,m,eV m) | 74.3e-6,1.8e-6, 1.71e+5 | 74.3e-6, 1.8e-6, 1.70e+5 | 74.3e-6, 1.8e-6, 1.71e+5 | 229.7e-9,3.7e-9, 2.87e+3
FINAL gex, gey,szsp (m,m,eV m) | 229.7e-9, 3.76e-9, 2.88e+3 | 435.6e-9, 5.54e-9, 3.65e+3 | 458.5e-9, 3.61e-9, 1.58e+3 | 1.12e-6, 1.16e-8, 9.61e+3

## Slide 11
 | ex (m) | ey (m) | ez (eV m)
Injection | 13.27e-9 | 321.6e-12 | 1.71e+5
Extraction (SIRE) | 4.104e-11 | 6.72e-13 | 2.88e+3
Extraction (MAD-X) | 4.102e-11 | 6.69e-13 | 2.87e+3
Simulation of the CLIC Damping Rings case A:
Beam parameters
CLIC DR A: Damping + QE

## Slide 12
SIRE: IBS Distribution study A: Damping + QE
Parameter | Value
Eq. ex (m rad) | 4.1039e-011
Eq. ey (m rad) | 6.7113e-013
Eq. sd | 1.0901e-3
Eq. sz (m) | 9.229e-4
Parameter | c2999 | Confidence
DP/P | 964.2251 | 0.7876
X | 976.2195 | 0.6988
Y | 957.4559 | 0.8290

## Slide 13
 | ex (m) | ey (m) | ez (eV m)
Injection | 1.327e-8 | 3.177e-10 | 1.704e+5
Extraction (SIRE) | 7.783e-11 | 9.901e-13 | 3.651e+3
Extraction (B-M) | - | - | -
Simulation of the CLIC Damping Rings case B:
Beam parameters
CLIC DR B: Damping + IBS + QE
 | 1/Tx (s-1) | 1/Ty (s-1) | 1/Tz (s-1)
Bjorken-Mtingwa | 448 | 244 | 372
SIRE compressed (Gauss) | 309 | 209 | 283
SIRE not compressed (Gauss) | 310 | 213 | 289
SIRE compressed | 294 | 200 | 262
SIRE not compressed | 283 | 191 | 258

## Slide 14
SIRE: IBS Distribution study B: Damping + IBS + QE
Parameter | Value
Eq. ex (m rad) | 7.783e-11
Eq. ey (m rad) | 9.901e-13
Eq. sd | 1.228e-3
Eq. sz (m) | 1.04e-3
Parameter | c2999 | Confidence
Dp/p | 1166 | 2.0e-4
X | 1212 | 4.1e-6
Y | 1121 | 4.3e-3

## Slide 15
SIRE: IBS Distribution study B: Damping + IBS + QE
Parameter | Value
ap | 1.166e+6
bp | 1.108252
ax | 1.325e+10
bx | 1.160051
ay | 4.3711e+11
by | 1.058449
Parameter | c237 | Confidence | Sample %
DP/P | 37.86 | 0.430 | 67
X | 37.49 | 0.450 | 44
Y | 44.84 | 0.176 | 100

## Slide 16
 | ex (m) | ey (m) | ez (eV m)
Injection | 1.328e-8 | 3.153e-10 | 1.71e+5
Extraction (SIRE) | 8.19e-11 | 6.46e-13 | 1577
Extraction (B-M) | - | - | -
Simulation of the CLIC Damping Rings case C:
Beam parameters
CLIC DR C: Damping + IBS
 | 1/Tx (s-1) | 1/Ty (s-1) | 1/Tz (s-1)
Bjorken-Mtingwa | 1021 | 846 | 1928
SIRE compressed (Gauss) | 725 | 734 | 1466
SIRE not compressed (Gauss) | 705 | 706 | 1441
SIRE compressed | 619 | 616 | 1231
SIRE not compressed | 611 | 603 | 1244

## Slide 17
SIRE: IBS Distribution study C: Damping + IBS
Parameter | Value
Eq. ex (m rad) | 8.192e-11
Eq. ey (m rad) | 6.460e-13
Eq. sd | 8.072e-4
Eq. sz (m) | 6.833e-4
Parameter | c2999 | Confidence
Dp/p | 2497 | <1e-15
X | 2770 | <1e-15
Y | 1346 | 1.313e-12

## Slide 18
SIRE: IBS Distribution study C: Damping + IBS
Parameter | Value
ap | 1.722e+8
bp | 1.4350
ax | 9.0614e+10
bx | 1.2576
ay | 2.7499e+13
by | 1.2036
Parameter | c237 | Confidence | Sample %
DP/P | 39.04 | 0.38 | 35
X | 73.19 | 3.60e-4 | 44
Y | 38.71 | 0.39 | 38

## Slide 19
 | ex (m) | ey (m) | ez (eV m)
Injection | 4.104e-11 | 6.663e-13 | 2871
Extraction (SIRE) | 2.001e-010 | 2.064e-12 | 9609
Extraction (B-M) | - | - | -
Simulation of the CLIC Damping Rings case D:
Beam parameters
CLIC DR D: IBS
 | 1/Tx (s-1) | 1/Ty (s-1) | 1/Tz (s-1)
Bjorken-Mtingwa | 29.6 | 21.0 | 28.9
SIRE compressed (Gauss) | 21.6 | 17.8 | 20.6
SIRE not compressed (Gauss) | 18.1 | 18.0 | 19.3
SIRE compressed | 17.0 | 14.6 | 17.2
SIRE not compressed | 18.3 | 15.3 | 16.5

## Slide 20
SIRE: IBS Distribution study D: IBS
Parameter | Value
Eq. ex (m rad) | 2.001e-10
Eq. ey (m rad) | 2.064e-12
Eq. sd | 1.992e-3
Eq. sz (m) | 1.687e-3
Parameter | c2999 | Confidence
Dp/p | 3048.7 | <1e-15
X | 1441.7 | <1e-15
Y | 1466.9 | <1e-15

## Slide 21
SIRE: IBS Distribution study D: IBS
Parameter | Value
ap | 5.281e+7
bp | 1.568
ax | 3.840e+10
bx | 1.280
ay | 4.557e+12
by | 1.196
Parameter | c237 | Confidence | Sample %
DP/P | 38.81 | 0.39 | 26
X | 36.73 | 0.48 | 25
Y | 46.83 | 0.13 | 22

## Slide 22
SIRE: SLS simulations
 | 1/Tx (s-1) | 1/Ty (s-1) | 1/Tz (s-1)
MADX (B-M) | 20 | 37 | 59
SIRE (compressed) | 15.6 | 24.5 | 47.2
SIRE (not compressed) | 14.4 | 23.4 | 42.2

## Slide 23
 | ex (m) | ey (m) | ez (eV m)
Initial | 1.68e-8 | 6.01e-12 | 71571
Final | 6.08e-9 | 2.33e-12 | 8945
Equilibrium (NO IBS) | 5.59e-9 | 2.02e-12 | 7921
Beam parameters
IBS ON
IBS OFF
IBS ON
IBS OFF
SIRE: SLS simulations
IBS ON
IBS OFF

## Slide 24: Conclusions
Investigation of IBS effect in the CLIC DR has been carried out with the simulation code SIRE:
  Benchmarking with conventional IBS theories gave good agreement.
  Evolution of the particle distribution shows deviations from Gaussian behaviour due to IBS effect.
  IBS tends to develop tails of the particle distribution with a faster decay than for a Gaussian corresponding to the same beam parameters.
  IBS effect on the actual distribution is reduced compared to the effect evaluated on a Gaussian corresponding to the same beam parameters.
  In the CLIC DR this deviation is small (also due to the short cooling time) and discrepancy with Bjorken-Mtingwa calculation remains within the usual discrepancy of the theories.

## Slide 25: Outlook
Simulation code SIRE has been developed to simulate IBS effect in storage/damping rings.
  Benchmarking with conventional IBS theories gave good agreement.
  Evolution of the particle distribution shows deviations from Gaussian behaviour due to IBS effect.
Comparison with data from SLS could provide the possibility of
  Benchmarking with real data
  Tuning of code parameters (number of cells, number of interactions, etc.)
  Revision of the theory or theory parameters (Coulomb log, approximation used, etc.)

## Slide 26: THANKS.
The End