## Slide 1: CLIC space requirements
We use many facilities but the main one at CERN is CTF3:
Today we look for space for key activities (in terms of resources 30-40% of the program )

## Slide 2
50 MW
6 MW
1GHz klystron area
Control room
Rack space
Storage space
~ 25 m
~ 30m
High Power structure testing facility
160 MW
160 MW

## Slide 3
High Power structure testing facility
Aim to perform a large number of structure high power tests per year to enable CLIC structure optimization and industrialization
Space needed: 25 x 30 x5 m Height needed ~5 m,
Crane for klystron manipulation would be desirable
Temperature controlled demineralized cooling water for klystrons and structures
Shielding enclosures for structures, radiation area (klystrons)
Electrical power, 400 V, ~ several 100 kW ?
Schedule: Area preparation 2012, first test stand 2012/2013
Similar installations exists already in SM18 for example
Possible options: SM18, 175,156, 112,185

## Slide 4
Slit
53 MeV
6 MeV
26 MeV
Prebuncher
Buncher
Accelerating cavity
SHB
Solenoids
CLIC DB injector
schematics
Thermionic gun
Documented in the CDR; a scaled version of CTF3

## Slide 5
CLIC DB injector test facility
Bunker ~3m concrete
~ 4 m
~ 50/80 m
Access system
Rack space for electronics and power supplies
~ 10 m
~ 6 m
~ 10 m
KLY
MOD
KLY
MOD
KLY
MOD
KLY
MOD
CLIC 0: ~ 400 m
Rack space for electronics and power supplies

## Slide 6
CLIC DB injector test facility
Aim to develop and test realistic CLIC hardware and perform beam stability studies at nominal beam power
Space needed: 50 x 30 x10 m if possible extendible to ~80 m length Height needed ~10 m
Option: Tunnel with equipment gallery
Crane for manipulation of heavy equipment, concrete blocs, klystrons, accelerating structures
Temperature controlled demineralized cooling water for klystrons, structures and magnets
Shielding enclosures for linac with access control, radiation area (tunnel, klystrons)
Electrical power, 400 V, ~ 1-2 MW for full installation ?
Schedule: Area preparation 2012, first installation 2013, more space needed >2016
How about some space around the ISR, TT1 tunnel

## Slide 7
Space needs for future two-beam module production

## Slide 8
Option for the CLLIC DB injector in the TT1 tunnel

## Slide 9
Option for the CLLIC DB injector in the TT1 tunnel

## Slide 10
Conclusion
Space need identified and active research started
Department space officers involved
No concrete results so far, closer look into TT1 and Bldg 185