## Slide 2
A la LHC approach

## Slide 3
Phase 1: Alignment of the supports
Base plate aligned to +/- 1 mm with respect to a reference line.
Shimming to ensure a good horizontality of the transversal beams (+/- 1 mrad?).
Perpendicularity of the support w.r.t. reference line?

## Slide 4
Phase 2: Alignment of the end supports
Positioning to +/- 1 mm with respect to a reference line.

## Slide 5
Phase 3: Alignment of the end caps
A1
C
C1
Target interface
The positioning of the end caps (EC) is done with respect to and
A
C
A: best plane defined by the lower transversal beams
B
D
A
B: best plane defined by the upper transversal beams
C: best line defined by the lower transversal beam extremities
D: best line defined by the upper transversal beam extremities
B
D
+/- 0.5 mm?

## Slide 6
Phase 3: Alignment of the mobile beam
The positioning of the mobile beam is done with respect to
A
EC1-EC2
B
A
+/- 0.2 mm?
Target interface
EC1-EC2

## Slide 7
Phase 4: Installation of the chambers
Installation of chambers on dedicated adjustable supports

## Slide 8
Phase 4: Installation of the chambers
Installation of chambers on dedicated adjustable supports.
Adjustment of the chamber extremities to enable the sleeve sliding, alignment with respect to .
EC1-EC2
EC1-EC2

## Slide 9
Phase 5: Suspension of the chambers
Alignment of the chamber in vertical directions (cable length).
+/- 0.5 mm with respect to EC1-EC2 ?
EC1-EC2

## Slide 10
Phase 6: Upper chamber
Same approach for the upper chamber

## Slide 12
A la ET approch

## Slide 13
Phase 1: Alignment of the supports
Base plate aligned to +/- 1 mm with respect to the reference plane B1-B2.
Shimming to ensure a good horizontality of the transversal beams (+/- 1 mrad?).
Perpendicularity of the support w.r.t. B1-B2.
Theoretical laser axis are defined first.
B1
B2

## Slide 14
Phase 2: Alignment of the end supports
Positioning to +/- 1 mm with respect to the reference plane B1-B2.

## Slide 15
Phase 3: Alignment of the end caps
Target interface
+/- 0.5 mm?
The positioning of the end caps (EC) is done with respect to B1 and B2.

## Slide 16
Phase 3: Alignment of the mobile beam
The positioning of the mobile beam is done with respect to
B1-B2
+/- 0.2 mm?
Target interface
B1-B2

## Slide 17
Phase 4: Installation of the chambers
Installation of chambers on dedicated adjustable supports

## Slide 18
Phase 4: Installation of the chambers
Installation of chambers on dedicated adjustable supports.
Adjustment of the chamber extremities to enable the sleeve sliding, alignment with respect to .
B1
B1