## Slide 1: My work in CERN (in pictures)
Iryna Kapran
Mentor: Chris Neu
Team: Braden Allmond, Giulia Sorrentino

## Slide 2
BTL
2

## Slide 3
Measuring instruments
Caliper
Micrometer
3

## Slide 4
CC Measurements
CC Length Left
CC Length Right
CC central screw
CC Total Length
CC Width
CC Width = (149,99 ± 0,01) mm
CC Total Length = (279,90 ± 0,06) mm
4

## Slide 5
PCC Measurement
PCC width
PCC width = (58,96 ± 0,01) mm
5

## Slide 6
PCC-CC-PCC Measurements
СС height + space
Height without PCC
Height with PCC
Height of metal plate
Caliper:
СС height + space = (2,77 ± 0,04) mm
Height without PCC = (17,37 ± 0,05) mm
Height with PCC = (26,17 ± 0,03) mm
Height of metal plate = (4,32 ± 0,02) mm
6
Micrometer:
СС height = (1,771 ± 0,009) mm
Height without PCC = (17,229 ± 0,075) mm
Height with PCC = (24,587 ± 0,188) mm
Height of metal plate = (4,026 ± 0,001) mm

## Slide 7
PCC-CC-PCC Measurements
Caliper:
Copper Housing center = (0,51 ± 0,04) mm
All in one = (13,86 ± 0,11) mm
7
Micrometer:
Copper Housing center = (0,551 ± 0,018) mm
All in one = (13,134 ± 0,079) mm

## Slide 8
CC repeated measurements
CC Length Left
CC Length Right
CC central screw
CC Total Length
CC Width
CC Width = (149,95 ± 0,05) mm
CC Total Length = (279,92 ± 0,01) mm
8

## Slide 9
PCC repeated measurements
PCC width
PCC width = (58,97 ± 0,01) mm
9

## Slide 10
PCC-CC-PCC repeated measurements
СС height + space
Height without PCC
Height with PCC
Height of metal plate
Caliper:
СС height + space = (2,80 ± 0,01) mm
Height without PCC = (17,27 ± 0,01) mm
Height with PCC = (26,02 ± 0,02) mm
Height of metal plate = (4,31 ± 0,01) mm
10
Micrometer:
СС height = (1,765 ± 0,002) mm
Height without PCC = (17,278 ± 0,011) mm
Height with PCC = (24,724 ± 0,076) mm
Height of metal plate = (4,080 ± 0,018) mm

## Slide 11
PCC-CC-PCC repeated measurements
Caliper:
Copper Housing center = (0,51 ± 0,01) mm
All in one = (13,11 ± 0,06) mm
11
Micrometer:
Copper Housing center = (0,547 ± 0,008) mm
All in one = (13,230 ± 0,050) mm

## Slide 12
PCC-CC-PCC Measurements
Mass [g]
Front End Card = (28 ± 2) g
Front End Card w Thermal Pads = (29 ± 2) g
Copper Housing = (32 ± 2) g
Airex Pad with Size of Front End Card = (1,15 ± 0,15) g
All in one = (221 ± 2) g
LYSO c25-2-T1 = (77 ± 2) g
LYSO c30-3-T2 = (62 ± 2) g
LYSO c25-2-T3 = (51 ± 2) g
LYSO Hpk-2-30 = (64 ± 2) g
CC = (215 ± 2) g
12

## Slide 13
PCC-CC-PCC Measurements
13

## Slide 14
PCC-CC-PCC repeated measurements
14

## Slide 15
PCC-CC-PCC repeated measurements
15

## Slide 16
Module measurements
16
Height = (14,06 ± 0,34) mm
Width = (61,18 ± 0,03) mm
Length = (103,20 ± 0,02) mm

## Slide 17
Module measurements
17

## Slide 18
Module measurements
18

## Slide 19
Module measurements
19

## Slide 20
Сonclusions
20
During the first measurements, we took an average of 6-7 data per value. The small number of experiments and the human factor influenced the fact that the results of caliber and microment measurements differ in some places. Next, we took twenty data per value. As a result, the final data has less divergence. We have big differences in the Height with PCC measurement. This is due to the Airex Pad, because it is quite soft and this distorts the results. All other data is quite accurate, which is confirmed by our final calculations.

## Slide 21
Thank you for your attention

## Slide 22
Thank you for your attention

## Slide 23
Thank you for your attention