## Slide 1
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
FCC week 2024 - DATE
Roxana SOOS, Xavier BUFFAT, Angeles FAUS-GOLFE, FCC-ee collective effects study group

## Slide 2
Summary
Introduction
  Study context for FCC-ee
  Xsuite and parameter sets for simulations
Simulation tools
  Circulant matrix model
  Xsuite versus mode analysis algorithm
Simulation of Beam-Beam
  Intensity scans – coherent instability
  Tune scans – study of different characteristics
Simulation of wakefields
  Circulant matrix model for wakefields
  Transverse mode coupling instability simulations
Summary
  Summary and outlook
FCC week 2024 - DATE
Roxana SOOS, Xavier BUFFAT, Angeles FAUS-GOLFE, FCC-ee collective effects study group.
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.

## Slide 3
3
12/06/24
Roxana SOOS
Introduction
Study context for the FCC-ee
Context:
Interplay between impedance (wakefields) and beam-beam has a growing interest for building new accelerators [1]
BimBim (CMM) and Xsuite showed agreement with LHC and VEPP measurements [2], [3]
[1] Y. Zhang, et al., Phys. Rev. Accel. Beams 26, 064401 (2023)
[2] S. White, et al., Phys. Rev. ST Accel. Beams 17, 041002 (2014)
[3] E. A. Perevedentsev and A. A. Valishev, Phys. Rev. ST Accel. Beams 4, 024403 (2001)
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.

## Slide 4
4
Roxana SOOS
Introduction
Study context for the FCC-ee
Context:
Interplay between impedance (wakefields) and beam-beam has a growing interest for building new accelerators [1]
BimBim (CMM) and Xsuite showed agreement with LHC and VEPP measurements [2], [3]
[1] Y. Zhang, et al., Phys. Rev. Accel. Beams 26, 064401 (2023)
[2] S. White, et al., Phys. Rev. ST Accel. Beams 17, 041002 (2014)
[3] E. A. Perevedentsev and A. A. Valishev, Phys. Rev. ST Accel. Beams 4, 024403 (2001)
Xsuite and BimBim simulation tools for beam-beam and impedance studies
https://indico.cern.ch/event/1326738/
https://indico.cern.ch/event/1326738/
https://indico.cern.ch/event/1202105/
12/06/24

## Slide 5
5
Roxana SOOS
Introduction
Study context for the FCC-ee
Context:
Interplay between impedance (wakefields) and beam-beam has a growing interest for building new accelerators [1]
BimBim (CMM) and Xsuite showed agreement with LHC and VEPP measurements [2], [3]
Goal:
Understand the different effects due to the contribution of beam-beam and impedance and the dependence on different parameters.
As announced in [1] and other literature, it is difficult to find a stable tune area when the two effects are considered.
[1] Y. Zhang, et al., Phys. Rev. Accel. Beams 26, 064401 (2023)
[2] S. White, et al., Phys. Rev. ST Accel. Beams 17, 041002 (2014)
[3] E. A. Perevedentsev and A. A. Valishev, Phys. Rev. ST Accel. Beams 4, 024403 (2001)
Xsuite and BimBim simulation tools for beam-beam and impedance studies
https://indico.cern.ch/event/1326738/
https://indico.cern.ch/event/1326738/
https://indico.cern.ch/event/1202105/
12/06/24

## Slide 6
6
Roxana SOOS
Introduction
Xsuite and parameter sets for simulation
Turn by turn tracking of particles, calculating nonlinear forces around the specified accelerator components.
FCC-ee (Z) approximated model:
Why:
Limits the numerous complicated non studied effects.
Faster simulations.
What:
FCC-ee (Z) parameters table (bunch lengths/sizes, RF power, crossing angle, …)
Synchrotron radiation (SR) + Radio frequency cavities (RF)
Single beam-beam interaction point + Beamstrahlung (BS)
Crab sextupoles (when crossing angle)
Longitudinal + Transverse wakefields (2023 - M. MIGLIORATI)
Simulation tools
SEXTUPOLE
SEXTUPOLE
BEAM BEAM INTERACTION
RF CAVITIES
SYNCHROTRON RADIATION
WAKEFIELDS
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 7
7
Roxana SOOS
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
=
Slicing structure
Polar longitudinal phase space
Circulant Matrix Model (CMM)
Introduction
Simulation tools
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 8
8
Roxana SOOS
=
Slicing structure
Polar longitudinal phase space
1 turn system matrix
Diagonalize to get eigenvalues
Circulant matrix
Circulant Matrix Model (CMM)
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Simulation tools
Synchrotron (permutation)
+
betatron motion
Linear beam-beam perturbation
Wakefield perturbation
Real part = oscillation modes
Imaginary part = growth rate
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 9
9
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
Transverse beam-beam kicks reprensentation
(Given by Bassetti – Erskine formula)
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Simulation tools
Coherent = over all particle
Incoherent = single particle
Beam-beam kick
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 10
10
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
What is in the beam-beam model?
Flat beams
Crossing angle
Drifts (IP -> CP -> IP)
Hourglass effect
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Simulation tools
Transverse beam-beam kicks reprensentation
(Given by Bassetti – Erskine formula)
Coherent = over all particle
Incoherent = single particle
Beam-beam kick
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 11
11
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Simulation tools
Transverse beam-beam kicks reprensentation
(Given by Bassetti – Erskine formula)
Coherent = over all particle
Incoherent = single particle
Beam-beam kick
What is in the beam-beam model?
Flat beams
Crossing angle
Drifts (IP -> CP -> IP)
Hourglass effect
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 12
12
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Simulation tools
Transverse beam-beam kicks reprensentation
(Given by Bassetti – Erskine formula)
Coherent = over all particle
Incoherent = single particle
Beam-beam kick
What is in the beam-beam model?
Flat beams
Crossing angle
Drifts (IP -> CP -> IP)
Hourglass effect
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 13
13
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Introduction
Simulation tools
Transverse beam-beam kicks reprensentation
(Given by Bassetti – Erskine formula)
Coherent = over all particle
Incoherent = single particle
Beam-beam kick
What is in the beam-beam model?
Flat beams
Crossing angle
Drifts (IP -> CP -> IP)
Hourglass effect
Disclaimer: schematic not 100% accurate representation.
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 14
14
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
[4] K. HIRATA, Nuclear Instruments and Methods in Physics Research A269, 7-22 (1988)
[4]
Bassetti – Erskine formula
Coupled forces
Normal forces
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Introduction
Simulation tools
Transverse beam-beam kicks reprensentation
(Given by Bassetti – Erskine formula)
Coherent = over all particle
Incoherent = single particle
Beam-beam kick
Coherent force
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 15
15
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
[4] K. HIRATA, Nuclear Instruments and Methods in Physics Research A269, 7-22 (1988)
[4]
Bassetti – Erskine formula
Coupled forces
Normal forces
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Introduction
Simulation tools
Coherent force
[4]
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 16
16
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
Circulant Matrix Model (CMM)
[4] K. HIRATA, Nuclear Instruments and Methods in Physics Research A269, 7-22 (1988)
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Introduction
Introduction
Simulation tools
BEAM 1
BEAM 2
Simple case with the beam beam kick only applied to the horizontal space
This can be generalized to the vertical space and for x mesh elements.
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 17
17
Roxana SOOS
XSuite versus mode analysis algorithm
Introduction
Simulation tools
Study of BOTH wakefields and
beam-beam interactions possible
Xsuite
CMM*
Output:
Turn by turn parameters of the particles in the beam
Output:
Eigenvalues

tunes and growth rates
Advantages:
We can see all oscillation modes and the growth rates quickly
*Circulant Matrix Model
Drawbacks:
Linear model, cannot show non-linear effects
Advantages:
Closer to reality, non-linear models,
Landau damping,…
Drawbacks:
Difficult to interpret results, slower
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 18
18
Roxana SOOS
Intensity scans – coherent instability
The intensity scan is a simulation where we study growth rates of the instabilities and modes of oscillation, varying the intensity. The CMM outputs are modes of oscillation and growth rates.
Introduction
Simulation tools
Simple case: Only beam-beam, with circular beam, no hourglass, low intensity, to demonstrate ‘simple’ intensity scan
Simulations of beam-beam
Smaller vertical tune: farther from 0.5 resonance
Higher vertical tune: closer to 0.5 resonance
0.5 resonance hit
=
Coherent instability
FCC-ee (Z) base parameters with = 0.15 m, = 7.1e-10m, = 0 mrad
[5] A. CHAO, Coherent Beam-Beam Effects (1991)
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24

## Slide 19
19
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
Simple case: Only beam-beam, with circular beam, no hourglass, low intensity, to demonstrate ‘simple’ tune scan
FCC-ee (Z) base parameters with = 0.15 m, = 7.1e-10m, = 0 mrad
[5] A. CHAO, Coherent Beam-Beam Effects (1991)
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_0/

## Slide 20
20
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
MAX TURNS = 2/GROWTH RATE
STABLE
UNSTABLE
[5]
[5] A. CHAO, Coherent Beam-Beam Effects (1991)
Simple case: Only beam-beam, with circular beam, no hourglass, low intensity, to demonstrate ‘simple’ tune scan
FCC-ee (Z) base parameters with = 0.15 m, = 7.1e-10m, = 0 mrad
UNSTABLE
STABLE
UNSTABLE
UNSTABLE
Missing data points
Missing data points
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_0/

## Slide 21
[5] A. CHAO, Coherent Beam-Beam Effects (1991)
Simple case: Only beam-beam, with circular beam, no hourglass, low intensity, to demonstrate ‘simple’ tune scan
FCC-ee (Z) base parameters with = 0.15 m, = 7.1e-10m, = 0 mrad
21
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
MAX TURNS = 2/GROWTH RATE
STABLE
[5]
STABLE
UNSTABLE
UNSTABLE
UNSTABLE
UNSTABLE
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_0/

## Slide 22
22
Roxana SOOS
Intensity scans – coherent instability
Simple case: Only beam-beam, with flat beam, no hourglass, low intensity, to demonstrate ‘simple’ intensity scan
Smaller vertical tune: farther from 0.5 resonance
Higher vertical tune: closer to 0.5 resonance
0.5 resonance hit
=
Coherent instability
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
The intensity scan is a simulation where we study growth rates of the instabilities and modes of oscillation, varying the intensity. The CMM outputs are modes of oscillation and growth rates.
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam

## Slide 23
23
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
Simple case 2: Only beam-beam, with flat beam, no hourglass, low intensity, ONLY Y PLANE.
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
Y PLANE RESONNANCES
Y PLANE RESONNANCES
Y PLANE RESONNANCES
Y PLANE RESONNANCES
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_13/

## Slide 24
24
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
Simple case 2: Only beam-beam, with flat beam, no hourglass, low intensity, Y AND X PLANES.
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
X PLANE RESONNANCE
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_13/

## Slide 25
25
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
Simple case 2: Only beam-beam, with flat beam, no hourglass, low intensity, Y AND X PLANES.
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
LANDAU DAMPING?
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_13/

## Slide 26
26
Roxana SOOS
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
HIGHER ORDER COHERENT INSTABILITY?
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
Simple case 2: Only beam-beam, with flat beam, no hourglass, low intensity, Y AND X PLANES.
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_13/. (0.7,2) sigma

## Slide 27
27
Roxana SOOS
Transverse wake kick
Matrix elements example
Circulant Matrix Model (CMM) for wakefields
X. BUFFAT CERN– EPFL Thesis 2015
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
s
x
x1
x2
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Simulations of wakefields

## Slide 28
28
Roxana SOOS
Transverse wake kick
Matrix elements example
X. BUFFAT CERN– EPFL Thesis 2015
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
s
x
x1
x2
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Circulant Matrix Model (CMM) for wakefields
Introduction
Simulation tools
Simulations of beam-beam
Simulations of wakefields

## Slide 29
29
Roxana SOOS
Talk earlier this morning on the effects of wakefields in FCC-ee, and mitigation techniques.
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Circulant Matrix Model (CMM) for wakefields
Introduction
Simulation tools
Simulations of beam-beam
Simulations of wakefields

## Slide 30
30
Roxana SOOS
Intensity scan with CMM
Growth rate [2pi/trun]
Re()/
Intensity scan with Xsuite - PyHT
2,3.1011
2,6.1011
2,6.1011
2,3.1011
Transverse wakefields for FCC-ee at Z energy; perfect agreement!
Bunch length without beamstrahlung (5.2mm), L = 90.66 km , linearized RF, no longitudinal wakes.
Bunch population
Bunch population
Growth rate [1/trun]
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Transverse mode coupling instability simulations
Introduction
Simulation tools
Simulations of beam-beam
Simulations of wakefields

## Slide 31: Summary and outlook
31
Roxana SOOS
The circulant matrix model (CMM) has successfully been tested for simple cases of flat beam collisions, x and y planes can be studied separately, but coupled forces can also be calculated.
Another method should be applied to predict higher order collective resonances.
CMM has shown perfect agreement for simulations involving transverse wakefields.
Further development should allow longitudinal wakefields to be considered.
Studies with a crossing angle and Crab waist are ongoing, with both the CMM and Xsuite, a correct setup is yet to be done with strong-strong simulations
Once the setup is totally controlled, reliable simulation with both beam beam and wakefields can be obtained with both Xsuite and CMM
Xsuite and Circulant Matrix Model simulations for FCC-ee beam-beam and wakefield effects.
12/06/24
Introduction
Simulation tools
Simulations of beam-beam
Simulations of wakefields
Summary

## Slide 32
Thank you!

## Slide 33
Thank you!

## Slide 34
34
DATE
Roxana SOOS
XSuite versus mode analysis algorithms
Xsuite simulations of beam-beam effects with impedance contribution
Backup slide on the coupled forces benchmark,
On the slice analysis
The precise calculation of the force
The matrices in the CMM, basically what I did with HIRATA
On SR?
TITRE
Introduction
Simulation tools

## Slide 35
Computational cost
Fully numerical method
Fully analytical model
35
04/06/2024
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
FCC-ee collective effects:
wakefileds and beam-beam interactions
Circulant Matrix Model (CMM)
transverse beam-beam kicks,
main frequencies = coherent kick
[4] K. HIRATA, Nuclear Instruments and Methods in Physics Research A269, 7-22 (1988)
[4]
Bassetti – Erskine formula
Coupled forces
Normal forces
1000 pts ~6h
~ 5s
Dependent on numerical values
Independent of numerical values
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
TITRE
Introduction
Simulation tools

## Slide 36
Computational cost
Fully numerical method
Fully analytical model
36
04/06/2024
Roxana SOOS
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
FCC-ee collective effects:
wakefileds and beam-beam interactions
Circulant Matrix Model (CMM)
transverse beam-beam kicks,
main frequencies = coherent kick
1000 pts ~6h
~ 5s
Dependent on numerical values
Independent of numerical values
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
[4] K. HIRATA, Nuclear Instruments and Methods in Physics Research A269, 7-22 (1988)
TITRE
Introduction
Simulation tools
Linearized coherent kick benchmark

## Slide 37
37
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
TITRE
DATE
Simple case 2: Only beam-beam, with flat beam, no hourglass, low intensity, to understand some effects of having a flat beam.
Introduction
Simulation tools
Tune scans
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_13/

## Slide 38
38
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
TITRE
DATE
Simple case 2: Only beam-beam, with flat beam, no hourglass, low intensity, to understand some effects of having a flat beam.
Introduction
Simulation tools
Tune scans
LANDAU DAMPING?
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_13/ (2,2) sigma

## Slide 39
39
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
TITRE
DATE
Case 2 bis: Only beam-beam, with flat beam, hourglass, low intensity, kick beams by a fraction of sigma to see some coupled modes.
Introduction
Simulation tools
Tune scans
HIGHER COHERENT INSTABILITY ?
FCC-ee (Z) base parameters with = 0.1 m, = 7.1e-10m, = 0 mrad = 0.3 sigmas
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_16/. (10,25 sigma)

## Slide 40
40
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
TITRE
DATE
Case 3: Only beam-beam, with flat beam, hourglass, low intensity, to understand some effects of having a flat beam.
Introduction
Simulation tools
Tune scans
FCC-ee (Z) base parameters with = 0.15 m, = 1.42e-12m, = 0 mrad
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_1/

## Slide 41
41
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Tune scans – study of different characteristics
The tune scan is a simulation where we study the growth rate of the instabilities in a bunch, varying the intensity and/or the tune(s).
TITRE
DATE
Case 3: Only beam-beam, with flat beam, hourglass, low intensity, to understand some effects of having a flat beam.
Introduction
Simulation tools
Tune scans
COHERENT INSTABILITY
NON-COHERENT INSTABILITY
FCC-ee (Z) base parameters with = 0.15 m, = 1.42e-12m, = 0 mrad
Notes: /eos/project/f/fcc-ee-bbeam-wake-studies/rosoos/beambeamStudies/intyVStune/tune_scan_1/

## Slide 42
42
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
Xsuite - PyHT
PyHEADTAIL
Simulation executed by M. Migliorati
Simulation executed by M. Migliorati
Sum of the Fourier transforms of the higher order momentas.
Average on the macroparticles
Longitudinal positions relative to the bunch
Horizontal positions
Momentum of order k at a turn t
Introduction
Perfect agreement (Radio frequency cavities and synchrotron radiation + wakes for FCC-ee Z).
TITRE
TITRE

## Slide 43
43
04/06/2024
Roxana SOOS
Introduction
Use linear algebra on a one turn matrix that represents a system, applied on discretized longitudinal phase space
Linearized coherent flat beam-beam kick
(from Bassetti – Erskine formula)
Matrix elements example
FCC-ee collective effects:
wakefileds and beam-beam interactions
Circulant Matrix Model (CMM)
[4] K. HIRATA, Nuclear Instruments and Methods in Physics Research A269, 7-22 (1988)
BETTER PLOT OF THIS IN THE BACKUP SLIDES
+
ANALYTIC FORCE
NEXT PUT THE WEIRD COIUPLING THAT COULD BE SECOND ORDER AND SEE WITH HIRATA MAYBE

## Slide 44
Beam-beam interactions with wakefield contributions
44
Roxana SOOS
Introduction
FCC-ee collective effects:
wakefileds and beam-beam interactions
Overview
Transverse wakefields
Longitudinal wakefields
Slice Analysis
Synchrotron radiation
Round beam collision
Flat beam w/o hourglass
Crossing angle
Flat beam w hourglass
SLIDE ON SLICE ANALYSIS WHEN HTC SUPPORT FIXES THE SERVICE

## Slide 45
45
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
What is in the wake fields?
elements = [arc, wake_field]
142
What is in the arc?
Synchrotron radiation
Energy loss
Damping rates
Equilibrium emittances
RF Cavities
Nonlinear RF forces
Energy compensation
Transverse wakes /
Longitudinal wakes
Introduction
Bellows
RF Cavities
NO geometrical contribution of the collimators
Resisitive wall ( Beam pipe + collimator RW)
Beam Position Monitors (BPM)

## Slide 46
46
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
LineSegmentMap already benchmarked; add synchrotron radiation
Test damping times
Linear map, SR ( ), no wakes, same inital distribution
Introduction

## Slide 47
47
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
Test equilibrium emittances
Linear map, SR ( ), no wakes, same inital distribution
LineSegmentMap already benchmarked; add synchrotron radiation
Test damping times
Linear map, SR ( ), no wakes, same inital distribution
8%
8%
8%
SYSTEMATIC DISCREPENCY
PERFECT OVERLAP / EXPECTED VALUES
Introduction

## Slide 48
48
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
Implemented flag in LineSegmentMap with partition ratio.
Full matrix? "From the beam envelope matrix to synchrotron radiation integrals",
Kazuhito Ohmi, Kohji Hirata, Katsunobu Oide, in Phys.Rev.E 49 (1994) 751-765
damping
eq emittance
Xsuite - PyHT
PyHEADTAIL
eq emittance
damping
damping
eq emittance
R = damping time
n = random number
Xtrack/xtrack/beam_elements/elements.py in class LineSegmentMap l.1955 to l.1966 and Xtrack/xtrack/beam_elements/elements_src/linesegmentmap.h l.281 to l.290 and l.337 to l.350
Introduction
Different synchrotron radiation models (in both longitudinal and transverse planes)

## Slide 49
49
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
Different synchrotron radiation models (in both longitudinal and transverse planes)
162
arc = xt.LineSegmentMap(
sync_ratio = 1,
)
163
164
162
arc = xt.LineSegmentMap(
sync_ratio = 0.5,
)
163
164
Introduction
Perfect agreement when the same model is used.

## Slide 50
50
04/06/2024
Roxana SOOS
FCC-ee collective effects:
wakefileds and beam-beam interactions
Simulation of impedance
Introduction
Simulation of beam-beam
Arbitrary tunes used for simulation to reduce numerical noise.
Xsuite results show a 20% error with respect to Yokoya (self-consistent)
Errors improve to only 5% when compared to Yokoya (soft-gaussian) -> Due to an artificial transverse kick
Benchmark Xsuite
Aspect ratio versus form factors
Scan on aspect ratio versus mode tune shift