## Slide 1: RFD SPS TUNER SM18 tests CD1 + CD2
18.06.2024 Experience from RFD CM tests
K. Artoos, A. Edwards, D. Glenat, N. Stapley, K. Turaj, N. Valverde

## Slide 2: Reminder: Tuning principle HL LHC RFD
RFD
RFD
Tuning Sensitivity:
512 kHz/mm*
Cavity tuning stiffness:
2.8 kN/mm*
Specified tuning range at 2 K:
± 150 kHz
Elastic limit range at 2 K:
± 1.22 MHz
± 2.38 mm*
± 6.7 kN
Requested precision ~ 80 Hz

## Slide 3: Overview components
ACTUATOR SPS proto
Limit switches
Difficult to set, not so reliable
Mechanical end stops with max load interlock on load cell conditioner
Stepper motor
1.3 Nm bipolar, motor step 1.8 deg, micro stepping 8000/360 , not ramped open loop, limited to 2000 steps/sec
Harmonic drive HFUS-20-100-2SO Ratio 100, Accuracy < 1 arcmin, precision <0.1 arcmin (5 nm)
Fa Dyn 7.7 kN
Roller screw Rollvis RV 12 x 1 static load capacity 17 kN
Sferax Compact GBL 1219 bearings XA +A (all metal) and guides
Radhard grease SYNRAD 1252
Loadcell
So far: Kistler 10 kN 4576A55C1 class 0.1
Actuator coupling
Allows quick change of actuator + connection without frequency change
Incorporates heater
coupling
Vertical Spring pre-load from alignment plate

## Slide 4: Installation Actuators + RT test
Interference actuator springs with turned and tilted waveguide
Interference between cable gauge FPC with actuator support

## Slide 5: RT cycle before CD 1, OVC open
*Cycle on Cav1 shortened due to x-rays in evening

## Slide 6: RT before CD 1, OVC open
Additional: 14/11/23 Tuner and HOM measurements at RT

## Slide 7: Cool Down 1 to 2 K
No tuner force measurements during cool down
Non-linearity measured on cavity 2 and cavity 1 (backlash with a twist)

## Slide 8: Cav 1 + 2, CD1 several cycles

## Slide 9: Small precision cycle CD1
Stick slip

## Slide 10: CD1 Other observations tuner
Tuner laterally blocked on sliding pads support
During assembly tuner, bearings very hard to align, some “hard points” in guidance
No ice nor condensation observed during CD1 run on tuner feed through

## Slide 11: Adjustments actuator before CD2
Solution:
spacer added
We will improve design
Reason for the backlash: play in actuator clamp reproduced on actuator test bench, part out of tolerance
Removed the actuator support + springs. The actuator now “sits” completely on cavity. This to reduce the restraints on bearings + bonus: no more interference with waveguide or cable FPC

## Slide 12
?

## Slide 13: Tuning SPS-RFD SM18 Cavity 2 CD2
Small cycle
(Frequency is drifting during test)

## Slide 14: Acceptance testing tuner
Remark: The 80 Hz precision steps (uni directional + bidirectional) are difficult to measure: the frequency measured is drifting slowly + superimposed noise.
Up to LLRF to say if tuner precision is sufficient.

## Slide 15
Actuator support with flexural guide
3 times less ball bearings
Limit switches + mechanical stops: improved reliability + better access: on going
Rad-hardness components+ dismountability in situ: ongoing
Improving the load cell + rad –hardness
Need to improve reliability + easier access heater: idea to include in clamp to be verified
Reintroduce a pre-load spring (AUP RFD)
Preparing purchase components
Ongoing upgrade design actuator: