## Slide 1: New Concepts for a High Power 805 MHz RF Amplifier for LANSCE Using Gallium Nitride Semiconductors
J. T. M. Lyles, M.S. Barrueta, J. T. Bradley III, E. N. Brown, M. C. Brown, J. L. Castellano, B. N. Comiskey, T. W. Hall, S. I. Kwon, M. S. Prokop, M. B. Rodriguez, P. J. Van Rooy, S. J. Russell, J. A. Valladares
Accelerator Operations and Technology Division
13th CWRF Workshop
September 10, 2024
Work supported by the U.S. Department of Energy through the Los Alamos National Laboratory, operated by Triad National Security, LLC, for the National Nuclear Security Administration of U.S. Department of Energy (Contract No. 89233218CNA000001). Research presented in this article was supported by the Laboratory Directed Research and Development program of Los Alamos National Laboratory under project number 20240723DI.

## Slide 2
Outline
CCL RF System
Reliability Concerns with Vintage UHF Powerplant (RF and HV)
Long Term Klystron Concern – Alternatives?
Solid State Amplifier (SSA) Feasibility as a Long Term Source
Breakthru Technology is GaN on SiC
Combining
Amplitude Control
Next Steps

## Slide 3
LANSCE Coupled Cavity Linac
Coupled-cavity linac is 727 m long, normal conducting copper, first one built and commissioned 1972 as LAMPF
H- accelerated from 100 MeV to 800 MeV, also protons in earlier years
Mandate to operate to 2050, for pRad, UCN, Neutron Scattering, ICE, WNR, IPF

## Slide 4
CCL High Power RF System
44 tubes, 1.25 MW peak, 805 MHz, 1 mS pulse, 120 Hz, 12% DF
Production of VA862A1 Klystrons needed for 25 more years
2010 tube run had increased early failures compared to 1980-90 tubes
“LANSCE CCL Klystron Reliability, Evaluation, and Path Forward”, Waghmare, Lyles, Bradley, 13th CWRF Workshop, 2024
“LANSCE 805 MHz Klystron Design and Performance”, Waghmare, Valladares, Linac’24, 2024

## Slide 5
CCL RF HV System
Klystron beam voltage -85 kV DC
One mains charging supply plus 220 kJ capacitor bank and crowbar per 6 or 7 tubes
Power supply and AC regulator no longer made by GE, over 1 year to rebuild (by 3rd party). Some rebuilds have failed.

## Slide 6
Alternative RF Amplifiers to Meet Requirements

## Slide 7
Examples of UHF LDMOS
Below 500 MHz LDMOS ~2 kW Psat
Massive transistor structures used for higher power, have higher drain-source capacitance, 805 MHz power < 1 kW

## Slide 8
Type Number Launch Date Longevity Date Longevity Duration |  |  | 
ART150FE | 2020/12/04 | 2035/12/05 | 15 years
ART150PE | 2023/01/10 | 2038/01/10 | 15 years
ART150PEG | 2023/01/10 | 2038/01/10 | 15 years
ART1K6FH | 2020/09/15 | 2035/09/16 | 15 years
ART1K6FHG | 2022/03/18 | 2037/03/18 | 15 years
ART1K6FHS | 2022/03/18 | 2037/03/18 | 15 years
ART2K0FE | 2020/05/01 | 2035/05/02 | 15 years
ART2K0FEG | 2022/03/18 | 2037/03/18 | 15 years
ART2K0FES | 2022/03/18 | 2037/03/18 | 15 years
ART2K0PE | 2023/05/25 | 2038/05/25 | 15 years
ART2K0PEG | 2023/05/25 | 2038/05/25 | 15 years
ART2K0TFEG | 2023/06/06 | 2033/06/06 | 10 years
ART2K0TFES | 2023/06/06 | 2033/06/06 | 10 years
ART35FE | 2020/11/27 | 2035/11/28 | 15 years
ART450FE | 2023/06/23 | 2033/06/23 | 10 years
ART700FH | 2021/09/17 | 2036/09/17 | 15 years
ART700FHG | 2022/06/15 | 2037/06/15 | 15 years
ART700FHS | 2022/06/15 | 2037/06/15 | 15 years
ART800PE | 2023/09/19 | 2038/09/19 | 15 years
Ampleon Product Longevity Overview
LDMOS Product Lifecycle

## Slide 9
On Gallium Nitride:
“The energy gap of GaN is three times that of silicon, resulting in reduced performance degradation at high temperatures. Similarly, breakdown at a six-fold electric field and two-and-a-half-fold carrier saturation velocity enable much greater power densities, resulting in the same output power capability at a much higher impedance level.”
High Efficiency Power Amplifiers, Ericsson Review No. 3, 2006
Beyond LDMOS

## Slide 10
Examples of GaN Devices for L Band

## Slide 11
GaN with High Vds => Simple Matching due to Higher Impedance

## Slide 12
GaN are Depletion Mode FETs
Require negative gate bias to pinch off channel to cutoff drain current
Less negative bias increases Iq to operating level
Zero bias with drain voltage applied can kill transistor
Disadvantage compared to LDMOS, needs bias controller

## Slide 13
SSA Progress
Three year project funded by Laboratory Directed R&D to determine if SSA is feasible for megawatt-level pulsed PA
SSA should fit in space of a Klystron/HV modulator tank; need high power density
Engineering team formed from multiple groups, new SSA laboratory
Trade study of amplifying devices, accelerators using SSA, combining topologies
System simulations underway
Eight 3.6 kW SSA test boards acquired
Working with GaN transistor and combiner/circulator manufacturers
“2024 Overview of Solid-State RF Amplifiers for Accelerators”, Lyles, Internal Colloquim, LA-UR-24-22830

## Slide 14
GaN on SiC RF Transistors
425 MHz GaN, 800 Watts, for another project in 2020
805 MHz GaN, 3.6 kW, 100 Volt Vds

## Slide 15
Integra Technologies GaN/SiC Architectures
Transistor for 805 MHz SSA is Gen4 where 5 kW Psat device expected to operate at ~15W/mm power density for it’s gate periphery. Expected channel temp 170-185 deg C. (225 deg results in 1 x 106 hour lifetime in GaN).

## Slide 16
Some High Power Combiners
Proposed Spring 8 SSA
SPS 200 MHz 1.6 MW prototype
Werlatone Design
R&K Design

## Slide 17
Present Baseline Design
Only output combining shown, 72 blades or pallets used plus driver architecture

## Slide 18
Spreadsheet Analysis of Gain Distribution
Solid State Amplifier Configuration Planner |  |  |  |  | 3 stage (11 dB < gain < 19 dB)
 |  |  |  |  | Notes
Output Power from LLRF | 6.9 | Watts | 38.39 | dBm | 10-200 Watts
Number of Driver Modules | 2 |  |  |  | 2 drive modules for out-phasing
Driver Splitter Insertion Loss | 0.95 |  | -0.20 | dB | 
Driver Module input Power | 3.29 | Watts | 35.18 | dBm | 
Driver Module Gain | 63.10 |  | 18.00 | dB | 
Driver Module Power Rating | 5000 | Watts | 66.99 | dBm | 
Driver Output Power | 207.88 | Watts | 53.18 | dBm | 
Stage 2 Divider Ports | 1 |  |  |  | 
Stage 2 Divider Insertion Loss | 0.93 |  | -0.30 | dB | includes 4-way in pallet
Stage 2 Driver Module input Power | 194.01 | Watts | 52.88 | dBm | 
Stage 2 Driver Gain | 63.10 |  | 18.00 | dB | 
Stage 2 Driver Output Rating | 20000 | Watts | 73.01 | dBm | 4 - amp pallet
Stage 2 Driver Output Power | 12241.06 |  |  |  | 
Stage 3 Divider Ports | 38 |  |  |  | 
Stage 3 Divider Insertion Loss | 0.93 |  | -0.30 | dB | includes 4-way in pallet
Stage 3 Driver Module input Power | 300.63 | Watts | 54.78 | dBm | 
Stage 3 Driver Gain | 63.10 |  | 18.00 | dB | 
Stage 3 Driver Output Rating | 20000 | Watts | 73.01 | dBm | 4 - amp pallet
Stage 3 Driver Output Power | 18968.61 |  |  |  | 
Stage 4 Power Combiner Ports | 38 |  |  |  | 
Stage 4 Power Combiner Insertion Loss | 0.98 |  | -0.10 | dB | 
Stage 4 Power Combiner Output Power | 704399.6 |  |  |  | 
Final Combiner Ports | 2 |  |  |  | 
Final Combiner Insertion Loss | 0.98 |  | -0.10 | dB | 
Final Output Power | 1408799.2 |  |  |  | 
Input Divider | 76 |  |  |  | 
Output Combiner | 76 |  |  |  | 
Total Gain | 199526.23 |  | 53.00 |  | 

## Slide 19: GaN Thermal Measurement at Integra Technologies
Thermal measurement performed at worst case conditions
  This is for another transistor, not 805 MHz
  Worst case power dissipation of 1.87kW
  Flange temperature = 85°C
  Transient infrared detector used to capture peak temperature during RF pulse
This property of Class AB amplifiers can kill transistors during power rollback

## Slide 20: Varying CCL power requirements at different locations
Turning down drive power is a concern for Class AB SSA devices
When conditioning a CCL cavity
Ramping up power slowly
During accelerator beam tuning
Normal uneven RF power distribution along linac from physics tune
Fast power fluctuation for beam loading
Need about 12 dB of output dynamic range for these situations

## Slide 21: Techniques for Variable Power that Avoid High Drain Pdissp
Reduction of Vds below 100 V to keep high efficiency at lower power
  20% is safe but it cannot be fast with large power converters
  How would it be automatic?
Turning off pallets before combiner
  Must account for reverse power to other pallets
  Modeling is being done to understand which ones are best
  Difficult to remove RF driver power but can raise gate bias to disable output
Outphasing modulation for fast control, beam compensation

## Slide 22
Outphasing Modulation
“Not Just a Phase”, Barton, IEEE Microwave Magazine, Feb. 2016
“High power outphasing modulation,” Chireix, Proc. IRE., vol. 23, no. 11, Nov. 1935

## Slide 23: Outphasing Amplifier
  Outphasing amplifiers run at constant power at Psat, highest efficiency
  A binary pair of PAs operate constant envelope -,driven hard, while phase modulation is applied to both input signals
  If one PA is +90 and other is -90 deg, combined output is zero power; If both PA are in-phase, then combined output is 2 times one PA
  The combined output is a linearly amplified replica of the desired input yet uses two nonlinear PAs
  The load impedance to each PA varies from 25 Ohms (when in phase) to infinity (when out of phase and zero combined output). Add circulators for each PA to isolate transistors from this wildly varying load.
  RCA commercialized outphasing in AM broadcast transmitters in 1954 using tubes
“The Circuit Development of the Ampliphase Broadcasting Transmitter”,Price, Proc IEE, 1954

## Slide 24: Improved Efficiency Outphasing Amplifier
  We ran Matlab-Simulink comparisons of varying phases and amplitudes of the binary amplifier pair by +/-5% and +/-5 deg to understand effect on outphasing PA
  With circulators for each PA to isolate transistors we end up with an overall amplifier that is similar to a klystron, constantly delivering power to either RF or to the circulator loads.
  Techniques to reuse this wasted load power would raise system efficiency
    Convert RF load thermal heat to electricity, or rectify RF back to DC to the bus
“A Power Re-Use Technique for Improved Efficiency of Outphasing Microwave Power Amplifiers”,Langridge et al., IEEE Trans MTT, August, 1999
“Analysis of Power Recycling Techniques for RF and Microwave Outphasing Microwave Power Amplifiers”,Zhang et al., IEEE Trans Circuits and Systems II, May, 2002
“Efficiency of Outphasing RF Power Amplifying Systems”, Raab, IEEE Trans Communications, October ,1985

## Slide 25
Outphasing with Regenerated Power

## Slide 26
Planned Work in FY25-26
Development of long pulse GaN on SiC packaged transistor, 5 kW Psat
  Wafer fab with mask to provide multiple devices with up to 4 wafers
  Packaged transistors qualified, tested, provided to LANL for testing
Refine SSA architecture, add ADS simulation with variation of passive parameters
Determine peak and avg power rating for connectors and cables on blades
Determine prime AC/DC power system architecture, stored energy location
Prototype 20-40 kW blades in lab using water-cooled plates and chiller
Develop commercialization plan
Scaled prototype to a hundreds of KW with WG circulators and magic tee