## Slide 2: Status and operational readiness of the ESS RF Systems
PRESENTED BY Morten Jensen on behalf of the RF Group

## Slide 3: We will miss you Mats
Mats Lindroos passed away in May, after a long time of illness.
This fills us with deep sadness.
Mats was among the first to join the ESS initiative in 2009, bringing his expertise in accelerators together with an abiding passion for science to the service of the organisation and the many colleagues that he has led and worked with over the last 15 years.
Mats was relentlessly working for the ESS, a job that he embraced with his mind and his heart.
We owe him a lot and in particular to realise his dream.

## Slide 4: Content
ESS and RF Overview
Operational Experience
    Window Conditioning
    Warm Coupler Conditioning
    HP issues on TS2
    Update on new test stands

## Slide 5
ESS and RF Overview

## Slide 6: Accelerator Overview
Key parameters:
Average Beam Power: 5 MW
Peak Beam Power: 125 MW
Beam pulse width: 2.86 ms
Beam energy: 2 GeV
Final Beam current: 62.5 mA peak
Repetition rate: 14 Hz
352 MHz
704 MHz
2024-09-08
3 MW Klystrons
200 kW Tetrodes
30 kW Solid State Amplifiers
ISrc
LEBT
RFQ
MEBT
DTL
SPK
MBL
HBL
HEBT
Dump
Target
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
User mode (2 MW)
Early Beam commissioning
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
1.5 MW Klystrons
6
 | RF Systems | High Power Technology | Peak RF Output Power | Average Beam power
RFQ | 1 | Klystrons | 3 MW | 
MEBT | 3 | SSPA | 30 kW | 
DTL | 5 | Klystrons | 3 MW | 
Spoke | 26 | Tetrodes | 400 kW | 
MB | 36 | Klystrons | 1.5 MW | 
HB (p1) | 20 | Klystrons | 1.5 MW | 2 MW
HB (p2) | 24 (later) | Klystrons | 1.5 MW | 3 MW*
HB (p3) | 40 (later) | Klystrons | 1.5 MW | 5 MW*
* Not yet funded

## Slide 7: CWRF 2022
As reported previously:
NCL done
Spoke just starting
Approx 1/3rd MB done
HB not started

## Slide 8: G02 – Status of RF Systems Aug 2024
Ready for Beam on Target (RBOT) Baseline
RACKS
1
RACKS
4
2
3
M2
4
1
3
2
M3
MBL-020 Cell 160 – MBL-030
RACKS
1
RACKS
4
2
3
M4
4
1
3
2
M5
RACKS
4
1
3
2
M1
RACKS
1
RACKS
4
2
3
M6
4
1
3
2
M7
RACKS
1
RACKS
4
2
3
M8
4
1
3
2
M9
RACKS
020-s1
RACKS
CELL 120
010-s1
030-s1
020-s2
010-s2
030-s2
RACKS
060-s1
RACKS
CELL 130
050-s1
080-s1
070-s1
060-s2
050-s2
080-s2
070-s2
RACKS
100-s1
RACKS
CELL 140
090-s1
120-s1
110-s1
100-s2
090-s2
120-s2
110-s2
RACKS
130-s1
RACKS
CELL 150A
130-s2
RACKS
RACKS
RACKS
M1
M2
K1
K2
K3
K4
M3
K5
K6
B1
B2
B3
CELL 100/110
NCG + SPK
MB
#
#
#
#
Installation on-going
Installation complete ready for test
Low Power Tested
High Power Tested
352.21 MHz
704.42 MHz
#
Special test
TS2
M2
K1
K2
040-s2
040-s1
Cell 150 – MBL-010
MBL-040 Cell 170 – MBL-050
MBL-060 Cell 180 – MBL-070
MBL-080 Cell 190 – MBL-090
ESS-4726471
Thales klystron testing
CPI klystron testing
System used for window testing
NCL: Klystron@3 MW
Bunchers: SSPA@30 kW
SPK: Tetrodes@400 kW
MB: Klystron@1.5 MW
HB: Klystron@1.5 MW
RACKS
1
RACKS
4
2
3
M1
4
1
3
2
M2
RACKS
1
RACKS
4
2
3
M3
4
1
3
2
M4
RACKS
1
RACKS
4
2
3
M5
4
1
3
2
M6
RACKS
1
RACKS
4
2
3
M7
4
1
3
2
M8
RACKS
1
RACKS
4
2
3
M9
HB
2024 2 MW Capable
HBL-010 Cell 200 – HBL-020
HBL-030 Cell 210 – HBL-040
HBL-050 Cell 220 – HBL-060
HBL-070 Cell 230 – HBL-080
HBL-090 Cell 240 – HBL-100
RACKS
1
RACKS
4
2
3
M11
HBL-110 Cell 250
4
1
3
2
M10
Post BOT Scope 3 MW
704.42 MHz
Canon klystron testing

## Slide 9
180 degree view of Gallery
Total of 91 High power RF Systems, MO, and PRL incl all controls, interlock, aux and LLRF. Approximately 245 racks, > 21000 cables

## Slide 10: Huge Installation largely complete and tested
RFQ and DTL klystrons
MB Klystrons
MB/HB Klystrons
MB/HB Klystrons

## Slide 11: Commissioning
Phase 1: 2 MWavg beam power on the target
To date we have run beam up to DLT 4
Next
Beam-on-Dump Feb 2025
Beam on target Autumn 2025
User Operation January 2028

## Slide 12
Operational Experience

## Slide 13: CWRF 2022
Please refer to the specific talks in 2022 for:
ESS arc-detector systems, development and experience
Tomas Olsson
RF distribution systems at ESS
Walther Borg
MEBT Installation, test, performances and operation at ESS
Bruno Lagoguez

## Slide 14: Other ESS talks at CWRF 2024
Talk on High Power Loads: Walther Borg
Talk on high power klystron testing: Patrick Krämer
Talk on the 400 kW SSPA development: Dragos Dancila

## Slide 15: Window Conditioning
Windows for DTLs delivered by INFN to warm linac group.
Early operation of DTL2 and 4 showed issues with arcing and MP.
Inspection shows melting of the o-ring, multipacting and relatively high pressure.
Window test schematic
Window mounted below DTL Tank

## Slide 16: Window Conditioning
RF system for DTL 5 was reconfigured and a test stand was constructed
Back-to-back window assembly
DTL5 3 MW RF System

## Slide 17: High-power tests @ ESS -1st phase
Large outgassing below 500 kW, light, vacuum and reverse power effects - Initially conditioned away.
But at 40us pulses the window started to worsen. Ramping 10-1000 kW @14Hz.
Two key technical issues:
Poor vacuum and melting of the o-ring
TIN coating most likely too thin
S/N 2056606 (report just one window test as example)
Courtesy of Francesco Grespan
Green = light
Pressure
Power
Ramp
10 ‘good’ windows available for operation. More on order or being refurbished.

## Slide 18: Warm Coupler Conditioning
For technical details of the Spoke Power stations
See CWRF 2022,
Radio Frequency RF Power Stations at ESS Rutambhara Yogi
Warm Coupler Conditioning (WCC) brought forward
Needs RF to the tunnel before Personal Safety System ready
Is it safe?
Cavity are naturally detuned
Ensure that the RF frequency does not match the cavity resonant frequency
Installation of narrow band pass at nominal frequency
Setup local monitoring and exclusion zone
Filter provides around 60 dB attenuation at warm cavity resonance

## Slide 19: First WCC in open tunnel
SRF/RF/LLRF/ICS/OPS/RP
It took months to make the safety case and have it approved
but finally the conditioning was quick.
All 26 spoke cavities conditioned and MB started

## Slide 20: 704 MHz circulator arcing
56 circulators circulators installed and operational on MB and HB
2 units on Test Stand 2
Circulators on MB started to suffer from occasional, apparently random arcing
Investigation started:
Multiple visual inspections – no obvious signs
Cleaning seemed to work – but not for long
Temperature dependence?
Humidity dependence – deliberately increased humidity
Where was the arc originating?
  Designed and built multiport viewer
  Added viewing port to taper
Circulators on TS2 had been operational for several years without incident, until
Sudden arcing on the circulator. Initially conditioned up and ran for weeks again
Then came back and did not recover.
New visual inspection

## Slide 21: 704 MHz circulator arcing
No obvious signs until small marks noticed on tuning post
Decision to remove post, but
bolts had gauled. Had to be cut.
Not possible to replace bolt due to poor access.
Finally machined new threaded hole post.

## Slide 22: 704 MHz circulator arcing
Immediately inspected other circulators on MB which were arcing.
Similar arcing noticed.
Re-tightened bolts on MB and HB systems with occasional arcing but many bolts have gauled.
New posts manufactured and ready for deployment.
Since intervention, no further arcing
Take care if you have similar devices

## Slide 23: VPD – Variable Power Divider
Rated for 1.5 MW full reflection but typically operate at lower power
Designed to allow one input to be split into two outputs
Phase adjustment allows for any power split or option to supply either output.
Two units installed, but only one unit getting hot.
However, when re-testing the circulator on TS2 noise heard from the Variable Power Divider and it one arm was getting warm!
No arc detection installed on the side branch.
Power in
Power out

## Slide 24: VPD
Arcs on the “buckets”
Spacers severely burnt

## Slide 25: VPD
5 mm spacer
Damaged WG
Waveguide severely burned
  Urgent clean up and damaged waveguide replaced with a ‘standard’ section of waveguide plus a new spacer
Installed additional arc detection

## Slide 26: New Test Stands
Soon future test places become limited:
TS2 in continuous use for cryomodule testing
Other systems needed for beam
Long term plan is to construct a full SRF facility including test benches for each type of RF system
  Testing and conditioning of:
  Klystrons
  RF windows and couplers
  RF loads
  Spares, upgrade procurements, technical issues
Short term

## Slide 27: New ‘temporary’ Test Stands
352 MHz, 3 MW capable
704 MHz, 1.5 MW capable
S1: CPI
S4: Canon
S2 and 3: Thales
Re-configurable with floor space.
Pre-installed klystron setup for rapid testing of new klystrons

## Slide 28: New Test Stands
352 MHz, 3 MW capable
704 MHz, 1.5 MW capable
S1: CPI
S4: Canon
S2 and 3: Thales
Re-configurable with floor space.
Pre-installed klystron setup for rapid testing of new klystrons
Any Questions?