## Slide 1: Status update and operational experience of the 200 MHz SSPA system for the CERN SPS
Sam Pitman on behalf of the entire SY-RF-AC section
09-12 September 2024 – Thirteenth CW and High Average Power RF Workshop

## Slide 2
Contents
  Introduction
  Early Life Failures
  Notable Events
  Obsolescence
  Conclusions

## Slide 3: SPS – Super Proton Synchrotron
SPS – 1976 (7 km)
LHC Injector also North Area, AWAKE, and HiRadMat
SPS-LIU Project presented in 2022
High power RF for the SPS was upgraded for HL-LHC
Cavities were re-arranged in the tunnel
New SSPA system was installed to power two cavities
Chart: 

## Slide 4: RF Cycles in the SPS
3.2
10.8
21.6 s
10 kW
750 kW
7.6
0
LHC
1.8
1.2
3.0
2.2
8.2 s
16.2 s
3.4
9.6
3.2
9.8 μs / 23.04 μs (43.4 kHz) or
2.75 μs / 5.76 μs (173.6 kHz)
SHIP
FT
Average power limited to 750 kW due to 350 mm coaxial lines
1600 kW
This kind of cycling is a killer for the RF power amplifiers

## Slide 5: Layout
Above Ground
Tunnel

## Slide 6: 2x Transmitters
One Transmitter is composed of
  16 x 160 kW RF amplifiers
One RF amplifier is composed of
  1:80 cavity splitter
  80 x 2 kW RF blocs (160 transistors)
  80:1 cavity combiner
In total
  Two transmitters
  32 RF amplifiers
  2560 RF blocs
  5120 transistors
From Beam Control
1/16 splitter
Cavity
Transmitter Layout

## Slide 7: Thales System Architecture
Thales Tower
LLRF
Pre-driver
2 kW RF 01
2 kW RF 80
Output combining cavity
80 * 2 kW : 1 * 160 kW
Input distribution cavity
1 * 1 kW : 80 * 12 W
Hybrids
80 * 2 kW modules
Relays to decouple broken modules
Note: Circulator free system

## Slide 8: Thales System Architecture
80 x (2 x 1) kW
modules total
1:80 cavity splitter
320:1 cavity combiner

## Slide 9: Hybrids
To Cavity
Notes: 90 degree quadrature hybrids
Directional couplers

## Slide 10: Early life failures

## Slide 11: Timeline of Transistor Failures
Chart: Module Failures
| 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105 | 44136 | 44166 | 44197 | 44228 | 44256 | 44287 | 44317 | 44348 | 44378 | 44409 | 44440 | 44470 | 44501 | 44531 | 44562 | 44593 | 44621 | 44652 | 44682 | 44713 | 44743 | 44774 | 44805 | 44835 | 44866 | 44896 | 44927 | 44958 | 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261 | 45292 | 45323 | 45352 | 45383 | 45413 | 45444 | 45474 | 45505
Cavity 3 | 1 | 8 | 0 | 0 | 8 | 1 | 2 | 0 | 3 | 1 | 1 | 2 | 3 | 5 | 3 | 2 | 3 | 10 | 16 | 32 | 27 | 28 | 29 | 46 | 1 | 31 | 14 | 36 | 29 | 49 | 67 | 47 | 10 | 4 | 33 | 77 | 74 | 71 | 70 | 25
Cavity 6 | 0 | 1 | 1 | 4 | 4 | 10 | 1 | 1 | 2 | 14 | 18 | 12 | 0 | 18 | 45 | 14 | 4 | 5 | 2 | 27 | 21 | 11 | 9 | 0 | 9 | 14 | 7 | 20 | 28 | 25 | 42 | 16 | 8 | 6 | 13 | 12 | 12 | 59 | 45 | 16
Cumulative | 1 | 1 | 1 | 1 | 10 | 11 | 11 | 11 | 11 | 11 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 27 | 27 | 38 | 41 | 42 | 47 | 62 | 81 | 95 | 95 | 98 | 121 | 169 | 185 | 192 | 207 | 225 | 284 | 332 | 371 | 409 | 455 | 455 | 465 | 510 | 531 | 587 | 644 | 718 | 827 | 890 | 908 | 908 | 908 | 908 | 918 | 964 | 1053 | 1139 | 1269 | 1384 | 1425
SPS cold checkout
MTEbeam nominal to SPS & LHC 25ns
AWAKE Beam water problems
LIU parallel MD and LHC ions setting up flow monitoring all ok
Ions to SPS & SFT_pro intensity between 2.7E+13eV to 3.3E+13eV
Cavity 3 Conditioning
Cavity 6 Conditioning
SPS Beam commissioning & scrubbing run polar loop instabilities
Collars modification & matching steps & new air-outlets on Cav 6
Collars modification on Cav 3 & Cav 6
Broken Load on H1-04
Cavity 6 Conditioning
Cavity 3&6 Conditioning & Scrubbing run
Scrubbing run
Half towers not driven Cav 6
HOM Coupler burned Cav 3
Notes: Normal infantile mortality in first 18 months
Some towers have high failure rate and some low.
More failures seen during certain cycles such as AWAKE (High peak power AM)
Cavities exchange positions

## Slide 12: Towers have different failure rates
Cavity 3
Cavity 6
Chart: Tower
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Faults | 5 | 6 | 5 | 173 | 55 | 23 | 3 | 9 | 17 | 87 | 10 | 38 | 33 | 64 | 6 | 24
Chart: Tower
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Faults | 169 | 51 | 70 | 50 | 70 | 13 | 7 | 52 | 25 | 35 | 49 | 4 | 43 | 128 | 53 | 53

## Slide 13: Difference in line length to hybrid
Cavity 3
Cavity 6

## Slide 14: Reverse Power
Cavity 3 -14 dB
Forward power Reverse power
Cavity 6 -20dB
Notes: Go deeper on the power levels in dB return loss – db
10dB – 10%
14dB – 4%
20dB – 1%

## Slide 15: Notable Events

## Slide 16: Thermal Paste
Thermal paste was introduced to the cooling system
This blocked the cooling channels of the transistors and caused overheating
System was flushed of impurities
Uncertain if there are still blockages causing problem
We still see burned transistors
Transistor Cooling Channels
Cleaning System Water Filter
Water Cleaning System

## Slide 17: Scrubbing
A scrubbing beam is a high intensity beam sent to clean the vacuum surfaces
14 Modules broken within 30 minutes on one cavity
30 broken in the event
Reflected Power?
Was cooling disturbed?
Scrubbing run vacuum signals over 4 days
Notes: Broadband Beam
The intention is to outgass
Peak is around 4e-6

## Slide 18: Bad connection
Connection from transistor to cavity combiner
C-type connector on 10240 connections
One was poorly connected
Up to 1kW can pass through these connections
Module broken as a result
Interlock is difficult to implement
Notes: Human error

## Slide 19: Technical stop event
A connection error lead to the LLRF signal being missing on one half of system
Some towers were full power and some zero
This was very unbalanced due to the integration
T26 first lost 13 modules
Then the load broke
Next the final load broke
Finally the signal was re-established to the other towers
Around 100 modules broken as a result of this event
32
31
29
27
25
23
28
30
21
19
17
18
20
22
26
24
Notes: Interlocks were re-established afterwards

## Slide 20: Broken load
A broken load has previously been discovered to result in many module failures
High failure rate on T14 even with very low power
Shares a hybrid with T12 (one of the most stable running at more than 10 times the power)
The high power load on the hybrid between the towers was seen to be leaking water
After removal it was dismantled to find it had been arcing
Not a single module lost on T14 since even after increasing the power*
Notes: Remember the broken load from the history plot
**disclaimer about the modules.

## Slide 21: Short circuit test
6-1/8 line with 6 planes each with 3 fingers
every 5 seconds for one hour under various phase and power conditions
RF switch was off 100 ms after reverse was detected, in operation, it will be 1 ms maximum
Not having a circulator was THE challenge (I thought…)
It was fully successful, not a single module failed, the test was ok

## Slide 22: Obsolescence
In 2015 NXP said plastic transistors were best for design
Beginning of 2022 last buy order warning within 6 months
When you move to transistors big science isn’t always the priority to suppliers
Obsolescence is a concern – do not count on suppliers to supply your project for its lifetime
When a design a system you must procure a lifetimes supply of transistors
Do transistors degrade on the shelf?

## Slide 23: Ceramic transistors
We have procured a compatible ceramic transistor design
We have been testing them for some months in T12
No failures yet
When validated we aim to secure enough transistors for the future
Test bench is being recommissioned to do accelerated life tests with enhanced diagnostics
SSPA Module Test Bench

## Slide 24: Conclusions
Interlocks – balance between stable operation and protecting system.
Despite all the problems we have had 99.9% availability
Although failure rate is high now, we are ironing out the problem
Once robustness is demonstrated Transistors can be considered for FCC
Conclusions

## Slide 25
Thanks to all my colleagues and the meaningful collaborations who have contributed to this work.
Questions