## Slide 1
13th CWRF Workshop
John Moss
Spallation Neutron Source HPRF Sources – Past, Present, and Future

## Slide 2: The Spallation Neutron Source relies heavily on klystrons – which are difficult to fabricate and operate – as its high-power RF source. Are there viable alternatives?
To help answer that question we will discuss:
Present SNS High-Power RF sources
A Brief Glimpse of the Past
Why klystrons?
Recent Experience with Klystrons
The Future of SNS High-Power RF Sources

## Slide 3: Present: There are 131 distinct high power RF systems across the SNS complex.
FE RF Systems:
Ion Source (2)
RFQ
MEBT (5)
NC RF Systems:
DTL (6)
CCL (4)
SC RF Systems:
Medium Beta (33)
High Beta (76)
Ring RF Systems (4)
At present there are 3 solid state, 4 tetrode, and 124 klystron-based RF sources used to accelerate an H- beam and accumulate protons

## Slide 4: Present: There are eight high power RF sources for the front-end systems.
.
600W, 13MHz CW
80kW, 2MHz Pulsed
20kW x 4 (+1), 402.5MHz Pulsed
SOLID STATE
2.5MW, 402.5MHz Pulsed

## Slide 5: Present: The highest peak RF power levels at SNS are in the normal conducting Linac.
Six 2.5MW, 402.5MHz pulsed systems
Four 5MW, 805MHz pulsed systems
Frequency increase to 805MHz
In the normal conducting linac, the beam energy is relatively low and there is only one klystron per system. This creates a bottleneck that is important to note – we cannot bypass any of the cavities in the event of a high-power RF source failure.

## Slide 6: Present: The bulk of the high-power RF systems at SNS are in the superconducting linac – 109 of the 131.
Medium Beta - 33
550kW, 805MHz pulsed systems
High Beta - 76
550-700kW, 805MHz pulsed systems
The superconducting linac is more flexible. The beam energy is higher and there are 3 – 4 klystrons per cryomodule. Here, we can bypass up to 3 cavities (and the associated klystron) with no loss in energy.

## Slide 7: Present: The Ring high-power RF systems are used to counteract space charge as the protons are accumulated.
1MHz – 2 500kW pulsed systems
2MHz – 2 500kW pulsed systems
x4

## Slide 8: Glimpse of the Past: The SNS RF systems first started operation in the early 2000s.
…but the rest of the accelerator is essentially the same – vacuum-tube-based – and primarily klystrons.
RF sources in the front end have changed since the start…

## Slide 9: Glimpse of the Past: Historically, Klystrons are the single largest source of HPRF downtime, in terms of frequency.
Chart: Sources of HPRF Downtime Since 2013
| Klystrons | AC Power Supply | Amplfier | DC Power Supply
Sales | 8.2 | 3.2 | 1.4 | 1.2
Output RF Instabilities
Cathode Overcurrent

## Slide 10: Why klystrons? Part of the answer is power levels.
1.7MW today
2.0MW in 2026
SNS is only increasing in beam power, requiring more (~hundreds of kW, peak) high power RF with each step.

## Slide 11: Why klystrons? In short, infrastructure, age of our operating tubes, and spares.
Linac Segment | In Operation | Spares (Untested)
RFQ/DTL | 7 | 1(+2)
CCL | 4 | 1
SCL | 109 | (39)
Longest operating klystrons in these segments have ~ 100,000 filament hours
Longest operating klystrons in this segment have ~ 70,000 filament hours
In addition to the power levels, to move to a new high-power source would require major changes to infrastructure.
The spares situation also requires that we engage klystron vendors – which we have been doing since 2018. Remember the bottleneck in the NCL. Developing klystrons here is imperative!

## Slide 12: Why klystrons? The near future of SNS relies on stable klystron sources – both in fabrication and operation.
Awarded contract in 2018. 3 of 3 klystrons delivered.
Awarded contract in 2018. 1 of 4 klystrons delivered.
Awarded contract in 2018. 28 of klystrons delivered.
5MW
3MW
770kW

## Slide 13: Recent Experience: Fabrication of large klystrons has proven to be difficult...
Collector failed pressure test on the first article
Vacuum leak discovered on first cavity during bakeout.
High perveance on first article led to low peak output power
All 3 klystrons show persistent ”micro-discharge” on the cathode current. Micro-discharge prohibited operation on 2/3.
Persistent vacuum leaks on first cavity led to the redesign of the structural support.
Incorrect radius on first article cathode led to low perveance and low output power
5MW
3MW

## Slide 14: Recent Experience: …and stable operation…
Cathode “micro-discharge” on 3/3 klystrons. Removed from operation in CCL-1 in August 2024 after significant vacuum degradation. Returning to vendor.
5MW
Instantaneous 5A “spike” in klystron beam current

## Slide 15: Recent Experience:... even more so.
Vacuum leak. Removed from DTL-3 in May 2024. Will be returned to vendor.
3MW

## Slide 16: Recent Experience: Stable operation has even been elusive on the lower power tubes.
Removed 4 out of 28 klystrons from HV for repeated cathode arcing. Three returned to vendor.
770kW

## Slide 17: Future: SNS relies on 124 tubes, but we are open to better sources or power delivery schemes. Other options?
?
Potential for combining of lower power tubes for greater flexibility
Potential for solid-state in SCL and Ring

## Slide 18: Conclusion: The Spallation Neutron Source relies heavily on klystrons – which are difficult to fabricate and operate – as its high-power RF source. Are there viable alternatives?
?
There are viable alternatives long-term (10 years). Near term, SNS must continue to focus on the continued development of high-power klystrons for use in the normal conducting segments of our linac. As of today, we are > 6 years into that development.

## Slide 19: In keeping with CWRF tradition, here is a picture of a burned second cavity load connection on a 2.5MW klystron.