## Slide 1: Installation Of New Solid-State Amplifiers For CEBAF’s Pass 5 Extraction Cavities
Mark Wissmann, Curt Hovater, Larry Farrish, Rick Nelson, Mike Spata,Young-Min Shin
May, 2024

## Slide 2: Outline
A Brief CEBAF Separator History
  • Three Energy Changes
  • RF Separator Changes
Operational Challenges Along The Way
• Power limit of components, cables & cavities
• Single HVPS for all four IOTs
  • Vector Sum Control
  • Cavity to Cavity Phasing
  Rationale For Switching
  • DC Power Supply
  • Easier Phasing
  • Quick Recovery

## Slide 3: Two Beam Energy Upgrades
  • Originally designed as a 4 GeV Accelerator
  • Operating up to 6 GeV 2004 – 2012
  • 2014 Started Operations with 12 GeV Beam
Two 0.5 GeV linacs

## Slide 4: CEBAF Extraction History
• 1998 - Delivery of 4 GeV Beam simultaneously to three experimental Halls
• 2004 to Spring of 2012 delivered up to 6 GeV electron beam to three Halls
simultaneously
- 2004 investigation of using Inductive Output Tubes (IOTs) started
- 2008 replaced 1 kW SSAs with IOTs to amplify 499 MHz to cavities
• 2014 to present – simultaneously up to 11 GeV to halls A, B, & C
and 12 GeV to Hall D
- converted and tuned Pass 5’s IOT from 499 to 750 MHz

## Slide 5: 4 - 6 GeV Separator Cavity Power Source
SSA AMPS PASS 1 – 5 Horizontal
Pass 1
Pass 3
Pass 4
Pass 5
RF Separators
Septa Magnets
YAs YBs
Hall A
Hall B
Hall C
Lambertson
Pass 2
1kW design – Combined 2 to operate Pass 2
Configuration until ~2004
2004 – 2008 replaced SSAs with Inductive Output Tubes (IOT)
- Transistors became obsolete
- Reliability problems with increased power requirements
- Future 12 Gev power requirements (>10000 kW)

## Slide 6: 20012 – 2014 CEBAF 12 GeV UPGRADE
CHL-2
Two 1.1 GeV linacs
Added 4 750 MHz Horizontal Cavities
Added 4, 499 MHz Vertical Cavities

## Slide 7: 12 GeV Separator Cavity Power Sources
Pass 1
499 MHz Cavities
750 MHz Cavities
499 MHz Cavities
RF Separators
Septa Magnets
YAs YBs
Hall A
Lambertson
Hall B
Hall C
Hall D
Pass 2
Pass 5
Pass 4
Pass 3
IOT Amps Pass 2-5 Horizontal
SSA Pass 1
10 kW SSAs Pass 5 Vertical

## Slide 8: Power and Energy
Energy Pass 1 (GeV) | RF Power Pass 1 | Energy Pass 2 (GeV) | RF Power(W) Pass 2 w/ One Cavity | Less power needed for Pass 1 (dB)
0.86 | 141 | 1.66 | 525 | -5.71
1.16 | 256 | 2.26 | 973 | -5.79
2.24 | 956 | 4.42 | 3720 | -5.90
6 GeV Energy/Power
12 GeV Energy/Power

## Slide 9: RF Power Requirements
12 GeV Extraction: RF Power Requirements (x’ = 200 mrad) Calculated |  |  | 
Pass | Number of Cavities | Energy (MeV) | Power per Cavity (W)
1 | 1 | 2281 | 991
2 | 2 | 4441 | 939
3 | 2 | 6601 | 2074
4 | 3 | 8760 | 1624
5 | 4 | 10920 | 1420
Power Per Cavity (W)
850
1230
2800
2100
2000
Actual

## Slide 10: Operational Challenges
1. Power limit of components, cables & cavities
2. Single HVPS for all four IOTs
  3. Vector Sum Control
  4. Cavity to Cavity Phasing

## Slide 11: Op Challenge #1: Power Limit of Components, Cables & Cavities
• 1st SSAs – 1 kW
• Phase Shifters, Circulators, Couplers – 5 kW
• Cavities: 499 MHz – 5 kW, 750 MHz – 3 kW
1 kW SSAs
Phase Shifter
Circulator

## Slide 12: Cable Burns

## Slide 13: Cables – LDF7 & Rigid Line Power Specs

## Slide 14: Op Challenge #2: Single HVPS
One HVPS powers all four IOTs – If it goes down, Beam Separation from Passes 2-5 down

## Slide 15: Op Challenge #3 Vector Sum & Resonance Control
Resonance control system to maintain cavity frequency
Requires one heater module per cavity
Mixing valve and Cavity Resonance Monitor
Cavity
Coupler
Splitter
Cavity
Cavity
Phase
Shifters
LLRF
Controls
RF Amplifier
Combiner
Transmitted Power
Forward Power
Reflected Power
Transmitted
Power
Circulators
LCW
Supply
Mixing
Valve
LCW
Supply
Heater
Cavity Resonance Monitor
Resonance Control System
Heater Modules

## Slide 16: #3 Vector Sum Control
• One SSA (IOT) to four Cavities (Pass 5) to one FCC
• All cavity’s gradients vector summed together
• FCC (LLRF Controls) maintains this gradient
• Maintain all four cavities on resonance
Cavity
Coupler
Splitter
Cavity
Cavity
Phase
Shifters
LLRF
Controls
RF Amplifier
Combiner
Transmitted Power
Forward Power
Reflected Power
Transmitted
Power
Circulators
LCW
Supply
Mixing
Valve
LCW
Supply
Heater
Cavity Resonance Monitor

## Slide 17: Op Challenge #4: Cavity to Cavity Phasing
Pass 1
499 MHz Cavities
750 MHz Cavities
499 MHz Cavities
RF Separators
Septa Magnets
YAs YBs
Hall A
Lambertson
Hall B
Hall C
Hall D
Pass 2
Pass 5
Pass 4
Pass 3

## Slide 18
Pass 5: Old vs New
• One SSA to four Cavities (Pass 5) to one FCC vs One SSA for each cavity
• All cavity’s gradients vector summed vs Independent control each cavity’s gradient
• Cavity phasing mechanically vs cavity phasing from the FCC (LLRF Controls)

## Slide 20
2019 Downtime Stats
4.66
2.75
3.85
5.3
10.9
2.4
0
2
4
6
8
10
12
2019
Hours of Separator System Downtime By Month In 2019
Feb
Mar
Apr
Aug
Sept
0
June
July
2
2
5
5
6
6
0
1
2
3
4
5
6
7
2019
Number of Separator System Failure Incidents In 2019
Feb
Mar
Apr
June
July
Aug
Sept
0

## Slide 21: Rationale For New 750 MHz SSAs
  1. Reliability and power capabilities of SSAs are much improved so now viable.
  2. The 750 MHz cavities are more sensitive/responsive to resonance control. With each cavity powered through it’s own amplifier:
  • No longer one DC Power Supply for all amps
  • Now have individual Control of each cavity’s gradient vs vector sum method
  • Easier Phasing – cavity to cavity phasing done in each cavity’s FCC
  • Much Easier & Faster Recovery - <10 minutes vs >30 minutes/trip
Notes: On the highlights slide you mentioned that this was done with ARRA funds. They may miss that or they may not remember at this point. Please add the “part of ARRA project” into the first bullet.
In first bullet you mention “high power testing”. In the 2nd bullet you say “rf measurements”. My brain assumed you were talking about high-power “rf measurements”. I suggest you add “low-power” in the 2nd bullet.

## Slide 22: Planned Separator Cavity Power Sources 2025
IOT AMPS PASS 2 – 4 Horizontal
SS AMPS For PASS 5 VERTICAL
SSAs PASS 5
Pass 1
499 MHz Cavities
750 MHz Cavities
499 MHz Cavities
RF Separators
Septa Magnets
YAs YBs
Hall A
Lambertson
Hall B
Hall C
Hall D
Pass 2
Pass 5
Pass 4
Pass 3
SSA Pass 1

## Slide 23: New SSAs & Components

## Slide 24: Summary
  • IOTs will amplify 499 MHz RF to passes 2 through 4.
  • SSAs will amplify 499 MHz RF to pass 1 & 750 MHz to
  pass 5
  • Transistors to tubes back to transistors – Rick Nelson
  • The bottom line is expected reduction in accelerator down time.
  Thank You For Your Time

## Slide 25: Inside A Separator Cavity
Tuning Plate and Rods
Close up of Tuner Plate Studs

## Slide 26: Inside A Separator Cavity
Tuning Plate Removed

## Slide 27: IOT vs. Solid State Amp
Rick Nelson did pricing of IOTs earlier this year, had $325 k in procurements plus about 1.4 FTEs. That's for 2 IOT systems, fully separate from the existing systems. We had 60% rated efficiency for 10 kW. A single 50 kW supply wouldn't give us any margin in operating 2 IOTs, hence the dual HVPS and dual crowbars (55+55+16+16=142k alone).
Estimation of the costs Solid State Amp:
1 X 15kW @ 499MHz with 3 outputs = $115,000
Costs are for single unit – NEED 2 = $230,000
Or
4 x 10kW @ 499MHz with single output = $110,000
Costs are for single unit (NEED 4) = $230,000
Or
Estimation of the costs IOT Amp:
Hardware procurements = $325,000
Several support systems will need upgrading = 1.4 FTEs

## Slide 28: Present IOT Amplifiers
Existing HV Deck
RF IOTs & Equipment Rack

## Slide 29: Amplifier Power Requirement
Calculation:
Summary:
Number Of Cavities | Deflection (μrad) | Energy (MeV) | Shunt Impedance | PWR per Cavity(w)
4 | 260 | 11023 | 210 | 3260

## Slide 30
Resonance Control
PLC Controller
Heater System
Cavity Temp. vs. Frequency Response
Heater Module

## Slide 32
New TOMCO 10kW Solid State Amplifiers

## Slide 33
ΔHz/°C | TOTAL ΔHz | TOTAL ΔT(°C)
8000 | 165000 | ~21
Summary:

## Slide 34: Summary
Normal conducting solution requires 6 cavities
Cavity has been tested at the required power
Resonance Control System and RF Hardware match existing systems
New Solid State Amplifier instead of an IOT system
Ready to start procurement phase
Beneficial occupancy of building on 4/1/2013
Install cavities before the end of the LSD
Install hardware as soon as we get in building
Project complete by 4/1/2014
Questions?