## Slide 1: THE INTERLOCK SYSTEMS FOR HIGH POWER RF SSA SYSTEMS AT ARGONNE APS AND ATLAS
Yong Luo
CWRF 2024
On Behalf of A. Goel, D. Horan, T. Madden,
A. Nassiri, B. Popovic, G. Trento
Not for further Distribution without Permission. If distributed beyond attendees the slides will need to be re-reviewed for copyrighted materials.

## Slide 2: INTERLOCK SYSTEM
WAVEGUIDE SYSTEM: PRESENT WG AND WG after S36 SSA UPGRADE
RF DRIVE INTERLOCK CHAIN
MPS (MACHINE PROTECTION SYSTEM)
PSS (PERSONAL SAFETY SYSTEM)
PLC
PM (POWER MONITOR)
ATLAS ARIS (ATLAS RADIATION INTERLOCK SYSTEM) [SIMINAR AS APS ACIS]
SUMMARY
FUTURE WORK

## Slide 3: PRESENT WAVEGUIDE SYSTEM
3dB Hybrid and 50 Ohm Load
RF Test Station
S38 was removed for Bunch Lengthening System (BLS)

## Slide 4: WAVEGUIDE SYSTEM after S36 SSA UPGRADE (HYBRID MODE)
Four R&K 160KW SSA for Sector 36
RF2 will be removed

## Slide 5: RF DRIVE INTERLOCK CHAIN
RF drive will be muted when there is any interlock event detected/received by sub-systems
Besides the RF drive muting, SSAs will also be interlocked by putting them into Off (Standby) state when necessary
PSS
ACIS: Accelerator Control Interface System

## Slide 6
SR MPS SYSTEM – EXAMPLE (ONE CHANNEL/CAVITY)
D-LLRF
Primary MPS Fiber 1
Fiber to TTL Interface chassis W/ RF SSA SWs
PSS RF Relay
ACIS
PM
SSA 1
RF Drive
TTL (MPS TRIP)
Multiple Chassis
PSS Chassis and ACIS Relay Box:
D. Horan
PM: T. Madden and B. Popovic
Secondary MPS Fiber 1
Fiber to TTL Interface chassis W/ RF SSA Relays
SSA1 RACK A
SSA1 RACK B
Relay (On/Off),
Status Back from SSA Racks
Diode Detector Chassis
Copper to Fiber
Time Stamp
(Control System)
P Forward after D.C.
2 Fiber Outputs to each SR Sector (6 for 3 Sectors)
Each Cavity SSA System: 1 Time Stamp Output

## Slide 7: MPS RF MUTING SIMPLIFIED BLOCK DIAGRAM
Total 4 Channels
(4 cavities/sector)
The functions have been tested and verified.
DC power with redundance (not shown here)

## Slide 8: MPS RF MUTING FRONT PANEL
Front Panel
PCB board mounting holes
DC power switch
(24V DC from PLC)
Green LEDs: DC Power
Red LED: MPS Trip

## Slide 9: MPS RF MUTING BACK PANEL
Back Panel
4 SMA mounting holes for TTL signals to LLRF modules.
MPS Fiber Optical Signal In
4 SMA mounting holes
4 N mounting holes
DC Power Entry:
TB 3-Pin
24V DC from PLC

## Slide 10: PCB BOARDS: MPS LLRF and RF MUTING PCB
Main bd
Front bd

## Slide 11: MPS SSA CONTROL SIMPLIFIED BLOCK DIAGRAM
Total 4 blocks
(4 racks/sector). Output status is A&B for specific SSA
DC power with redundance (not shown here)
2 Switches in series for SSA ILK
SSA Status to PLC (newly added)
The functions have been tested and verified.

## Slide 12: MPS SSA CTRL FRONT PANELS
Front Panel
PCB board mounting holes
Green LEDs: DC Power
Red LED: MPS Trip or SSA Racks Off (Standby)
DC power switch
(24V DC from PLC)

## Slide 13: MPS SSA CTRL BACK PANELS
Back Panel
Eight 4 Pin Military Connectors
(Relay Interlock, SSA Rack Status)
MPS Fiber Optical Signal In
4 Fiber TX (Rack
Status) Out
DC Power Entry:
TB 3-Pin
Recently added:
SSA Status to PLC, TB 6-Pin
24V DC from PLC

## Slide 14: PCB BOARDS: MPS SSA CTRL PCB
Main bd
Front bd
Test
bd

## Slide 15: MPS DIODE DET. TIMESTAMP SIMPLIFIED BLOCK DIAGRAM
Total 4 blocks
(4 Cavities/sector)
DC power with redundance (not shown here)!
-9 dBm: Diode Det. ~ 1.9 V
(120KW after 80 dB atten.->
1.2 mW, ~1 dBm. After 10 dB atten. -> -9 dBm)
Gain is adjustable (in a range) for different power level
The functions have been tested and verified.

## Slide 16: MPS DIODE DET. TIMESTAMP PANEL (Preliminary)
Proposed Back Panel: 1 U
4 N Power Input.
1 N/Cavity
2 D-sub 9 for Testing
4 Fiber TX (RF Power
Timestamp) Out
Optional: AC Power Entry:
Reuse Adi’s Power Entry Module
DC (from PLC) Power Entry:
TB 3-Pin
Front Panel is not be needed. The plan is to use existing front panel of diode detector unit. Four Green LEDs will be added to the front panel for power status indication.

## Slide 17: PCB BOARDS: MPS DIODE DET. TIMESTAMP PCB (MAIN BOARD)

## Slide 18: POPULATED PCB BOARDS
Major functions (All boards) have been bench tested and verified.
MPS SSA Control
MPS RF Muting
Front Boards not Shown
MPS Time Stamp
RF Drive Signals to RF SWs Directly
Diode det. not shown here.

## Slide 19
EPICS
RS-232
TCU
SW1->5=Unmanaged Ethernet switch
36-1 SSA PLC
36-1
remote
Local
Network
SW1
MEZZ
HMI
36-1 System
Mezzanine Rack
EPICS
36-2
HMI
36-2 System
EPICS
36-3 System
EPICS
36-4 System
SW5
SSA – PLC Architecture with Cavity Isolation
SW2
SW3
SW4
36-1
HMI
TCU
TCU
TCU
36-3
HMI
36-4
HMI
Cavity Rack PLC
36-2 SSA PLC
36-3 SSA PLC
36-4 SSA PLC
36-2
remote
36-3
remote
36-4
remote
PLC contains µP
EPICS
RS-232
RS-232
RS-232
TCU= circulator TCU
PLC ARCHITECTURE (G. Trento)

## Slide 20
EPICS
Circulator
TCU
S36-1
MAIN RACK
PLC
36-1
HMI
Water Flow
& Temps
Power Monitor
Chassis
ACIS/RF
Chassis
SSA
PLC
RF Relay
Chassis
Solenoid
Valves
Cavity &
Coupler Temps
EPICS
S36
CAVITY RACK
PLC
Waveguide
Pressure
InfraRed
Temperatures
Blower Control
Chassis
Ion Gauge &
Pump Status
PSS
Chassis
Tuner
Chassis
MPS
Chassis
Transformer
Qualitrol
HOM Switch
System
PLC SIGNALS MONITORED/CONTROLLED (G. Trento)
Same for 36-2,3,4

## Slide 21: PSS BLOCK DIAGRAM (D. HORAN)
Pressure sensor signals are monitored by PSS and PLC.
RF drive is muted and SSA is interlocked when pressure is out of range.
Trip from and to RF6
(Interlock sum of other sectors)

## Slide 22: NEW POWER MONITOR DESIGN OVERVIEW (T. Madden, B. Popovic)
Single Power Monitor, one per cavity/SSA System
  No More Primary/Secondary PMs*
  Use the slightly modified circuits from the original design
    RF Diode
    IR Detector
    Arc Detector/RS422 Fault
    Ion Pump Fault
  New CPLD on Daughter Board
  Add EPICS interface
    Coming from CPLD to PLC then to EPICS
Communicate to each other via PLCs/EPICS
  Fault Reset to each PM, Fault Out from Each PM
*Unless you need more channels

## Slide 23: PM MAIN BD: SIMPLIFIED FUNCTION BLOCK DIAGRAM
RF SW Control

## Slide 24: POWER MONITOR: 5+1* BOARDS
Front Panel Board
  LEDs showing fault status
  Switches to reset and test RF & Arc Det Faults
    I/O: Main Board
Mainboard
  Contains majority of PM circuitry
    I/O: Back & Front panel boards, PLC Interface Board
    Output: CPLD Board
CPLD Daughter Board
  Contains CPLD, which Latches the Faults
    Inputs: Main Board
    Outputs: PLC Interface Board
PLC Interface Board
  Provides 15 V signals and isolation for Digital PLC I/O
    Inputs: CPLD Board
    I/O: Main Board
Back Panel Board
  Connectors to PLC, Arc Detectors, RF Diode Unit etc.
    I/O: Main Board, PLC Interface Board
* RF Diode Detector Board in a Separate Chassis
Mainboard
Front Panel: Both Sides Shown
Back Panel : Both Sides Shown
CPLD
PLC Interface
RF Det.
PS
PS

## Slide 25: POWER MONITOR DESIGN: TWO RACKS
3 RU Main Unit
  Contains the power monitor
  No RF inside this box
    Reduce noise
1 RU RF Box
  All detector diodes
    Outputs DC detector signals to the main unit
  RF SW
    Controlled by TTL signal from main unit
Front Panel Designs
Back Panel Designs

## Slide 26: CAD DRAWING (ILLUSTRATION ONLY)

## Slide 27: ATLAS ARIS 2 (SIMILAR AS APS ACIS)
One Main Control: Watchdog Timer
ARIS2:
ARIS 2: Newly Upgrade from ARIS
Safety PLC Used

## Slide 28: ATLAS ARIS 2 CONTROL/WATCHDOG TIMER-SIMPLE BLOCK DIAGRAM
Watchdog Timer Performs Critical Interlock Functions: Source Deck HV Off when ILK Present; Different Area SSAs Power Supplies Enabling/Disabling

## Slide 29: ATLAS ARIS 2 CONTROL/WATCHDOG TIMER-PCB BOARD
CPLD
Main bd
Front bd

## Slide 30: ATLAS ARIS 2 CONTROL/ WATCHDOG TIMER-PANELS
Panic Button (Covered)
Reset BUttons/Key
Beam Control Key
Mute @ Testing Only

## Slide 31: ATLAS OTHER INTERLOCK: EXAMPLE OF WATER AND HV ILK
Water ILK: Monitoring Flow, Trip when Low Flow
HV ILK: Monitoring HV (thru HV Divider), Trip when Low HV value
Those three chassis are used for G Cryomodule (a 109 MHz superconducting, low Beta (0.15) 8 cavities cryomodule)

## Slide 32: SUMMARY
Majority Work of MPS: PCB, Panels, etc. 
Majority Work of PSS and ACIS Relay Box: Chassis (or Box) Assembly Ongoing. 
PLC: Hardware Assembly Done, Software Almost Done 
Majority Work of PM: PCB, Panels, etc. 
Work supported by the U.S. Department of Energy, Office of Science, under Contract No. DE-AC02-06CH11357.

## Slide 33: FUTURE WORK (INTERLOCK SYSTEM)
Chassis and other Hardware Assembly of Some Systems.
Make and Run Cables Required including RF Cables.
Deployment and Test.
Test the Interlock Functions with the 1st SSA System SAT (Site Acceptance Test) around November, 2024.
Electronic Document Control Center (EDCC): All Documents Check In.
Other