## Slide 1: Overview of Tetrode-Based RF System for High-Power Plasma Heating Operation in the 4-9 MHz Range for the MPEX Project at ORNL
Confid
ential
Bodo Fritsche

## Slide 2: A Heritage of Excellence
1937
1988
1993
2000
2006
2010
2012
Opening of the Broadcast division at BBC.
BBC and Asea merge to new ABB Group
ABB Infocom sold to Thomson-CSF
Thomson-CSF is renamed to Thales, the Broadcast Division to Thales Broadcast & Multimedia
Thales Broadcast & Multimedia is sold to Thomson
Thomson is renamed to Technicolor and the Broadcast Division to Thomson Broadcast
2012: The Ampegon Brand is established by financial investors out of Thomson Broadcast, as Technicolor restructures.
2019: A new company, Ampegon Power Electronics, is founded by A&CT to take over the Ampegon Brand
2019

## Slide 3: SKxx Transmitter Family
1937
1988
1993
2000
2006
2010
2012
2019
build since 1980’s
Naming convention:
SK51: 100kW
SK53: 300kW
SK55: 500kW
tube: CQK-650 (BBC)
Control system: TTL
First with push-pull tube based modulator,
later with Pulse Step Modulator (PSM)

## Slide 4: TSW2xxx Transmitter Family
1937
1988
1993
2000
2006
2010
2012
2019
build since 1990’s after ABB went to Thomson
Naming changed to:
TSW2100: 100kW
TSW2300: 300kW
TSW2500: 500kW
tube: TH-576
Control system: ECAM, later ECOS (computer based)
Capability for digital transmission (DRM)

## Slide 5: TSW2xxx Transmitter Family
1937
1988
1993
2000
2006
2010
2012
2019
RF network solid and reliable since the 80’s
Tube: TH-576 (500kW)
Tube: TH-588E (250kW and 300kW)
Control system: now UCS (based on FPGA & Linux)
>150 units sold worldwide
Time for something new?

## Slide 6: Difficult Improvements
1937
1988
1993
2000
2006
2010
2012
2019
Devices must work under severe conditions
“Good old solution” often the best
New components have problem with RF
control crashes
communication problems
items catching fire

## Slide 7: Why not solid state
1937
1988
1993
2000
2006
2010
2012
2019
Challenging issues to solve:
Combining 3.9…26.1MHz
Protection from lightning and arcing
Efficiency
Price

## Slide 8: Why not solid state
2000
2006
2010
2012
2019
DSB and DRM transmission require high peak power
LDMOS efficiency is good in P1dB… P3dB
To solve efficiency issue: drain-voltage modulation

## Slide 9: TSW2500 at ORNL

## Slide 10: TSW2500 for ORNL
1937
1988
1993
2000
2006
2010
2012
2019
RF system (green)
PSM (orange)
UCS (pink)
Safety System (yellow)
Power supply (red)
Cooling system (blue)

## Slide 11: TSW2500 for ORNL
1937
1988
1993
2000
2006
2010
2012
2019

## Slide 12: PSM Technology
Advantages:
Limitations:
High efficiency >97%
Flexible waveforms, CW output
Overshoot possible
Pulse ripple (module switching)

## Slide 13: TSW2500 for ORNL
1937
1988
1993
2000
2006
2010
2012
2019
LLRF: supplied by ORNL
Pre-Amp: 1kW SSPA
V1: CTK-12
V2: TH-576

## Slide 14: Tubes for TSW2500
1937
1988
1993
2000
2006
2010
2012
2019

## Slide 15: Matching Network TSW2500
1937
1988
1993
2000
2006
2010
2012
2019

## Slide 16: TSW2500 for ORNL
1937
1988
1993
2000
2006
2010
2012
2019

## Slide 17: TSW2500 for ORNL
1937
1988
1993
2000
2006
2010
2012
2019

## Slide 18: Thank you for your attention
Confid
ential
Bodo Fritsche