## Slide 1
Beam polarization at CEPC
Zhe Duan
On behalf of the CEPC Polarization Working Group
18 Jun 2024, ECFA Meeting on e+e- to ZH angular measurements email: duanz@ihep.ac.cn
Circular Electron Positron Collider
Institute of High Energy Physics, CAS

## Slide 2: Motivation of CEPC polarized beam program
Vertical polarization for resonant depolarization
Essential for precision measurements of Z and W masses
> 5% ~ 10% polarization
Longitudinal polarization for colliding beams
Measurements of AFB and ALR @ Z-pole in the same experiment
Other benefits at W & Higgs energies, e.g. CP studies
> 50% polarization with a high luminosity
Summarized as a chapter in the Appendix of CEPC TDR.
L. Arnaudon, et al., Z. Phys. C 66, 45-62 (1995).
polarimeter
depolarizer
IP/detector
IP/detector
G. Moortgat-Pick’s talk on CEPC Workshop EU @ Marseille, 2024 April
unpolarized e+/e-
polarized e- & unpolarized e+

## Slide 3: Self-polarization in the CEPC
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
Polarization build-up time w/o radiative depolarization (hour) | 256 | 15.2 | 2.0
Beam lifetime (hour) | 2.5 | 1.4 | 0.43
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
 | 256 | 15.2 | 2.0
 | 2.5 | 1.4 | 0.43
Beam polarization build-up rate much slower than the beam decay rate @ Z
  Boosted with asymmetric wigglers in the Collider (FCC EPOL)
  Hard to achieve a high-level polarization
  In conflict with a high luminosity
e+/e- beams become “self-polarized” via the Sokolov-Ternov effect in a storage ring

## Slide 4: How to achieve a high-level polarization?
Sawtooth-shape evolution during top-up injection
A high-level polarization (time-averaged) Pavg in the Collider is attainable if
  Top-up injection of highly polarized beam
  Depolarization rate () << beam loss rate (
Injected beam
Pinj > PDK
> 50% requires a minimum value of
depends on machine imperfections, spin rotators
Assume
 | 45.6 GeV (Z) | 80 GeV (W) | 120 GeV (Higgs)
Pinj = 50% | >50% | >50% | >50%
Pinj = 60% | >4% | >23% | >33%
Pinj = 70% | >2% | >15% | >25%
Pinj = 80% | >1% | >11% | >20%
 | 45.6 GeV (Z) | 80 GeV (W) | 120 GeV (Higgs)
Pinj = 50% |  |  | 
Pinj = 60% |  |  | 
Pinj = 70% |  |  | 
Pinj = 80% |  |  | 
Amplitude of sawtooth ~

## Slide 5: Polarized injector for CEPC
Polarized source
  Polarized electron source
    parameters less challenging than ILC, EIC
  Positron damping/polarizing ring
Linac & Transport lines
  spin direction matching @injection/extraction
  helicity adjustment after e+ damping/polarizing ring
Booster
  free from intrinsic spin resonances
T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).

## Slide 6: Positron damping/polarizing ring
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.983 | 
Circumference (m) | 144.2 | 
Number of trains | 2(4) | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Dipole strength B0 (T) | 1.92 | 
U0 (kev/turn) | 397.9 | 
Damping time x/y/z (ms) | 4.8/4.8/2.4 | 
Momentum compaction | 0.0078 | 
Storage time | 20 ms | 10 min
0 (%) | 0.0917 | 
0 (mm.mrad) | 132 | 
injection z (mm) | 6 | 
Extract z (mm) | 6.7 | 6.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 133/13 | 132/13
inj /ext (%) | 0.18 /0.092 | 
RF acceptance (%) | 1.85 | 
Longitudinal tune | 0.025 | 
Using the self-polarization to generate polarized e+ beams
  For Resonant depolarization (very promising)
    polarization build-up time ~ 14.5 min
    extracted beam polarization @ 10min ~ 44%
  For polarized colliding beams, more frequent top-up (under study)
    Higher energy and/or asymmetric wigglers
    More bunches

## Slide 7: Depolarization in the booster
The spin tune changes and could cross spin resonances
  The spin resonances are spaced by 440 MeV for e+/e-
The non-adiabatic crossing could vary and lead to depolarization [1]
  Acceleration rate [km]
  Spin resonance strength ε: highly periodic lattice design -> much weaker at lower beam energies
  Δ|P| < 1% in the regimes of fast crossing & slow crossing
Previous studies suggested using Siberian snakes to maintain polarization for future 100km-scale boosters[7]
[1] Froissart and Stora, NIM 7, 297 (1960) [2] A. K. Barladyan, et al., PRAB 22, 112804, (2019)
[3] S. Nakamura, et al., NIM A 411, 93 (1998) [4] T. Khoe et al., Part. Accel. 6, 213 (1975)
[5] Configuration Manual: Polarized Proton Collider at RHIC, 2006 [6] V. Ranjbar, et al., PRAB 21, 111003 (2018)
[7] I. Koop et al., Phys. Part. Nucl. Lett. 13. 7 (2016); S. Nikitin, IJMPA 34, 1940004(2019); IJMPA 35, 2041001 (2020).
Fast crossing
Slow crossing
Spin precession
Orbit motion in a helical snake @ RHIC
Data from Ref [2-6]

## Slide 8: Depolarization effects: simulation vs. estimation
Z-mode
W-mode
H-mode
In the acceleration to Z & W
  The spin resonances are generally weak
  Polarization is mostly maintained
  Estimations agree fairly well with simulations
In the acceleration to H
  The spin resonances become stronger at higher energies
  Severe depolarization occurs
  Mitigation methods to be explored
[1] T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).
This study supports injecting highly polarized beams into the collider rings as a very attractive solution, for applications @ Z & W.
Polarization transmission to Z, W and Higgs energies in Booster:
Z: over 99%, W: 77.5%~ 98%, Higgs: no better than 40%

## Slide 9: A high-level longitudinal polarization @ Z-pole
50%-70% longitudinal polarization for e- bunches is a reasonable goal
Over 70% injected e- beam polarization is possible.
Polarized e+ source is challenging for CEPC [1],
  self-polarization at a low energy e+ ring is possible, a tradeoff between the challenges & costs of the ring versus reduction injection rate & luminosity (need more study);
  polarization transmission efficiency is similar otherwise.
[1] P. Musumeci et al., Positron Sources for Future High Energy Physics Colliders, ArXiv:2204.13245 Phys. (2022).

## Slide 10: A high-level longitudinal polarization @ Z-pole
50%-70% longitudinal polarization for e- bunches is a reasonable goal
Over 70% injected e- beam polarization is possible.
Simulated equilibrium longitudinal polarization > 70%,
>> the minimum 2% to attain > 50%
leaving a large margin for effects not yet covered.
Simulated equilibrium polarization for an imperfect lattice w/ rotators after closed orbit correction
Implementation of the spin rotators adjacent to the IR

## Slide 11: Polarization, luminosity and beam lifetime
It is possible to attain 50%-70% e- longitudinal polarization at the nominal luminosity and simultaneously with a decent lifetime @ Z-pole
Comparison of the dynamic aperture
Contributors to the beam lifetime
Two pairs of spin rotators
240 Tm solenoid each
Occupy a space of 2.8 km, can be optimized
No interference with the complicated IR design
Influence to DA & beam lifetime can be recovered by dedicated sextupole optimization.
W. Xia et al., Investigation of spin rotators in CEPC at the Z-pole,
Radiat. Det. Tech. Meth. 6:490 (2022).

## Slide 12: Prospects of Z-pole polarization for CEPC
Injecting polarized beam(s) to the Collider
50%-70% longitudinal polarization for e- versus unpolarized (or lower polarization) e+
  Polarized e+ source needs more study;
Spin helicity adjustment
  e- : changing laser helicity at polarized e- source
  e+ : a solenoid spin rotator (21 Tm for 2 GeV) in the transport line following the polarizing ring, or a programmed spin flip in the polarizing ring prior to extraction
RD measurements w/ a few pilot non-colliding bunches, no physics deadtime
Accurate 3D polarimetry is needed
  Inside the IR -> deduce longitudinal polarization @ IP
  Outside the IR -> RD measurements

## Slide 13: Longitudinal polarization at W?
A good chance for >50% e- longitudinal polarization at W
  Assume injected polarization > 60%, then PDK needs to be above 23%
Interleaved solenoid + dipole spin rotators to cover a larger energy range (under study)
  solenoid strength scales ~ linearly with energy
Simulated equilibrium polarization of Collider at W
W. H. Xia, et al, Evaluation of radiative depolarization in the future circular electron-positron collider, Phys. Rev. Accel. Beams, 26, 091001, (2023).

## Slide 14: Useful polarization level at Higgs?
More challenging but possible at Higgs (Under study)
  Simulated injected polarization < 30% -> improvements in Booster lattice design & mitigation to machine imperfections
  Simulated equilibrium polarization ~ 1% -> mitigate depolarization by harmonic spin matching, cancellation of Sokolov-Ternov effect
Interleaved solenoid +dipole spin rotators to cover a larger energy range (under study)
Simulated equilibrium polarization of Collider at Higgs
The key is to reduce the spin
resonance strength by a factor of 10
Prediction of resonant spin diffusion theory at ultra-high energies
W. H. Xia, et al, Evaluation of radiative depolarization in the future circular electron-positron collider, Phys. Rev. Accel. Beams, 26, 091001, (2023).

## Slide 15: Polarization R&D plan in the CEPC EDR Phase
A Compton polarimeter for BEPCII
R&D of high-field SC solenoids
Modify the PAPS photocathode DC gun to a Polarized Electron Source
Implement the spin components in the post-TDR lattice designs
Study the polarization utilities at Higgs and W energies
Polarization-related key hardware R&D
RD @ BEPCII

## Slide 16: Summary
Injecting polarized beams is promising for longitudinal polarization and RD measurements.
50%-70% longitudinally polarized e- versus unpolarized (or a lower polarization) e+ at Z with the nominal luminosity is a reasonable goal.
Further studies of polarized beams towards higher energies as well as related hardware R&D are planned for the CEPC EDR phase.
Physics motivations for polarized beams are warmly welcome.

## Slide 17: Thank you for your attention!

## Slide 18: Spin resonance structure of a CEPC Booster lattice
Intrinsic resonances:
Super strong resonances:
Imperfection resonances:
Super strong resonances:
Strength of intrinsic & imperfection resonances can be approximated by[1]
Enhancement occurs near , νB is the total νy in all standard arc cells [2]
Resonances at K<< νB tend to be weak due to cancellation [2]
due to P superperiods
due to M identical FODOs in each arc
[1] S. Y. Lee, Spin dynamics and snakes in synchrotrons (World Scientific, 1997).
[2] T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).

## Slide 19: Resonant Depolarization at Z
It’s possible to inject > 20% polarized beams to enable RD measurements at Z-pole
  No dead time for physics, a few pilot bunches
  Polarized e+ source ? Dual-purpose damping/polarizing ring (could accommodate both e+/e- beams to gain sufficient polarization)
One typical design:
beam energy ~ 2 GeV, circumference ~ 150 m
polarization build-up time ~ 14.5 min
Extracted beam polarization @ 10min ~ 44%

## Slide 20: RD measurements: endorsed by recent FCC-ee studies
F. Zimmermann, FCC Accelerator Status, FCC Week 2024