## Slide 1: Muon ID Electronics: plastic scintillator option
October 10, 2024
Guillermo Tejeda, for the MID-Mexico electronics group

## Slide 2
Outline
Introduction
FEC Design
Patch Panel Design
FEC Version 2
Organization
Summary

## Slide 3: MuonID Detector Plastic Scintillator Option
Assumptions:
  10 rings
  16 segments per ring
  1 chamber per segment
  40 channels per chamber

## Slide 4: Channels Distribution (Option)
FEC
16 FEC per ring
10 m (10 rings)
. . .
160 FECs in total
40 channels/FEC
Energy & Time measuremnt
Required 160 optical links
for all modules
MID Module

## Slide 5: MuonID FEC details
FPGA
Petiroc 2A
Top
Petiroc 2A Bot
Trigger
Trigger
Control
Control
USB
Uplink
Downlink
1 FEC/Module 160 (10 spares) FEC in total
2 Erni connectors with 32 ch each
2 ASIC Petiroc 2A
1 FPGA Cyclone V (non Rad-Hard 5cgtfd5c5f23c7n)
1 LpGBT + VtRx
(for communication and Slow control)
Power supply regulators zone
Clk
Clk_ext

## Slide 6: FEC + Patch Panel (Version 1)
Petiroc 2A
Cyclone III
Input 0-31
FPGA 1
ASIC 1
Power Supply
DC-DC converters
USB
ADC 1
LEDs
D_Out 1
Digital I/Os
Top SiPM
Bot SiPM
Spare SiPM
Power Supply + DC-DC converters
1 ASIC Petiroc 2A
1 FPGA Cyclone III (non Rad-Hard)
USB communication and debugging
32 Channels input
Charge and Time measurements
Channel by channel SiPM high voltage adjustment
6mW/channel power consumption
Current – Voltage an temp sensor

## Slide 7: FEC Final Design
25 x 20 cm
1 PETIROC 2A (32 Ch)
FPGA Cyclone
In production (PCBWay)
Many details
  Wrong gerber generation
  Extra ring around PCB
  No drill files
  No outline layer

## Slide 8: In production
Fabrication in progress after many issues

## Slide 9
Fabrication Progress
54 % today

## Slide 10: Patch Pannel (V1)
5 Channels PCB completed
Power regulator included in PP for 5 SiPM
To test Power regulator, noise and signal integrity

## Slide 11: Patch Pannel (V2)
50 Channels
Upgrade of the first patch pannel version
Schematic is in progress
Power Supply + DC-DC converters
Board Connectors

## Slide 12: User Interface
Compatible with Weeroc Test Board
Working on start procedure:
  Connnects USB cable
  Power up power supply
  Start Software
Slow Control:
  Load slow control parameters
  640 bits will be sent twice

## Slide 13
Calibration:
  Calibrate the 6-bits DAC settings of each channel
Data Acquisition:
  Number of acquiisitions
  Trigger mode (under revision)
  Output file and format
Preparing technical documentation
  Manual FEC
  Manual Interface

## Slide 14: FEC + Patch Panel (Version 2)
Petiroc 2A
Petiroc 2A
Cyclone V
Input 0-31
Input 32-63
FPGA 1
ASIC 2
ASIC 1
LpGBT
VtRx
Power Supply
DC-DC converters
USB
ADC 1
LEDs
D_Out 1
Digital I/Os
Top SiPM
Bot SiPM
Spare SiPM
Power Supply + DC-DC converters
2 ASIC Petiroc 2A
1 FPGA Cyclone V (non Rad-Hard 5cgtfd5c5f23c7n)
1 LpGBT + VtRx+ (for communication and Slow control)
USB communication for debugging
50 Channels input
Charge and Time measurements
Channel by channel SiPM high voltage adjustment
6mW/channel power consumption
Version 2 -> 2025
Current – Voltage an temp sensor

## Slide 15: Time Line (FEC Version 1)
2024 | Mar | April | May | June | July | Aug | Sept | Oct | Nov | Dec
PCB Design |  |  |  |  |  |  |  |  |  | 
Firmware |  |  |  |  |  |  |  |  |  | 
User Interface |  |  |  |  |  |  |  |  |  | 
Patch Panel |  |  |  |  |  |  |  |  |  | 
Assembly |  |  |  |  |  |  |  |  |  | 
Test |  |  |  |  |  |  |  |  |  | 
Integration |  |  |  |  |  |  |  |  |  | 
FEC V1 will be tested in 2025 Beam Test with the Muon ID module

## Slide 16: Radiation Tolerances
FEC located in a region with a “moderate” radiation dose estimated by simulations.
Not negligible for our FPGA. We are still investigating different ways for a save operation.
FEC will be tested under radiation sources to observe aging effects or SEU.

## Slide 17: Firmware
Slow control Register -> ok
Probe Register Parameters -> ok
Read Register for analogue Read Out -> ok
USB interface -> ok
ReadOut -> ok
Next steps:
  LpGBT (FPGA)
  Include second Petiroc
FEC PCB
-Schematic and PCB Version 1 -> 100% -Schematic Version 2 -> 20%
Patch Panel
-Version 1 -> 100 %
- Version 2 -> 20 %
User Interface
Testing USB port -> 80%
PCB -> In production
Summary 1/2

## Slide 18: Summary 2/2
Waiting for cards to start with test
Development of the FEC Version 2
Development of the PP version 2
Development of the LpGBT communication protocol
Integration of the FEC V1 with a Muon ID Module

## Slide 19: Muon ID Electronics Organization
Sinaloa
  Carlos Duarte Galvan
  Juan Manuel Mejia Camacho
  Cesar Regalado Elenes
  Juan Carlos Cabanillas
UNAM
  Enrique Patiño Salazar
  Saul Aguilar
Puebla
  Emigdio Jimenez Dominguez
  Yael Antonio Vazquez Beltrán
  Guillermo Tejeda Muñoz
  Luis A. Pérez Moreno
FEE
Grafic Interface
SiPM
FEC-PCB
FEC-Firmware
Communication protocols
Bi weekly meeting for preparation of the electronics proposal and TDR

## Slide 20: Thank You for your attention

## Slide 21: TOF design
PicoTDC board
PolarFire FPGA (blue)
2 PicoTDCs (red)
Ethernet connector subsystem (purple)

## Slide 22
FPGA based design
PolarFire MPF200T FCG784E

## Slide 23: Dose tolerances (from CMS)
TID (𝛾´s):
  FPGA Cyclone V (50Gy)
  Petiroc 2A (160Gy)
  Power Regulators (100Gy)
TNID (Neutrons):
  25e11 neq1MeV/cm2
Neutron flux:
  450e3 neq1MeV/cm2/s
SEU expected in FPGA
Expected fluence and dose (MID zone):

## Slide 25
-Design Rule Check (ok)
-Gerber Files
-8 layers
-32 Channels
-USB communication
-80% parts available
Recuerde que tiene que considerar una PCB para destrucción junto con un chip.
25 cm
20 cm

## Slide 26
Patch-Panel Schematic Partial
First version to test:
Crostalk
Noise
Stability

## Slide 27: Petiroc 2A

## Slide 28
Specifications