## Slide 1: Status of bERLINPro’s Injector
35s
36s
37s
38s
39s
40s
41s
42s
16/09/24,
CERN A. Neumann for the bERLinPro team @SEALAB
Status
For the LDG
PERLE Collaboration Meeting
BESSY II
bERLinPro
43s
44s
45s
46s
47s
48s
49s
50s
51s
28d
21h
19m
52s
bERLinPro Beam Countdown

## Slide 2: 2024, an exiting autumn and Winter are ahead of us
Reminder: What was bERLinPro meant for and how far is it assembled and financed?
Current status of the facility
2024: Finally the year of first beam?
  Milestones: Final setup of the injector beamline First cooldown and RF tests
2024: Beam commissioning plan, a first insight
The injector awakens

## Slide 3: Evolution of bERLinPro
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell SRF cavities
44 MeV
modified Cornell booster
3 x 2 cell SRF cavities
4.5 MeV
srf-gun
1.4 cell SRF cavities
1.5-2.3 MeV, single SC solenoid,
merger
dogleg
test and diagnostic line
History
From 4th generation light source prototype (2011), via generic high intensity ERL prototype (2012-2020) towards application driven facility (today)
Parameter | bERLinPro
Beam energy recirculator (MeV) | 50
Beam current ERL mode (mA) | 100
Frequency RF and Laser (GHz) | 1.3
Normalized emittance (mm mrad) | 1 (< 0.6 in simulations)
Bunch length (ps) | < 2 (ERL mode), 100 fs @ 10 mA
Beam losses | << 10-5 @ 100 mA
Single turn high intensity ERL
5 MW beam power
650 kW injector beam power
Important aspects:
Injector beam quality at high current/bunch charge
Beam loss control and monitoring  Radiation protection
Beam break-up in main Linac
Longitudinal control of beams for recovery process (low power margin)

## Slide 4: Stages at bERLinPro
Operations concept
Installed: 10-mA SRF gun + merger + recirculation + dump
Installed: Proof-of-principle UED experiment
Funded: Booster module. Produced but assembly required
Not funded: LINAC module
Not funded: 100-mA class photoinjector
Presently installed facility
CW photoinjector studies < 10 mA
Long-pulse injector studies < 100 mA
High-power beam studies (“long pulse”)
High-power energy recovery
Energy-efficient RF operation
BEAM

## Slide 5: Stages at bERLinPro
Operations concept
Installed: 10-mA SRF gun + merger + recirculation + dump
Installed: Proof-of-principle UED experiment
Planned: Waste water treatment demonstrator
Funded: Booster module. Produced but assembly required
Not funded: LINAC module
Not funded: 100-mA class photoinjector
UED Exp.
Presently installed facility
CW photoinjector studies < 10 mA
Long-pulse injector studies < 100 mA
High-power beam studies (“long pulse”)
High-power energy recovery
Energy-efficient RF operation
Waste Water
Applications
High power beam
Short pulse, low emittance
Low charge
Make use of injector’s flexibility for beam parameter range
 Cover in parallel ERL relevant beam studies

## Slide 6: Stages at bERLinPro
Operations concept
Installed: 10-mA SRF gun + merger + recirculation + dump
Installed: Proof-of-principle UED experiment
Planned: Waster water treatment demonstrator
Funded: Booster module. Produced but assembly required
Not funded: LINAC module
Not funded: 100-mA class photoinjector
UED Exp.
Presently funded facility
CW photoinjector studies < 10 mA
Long-pulse injector studies < 100 mA
High-power beam studies (“long pulse”)
High-power energy recovery
Energy-efficient RF operation
Waste Water
Applications

## Slide 7: Stages at bERLinPro
Operations concept
Installed: 10-mA SRF gun + merger + recirculation + dump
Installed: Proof-of-principle UED experiment
Planned: Waste water treatment demonstrator
Funded: Booster module. Produced but assembly required
Not funded: LINAC module
Not funded: 100-mA class photoinjector
UED Exp.
Full program (partially funded)
CW photoinjector studies < 10 mA
Long-pulse injector studies < 100 mA
High-power beam studies (“long pulse”)
High-power energy recovery
Energy-efficient RF operation
Waste Water
Applications

## Slide 8: Status of bERLinPro@SEALAB
status
Cathode
transfer
system
SRF gun
SRF booster
“1st meter” diagnostics +
Laser window for laser-beam transport
Recirculator
Merger section
Beam diagnostics
SRF photo-injector and diagnostics ready for commissioning
Cathode-laser beam transport tested, final alignment with cathode in cavity
1.3 GHz laser demonstrated 23 W CW sufficient for 100 mA @ 2.5% QE
1st Cool-down in Jan. 2024 successful
RF test of photoinjector Q2 2024 Reached about 20 MV/m CW and 25 MV/m pulsed
Cathode-transfer unit ready in final 120°C bake out these weeks
Beam operating permit expected Q3 2024  First beam from SRF Gun around 10-11/2024
Start of Booster assembly H1/2024 (all parts in house)
Injector installation at present
Six+ month delay due to severe HZB cyber attack

## Slide 9: Status of bERLinPro@SEALAB
status
Cathode
transfer
system
SRF gun
SRF booster
“1st meter” diagnostics +
Laser window for laser-beam transport
Recirculator
Merger section
Beam diagnostics
Injector installation at present
SRF photo-injector and diagnostics ready for commissioning
Cathode-laser beam transport tested, final alignment with cathode in cavity
1.3 GHz laser demonstrated 23 W CW sufficient for 100 mA @ 2.5% QE
1st Cool-down in Jan. 2024 successful
RF test of photoinjector Q2 2024 Reached about 20 MV/m CW and 25 MV/m pulsed
Cathode-transfer unit ready, in final 120°C bake out these weeks
Beam operating permit expected Q3 2024  First beam from SRF Gun around 10-11/2024
Start of Booster assembly H1/2024 (all parts in house)
Six+ month delay due to severe HZB cyber attack

## Slide 10: Status of bERLinPro@SEALAB
status
Cathode
transfer
system
SRF gun
SRF booster
“1st meter” diagnostics +
Laser window for laser-beam transport
Recirculator
Merger section
Beam diagnostics
Injector installation at present
SRF photo-injector and diagnostics ready for commissioning
Cathode-laser beam transport tested, final alignment with cathode in cavity
1.3 GHz laser demonstrated 23 W CW sufficient for 100 mA @ 2.5% QE
1st Cool-down in Jan. 2024 successful
RF test of photoinjector Q2 2024 Reached about 20 MV/m CW and 25 MV/m pulsed
Cathode-transfer unit ready, in final 120°C bake out these weeks
Beam operating permit expected Q3 2024  First beam from SRF Gun around 10-11/2024
Start of Booster assembly H1/2024 (all parts in house)
Six+ month delay due to severe HZB cyber attack

## Slide 11: Reminder: The SRF Gun
SiC HOM beampipe absorber (80 K)
SC- solienoid (4K)
1.4xl/2 cell shape (1.8K)
Steerer magnets
Full-cell
Half-cell
Choke-cell
Cathode insert + Petrov filter
Twin CW-modified TTF-III coupler (≤20 kW)
Transition to warm beamline
Blade-tuner with four piezos

## Slide 12
Cathodes: Na-K-Sb vs. Cs-K-Sb
Investigations into Na-K-Sb as more temperature robust alternative to Cs-K-Sb (baseline cathode)
Time after deposition | Na-K-Sb (WH09) QE @ 515 nm | Cs-K-Sb (P18) QE @ 515 nm
0 days | 2.0% | 3.4 %
8 days | 2.4% | 1.5 %
14 days | 2.2% | 0.3 %
22 days | 2.0% | -
Photocathode Preparation & Analysis System
Sepctral Response Na-K-Sb (WH09)
Spectral response Cs-K-Sb (P18)
High QE photocathodes for SEALAB photoinjector:
Explore multi-alkali Cs- and Na-K-Sb systems, from theoretical modeling (DFG fund), growth and characterization, towards operation in a SRF gun.
Complete infrastructure: growth and characterization system, UHV transport vessels, access to materials science lab EMIL at HZB, collaboration with theory.
J. Kühn, S. Mistry, C. Wang, J. Dube, C. Cocchi, R. Schier, H. Sassnick, et al.
Remember:
Best so far 16.8% at 515 nm (specs 1%)
Cathode for commissioning
Lifetime/Robustness

## Slide 13: 1st RF test at bERLinPro
Current status
Still RF processing during ramp
Successful RF test, beam energies up to 2.1 MeV  there is room for progress
Field emission was present, but continuously being processed by RF
Laser system, diagnostics, beam transport optics, beam loss monitoring (several systems) installed and ready
Cathode transfer system in final bake out

## Slide 14: Pulsed processing: Examples
Pulsed processing
Time (a.u.)
E0 (MV/m)
RF processing at 1 Hz repetition rate
Pulse length 30 and 100 ms
Processing event at 14:35, 14th of May: Vacuum in 1st meter 2e-8 mbar  Above threshold for closing gate valve in module, no alarm handler  Processing continued not noticing this event  Explains also absence of any dark current measurement by Faraday Cup
After event higher level pulsing showed this ripple effect, stopped and took last CW curve
Reached: CW 20 MV/m, 25 MV/m pulsed
100 ms
Beam energies between 1.7 to 2.1 MeV in reach

## Slide 15: First Commissioning steps
commissioning
https://www.i-tech.si/products/libera-blm/
Courtesy
Eric May, HZB
2nd RF test w/o cathode:
  Demonstrate achievable field level with final installations of all beam vacuum systems
  Measure dark current: Level, on-set field, energy range, determine source  Test beam loss monitoring system (PIN diodes, PMT based systems, Radiation sensitive films, Faraday Cup, foil monitor)
  Determine field stability: Setup LLRF control system, twin coupler operation  Measure SRF cavity parameter for control: LF detuning, microphonics…
Gafchromic RTQA2 on Gun cryostat
Twin coupling scheme,
Pic courtesy A. Ushakov, HZB

## Slide 16: First Commissioning steps
commissioning
2nd RF test with cathode:
  Demonstrate achievable field level with uncoated cathode  Measure position of cathode w.r.t. backwall: Impact on dark current, beam focusing, emission phase  Longitudinal and transverse beam dynamics……..training of cathode transfer into SRF gun
  Measure dark current: Level, on-set field, energy range, determine source  How to handle co-propagating dark current, how to separate further down-stream?
  Determine impact on cathode inserted on RF heating of cathode  adjust position Multipacting observed? DC bias as countermeasure  Impacts low field beam dynamics
  Measure eventually microphonics by cathode insert
Epeak
Emax
Ecath
„Echoke“
Eemitt: Beam emittance
Emax: Beam energy
Ecath: Beam emittance and level of dark current, eventually multipacting
 High current ERL issue: Balance Beam quality vs. dark current beam losses all within power limit by high power operation

## Slide 17: First Commissioning steps
commissioning
Cathode operation:
  Characterisation of cathode: Measure first beam, cathode quantum efficiency, QE maps  Cathode lifetime QE(t)
  Measure dark current: Level, on-set field, energy range, determine source  How to handle co-propagating dark current, how to separate further down-stream?
  Measure multi-parameter beam phase space:
    Beam based alignment of machine (Solenoid, steerer) Beam emittance vs. field level, emission phase, cathode position, pulse length, etc…
    Longitudinal beam phase space: Bunch length studies, short beam studies (TCav)
  Impact of field stability on beam parameter: Jitter studies, beam based feedback
J. Kühn et al., IPAC 18 Cu cathode QE map
A. Neumann et al., IPAC 11 First beam from fully SRF gun with lead cathode
Tcav: see Linac 18 G. Kourkafas et al.

## Slide 18: Field emission by cathode on laser windows
Does it harm?
Some parameters: E0=20 MV/m, elevated field in half cell, Solenoid off, 37 mT, 75 mT
Fowler-Nordheim field emission model
Focusing by RF and solenoid field
Solenoid off
Solenoid 37 mT
Cavity
1st meter
Solenoid=75 mT (here)
Laser window
Segmented emission

## Slide 19: bERLinPro@SEALAB injector studies
Topics to study
Funded: SRF gun/booster ops & UED mode
Not funded: 100-mA CW gun cavity + couplers + LINAC module (existing design)
Medium-power gun (20kW) / booster program
Parameter | Injector / UED | ERL
Beam energy (MeV) | 6.5 – 10 / 2 | 50
Max. average current (mA) | 10 / 0.0025 | 100
Bunch charge (pC) | 0.05 – 400 | 77
RF Frequency (MHz) | 1300 | 1300
Norm. Emittance (mm mrad) | 0.6 / 0.03 | 1 (0.6)
RMS bunch length (ps) | 0.02 – 2 | 2 (0.1)
Explore full parameter space of SRF injector @ Ib < 10 mA
100 mA can be potentially studied in long-pulse* regime
Bunch charge up to 0.5 nC with a high QE cathode
Proof of cathode exchange concept, test of more robust cathode materials: Replace Cs by Na
Studies of beam loss scenarios by dark current or beam halo formation by bunch tails
Propagation of beam and unwanted beam from injector to dump
Beam loss monitoring and machine protection concepts
High dynamic range diagnostic concepts for low-current start-up to high-power operation (< µA mA 100 mA*)
Beam arrival time and jitter studies
Digital twins, ML+AI assisted control methods

## Slide 20: A coarse 2024 schedule
2024
January
February
March
April
May
June
July
August
September
October
November
December
Cooldown 2K
RF operation permit
RF test 2K
Beam operation permit
Beam operation injector
LLRF ready
High power RF ready
Cryo ready
Module diagnostics
PSI operational
TCav ready
Readiness cathode transfer system, cathode laser
Beamline magnets, steerer magnets
Diagnostics: FOMs, Faraday Cups Camera tools, beam loss monitoring
Control system fully implemented for needed devices, MPS functional
Setup Laser
Setup transfer system
Check for beam condition: FOMS, magnets,…
Dry run injector
Final fixes, tests and repairs

## Slide 21: Merci!
If there is time left, questions are welcome or contact me at
Axel.Neumann at helmholtz-berlin.de
Thanks and acknowledgements to all partners, who contributed to this project
Funding: Bundesministerium für Bildung & Forschung Bundesland Berlin, Helmholtz Gemeinschaft