## Slide 1
Radionuclide production and radiation therapy with particle accelerators
Marco Silari
(retired from CERN, Geneva, Switzerland)
Research Associate with Polytechnic of Milano, Italy
marco.silari@cern.ch

## Slide 2
Brief historical introduction of particle accelerators and their use in medicine
Radionuclide production:
  - production routes
  - production methods
  - decay equation, decay scheme
  - nuclear reactions, production rate, cross section, targetry
  Radiation therapy:
  - external photon radiation therapy
  - hadron therapy
  - Boron Neutron Capture Therapy
Outline of the lecture

## Slide 3
Brief historical introduction of particle accelerators and their use in medicine

## Slide 4
The beginnings of modern physics and of medical physics
1895
discovery of X rays
Wilhelm Conrad Röntgen
1897
“discovery” of the electron
J.J. Thompson
Courtesy Prof. Ugo Amaldi

## Slide 5
Tools for (medical) physics: the cyclotron
1930
Ernest Lawrence invents the cyclotron
M. S. Livingston and E. Lawrence
with the 25 inch cyclotron
Courtesy Prof. Ugo Amaldi

## Slide 6
The beginnings of modern physics and of medical physics
James Chadwick
(1891 – 1974)
1932
Discovery of the neutron
Cyclotron + neutrons = first attempt of radiation therapy with fast neutrons at LBL
(R. Stone and J. Lawrence, 1938)
Courtesy Prof. Ugo Amaldi

## Slide 7
Tools for (medical) physics: the electron linac
1939
Invention of the klystron
Sigmur Varian
Russell Varian
William W. Hansen
1947
first linac for electrons
4.5 MeV and 3 GHz
1950’s: development of compact linear electron accelerators by various companies
Courtesy Prof. Ugo Amaldi

## Slide 8
Tools for (medical) physics: the synchrotron
1 GeV electron synchrotron
Frascati - INFN - 1959
1945: E. McMillan and V.J. Veksler
discover the principle of phase stability
6 GeV proton synchrotron
Bevatron - Berkeley - 1954
Courtesy Prof. Ugo Amaldi

## Slide 9
Particle accelerators operational in the world
A. P. Chernyaev and S. M. Varzar, Particle Accelerators in Modern World, Physics of Atomic Nuclei, 2014, Vol. 77, No. 10, pp. 1203–1215.
Three main applications: 1) Scientific research, 2) Medical applications 3) Industrial uses
Medical applications

## Slide 10
Particle accelerators for medical uses
Production of radionuclides with (low-energy) cyclotrons
  Imaging (PET and SPECT)
  Therapy
Electron linacs for conventional radiation therapy (including advanced modalities)
Medium-energy cyclotrons and synchrotrons for hadron therapy with protons (250 MeV) or light ion beams (400 MeV/u 12C-ions)
Compact proton accelerators for BNCT

## Slide 11
Radionuclide production

## Slide 12
The use of radionuclides in the physical and biological sciences can be
broken down into three general categories:
Radiotracers
Imaging (95% of medical uses)
SPECT (99mTc, 201Tl, 123I)
PET (11C, 13N, 15O, 18F)
Therapy (5% of medical uses)
Brachytherapy (103Pd)
Targeted therapy (211At, 213Bi)
Relevant physical parameters (function of the application)
Type of emission (α, β+, β–, γ)
Energy of emission
Half-life
Radiation dose (essentially determined by the parameters above)
Radionuclide production

## Slide 13
Production methods
All radionuclides commonly administered to patients in nuclear medicine are artificially produced
Three production routes:
(n,γ) reactions (nuclear reactor): the resulting nuclide has the same chemical properties as those of the target nuclide
Fission (nuclear reactor) followed by separation
Charged particle induced reaction (cyclotron): the resulting nucleus is usually that of a different element

## Slide 14
The cyclotron – The work horse for radionuclide production
Scanditronix MC40

## Slide 15
First practical application of a radioisotope (as radiotracer)
1911: first practical application of a radioisotope (as radiotracer) by G. de Hevesy, a young Hungarian student working with naturally radioactive materials in Manchester
1924: de Hevesy, who had become a physician, used radioactive isotopes of lead as tracers in bone studies

## Slide 16
Historical development of radioisotopes in medicine
1932: the invention of the cyclotron by E. Lawrence makes it possible to produce radioactive isotopes of a number of biologically important elements
1941: first medical cyclotron installed at Washington University, St. Louis, for the production of radioactive isotopes of phosphorus, iron, arsenic and sulphur
After WWII: following the development of the fission process, most radioisotopes of medical interest begin to be produced in nuclear reactors
1951: Cassen et al. develop the concept of the rectilinear scanner
1955: first cyclotron installed in a hospital (Hammersmith, London)
1957: the 99Mo/99mTc generator system is developed by the Brookhaven National Laboratory
1958: production of the first gamma camera by Anger, later modified to what is now known as the Anger scintillation camera, still in use today

## Slide 17
Emission versus transmission imaging
Courtesy P. Kinahan

## Slide 18
X-ray image versus CT scan
A conventional X-ray image is basically a shadow: you shine a “light” on one side of the body, and a piece of film or a silicon sensor on the other side registers the silhouette of the bones (to be more precise, organs and tissues of different densities show up differently on the radiographic film).
Shadows give an incomplete picture of an object's shape.
Look at the wall, not at the person. If there's a lamp in front of the person, you see the silhouette holding the banana, but not the pineapple as the shadow of the torso blocks the pineapple. If the lamp is to the left, you see the outline of the pineapple, but not the banana.

## Slide 19
J. Long, “The Science Creative Quarterly”,scq.ubc.ca
Cyclotron
Radiochemistry
PET camera
Positron Emission Tomography (PET)

## Slide 20
Positron Emission Tomography (PET)
COVERAGE:
~ 15-20 cm
SPATIAL RESOLUTION:
~ 5 mm
SCAN TIME to cover an entire organ:
~ 5 min
CONTRAST RESOLUTION:
depends on the radiotracer
511keV
511keV

## Slide 21
N(t) = N0e-t or A(t) = A(0)e-t
where:
  N(t) = number of radioactive atoms at time t
  N0 = initial number of radioactive atoms at t = 0
  A(t) = activity at time t
  A(0) = initial activity at t = 0
  e = base of natural logarithm = 2.71828…
   = decay constant = 1/τ = ln 2/T1/2 = 0.693/T1/2
  t = time
  and remembering that:
  -dN/dt =  N
  A =  N
Radionuclide production: fundamental decay equation

## Slide 22
Linear-Linear scale
Radionuclide production: fundamental decay equation
Linear-Log scale

## Slide 23
Generalized decay scheme

## Slide 24
The “ideal” diagnostics radiopharmaceutical
Be readily available at a low cost
Be a pure gamma emitter, i.e., have no particle emission such as alphas and betas (these particles contribute radiation dose to the patient while not providing any diagnostic information)
Have a short effective biological half-life (so that it is eliminated from the body as quickly as possible)
Have a high target to non-target ratio so that the resulting image has a high contrast (the object has much more activity than the background)
Follow or be trapped by the metabolic process of interest

## Slide 25
The essential steps in accelerator radionuclide production
Acceleration of charged particles in a cyclotron
Beam transport (or not) to the irradiation station via a transfer line
Irradiation of target (solid, liquid, gas) – internal or external
Nuclear reaction occurring in the target (e.g. AXZ(p,n)AyZ+1)
Target processing and material recovering
Labeling of radiopharmaceuticals and quality control
a = bombarding particle
b, c = emitted particles
A, B, D = nuclei

## Slide 26
Q values and thresholds of nuclear decomposition for the reaction of a deuteron with a 14N nucleus after forming the compound nucleus 16O
Example: d + 14N 16O*
Q value = the amount of energy absorbed or released during the nuclear reaction
Q (MeV) = 931.5 ( m1 + M2 – m3 – M4)

## Slide 27
Production rate and cross section
R = the number of nuclei formed per second
n = the target thickness in nuclei per cm2
I = incident particle flux per second (related to the beam current)
λ = decay constant = (ln 2)/T1/2
t = irradiation time in seconds
σ = reaction cross-section, or probability of interaction (cm2), function of E
E = energy of the incident particles
x = distance travelled by the particle
and the integral is from the initial energy (threshold of reaction) to the final energy of the incident particle along its path

## Slide 28
Energy dependence of the cross section σ
Excitation function of the 18O(p,n)18F reaction

## Slide 29
Cross-section versus energy plot for the 203Tl(p,2n)202Pb, 203Tl(p,3n)201Pb and 203Tl(p,4n)200Pb reactions
Competing nuclear reactions, example of 201Tl
The nuclear reaction used for the production of 201Tl is the 203Tl(p,3n)201Pb
201Pb (T1/2 = 9.33 h) 201Tl (T1/2 = 76.03 h)
(http://www.nndc.bnl.gov/index.jsp)
Above 30 MeV, production of 200Pb becomes significant
Below 20 MeV, production of 201Tl drops to very low level
Around threshold, production of 201Tl is comparable to that of 202Pb

## Slide 30
Internal (beam is not extracted from the cyclotron)
External (extracted beam + beam transport to target)
Simultaneous irradiation of more than one target (H– cyclotrons)
The target can be
Solid
Liquid
Gaseous
Principal constraints on gas targets
removal of heat from the gas (gases are not very good heat conductors)
the targets must be quite large in comparison with solid or liquid targets in order to hold the necessary amount of material.
Targets
18O water target
to produce 18F via 18O(p,n)

## Slide 31
Production reactions (1)
Radionuclide | Use | Half-life | Reaction | Energy (MeV)
99mTc | SPECT imaging | 6 h | 100Mo(p,2n) | 30
123I | SPECT imaging | 13.1 h | 124Xe(p,n)123Cs 124Xe(p,pn)123Xe 124Xe(p,2pn)123I 123Te(p,n)123I 124Te(p,2n)123I | 27 15 25
201Tl | SPECT imaging | 73.1 h | 203Tl(p,3n)201Pb →201Tl | 29
11C | PET imaging | 20.3 min | 14N(p,α) 11B(p,n) | 11–19 10
13N | PET imaging | 9.97 min | 16O(p,α) 13C(p,n) | 19 11

## Slide 32
Radionuclide | Use | Half-life | Reaction | Energy (MeV)
15O | PET imaging | 2.03 min | 15N(p,n) 14N(d,2n) 16O(p,pn) | 11 6 > 26
18F | PET imaging | 110 min | 18O(p,n) 20Ne(d,α) natNe(p,X) | 11-17 8-14 40
64Cu | PET imaging and radiotherapy | 12.7 h | 64Ni(p,n) 68Zn(p,αn) natZn(d,αxn) natZn(d,2pxn) | 15 30 19 19
124I | PET imaging and radiotherapy | 4.14 d | 124Te(p,n) 125Te(p,2n) | 13 25
Production reactions (2)

## Slide 33
Radionuclides for therapy
High LET decay products (Auger electrons, b-particles or a-particles)
Radionuclide linked to a biologically active molecule that can be directed to a tumour site
Beta emitting radionuclides are neutron rich they are in general produced in reactors
Some of the radionuclides that have been proposed as possible radiotoxic tracers are:
Click here to learn about radionuclide generators

## Slide 34
Radiation therapy

## Slide 35
Treatment planning and dose delivery to tumour volume

## Slide 36
Tumour control and therapeutic window
Tumour control
Therapeutic advantage
Probability (%)
Dose
Therapeutic window
Complications
Tumour control w/o complications

## Slide 37
Past radiation therapy equipment
Radiation therapy is much more than the radiation source. One also needs:
diagnostic equipment, CT scanners
treatment planning software
patient set-up devices
computers
a broad range of professional figures
Co-60 unit
45 MeV Betatron
Photo: Wikipedia
Betatron and microtron

## Slide 38
Medical electron linacs
e– + target  X-rays
target
Varian Clinac 1800
Multi-leaf collimator
Energy: 6-25 MeV
Dual e─ / g beams
Courtesy Varian Medical

## Slide 39
Cyber-knife robotic surgery system
http://www.accuray.com/Products/Cyberknife/index.aspx
6 MV Linac mounted on a robotic arm
No flattening filter
Uses circular cones of diameter 0.5 to 6 cm
Non-Isocentric
Average dose delivered per session is 12.5 Gy
Dose rate @ 80 cm = 400 cGy/min

## Slide 40
Intra-operative radiation therapy (IORT)
Small electron linac
Energy 6 – 12 MeV
Treatment with electrons only
Single irradiation
Courtesy: myself!

## Slide 41
Intensity modulated radiation therapy (IMRT)
E. Pedroni, Europhysics News (2000) Vol. 31 No. 6
An example of intensity modulated treatment planning with photons. Through the addition of 9 fields it is possible to construct a highly conformal dose distribution with good dose sparing in the region of the brain stem (courtesy of T. Lomax, PSI).

## Slide 42
Helical tomotherapy
www.tomotherapy.com
Integrated CT guidance
  Integrated CT scanner allowing efficient 3D CT imaging for ensuring the accuracy of treatment
A binary multi-leaf collimator (MLC) for beam shaping and modulation
A ring gantry design enabling TomoHelical delivery
  As the ring gantry rotates in simultaneous motion to the couch, helical fan-beam IMRT is continuously delivered from all angles around the patient
  Very large volumes can be treated in a single set-up

## Slide 43
Hybrid MRI linac

## Slide 44
Volumetric Modulated “ARC” Radiation Therapy
Rotate linac gantry while modulating the beam
Fixed 6 or so gantry angles
VMAT
Name-Prof Peter Metcalfe
BSOC lecture 08

## Slide 45
Particle therapy (hadron therapy)
“hadrons” are
made of quarks
carbon ion =
6 protons + 6 neutrons
atom
Proton or
neutron
quark “u” or “d”
electron “e”

## Slide 46
Particle therapy (hadron therapy)
Courtesy INFN, Italy

## Slide 47
Treatment planning

## Slide 48
Particle therapy (hadron therapy)
200 MeV
protons
4800 MeV
carbon ions
charged hadron beam
that loses energy in matter
27 cm
tumour
target
www.ptcog.ch

## Slide 49
Cyclotrons and synchrotrons for proton therapy
Accel-Varian
(superconducting)
Hitachi
Loma Linda (built by FNAL)
IBA

## Slide 50
The LLUMC proton synchrotron
Loma Linda University Medical Center

## Slide 51
Beam delivery: passive vs active
A. C. Kraan and A. Del Guerra, Technological Developments and Future Perspectives in Particle Therapy: A Topical Review, IEEE Transactions on Radiation and Plasma Medical Sciences 8, 453-480, 2024
This recent review provides an overview of technological advances in particle therapy hardware (accelerators, gantries and treatment veriﬁcation techniques), software (Monte Carlo simulations, treatment planning calculations), and studies toward clinical applications

## Slide 52
A proton therapy facility is not just the accelerator
A gantry is a massive structure that allows directing the beam to the tumour from any direction. It carries:
the final section of the beam line
the beam spreading ‘nozzle’
the proton ‘snout’ which carries the aperture and range compensator
HIT, Heidelberg
IBA
ISOCENTRIC GANTRIES
10 - 12 m

## Slide 53
PROSCAN at Paul Scherrer Institut (PSI), Switzerland
ACCEL
SC cyclotron
250 MeV protons
PROSCAN
TERA
Courtesy PSI and U. Amaldi , TERA
J.M. Schippers et al., NIM BB 261 (2007) 773–776

## Slide 54
Protons vs carbon: radiobiological effectiveness RBE of radiation

## Slide 55
Proton versus carbon-ion synchrotrons
G. Coutrakon, Accelerators for Heavy-charged-particle Radiation Therapy,
Technology in Cancer Research & Treatment, Volume 6, Number 4 Supplement, August 2007
Hitachi proton synchrotron Siemens ion synchrotron
Do you see the difference between the two?

## Slide 56
National Centre for Oncological Hadrontherapy, CNAO, Italy

## Slide 57
National Centre for Oncological Hadrontherapy, CNAO, Italy
Ion sources
LEBT components
Injector linac
Courtesy S. Rossi, CNAO
Dipole magnets
RF cavity
Quadrupole magnets

## Slide 58
National Centre for Oncological Hadrontherapy, CNAO, Italy

## Slide 59
Single room proton facilities
IBA Proteus Nano
Mevion Medical Systems

## Slide 60
Multi-room versus single-room facilities
29 m (87ft)
14 m (41 ft)
13 m (39 ft)
Other Proton Systems
28 m (84 ft)
812 m2
182 m2
2,240 m2
714 m2
Courtesy L. Bouchet, Still River Systems
Advantages of single-room facility:
Modularity
Reliability / back-up
PT treatment available at more hospitals
(Hopefully) cost

## Slide 61
Boron Neutron Capture Therapy (BNCT)
Interaction of an individual epithermal neutron being moderated by the hydrogenous tissue to thermal energies and thereafter being captured by a 10B atom, triggering the therapeutic α decay

## Slide 62
Accelerator-based BNCT
BudkerINP Vacuum Insulated Tandem (VITA)
Ibaraki prefecture RFQ + DTL

## Slide 63
Accelerator-based BNCT in Helsinki, Finland
Peeter Karihtala (Helsinki University CCC and University of Helsinki)

## Slide 64
Accelerator-based BNCT @ CNAO, Italy
Sandro Rossi, CNAO, Italy

## Slide 65
Dosimetry in BNCT
Four separate radiation components with different biological characteristics and spatial distributions
Incident neutrons (Dn, DH)
Leading to dose deposition mainly via (n,p) reactions
Photons (Dγ)
Incident with the n beam and internally generated – mainly 2.2 MeV from 1H(n,γ)2H reactions (radioactive capture)
Thermal neutrons (DN or DTh)
Mainly from 14N(n,p)14C reactions
Boron dose (DB)
From 10B(n,α)7Li reactions

## Slide 66
Availability of radiation therapy worldwide

## Slide 67
Availability of radiation therapy in African countries
A partnership in pursuit of innovative radiation therapy technology for use in challenging environments - ICEC (iceccancer.org)

## Slide 68
Challenges and expected developments in radiation therapy
September 2015
https://indico.cern.ch/event/560969/
CERN-ICEC workshop, CERN, November 2016
CERN-ICEC-STFC workshop, CERN, October 2017
https://indico.cern.ch/event/661597/

## Slide 69
Guidelines

## Slide 70
Challenges in Radiation Therapy in Africa
Technology
23 of 54 countries have teletherapy services
20 had high- or low-dose brachytherapy resources
293 radiotherapy machines serving 1 billion individuals
1 machine per 3.6 million people
Abdel-Waheb et al, Lancet Oncology, 2013 / Grover et al, Front in Oncology, Jan 2015 / Balogun et al, Radiation Oncology, Aug 2016
Taken from Surbhi Grover’s lecture at the CERN-ICEC-STFC workshop, CERN, October 2017
Human resources
a gap of 7,500 oncologists, 6,000 physicists and 20,000 technicians in LMICs (in Africa: 1600 medical oncologists, 1000 medical physicists and 4000 technicians)
Taken from Andras Fehervary’s lecture at the CERN-ICEC workshop, CERN, November 2016

## Slide 71
RT resources needed in 20 years from now
Taken from Mary Gospodarowicz’s lecture at the CERN-ICEC workshop, CERN, November 2016
LMICS = Low Medium Income Countries

## Slide 72
Developing RT for challenging environments
Linacs
Ability to operate in a difficult environment
  Interruptions in electricity / power supply
  Heat / problem with temperature control
  Dust and humidity
Highly modular, so that faulty parts can easily be replaced
Self-diagnosing, in case of accelerator malfunctioning
Low power consumption
…
Screening
Improve screening and early diagnosis to make RT more effective
Need for
Qualified professionals: radiation oncologists, medical radiotherapy physicists, radiotherapy technicians, radiation protection officers, maintenance engineers, etc.
Related training programmes
Development of medical infrastructure

## Slide 73
Some textbooks
On accelerators & radiation therapy:
C.K. Karzmark, Advances in linear accelerator design for radiotherapy, Medical Physics 11, 105- 128 (1984)
S. Humphries, Principles of charged particle acceleration, John Wiley and Sons
H. Wiedemann, Particle accelerator physics, Springer- Werlag
S. Baird, Accelerators for pedestrians, CERN AB-note-2007-014
PTCOG: Particle Therapy Co-Operative Group (http://ptcog.web.psi.ch/)
On radionuclide production:
Cyclotron Produced Radionuclides: Principles and Practice, IAEA Technical Reports Series No. 465 (2008)
(Downloadable from IAEA web site)
Targetry and Target Chemistry, Proceedings Publications, TRIUMF, Vancouver
(http://trshare.triumf.ca/~buckley/wttc/proceedings.html )
CLARK, J.C., BUCKINGHAM, P.D., Short-Lived Radioactive Gases for Clinical Use, Butterworths, London (1975

## Slide 74
Supplementary material

## Slide 75
Particle accelerators operational in the world
A. P. Chernyaev and S. M. Varzar, Particle Accelerators in Modern World, Physics of Atomic Nuclei, 2014, Vol. 77, No. 10, pp. 1203–1215.
Three main applications: 1) Scientific research, 2) Medical applications 3) Industrial uses
Medical applications
Chart: Particle Accelerators in Modern World
| 1968 | 1970 | 1989 | 1994 | 1998 | 2000 | 2004 | 2007 | 2009 | 2012 | 2014
Total | 2000 | 3000 | 6500 | 9700 | 13500 | 15000 | 18000 | 27500 | 30000 | 39500 | 41000
Industrial | 2000 | 2700 | 4000 | 4500 | 7500 | 8500 | 8500 | 17900 | 22500 | 25300 | 27000
Medicine | 306 | 2500 | 4200 | 4700 | 5200 | 8500 | 9650 | 11600 | 13000 | 14000
Science | 1000 | 1200 | 1200 | 1200 | 1200 | 1200 | 1200 | 1200

## Slide 76
Motion of a particle in a dipole magnetic field
Bρ = 33.356·p [kG·m] = 3.3356·p [T·m] (if p is in GeV/c)
where ρ = radius of curvature of the path
(p = momentum = mv)
Bρ is called “magnetic rigidity” of the particle and is an index of how difficult is to bend the motion of a charged particle by a magnetic field
(the field is in/out of the plane of this slide)

## Slide 77
The cyclotron
F = q(E + v x B)
mv2 / ρ = qvB ω = 2πf = v / ρ
Rev. frequency f = qB/2πm
Rev. period τ = 1/f is independent of v
Resonant acceleration with fRF = h∙f
Isochronism
Maximum energy/nucleon:
T/A = k (Bρ)2 (Z/A)2
with k = e2 / 2mp
K = k (Bρ)2 is called “bending limit”
K = 48 (Bρ)2 (MeV)
if B is in teslas and m in metres

## Slide 78
Magnetic fields of uniform-field cyclotron:
(top) Sectional view of cyclotron magnetic poles
showing shims for optimizing field distribution.
(left) Radial variation of vertical field magnitude
and field index.
B
F
Weak focusing
Decrease of rev. frequency f with r
Loss of isochronism
Two solutions to achieve higher energies: - synchrocyclotron
  - AVF cyclotron
The classical (non relativistic) cyclotron

## Slide 79
AVF = azimuthally varying field
B(r,θ) = <B(r)> + Mod(r, θ)
RF constant
<B> rises with radius r to compensate for the relativistic increase of the particle mass
f = q<B>/2πmγ
Vertical focusing achieved by the azimuthal variation of B
A further component of the axial focusing force is obtained by giving the sectors a spiral shape
The AVF (isochronous) cyclotron

## Slide 80
Experimental measurements of cross section σ
where
Ri = number of processes of type i in the target per unit time
I = number of incident particles per unit time
n = number of target nuclei per cm3 of target = ρNA/A
σi = cross-section for the specified process in cm2
x = the target thickness in cm
and assuming that
The beam current is constant over the course of the irradiation
The target nuclei are uniformly distributed in the target material
The cross-section is independent of energy over the energy range used

## Slide 81
Saturation factor, SF = 1 – e-λt
Tirr = 1 half-life results in an activity of 50% of the saturation (max) activity
2 half-lives  75%
3 half-lives  90%
The practical production limits of a given radionuclide are determined by the half-life of the isotope, e.g.
15O, T1/2 = 2 minutes
18F, T1/2 = almost 2 hours
For long lived species, the production rates are usually expressed in terms of integrated dose or total beam flux (µA·h)
1 – e-λt

## Slide 82
Radionuclide generators
Technetium-99m (99mTc) has been the most important radionuclide used in nuclear medicine
Short half-life (6 hours) makes it impractical to store even a weekly supply
Supply problem overcome by obtaining parent 99Mo, which has a longer half-life (67 hours) and continually produces 99mTc
A system for holding the parent in such a way that the daughter can be easily separated for clinical use is called a radionuclide generator

## Slide 83
Radionuclide generators

## Slide 84
Transient equilibrium
Between elutions, the daughter (99mTc) builds up as the parent (99Mo) continues to decay
After approximately 23 hours the 99mTc activity reaches a maximum, at which time the production rate and the decay rate are equal and the parent and daughter are said to be in transient equilibrium
Once transient equilibrium has been reached, the daughter activity decreases, with an apparent half-life equal to the half-life of the parent
Transient equilibrium occurs when the half-life of the parent is greater than that of the daughter by a factor of about 10

## Slide 85
Transient equilibrium

## Slide 86
Radionuclide generators

## Slide 87
The betatron
Magnetic field produced by pulsed coils
The magnetic flux inside the radius of the vacuum chamber changes with time
Increasing flux generates an azimuthal electric field which accelerates electrons in the chamber
= field at the orbit
= average flux density through the orbit
Schematic diagram of betatron with air gap

## Slide 88
MICROTRONE
Racetrack microtron
An “electron cyclotron”
Uniform magnetic field
Fixed-frequency RF system
Well-separated orbits
Bending radius
Revolution time
Isocronism only if γ ≈ 1
If γ > 1, Δτ per turn = Δγ
To have isochronism it must be Δτ per turn = hτRF
Required energy gain per passage
  for electrons ΔEe= 511 keV
  for protons ΔEp= 938 MeV
Magnet weight ≈ (energy)3
The microtron

## Slide 89
Electron acceleration in a waveguide
Particles initially in
cell 1 arrive in cell 2 to get further accelerating
kick. Frequency must match particles
velocity and cell periodicity = ½ λ:

## Slide 90
Schematics of a treatment head of a medical electron linac

## Slide 91
We have already seen the motion of a particle in a dipole field…
Bρ = 33.356·p [kG·m] = 3.3356·p [T·m] (if p is in GeV/c)
where ρ = radius of curvature of the path
(p = momentum = mv)
Bρ is called “magnetic rigidity” of the particle and is an index of how difficult is to bend the motion of a charged particle by a magnetic field
(the field is in/out of the plane of this slide)

## Slide 92
Trajectory of particles in a dipole field
Trajectory of a particle in a bending magnet
Two particles in a dipole field, with same momentum but different initial angles
Unfortunately an accelerator contains more than one particle!
Number of circulating particles in a synchrotron is typically in the order of 1010 - 1012 or more
Photo: courtesy ANL

## Slide 93
Quadrupole magnets as thin lenses
Light rays passing through a series of focusing and defocusing lenses
The lenses, which are concave in one plane, are convex in the other
In both cases the concave lenses will have little effect as the light passes very close to their centre, and the net result is that the light rays are focused in both planes

## Slide 94
The mechanical equivalent
The gutter below illustrates how the particles in a synchrotron behave due to the quadrupole fields.
Whenever a particle beam diverges too far away from the central orbit the quadrupoles focus them back towards the central orbit.
Photo courtesy Fermilab Visual Media Services
Beam “envelope” defined by the b function