## Slide 1
Radiation measurements and dosimetry
Marco Silari
(retired from CERN, Geneva, Switzerland)
Research Associate with Polytechnic of Milano, Italy
marco.silari@cern.ch

## Slide 2
Outline of the lecture
A very brief historical introduction
Directly and indirectly ionizing radiation
  Radioactivity
  Natural exposures
The effects of ionizing radiation
  Deterministic and stochastic effects
Radiological quantities and units
  physical, protection and operational quantities
Principles of radiation protection
  Justification, optimization and dose limitation
  The ALARA principle
Protection means
Instrumentation for measuring ionizing radiation

## Slide 3
Outline of the lecture
A very brief historical introduction
Directly and indirectly ionizing radiation
  Radioactivity
  Natural exposures
The effects of ionizing radiation
  Deterministic and stochastic effects
Radiological quantities and units
  physical, protection and operational quantities
Principles of radiation protection
  Justification, optimization and dose limitation
  The ALARA principle
Protection means
Instrumentation for measuring ionizing radiation

## Slide 4
1895
Discovery of X rays
Wilhelm C. Röntgen
1897
“Discovery” of the electron
J.J. Thompson
1897
First treatment of tissue with X rays
Leopold Freund
The discovery of radiation

## Slide 5
Henri Becquerel (1852-1908)
1896
Discovery of natural
radioactivity
Marie Curie Pierre Curie
(1867 – 1934) (1859 – 1906)
1898
Discovery of polonium and radium
Thesis of Mme. Curie – 1904
α, β, γ in magnetic field
Hundred years ago
The discovery of radiation

## Slide 6
Outline of the lecture
A very brief historical introduction
Directly and indirectly ionizing radiation
  Radioactivity
  Natural exposures
The effects of ionizing radiation
  Deterministic and stochastic effects
Radiological quantities and units
  physical, protection and operational quantities
Principles of radiation protection
  Justification, optimization and dose limitation
  The ALARA principle
Protection means
Instrumentation for measuring ionizing radiation

## Slide 7
Periodic table of elements
Notes: As a noble gas, radon is chemically and electrically inert, therefore after inhalation, it is immediately exhaled and it is weakly harmful in itself. However the radon daughter products attach to the ambient areosol, which may be inhaled and stick to the lung surface. Its importance in the exposure of human beings to terrestrial radiation is given by its transport from surface to atmosphere where its decay products may be inhaled. Radon tends to concentrate in enclosed spaces like underground mines or houses. Radon is the largest contributor to daily exposure of radiation.

## Slide 8
Chart of nuclides
neutrons
protons
α : AX -> A-4Y + 4He2+
α-decay
Unstable (=radioactive) nuclides ~ 3000
Stable nuclides ~ 250
β+ : p+ -> n + e+
β- : n -> p+ + e-

## Slide 9
http://www.fmboschetto.it/tde4/carta.htm
11C → 11B + e+ + e + 960 keV
14C → 14N + e_ + e + 156 keV
β+ and β- decays

## Slide 10
Directly ionizing radiation:
fast charged particles (e.g., electrons, protons, alpha particles), which deliver their energy to matter directly, through many small Coulomb-force interactions along the particle’s track
Indirectly ionizing radiation:
X- or g-ray photons or neutrons (i.e., uncharged particles), which first transfer their energy to charged particles in the matter through which they pass in a relatively few large interactions, or cause nuclear reactions
The resulting fast charged particles then in turn deliver the energy in matter
The deposition of energy in matter by indirectly ionising radiation is a two-step process
photon  electron
neutron  proton or recoiling nuclei
Directly and indirectly ionising radiation

## Slide 11
Radioactivity and ionising radiation
Radioactivity: the phenomenon whereby atoms undergo spontaneous random disintegration, usually accompanied by the emission of ionising radiation.
The rate at which this nuclear transformations occurs in matter containing radionuclides is called activity and it is expressed in Bequerels:
A(t) = -dN/dt [Bq] 1 Bq = s-1
where N is the number of nuclei of the radionuclide, and hence the rate of change of N with time is negative
The radioactive half-life (T1/2) of a radionuclide is the time necessary for half of the nuclei present in the sample to decay
Radionuclides are either of natural origin or produced by nuclear reactions (artificial radionuclides)
(the old unit is the Curie: 1 Ci = 3.7 x 1010 Bq)

## Slide 12
BETA
  Electrons or positrons
  Energy: a few keV to a few MeV
  Limited penetration
  Dangerous for skin and eyes in case of external irradiation
  Increased radiological hazard if inhaled, ingested or absorbed through a wound (internal irradiation)
ALPHA
  Helium nuclei (2 protons + 2 neutrons)
  Energy: a few MeV
  Non-penetrating
  Radiological hazard only if inhaled, ingested or absorbed through a wound (internal irradiation)
Radioactivity and ionising radiation / hazard
(Emitted in the de-excitation of unstable nuclei)

## Slide 13
PHOTONS
  Electromagnetic radiation
  Energy: a few keV to a few MeV
  Very penetrating
  Radiological hazard only by external irradiation
NEUTRONS
  Neutral particles (constituents of the atomic nucleus together with protons)
  Very penetrating
  External irradiation
  Enhanced biological effect (high LET – Linear Energy Transfer radiation), which depends on their energy
HEAVY CHARGED PARTICLES (protons, ions)
  External irradiation
  Enhanced biological effect (high LET – Linear Energy Transfer radiation)
Radioactivity and ionising radiation / hazard

## Slide 14
Radioactivity and ionising radiation
b-, g-emitter
b+
b-
Pure b-emitter
e
a-, b- and g are emitted with end energies up to few MeV

## Slide 15
Absorption / attenuation of radiation
- and -particles are degraded in energy while traversing a material, until they are completely brought to rest
-rays are attenuated in intensity by the material

## Slide 16
Absorption / attenuation of radiation
Alpha
Beta
Gamma
Neutron
Paper Plastic Lead Concrete
mm mm – cm cm – tens tens of cm –
of cm metres
Qualitative!
Beta sources are usually shielded with Plexiglas, gamma sources with lead

## Slide 17
Production and decay of radionuclides
For a given particle, target element and nuclide
Interaction probability, σ (cross section)
Flux (spectrum), F
Beam intensity, Ip
Nuclide production rate

## Slide 18
Production and decay of radionuclides
Rule-of-thumb (probably very obvious):
The shorter the half-life, the fastest the build-up, the fastest the decay
It takes about 5 half-lives to reach saturation of activity

## Slide 19
Unit
The absorbed dose is the energy deposited by a given radiation in a unit mass of matter
The unit of absorbed dose is the Gray (mGy, µGy):
1 Gy = 1 J/kg
(the old unit is the rad: 1 rad = 10-2 Gy)
Radiation protection uses the operational quantity “dose equivalent H” in Sievert (mSv, µSv)
H=Q∙D
1 Sv = 1 J/kg
Q = quality factor of the radiation
Notes: Ionizing radiation can also produce gross changes, either desirable or deleterious, in organic compounds by breaking molecular bonds, or in crystalline materials by causing defects in the lattice structure. Even steel can be damaged by large fluxes of fast neutrons, suffering embrittlement and possible fracture under mechanical stress (e.g., ITER)

## Slide 20
Are we all exposed (voluntarily or not) to some radiation sources?
Yes/No?
If the answer is yes,
what are the natural radiation levels?
QUESTION 1

## Slide 21
Natural radiation exposures
Annual exposure to natural radioactivity in France = 2.5 mSv
(3.3 mSv including medical exposures)

## Slide 22
Terrestrial radionuclides
During the creation of the Earth, terrestrial nuclides had been incorporated into the earth crust (T1/2 some millions to billions of years)
Nuclide | Symbol | Half-life | 
Uranium-235 | 235U | 7.04 x 108 y | 0.72% of natural Uranium
Uranium-238 | 238U | 4.47 x 109 y | 99.3% of natural Uranium
Thorium-232 | 232Th | 1.41 x 1010 y | 
Potassium-40 | 40K | 1.28 x 109 y | Earth: 0.037-1.1 Bq/g
...and some more: 50V, 87Rb, 113Cd, 115In, … 190Pt, 192Pt, 209Bi, …

## Slide 23
Cosmogenic radionuclides
Cosmogenic nuclides are produced by nuclear reactions of cosmic particles with stable nuclei of the atmosphere
Nuclide | Symbol | Half-life | Nuclear Reaction
Carbon-14 | 14C | 5730 y | e.g. 14N(n,p)14C
Tritium-3 | 3H | 12.3 y | Interaction of cosmic radiation with N or O 6Li(n,a)3H
Beryllium-7 | 7Be | 53.28 d | Interaction of cosmic radiation with N or O
More cosmogenic radionuclides:
10Be, 26Al, 36Cl, 80Kr, …

## Slide 24
The radioactivity inside our body
Nuclide | Total activity in human body (~ 70 kg)
Potassium-40 | ~ 5 kBq
Carbon-14 | ~ 3 kBq
Tritium | ~ 20 Bq
Polonium-210 | ~ 18 Bq
Uranium | ~ 1 Bq
Radium | ~ 1 Bq
Thorium | ~ 0.1 Bq
TOTAL ~ 8 kBq

## Slide 25
Cosmic radiation exposure versus altitude
Courtesy PTB, Braunschweig

## Slide 26
Outline of the lecture
A very brief historical introduction
Directly and indirectly ionizing radiation
  Radioactivity
  Natural exposures
The effects of ionizing radiation
  Deterministic and stochastic effects
Radiological quantities and units
  physical, protection and operational quantities
Principles of radiation protection
  Justification, optimization and dose limitation
  The ALARA principle
Protection means
Instrumentation for measuring ionizing radiation

## Slide 27
Why is radiation dosimetry important?
Unique effects of interaction of ionizing radiation with matter
Biological systems (humans in particular) are particularly susceptible to damage by ionizing radiation
The expenditure of a trivial amount of energy (~ 4 J/kg = 4 Gy) to the whole body is likely to cause death…
…even if this amount of energy can only raise the gross temperature by about 0.001 °C
This is because of the ability of ionizing radiation to impart their energy to individual atoms and molecules
The resulting high local concentration of absorbed energy can kill a cell either directly or through the formation of highly reactive chemical species such as free radicals (atom or compound in which there is an unpaired electron, such as H or CH3) in the water medium that constitutes the bulk of the biological material
Main aim of dosimetry = measurement of the absorbed dose (energy/mass)
Notes: Ionizing radiation can also produce gross changes, either desirable or deleterious, in organic compounds by breaking molecular bonds, or in crystalline materials by causing defects in the lattice structure. Even steel can be damaged by large fluxes of fast neutrons, suffering embrittlement and possible fracture under mechanical stress (e.g., ITER)

## Slide 28
delta rays
Ionization event (formation of water radicals)
Light damage - reparable
Clustered damage - irreparable
Water radicals attack the DNA
The mean diffusion distance of OH radicals before they react is only 2-3 nm
OH•
e-
Primary particle track
Courtesy R. Schulte
DNA damage

## Slide 29
Radiobiological effectiveness (RBE)
DIFFERENT TYPES OF RADIATION MAKE DIFFERENT DAMAGE

## Slide 30
QUESTION 2
What are the biological effects of radiation?

## Slide 31
Biological effects of radiation
Stochastic effects
no dose threshold (linear function of dose)
increase of probability by 5% per Sv for:
  genetic defects
  cancer
result does not dependent on the amount of absorbed dose
delayed health detriments
Deterministic effects
dose received in short time interval
dose threshold: > 500 mSv
immediate consequences:
vomiting
immun deficiency
erythema and necrose
health detriments are function of the dose
lethal dose: 5 – 7 Sv

## Slide 32
The biological actions of radiation
deterministic
deterministic
stochastic

## Slide 33
Lethal dose (LD50/30) for various organisms
Source: Martin Volkmer, Radioaktivität und Strahlenschutz, Informationskreis Kernenergie

## Slide 34
LD50 and effect of acute irradiation to humans
Whole body dose (Gy) | Organ or tissue failure responsible for death | Time at which death occurs after exposure (days)
3-5 | Bone marrow | 30-60
5-15 | Intestine and lungs | 10-20
>15 | Nervous system | 1-5
Lethal effects: LD50 for humans 3-5 Gy due to damage to bone marrow, in absence of bone marrow transplantation

## Slide 35
Outline of the lecture
A very brief historical introduction
Directly and indirectly ionizing radiation
  Radioactivity
  Natural exposures
The effects of ionizing radiation
  Deterministic and stochastic effects
Radiological quantities and units
  physical, protection and operational quantities
Principles of radiation protection
  Justification, optimization and dose limitation
  The ALARA principle
Protection means
Instrumentation for measuring ionizing radiation

## Slide 36
General principles of radiation protection
Justification
any exposure of persons to ionizing radiation has to be justified
2) Limitation
the personal doses have to be kept below the legal limits
3) Optimization
the personal doses and collective doses have to be kept As Low As Reasonably Achievable (ALARA) – including social and economical factors into account

## Slide 37
Physical, protection and operational quantities
Source: Wikipedia
International Commission on Radiological Protection

## Slide 38
Radiological quantities and units
Absorbed Dose D: energy absorbed per mass
Unit: Gy 1 Gy = 1 J/kg
(1 Gy = 100 rad)
Equivalent Dose H: absorbed dose of organs weighted by
the radiation weighting factor wR of radiation R:
Unit: Sv (1 Sv = 100 rem)
Effective dose E: Sum of all equivalent doses weighted with the weighting factor wT for tissue T
Unit: Sv (1 Sv = 100 rem)

## Slide 39
Radiation weighting factors, WR
Type and energy of radiation R | wR
Photons, all energies | 1
Electrons and muons, all energies | 1
Protons and charged pions | 2
Alpha particles, fission fragments, heavy ions | 20
Neutrons | 

## Slide 40
Tissue sensitivity and tissue weighting factors, WT
Organ / tissue | No of tissues | wT | Total contribution
Bone-marrow, colon, lung, breast, stomach, remainder tissues | 6 | 0.12 | 0.72
Gonads | 1 | 0.08 | 0.08
Bladder, esophagus, liver, thyroid | 4 | 0.04 | 0.16
Bone surface, brain, salivary glands, skin | 4 | 0.01 | 0.04
The tissue weighting factors are sex- and age-averaged values for all organs and tissues

## Slide 41
Operational quantities
Quantities on which limits are based (effective dose, organ equivalent dose) are not measurable
So operational quantities are defined
  measurable quantities
  quantities which are representative of the quantities on which limits are based (where possible overestimating these)
For external exposure:
  ambient dose: H*(10)
  personal dose: Hp(10) and Hp(0,07)
For internal exposure (after an intake):
  committed effective dose (over 50 years): E(50)

## Slide 42
History of radiation protection
Chart: Year
M. Curie
ICRP 103
Source: Los Alamos Science
Nr. 23, 1995, p. 116

## Slide 43
Radiological risks
Contamination
Surface
Volumetric (air)
External radiation source external exposure
Internal radiation source internal exposure

## Slide 44
Basic concepts in radiation protection
Person occupationally exposed to radiation (> 1 mSv/y)
  Category A workers: > 6 mSv/y
  Category B workers: < 6 mSv/y
Supervised area: area with dose > 1 mSv/y
  (accessible to categories A and B workers)
Controlled area: area with dose > 6 mSv/y
  (accessible to categories A workers, and with limited stay to category B workers)
Exposure situations:
  risk of external exposure only (sealed radioactive sources, radiation generators, for example X-ray tube)
  risk of internal and external exposure (use of unsealed radioactive sources)

## Slide 45
QUESTION 3
Can you protect yourself from radiation?
How?

## Slide 46
How to reduce external exposure
Distance: the dose rate
decreases with the inverse
squared of the distance
(from a point-like source)
Time: the dose is proportional
to the time spent close to the
source D = dD/dt x t
Shielding: the dose rate approximately
reduces as exp(-d/λ)
λ = shielding properties of the material
For β radiation: plexiglass For γ radiation: iron or lead For n: concrete
Three means: distance, time, shielding

## Slide 47
Protection against external exposure
Time: limit the duration of the stay in the radiation field
  Job preparation
  Dry run
  Monitoring of the duration of exposure
Distance: stay as far as possible from the source
  Dispersion law: 1/r2 for a point source, more like 1/r for an extended source
  Very important at short distances
  Factor of 100 between 1 cm and 10 cm (use of tongs/tweezers)
Shielding: use of protective shields
  Material and thickness of the shield depend of the type and energy of the radiation and of the reduction factor required

## Slide 48
Monitoring of external exposure
Wearing a personal dosimeter on the chest or at the waist
  monthly measurement (at least)
  Information may be delayed (depends on dosimeter)
  measurement threshold ~0.1 mSv/month
Wearing an electronic dosimeter
  instantaneous information
  possibility to setting a dose or dose rate alarm
Wearing an extremity dosimeter
  In the case of specific hand exposure risk (handling of radioactive substances)

## Slide 49
Operational quantities and dose limits
The dosimeter is calibrated to measure:
  Hp(10): personal equivalent dose at a depth of 10 mm in the chest
  Hp(0.07): personal equivalent dose at a depth of 0.07 mm in the chest
At low measured doses (less than the limits) it is assumed that:
  the effective dose and the equivalent dose to each organ is equal to Hp(10);
  the equivalent dose to the skin is equal to Hp(0.07);
At high measured doses (exceeding the limits),
  an investigation is undertaken (dosimetric reconstruction) to determine the effective dose and the equivalent doses to the organs which were actually received.

## Slide 50
Personal dosimetry for monitoring external exposure
Personal dosimeter: "Legal dose”
Operational dosimeter DMC: “Operational dose”
Kodak film badge
RADOS DIS
Finger dosimeter
Quartz-fiber dosimeter (ionisation chamber and electroscope)

## Slide 51
Radioactive contamination at particle accelerators
Radioactive contamination at particle accelerators can arise from:
the use of unsealed radioactive sources
activation of air and dust around the accelerators
activation of oils or cooling fluids
the machining or treatment of radioactive components
normal or accidental emissions from targets whilst they are irradiated or after irradiation
Two factors should be considered in defining precautions for the control of unsealed radioactivity:
the prevention of the contamination of
  personnel
  equipment

## Slide 52
Radioactive contamination at particle accelerators
  Material that has been brought into and removed from an accelerator tunnel or bunker during shutdown (maintenance) will no be activated BUT …
  … it might be contaminated
  If there is a suspicion of contamination, it has to be checked before leaving the area

## Slide 53
Contamination
Internal (+ external) exposure: the incorporated radionuclides irradiate the organs and tissues to which they attach
Exposure lasts until the complete elimination of the radionuclides by radioactive decay and biological metabolism
Internal exposure can occur by:
- ingestion
- inhalation
- skin

## Slide 54
Monitoring of internal exposure
Determination of the activity taken into the body and calculation of the committed effective dose with a standard model
Measurements to determine the activity taken into the body:
  direct measurement of the radiation emitted by the person using a thyroid monitor, a lung monitor or a whole body monitor (WBC, whole body counter)
  measurement of the activity in the excreta (urine, faeces)
Two stages strategy:
  screening measurement (with a simple laboratory instrument)
  If a threshold is exceeded, actual measurement of the intake

## Slide 55
Operational quantities and dose limits
Operational quantity: committed effective dose E50
For radionuclides with short half-live, the dose is received in the days following the intake;
For radionuclides with a long half-live (strontium-90, actinides), the dose is received over many years following the intake;
The committed dose is attributed to the period of intake;
Dose is calculated using standard metabolic models;
If dose limits are exceeded an investigation is undertaken (dosimetric reconstruction) to determine the committed dose; an adaptation of the model may be necessary.

## Slide 56
Personal protection equipment against contamination
« Tyvek » overall (synthetic paper)
Rubber gloves
… generally completed by overshoes
For low level contamination / low risk

## Slide 57
Outline of the lecture
A very brief historical introduction
Directly and indirectly ionizing radiation
  Radioactivity
  Natural exposures
The effects of ionizing radiation
  Deterministic and stochastic effects
Radiological quantities and units
  physical, protection and operational quantities
Principles of radiation protection
  Justification, optimization and dose limitation
  The ALARA principle
Protection means
Instrumentation for measuring ionizing radiation

## Slide 58
Radiation measurements
*
-
-
-
-
-
+
+
+
+
+
45653

H*(10)
  Since the Radiation Protection quantities are not directly measurable, their estimate involves the measurement of a physical quantity.
Courtesy S. Agosteo, Politecnico di Milano

## Slide 59
Ionization chamber

## Slide 60
Scintillating crystal coupled to a PMT
From Glenn F. Knoll, Radiation Detection and Measurement

## Slide 61
AUTOMESS dose rate meter 6150 AD6
Detector: Geiger Müller counter
Range: 0.5 µSv/h – 10 mSv/h
Energy range: 60 keV – 1.3 MeV
Dimensions: 130 mm x 80 mm x 29 mm
Alimentation: 9 V standard battery
Push button 1
Push button 2
Push button 3
Push button 4
AD17 external probe
ADK surface contamination meter for a, b and g radiation
Detector: sealed proportional counter
Active surface 100 cm2

## Slide 62
State-of-the-art: B-RAD by ELSE NUCLEAR (Italy)
Developed for operating also in very intense magnetic fields (up to 3 T intensity)
Equipped with LaBr3 crystal, 15 mm diameter x 15 mm height
Energy resolution approximately 3% (137Cs)
User friendly, with double display (small with fast reading, big for detailed analysis)
Leather bag for easy transport
Radioisotope identification capability
A. Fazzi and M. Silari. Portable Radiation Detection Device for Operation in Intense Magnetic Fields. CERN/Politecnico joint patent. Patent Grant number 9977134 (2017)

## Slide 63
Contamination monitors
Hand and foot monitor
CMS2000
APA
ABPM203M
Air contamination monitors

## Slide 64
Whole body counting

## Slide 65
Slow neutron detection
Some elements have a very large cross section for slow neutrons and can be exploited for neutron detection
Boron 10B + n → 7Li + a Q = 2.793 MeV
    10B + n → 7Li* + a Q = 2.310 MeV
Lithium 6Li+ n → 3H + a Q = 4.78 MeV
3He 3He + n → 3H + p Q = 764 keV

## Slide 66
Neutron cross sections
Mean free path of thermal neutrons
in 3He gas ≈ 7 cm
in solid 10B ≈ 70 µm

## Slide 67
Moderator-type neutron detector
*
*
*
Courtesy S. Agosteo, Politecnico di Milano

## Slide 68
Proportional counters for slow neutron detection
BF3 gas and 3He gas make detectors for slow neutrons with excellent gamma discrimination
Gamma rays can interact in the walls and produce electrons in the gas, but the energy loss of electrons is small (≈ 2 keV/cm), so that these pulses are much smaller than those due to neutrons
A suitable pulse amplitude threshold can thus eliminate most gamma interactions.

## Slide 69
Pulse height spectrum from a BF3 proportional counter
pulse height
N
alpha
Li
The shape of the pulse height spectrum is due to the energy loss of the recoils in the gas
Reaction product full-energy peak
“Wall effect’ continuum
Deposited energy
Low-energy event cut

## Slide 70
Rem counters
Electronic
3He counter
PE
Cadmium absorber
Bore hole
Polyethylene
BF3 tube
Boron plastic
Studsvik 2202D
Berthold LB6411 (also LB6411Pb)
3He counter
Tungsten layer
Boron plastic
Eberline WENDI-2
MAB SNM500(X)

## Slide 71
Environmental monitoring
Active monitoring
  Ambient dose rate
  Water contamination
  Airborne contamination
  Weather parameters
  Gate monitors
Passive monitoring
  Thermoluminescent dosimeters placed in the environment

## Slide 72
Stray radiation
Air
Water
Other environ-
mental samples
Environmental monitoring at CERN

## Slide 73
Operational radiation protection monitoring at CERN
REM counter
Gas filled, high pressure ionization chamber
Beam-on: to protect workers in areas adjacent to accelerator tunnels and experiments against prompt radiation (mainly neutrons, E < some GeV)
Alarm function
Air filled ionization chamber
Beam-off: to protect workers during maintenance and repair against radiation fields caused by decay of radionuclides (mainly gammas, E < 2.7 MeV)
No alarm function

## Slide 74
Operational radiation protection monitoring at CERN
Radiation Alarm Unit (RAMSES)
Reading of radiation levels directly available
Site Gate Monitor

## Slide 75
Passive environmental monitoring at CERN
Thermoluminescence dosimeters (TLD) inside a polyethylene moderators are used to monitor neutron and gamma doses in the experimental areas and in the environment.
TLDs are passive devices used CERN-wide to integrate radiation doses over a period of several months.

## Slide 76
Some textbooks
Glenn F. Knoll, Radiation Detection and Measurement, 4th edition
Frank H. Attix, Introduction to Radiological Physics and Radiation Dosimetry
Annals of the ICRP (International Commission on Radiological Protection)
http://www.icrp.org/publications.asp
ICRU publications, International Commission on Radiation Units and Measurements
http://www.icru.org/

## Slide 77
Supplementary material

## Slide 78
Periodic table of elements
219Rn (Actinion), 220Rn (Thoron) and 222Rn (Radon)
Notes: As a noble gas, radon is chemically and electrically inert, therefore after inhalation, it is immediately exhaled and it is weakly harmful in itself. However the radon daughter products attach to the ambient areosol, which may be inhaled and stick to the lung surface. Its importance in the exposure of human beings to terrestrial radiation is given by its transport from surface to atmosphere where its decay products may be inhaled. Radon tends to concentrate in enclosed spaces like underground mines or houses. Radon is the largest contributor to daily exposure of radiation.

## Slide 79
Decay chain of uranium
Precursor

## Slide 80
Worldwide radon risk
http://www.mclaughlincentre.ca/research/map_radon/Index.htm
Designed by J.M. Zielinski & H. Jiang

## Slide 81
The biological actions of radiation
Step | Time of appearance | Mechanisms
Physical | ~ 10-16 s | Energy deposition by ionisation and excitation of the atoms
Physico-chemical | ~ 10-10 s | Production of chemical compounds (ions radicals) which diffuse in the cell
Chemical | ~ 10-6 s | Production of molecular lesions in the DNA
Cellular | ~ hours | Lesions at cellular level and cell repair involvement
Deterministic effects | ~ weeks | Expression of dysfunctions at the tissues and organs level
Stochastic effects | ~ tens of years | Cancer induction and induction of heritable disorders

## Slide 82
Classification of radiological areas at CERN
Area | Dose limit [year] | Ambient dose equivalent rate |  | Sign
 |  | Work place | Low occupancy | 
Non-designated | 1 mSv | 0.5 µSv/h | 2.5 µSv/h | 
Supervised | 6 mSv | 3 µSv/h | 15 µSv/h | 
Simple | 20 mSv | 10 µSv/h | 50 µSv/h | 
Limited Stay | 20 mSv |  | 2 mSv/h | 
High Radiation | 20 mSv |  | 100 mSv/h | 
Prohibited | 20 mSv |  | > 100 mSv/h | 
Radiation Area
Controlled Area

## Slide 83
Classification of radiological areas at CERN
New signage scheme introduced in March 2021 to better visualize the level of radiological risk

## Slide 84
Job and dose planning
Use of work processes and special tooling to reduce time in work area
Staging and preparation of necessary materials and special tools
Maximization of prefabrication in workshop
Use of mock-ups for complex tasks
“Dry-run” of the activities using applicable procedures
Engineering, design and use of temporary shielding
Use of remote handling procedures
Lead shielding

## Slide 85
Protection methods against intakes of radioactivity
Isolating the radioactive substance
  use of containment
  use of glove boxes
  use of fume cupboards
Isolating the person
  do not eat, drink, or smoke in a supervised or controlled area
  wear protection gloves and laboratory coats
  use respiratory protective equipment

## Slide 86
Personal dosimetry at CERN
Continuous measurement of bg-dose (DIS-system) and integration of the neutron dose (track dosimeter)
Obligation to wear the dosimeter in supervised and controlled areas
Wearing of the dosimeter on the chest
Reading at least once a month at a reader (about 50 readers available on the site)
Possibility of checking the dose associated with a given operation (read the dosimeter before and after)
Dosimeter to be returned to the dosimetry service at the end of stay or at the end of a 12 month period

## Slide 87
Operational dosimetry at CERN
Obligation to wear an operational dosimeter in a controlled area
Continuous bg-dose measurement
Instrument: DMC
Display of Hp(10) (resolution of 1 µSv)
Dose alarm at 2 mSv
Dose rate alarm at 2 mSv/h
Audible detection signal (« bip »)
Record the dose before and after the operation

## Slide 88
Operational dosimetry at CERN
Before Accessing
Start your DMC
Access
Exit
Reading
PAUSE
DOSE
Type your # IMPACT

## Slide 89
Tyvek overall
Tape-sealed gloves
Overshoes
Respiratory Protective Equipment
For higher levels of contamination = higher risk
Personal protection equipment against contamination

## Slide 90
Personal protection equipment against contamination
Ventilated, filter and over-pressurized
Tyvek
Whole body protection from contamination

## Slide 91
Personal protection equipment against contamination
Individual protection equipment is mandatory for work in areas with contamination risk (cleaning operations, machining of radioactive material or equipment, …)