## Slide 1
Dr. Karie Badgley
ASP 2024- Morocco
Fundamentals of Particle Accelerators I

## Slide 2: Fermilab

## Slide 3: Fermilab

## Slide 4: Fermilab

## Slide 5: Muon Experiments

## Slide 6: PIP-II
Upgrade to accelerator to enable experiments such as DUNE

## Slide 7: Overview
Why accelerate particles
A bit of accelerator history
Components of an accelerator
Magnets
Equations of Transvers Motion
  Weak Focusing
Matrix Representation
Strong Focusing
Betatron motion

## Slide 8: Accelerators Worldwide
IAEA.org
Accelerator-Based Neutron Sources
Boron Neutron Capture Therapy (BNCT) facilities
Electrostatic Accelerators
Synchrotron Light Sources
X-ray Free Electron Laser Sources

## Slide 9: Accelerator Applications
Cathode ray tube TVs
Notes: Not only for particle physics and research

## Slide 10: Accelerator Applications- Medicine
Of the ~35,000 accelerators worldwide, roughly half are medical
Proton Therapy
Imaging
Isotope Production
Device Sterilization
samsunghospital.com
www.triumf.ca
Looking to replace ethlylene oxide and cobalt-60 with x-rays from electron beams
Fnal.gov
Mo-99 to Tc-99m
Reduce dose to surrounding healthy tissue

## Slide 11: Accelerator Applications- Security

## Slide 12: Accelerator Applications- Energy/Environment
Transmute long lived nuclear waste
Subcritical - Safe
Produce power
Close nuclear fuel cycle

## Slide 13: Accelerator Applications- Energy/Environment
…and so many more!
Wastewater treatment
High energy electron to break down pollutants
Accelerator on a truck
Use electron beam to resurface road

## Slide 14: The Accelerator is Born
1919 Ernst Rutherford called for “copious supply” of particles more energetic than produced by natural radioactive sources
1924 Gustav Ising developed the concept of a linear particle accelerator (Linac)
Wideröe, Über ein neues Prinzip zur Herstellung hoher Spannungen, Archiv für Elektrotechnik 21, 387 (1928)
1928 Rolf Wideröe builds the first linac in Aachen, Germany
  He first tried to build a betatron, but when that was unsuccessful, switched to a linac for his thesis
Notes: Using radioactive decay(alpha particles) of radon to discover atomic nucleus

## Slide 15: Livingston Plot
It was estimated in a 2014 Symmetry article that there were over 30,000 operating particle accelerators
In his 1954 book, Stanley Livingston noted that advances in accelerator technology allowed a factor of 10 increase in energy every 6-7 years
Laboratory energy of particles colliding with a proton at rest to reach the same center of mass energy
https://www.symmetrymagazine.org/article/october-2009/deconstruction-livingston-plot

## Slide 16: Units
1 eV= energy of a particle when accelerated across a 1 V potential
Particle | Rest Mass, kg | Rest mass, eV/c2
Electron, |  | 
Proton, |  | 
Particle | Rest Mass, kg | Rest mass, eV/c2
Through the relationship between mass and energy, the rest mass can also be expressed in terms of eV

## Slide 17: Relativity Review
Momentum
Total energy
Kinetic energy
Particle velocity
Speed of light
non-relativistic
relativistic
When we refer to the energy of a particle, it is the kinetic energy
Rest mass

## Slide 18: Anatomy of an Accelerator
Source
  Electrons
  Protons
  Ions
Field emission - strong E field to induce emission
Thermionic- heated cathode
www.thermofisher.com
Photo emission - light to produce electrons through photoelectric effect
www.sciencedirect.com
Ion source – electron ionization, plasma, …
wikipedia.org
Charged particles

## Slide 19: Electromagnetic force on a charged particle
Lorentz Force:
Force from the Electric field is the direction of particle velocity
  Used to accelerate the particle in the direction of the E field
Force from the magnetic field is perpendicular to particle velocity
  Used to bend and focus the particle
0
q

## Slide 20: Electromagnetic force on a charged particle
Loretnz Force:
Magnitude of Force
  Force from magnetic field scales with velocity
  Velocity of high energy particle ~3x108 m/s
  Using a high E field of 1 MV/m and medium B field of 1 T
  the force from the B field will be ~300 times stronger

## Slide 21: Anatomy of an Accelerator
Source
  Electrons
  Protons
  Ions
Electric Field
  Electrostatic(DC)
  Time-varying(AC)
More on this when we get to longitudinal motion next lecture
A

## Slide 22: Anatomy of an Accelerator
Source
  Electrons
  Protons
  Ions
Electric Field
  DC
  AC
Magnets
  Dipole
  Quadrupole
  Sextupole
  …

## Slide 23: Types of magnets
Dipoles – bending (transport, energy selection…)
Quadrupoles - focusing
Sextupoles - correction
Combined function
Correctors
Septa
Kickers
Solenoids
Less common/specialty magnets

## Slide 24: Magnetic Field Harmonics
Plugging in , it takes the form:
where is the reference field, the coefficients and correspond to normal and skew terms, and n gives the order of the pole
n=1 corresponding to a dipole, n=2 a quadrupole, n=3 a sextupole…
More slides in the backup if anyone is curious about this
The magnetic field can be found from the expansion*:

## Slide 25: Dipole (two pole, n=1)
Equate real and imaginary parts:
C
“Normal”: C=real, =0
“Skew”: C=imaginary, =0
Force?

## Slide 26: Dipoles
Dipole (FNAL)
Window frame dipole
H dipole

## Slide 27: Dipoles
C dipole
Muon g-2

## Slide 28: Quadrupole (four pole, n=2)
The quadrupole field varies linearly with the distance from the magnet center. It focuses the beam in one direction and defocuses in the other. An F or focusing quadrupole focuses the particle beam along the horizontal plane.
Skew, C is imaginary:
Normal, C is real:
Gradient (T/m)
Force?
Notes: Can get net focusing

## Slide 29: Quadrupole
ALBA SR Quadrupole
Fermilab Quadrupole
Panofsky Quadrupole
Notes: Focus only in one direction

## Slide 30: Sextupole (six pole, n=3)
The sextupole field varies quadratically with the distance from the magnet center. It’s purpose is to effect the beam at the edges. An F sextupole will steer the particle beam toward the center of the ring.
Note that the sextupole also steers along the 60 and 120 degree lines.
Normal, C is real:

## Slide 31: Sextupole
ALBA SR Sextupole
Sextupole (FNAL)

## Slide 32: Optics Analogy
Dipole
Quadrupole
Incoming beam
High energy
Low energy
Sextupole
Desired focus
Low energy focus
High energy focus

## Slide 33: Anatomy of an Accelerator
Source
  Electrons
  Protons
  Ions
Electric Field
  DC
  AC
Magnets
  Dipole
  Quadrupole
  Sextupole
Vacuum system
Power Supplies
Cryogenics
Beam diagnostics
Control system

## Slide 34: Equations of Transverse Motion
0

## Slide 35: Motion in a uniform B field
In terms of momentum,
0
Magnetic rigidity
How hard a particle is to deflect [T m]

## Slide 37: Equations of motion
Particle motion will be expanded about the ideal or design trajectory (, )
Reference frame:
x : horizontal
y : vertical
s : longitudinal-along the ideal trajectory(x=y=0)

## Slide 38: Equations of motion
Particle motion will be expanded about the ideal or design trajectory (, )
Radial acceleration:

## Slide 39: Equations of motion- Horizontal
is the radius and is constant

## Slide 40: Equations of motion- Horizontal
so we can do a Taylor expansion

## Slide 41: Equations of motion- Horizontal
Divide by and multiply the r.h.s. by

## Slide 42: Equations of motion
We can also do a Taylor expansion of the field about the reference orbit if we assume is small
Define the gradient

## Slide 43: Equations of motion - Horizontal
Convert from t to s

## Slide 44: Equations of motion - Horizontal
We can define
and

## Slide 45: Equations of Motion - Vertical
A similar treatment of the vertical motion yields
We can define

## Slide 46: Quick Aside on Springs
The form of this equation should look familiar
Recall Hooke’s law for a mass, m, on a spring, k

## Slide 47: Solutions to the Equations of Motion
These look like our familiar harmonic motion equations with known solutions of the form:
Vertical:
Horizontal:

## Slide 48: Matrix Representation
The constants A and B can be found from initial conditions

## Slide 49: Matrix Reminder

## Slide 50: Matrix Representation
These equation can now be expressed in matrix form

## Slide 51: Horizontal Focusing
For , this is focusing
For , this is defocusing

## Slide 52: Weak Focusing
Fields of this shape lead to focusing when
Define a field index

## Slide 53: Weak Focusing
Several early machines relied on weak focusing
Cyclotrons relied on the uneven field between poles
  First cyclotron built by
  Ernest Lawrence in 1930, 4” diam.
The Betatron, first built by Donald Kerst in 1940, uses this field shape
In 1943, Marcus Oliphant develops the idea for the synchrotron
  The most famous weak focusing was the Bevatron built at Berkely in 1954, led to the discovery of the antiproton( Nobel Prize)

## Slide 54: Drift Space
For , this is just a drift space of length
Slope hasn’t changed

## Slide 55: Thin Lens Approximation
For a focusing quadrupole of length L
If the focal length is much longer than the length of the quadrupole
We can rewrite the focusing and defocusing matrices as:

## Slide 56: Focusing Thin Lens
Initial position hasn’t changed
Slope changed

## Slide 57: Sector Dipole Bend
Particle trajectory is perpendicular to the dipole edge
Horizontal plane:
Vertical plane:
If
r = bending radius
q = bending angle
Looks like drift

## Slide 58: Transfer Matrices
A simple beam line can now be constructed by combining these elements as a product of the matrices
From , the final position and divergence of the particle are
The elements of the transfer matrix can be referenced with the following notation:

## Slide 59: Strong Focusing
A common combination is a focusing(F) quadrupole followed by a drift, then a defocusing(D) quadrupole, and another drift. Often referred to as FODO or doublet
The result of this doublet, no matter the order FODO or DOFO, results in a net focusing in the horizontal and vertical direction
Strong focusing also has tunes greater than 1

## Slide 60: FODO
F
D
L
L
The particle moves from left to right, first encountering the F quadrupole, so we apply that matrix first, and so on
This is only for the x or y, the sign of the quadrupole will need to change for the other plane

## Slide 61: Periodic
We will build our accelerator out of cells which are periodic such that:
C is the length of a cell, could be circumference of a circular machine or the length of a FODO cell

## Slide 62: Twiss Parameters
The equations of motion found previously:
If K = constant => motion of harmonic oscillator
If K varies with s : Hill’s equation (well studied D. E.)
The solution of the Hill equation is given by:
Constants of integration
+ )
The constants can be distributed and the solution written:

## Slide 63: Twiss Parameters
As before, solving for initial conditions of at
Matrix for propagation over one period,
Phase of particle’s oscillation advances by

## Slide 64: Twiss Parameters
We can define new variables
The phase advance becomes:
are the Twiss parameters

## Slide 65: Twiss Parameters
The functions can also be transformed using the elements of the transport matrix
The matrix simplifies to:
or even more succinctly to:
phase advance over C

## Slide 66: Betatron Motion
We can now describe the particle motion or oscillation
Betatron function defines the beam envelope, similar to wavenumber
Deviation from nominal in one plane
Phase advance
Phase advance in one turn “Betatron Tune”
Small –lots of oscillations
Large –few oscillations

## Slide 67: Betatron Oscillation
Sinusoidal motion in vertical and horizontal are known as betatron oscillations
The betatron function represents a bounding envelope to the beam motion, not the beam motion itself
Particles oscillate around the closed orbit, a number of times which is determined by the betatron tune

## Slide 68: Computer Codes for Accelerator Design
The calculations with multiple elements can get complex quickly, so we can turn to computer codes
MAD-X is one of the standard codes, but there are many others
E. Prebys using g4beamline

## Slide 69: Beam Envelope
E. Prebys using g4beamline

## Slide 70: Tune
Why is the tune so important?
If not carefully chosen, it can lead to harmful resonances which in turn can lead to beam blow-up
Integer values should be avoided
Coupling between the x and y motion can also result from magnet or alignment errors
Coupling tunes to avoid:
  Integer sum
  Half integer tunes
  Walknsaw resonance
    ,
  Other higher order
Tune diagram showing the first(red), second(blue), and third(green) order resonances

## Slide 71: To be continued…

## Slide 72: Bonus Slides

## Slide 73: Laplace’s Equation
In a region free of currents and permeable materials, two dimensional magnetic fields can be derived from Laplace’s equation
Any analytic function of a complex variable satisfies Laplace’s equation

## Slide 74: Complex Functions
A complex function is analytic if it converges with its power series in a domain D. To be analytic, the real and imaginary parts of the function must obey the Cauchy-Riemann equations.
Augustin Louis Cauchy
French 1789-1857
Bernhard Riemann
German 1826-1866
Notes: Analytic definition- Function which can locally be expressed as a convergent power series

## Slide 75: Analytic Complex Function
:

## Slide 76
Vector potential
Using , we can define a vector potential such that
Adding a gradient to this potential () still satisfies
Scalar potential
For charge and magnetic material free regions, and we can define a scalar potential
0

## Slide 77: The function of a complex variable
A : Vector potential
V : Scalar potential
0 (Coulomb gauge)
A satisfies the Laplace equation!
V also satisfies the Laplace equation!
The complex function must also satisfy the Laplace equation
Notes: In a region with no sources, must satisfy laplace equation

## Slide 78: Fields from the 2D function of a complex variable
:

## Slide 79: Fields from the 2D function of a complex variable
,

## Slide 80: Vector Operations
Scalar “dot” product
Vector “cross” product
Resulting vector perpendicular to the plane formed by A and B

## Slide 81: Differential Operators
  Grad operator
  Gradient
  Divergence
  Curl

## Slide 82: Maxwell’s Equations (in vacuum)
Gauss’s law
Faraday’s law
Ampere’s law
James Clerk Maxwell
Scottish 1831-1879

## Slide 83: Gauss’s Law
The total electric flux through a closed surface is equal to the total (net) electric charge inside the surface, divided by
No known magnetic monopoles

## Slide 84: Faraday’s Law
The integrated electric field around any closed loop is proportional to the rate of change of the magnetic flux passing through the loop

## Slide 85: Ampere’s Law
The current passing through a surface is equal to the line integral of the B field around that closed surface
“Displacement current” in charging capacitor for example
Enclosed current
I
B
B